## Slide 1: TSVV15 programme – focus on PDT relevant reduced models
F. Imbeaux, R. Coosemans, P. David, F. Jaulmes

## Slide 2: The main principles
The present state of the community is that Pulse Design Tools have been developed by some experiments and used mostly for that experiment.
The new TSVV15 project consists in evolving from this situation to a more coordinated and harmonised landscape, by porting the existing tools to different experiments (task 1), develop interoperable components and framework that can benefit to all PDT prototypes (task 2 and 3), with a specific effort until the end of 2025 on transport+free boundary applications (task 4).
Maximise the mutualisation of modules (e.g. transport, fuelling, H&CD, equilibrium), coupling techniques and infrastructure solutions
Apply the tools to multiple experiments and benchmark them
Define a possible convergence strategy for the next period (2026-2027)
IMAS interfaces

## Slide 3: Some orders of magnitude for a typical Pulse Design run
Simulator time step : constrained by the communication time between Plant and the Plasma Control System: typically 10-3 s to control the plasma vertical instability
Pulse duration simulation: typically 10 s for a meaningful ITER plasma segment (i.e. with significant evolution of equilibrium and current profile) – PDT often used to design small segment – checkpointing/restart capability mandatory to assemble a full pulse
 Number of time steps : 104
Reasonable waiting time for a human to get a PDT result : 102 s – can be extended to 103 s with a good cup of coffee
 Wall clock time for a time step: 10-2 to 10-1 s
Transport and equilibrium must be evaluated within this time scale – can be reached with present day tools with some further optimization
Source terms will require similar time scales or be evaluated less frequently
Optimize data transfer between components
Possibility to increase the simulator time step by not solving for the vertical instability in the Grad-Shafranov solver but check it continuously with a linearized model. Works better in boring flat top phases than in phases with large transient events

## Slide 4: Task 2 overview : Development of Reduced Models and Workflow (not covered by other TSVVs)
The TSVV-15 task 2 will support the development and/or validation of new surrogate models that fill-in the gaps identified within current PDT frameworks, namely:
  Heating and current drive systems: Validation of model of EC and NBI deposition, interaction of NTM-EC wave (2 models will be developed and tested)
  Plasma fuelling and SOL-divertor description: Surrogate model for pellet injection (1 model), SOL neutrals description, model for plasma density and integration into density feedback, improvement of divertor model and real-time exhaust model (3 models)
  MHD and transport for accurate power balance: Prediction of NTM onset, surrogate model for prediction of no-wall beta limit and of error field induced locked-mode threshold (1 model)
Milestone: For each new module, finalisation of complete physics models / databases / datasets (learning+testing) for at least one machine - March 2025.
Deliverables:
  D2.1: interim report on the task 2 activities – December 2024
  D2.2: successful simulation of the given functionality (within given machine / experimental parameters) in a single PDT prototype for all models - October 2025
  D2.3: evaluation of the relevance of the various reduced models, aiming at merging their functionalities to have a single model for each physics topic - December 2025

## Slide 5: Task 3 overview : Design the PDT framework for integration of modules provided by other TSVVs
Reinforce synergies i) between works proposed by the different teams in TSVV-15, ii) between TSVVs and iii) with external activities
  Develop synergies with other TSVVs (in particular TSVV11)
    Discussion of what can be simplified for performance / what cannot be simplified for reliability
    Find out what reduced model strategy already exists in the other TSVVs, and what we could steer together
    We are just starting the TSVV15 activities, and eager to find out how to work together

## Slide 6: Task 1 overview : Demonstration of PDT prototype (porting at existing machines)
Application of PDT prototypes to new machines
    inform which parts of the physics need refinement and/or machine-specific tuning
    test of interoperability
IMAS (for input and output of the PDT at least)
    ease comparison of different PDT prototypes on different machines
    ease possible further integration
Deliverables:
  D1.1 interim report on task 1 activities - December 2024
  D1.2 PDT prototype (Fenix, ASTRA-MEQ-controller) validated for existing TCV data and ready for use for new discharges – July 2025
  D1.3 PDT prototype (METIS/RAPTOR-MEQ) validated for existing COMPASS data, and ready for use on COMPASS Upgrade - December 2025
  D1.4 PDT prototype (METIS-MEQ/NICE) validated for existing RFX-MOD data, and ready for use on RFX-MOD2 - December 2025

## Slide 7: Task 4 overview : Magnetic Equilibrium and Control for PDT
Group of codes for free boundary evolution, including (some) transients
Different initial targets for each group (connection to kinetic code, add breakdown phase, speed up,…)
Using existing code and ongoing development, but with the emphasis on interoperability (see also task 3)
Codes will be applied to at least one more device than the one it was originally made for
Deliverables:
  D4.1a Coupling between breakdown and early ramp-up for DYON-FIESTA & CREATE-BD – Dec. 2024
  D4.1b Coupling between magnetic codes and kinetic codes for NICE-METIS & RAPTOR-FBT – Dec. 2024
  D4.2 Test run with inputs and outputs for each code on their ‘home’ device – July 2025
  D4.3 Application of each code to a ‘foreign’ machine using D4.2 for comparison and cross-validation – Dec. 2024