## Slide 1
Overview of HL-3
Lijun CAI
on behalf of HL-3 Team
Southwestern Institute of Physics, CNNC
Karlsruhe, Germany，Mar.19，2024

## Slide 2
01
Introduction of HL-3 Tokamak
CONTENTS
02
HL-3 upgrades
03
Recent milestones and experiments
04
DT operation plan
05
Summary and outlook

## Slide 3
Introduction of HL-3 Tokamak
01

## Slide 4
HL-2M renamed as HL-3
Mar, 2019 | Tokamak assembly began
Oct, 2020 | Assembly complete
Dec, 2020 | First plasma
Mar, 2021 | Project passed the Acceptance Test
HL-3 tokamak (known as HL-2M before) constructed in Chengdu, 2020
HL-3 was officially named at the ZGC Forum in Beijing in May, 2023
Notes: HL-3创新成果入选2023年中关村论坛成果发布会“20大重大成果”

## Slide 5
Main parameters | HL-3 | HL-2A
Major radius, R | 1.78m | 1.65m
Minor radius, a | 0.65m | 0.4m
Aspect ratio | 2.8 | 4.1
Plasma current, Ip | 3 MA | 0.45MA
Toroidal magnetic field, Bt | 3 T | 2.8T
Elongation | >1.8 | <1.3
Plasma Volume
~40 m3
Ion Temperature
150 million degree
Plasma Current
3 MA
n × Ti × τE
~1021 m-3·keV·s
Parameters of HL-3

## Slide 6
ITER-related scenarios, such as baseline H-mode, hybrid & steady state; high-performance operation regimes toward fusion reactors, such as N >3, high density with Greenwald fraction >1, etc.
ITER-related key plasma physics and technologies, including EP / VDE / NTM / ELM control, disruption alerting & mitigation, etc.
Advanced divertor configuration concept and physics，test and validation of high heat flux PFCs.
D-T fusion experiments to explore burning plasma physics and technologies.
Addressing critical physics and technology issues for ITER & fusion reactors
Mission of HL-3

## Slide 7
ITER
Support ITER
Support fusion reactor design and construction
Fusion Reactor
HL-3
Mega-ampere plasma current operation
  High current → Increase plasma density and energy confinement time
  Fusion Reactor：
Highly deformable, flexible plasma configuration
  Strong shaped SN，DN configuration
  Advanced divertor configuration，SF, Tripod, Negative Triangular
Powerful plasma heating/current drive capability
  NBI+ECRH＋LHW＋ICRF ，Total power ~44MW
  ECCD injection Angle real-time feedback control, LHCD spectrum adjustable
Flexible heat flow and particle flow control
  The geometry is compatible with a variety of advanced divertor configurations
  Active cooling, a single ring cryogenic pump for deuterium pumping speed up to 38m3/s
Physical research is flexible
  The device is compact and thus plasma is more accessible
  128 Windows can be used for the flexible arrangement of high spatiotemporal resolution diagnosis and operation control system
Characteristics of HL-3

## Slide 8
Ip(MA)/ Bt(T) | 2.5/2.2 | 2.5/2.2 | 2.5/2.2
κ/δ | 1.8/0.5 | 1.8/0.5 | 1.8/0.5
a/R(m) | 0.65/1.78 | 0.65/1.78 | 0.65/1.78
fG | 0.6 | 0.6 | 0.5
PNBI/PEC/PLH | 15 /8 /2 | 15 /8 /4 | 15 /8 /4
XEC/XLH | 0.3 /0.7 | 0.3 /0.7 | 0.3 /0.7
q95 | 3 | 3 | 3
βp | 0.98 | 1.00 | 0.95
βN /4li | 2.8 /3.6 | 2.9 /3.5 | 2.8 /3.4
fBS /fni | 0.26 /0.32 | 0.28 /0.35 | 0.28 /0.37
Te0/Ti0 (keV) | 8.5/9.2 | 8.7 /9.4 | 9.2 /11
Teped/Tiped (keV) | 1.5 /1.4 | 1.6 /1.5 | 2.2 /2
neped/nesep (1e19) | 7.3 /4.1 | 7.3 /4.1 | 5.4 /2.9
Wth (MJ) | 3.3 | 3.5 | 3.3
H98(y,2) | 1 | 1 | 1
n(0)Ti(0) (1e19m-3skeV) | 18.0 | 18.4 | 17.2
Ti0 >10keV, at fG=0.5 (linear density 9.4×1019 m-3)
The fusion triple product can reach the order of 1020 m-3skeV
βN ~ 3
Plasma parameter evolution and flat-top temperature density profile (Ip=2.5MA,Bt=2.2T,Paux=27mw, fG=0.5)
Scenario of high parameter plasma

## Slide 9
Ip(MA)/ Bt(T) | 1.4/2.2 | 1.0/2.0 | 1.0/2.0
κ/δ | 1.8/0.5 | 1.8/0.5 | 1.8/0.5
a/R(m) | 0.65/1.78 | 0.65/1.78 | 0.65/1.78
fG | 0.47 | 0.5 | 0.5
PNBI/PEC1/PLH (PEC2) | 10 /5 /(2) | 6 /7 /(1) | 6 /6 /3
XEC/XLH | 0.34 /(0.28) | 0.4 /(0.2) | 0.3 /0.7
q95 | 5.5 | 4.8 | 4.7
q0 / qmin | 1.10 /0.80 | 1.10 /1.00 | 0.93 / 0.88
βp | 1.3 | 1.7 | 1.6
βN /4li | 2.3 /3.8 | 2.5 /3.9 | 2.4 /3.4
fBS /fni | 0.33 /0.76 | 0.40 /0.86 | 0.41 /0.89
Te0/Ti0 (keV) | 8.4/9.2 | 6.7 /6.1 | 6.5 /5.8
Teped/Tiped (keV) | 1.0 /0.87 | 1.2 /0.86 | 1.3 /0.89
neped/nesep (1e19) | 3.9 /1.1 | 2.7 /1.1 | 2.5 /1.3
Wth (MJ) | 1.3 | 0.85 | 0.82
H98(y,2) | 1.05 | 1.1 | 1.03
Ip=1.4MA, The heating and current waveforms
Plasma temperature, density, safety factor and current profile
fG~0.5 , NBI+ECRH&CD+ LHCD，Ip=1.0~1.4MA , Hybrid scenario
fBS : 30%~45%,fni :70%~90%, N ~2.5, H98(y,2)~1.1
Hybrid scenario with MA plasma current

## Slide 10
Ip(MA)/ Bt(T) | 1.2/1.7 | 1.0/1.85
κ/δ | 1.8/0.5 | 1.8/0.5
a/R(m) | 0.65/1.78 | 0.65/1.78
fG | 0.5 | 0.73
PNBI/PEC1/PLH | 10 /5.5 /- | 1.5 /3.5 /4
XEC/XLH | 0.42 /- | 0.45 /0.6
q95 | 5.1 | 4.8
q0 / qmin | 1.0 /1.0 | 1.10 /1.00
βp | 1.8 | 1.9
βN /4li | 3.4 /4.0 | 2.3 /3.2
fBS /fni | 0.55 /1.00 | 0.63 /1.00
Te0/Ti0 (keV) | 7.5/12.0 | 4.0 /4.0
Teped/Tiped (keV) | 1.1 /0.79 | 0.57 /0.35
neped/nesep (1e19) | 2.9 /0.93 | 3.0 /1.0
Wth (MJ) | 1.3 | 0.95
H98(y,2) | 1.29 | 1.32
Reversed magnetic shear profile features
fBS>50% ，fni ~100%，H98(y,2)~1.3.
Flat magnetic shear
Diamagnetic shear
Full non-inductive with MA plasma current

## Slide 11
Heat flow width q : 1~10mm
In SN divertor, deposited target plate heat load >14MW/m2
Multiple advanced divertor configuration discharges, with MA Plasma Ip
Standard snowflake
Tripod
Conventional single null divertor configuration
Snowflake Plus
雪花右减
Double null
Negative triangular
Snowflake minus
Advanced divertor configuration

## Slide 12
HL-3 Research Plan
  2020.12.04 first plasma
  Limiter/divertor configuration
II. Initial research
  Ip ≥ 1 MA
  H mode discharge
  Advanced divertor control
I. First plasma
III. Integrated research
IV. Extended Research
  Ip ≥ 2 MA
  Ti ~ 10keV
  Advanced scenario
  Heat/particle control
  Configuration control
  Triple product ＞1020m-3·keV·s
  Fusion reactor grade plasma operation and physics research
  Fusion reactor related integration scheme verification
  Fusion reactor related critical components/diagnostic tests
2025
2030
2020
We are here now
—— Key Facility for Fusion Science

## Slide 13
Machine Support
CS, TF and PF coils
Vacuum chamber
First Wall
Divertor
Central control room
Power Supply
Diagnostics
Divertor
Heating System
HL-3 device and auxiliary systems

## Slide 14
中心段
外弧段
5.1m
2.97 m
Adopting a topology structure where the TF coils are detachable and the PF coils are integrated within the TF coils
Improving the coupling efficiency between the magnets and plasma, enhancing the capability of physical research
TF coils
PF coils
CS coils
20-piece (140turns) detachable D-shaped toroidal field (TF) coil (190kA/turn).
A/B dual sets of built-in ohmic solenoid (CS) coils (220 kA)
16-piece integrated and built-in poloidal field (PF) coil (14.5~40 kA/turn)
Magnet system

## Slide 15
Vacuum vessel: D-shaped cross-section double-thin-walled structure with 20 sectors. Material: Inconel625 (high nickel alloy).
Precision manufacturing technologies: difficulty of forming, high design precision, complex structure and welding deformation control.
Main vessel: Height ~3.2m，Dia. ~ 5.2 m；
Volume：42m3
Shell thickness（5.4mm），No. of Ports:128
Baking Tem.(with hot nitrogen)：300℃
Limited Vacuum：3×10-6Pa
Vacuum vessel

## Slide 16
It is the first high power vertical-shaft 6-phase pulsed MG in China, and the overall parameters have reached the international advanced level.
Main parameters：
Rated capacity 300MVA
Rated released energy 1.35GJ
Rated speed 500r/min
Total weight 800t
Rotor weight 400t
Total height 15.5m
Diameter 10.6m
Output current, 29kA
Six-phase (double Y shift 30°)
The 300MVA/1.35GJ MG was developed to meet the requirements of high power and high stored energy of HL-3 Tokamak
300MVA Motor Generator

## Slide 17
HL-3 upgrades
02

## Slide 18
HL-3 upgrades and operation from 2022-2023
15 task forces
>1000 construction tasks of subsystems
>150 subsystem commissioning tasks

## Slide 19
First wall (new)
Lower divertor (new)
Toroidal Cryopump (new)
25 diagnostic systems (new)
RMP coils (new)
Magnetic measurement (upgrade)
Wall conditioning (upgrade)
Pellet injection (new)
Main upgraded Systems of HL-3

## Slide 20
Power supply (upgrade)
Cooling system (upgrade)
Cryogenic system (new)
PCS (new)
Baking system (upgrade)
ECRH、LHCD (new)
NBI (new)
Pumping system (upgrade)
Main upgraded Systems of HL-3

## Slide 21
Full carbon wall has been installed in 2022.
  Heat load: ~ 1MW/m2
  Accuracy: <±2 mm, height difference of adjacent graphite tiles: < ±0.25 mm.
Carbon-based first wall 2022.08.31
Stainless steel first wall
2020-2021
First wall

## Slide 22
Lower Divertor :
Flexible divertor configurations for heat and particle flux control.
Tolerable heat flux: 7 MW/m2 for t ≥ 5 s & Ip >1.8 MA.
High accuracy: ±0.25mm at striking point
Installation of the final Divertor component
TCP
Toroidal Cryopump (TCP)
Pumping speed: 50m3/s for H2, 200 W/4.5K
Welding pipes of TCP
Lower Divertor and Toroidal Cryopump

## Slide 23
More than 20 diagnostics installed for plasma control and measurements of profiles, impurity, heat and particle flux.
Parameter | Diagnostic techniques | Channels, Resolution
ne | FIR interferometer FMCW reflectometer THz interferometer | 5 chs, 0.1ms, 10 cm Edge,10 μs, 1 cm 1 ch, 306.9 GHz, 5 μs
Te | Thomson scattering ECE | 5 chs, 100 ms, > 1cm 60 chs, 5μs, 1.5 cm (~ 30m corrugated WG)
Ip, Vloop, Wdia, Rdis, Zdis | Magnetic probes | >10us
Impurity | VUV SX array Bolometer | 500-2000Å, 1 ch, 2 MHz Poloidally 6 arrays 80 chs, 50 μs, 2 cm
Images | CCD | tangential, topview, wide field in midplane
Divertor parameters | Target Langmuir probes | 516 chs, 1.8 cm
Fueling | SMBI | 10 Hz, duration 0.5 ms, midplane&divertors
Parameter | Diagnostic techniques | Channels, Resolution
ne | FIR interferometer FMCW reflectometer THz interferometer | 5 chs, 0.1ms, 10 cm Edge,10 μs, 1 cm 1 ch, 306.9 GHz, 5 μs
Te | Thomson scattering ECE | 5 chs, 100 ms, > 1cm 60 chs, 5μs, 1.5 cm (~ 30m corrugated WG)
Ip, Vloop, Wdia, Rdis, Zdis | Magnetic probes | >10us
Impurity | VUV SX array Bolometer | 500-2000Å, 1 ch, 2 MHz Poloidally 6 arrays 80 chs, 50 μs, 2 cm
Images | CCD | tangential, topview, wide field in midplane
Divertor parameters | Target Langmuir probes | 516 chs, 1.8 cm
Fueling | SMBI | 
Diagnostics

## Slide 24
Present Status
Coil number: 2x8=16
Dominant perturbation: n=1, 2, 4
Chirikov factor: σ>1.1
RMP current: 10kAt
Perturbation: 0~100 Gs
Next step
Power debugging
ELM/RWM Suppression Experiments
Error field compensation
…
RMP coils
n=4
n=1
Resonant magnetic perturbation (RMP)

## Slide 25
Gas puffing : 4 sets
SMBI: 3 sets, LFS, HFS, Divertor (Multi-channel, mixture gas with different ratio)
Pellet: 2 set, 1 for fueling (1mm, 60Hz, 100-300m/s), and 1 for shattered pellet injection
#1
#5
#10
#15
GP1
GP2
GP3
GP4
SMBI_1
SMBI_HFS
SMBI_DIV
Pellet
Pellet injection system
SMBI system
Fueling systems

## Slide 26
NBI:
5 MW (80keV/45A/5s for D2)
Co (2) & counter(1) injection
Injection direction: 38.6
NBI
Heating & Current Drive System(Now)
LHCD：
2 MW (3.7GHz)
Fully Active Multi-junction launcher
Peak parallel refractive index N//(0)= 2.25
ECRH：
2MW equatorial launcher(105 GHz/3s)
2MW upper launcher(105 GHz/3s)
0.5MW equatorial launcher(68 GHz/1s)
Equatorial launcher
Upper launcher

## Slide 27
Recent milestones and experiments
03

## Slide 28
4 Dec.,2020
First Plasma
>100 kA, >100 ms
feedback control
29 March,2023
Advanced divertor configuration
Tripod configuration
~0.6 MA
19 Oct.,2022
1MA plasma current
Ip, max= 1.15MA,
κ= 1.25, δ= 0.14
25 Aug, 2023
H-mode discharge
Ip：0.5MA-1MA
11 July,2023
1MA divertor discharge
1.05MA, ~750ms
Heating systems commissioning
Recent milestones of HL-3
Upgrade

## Slide 29
Two advanced divertor configurations, the snowflake-minus (SF-) and snowflake-plus (SF+) achieved for the first time in HL-3.
magnetic surface broadening in the advanced configurations
increased contact area effectively reduced the heat flux
SN (red line, #1737)
SF (blue line, #1797)
Advanced divertor configurations

## Slide 30
The first discharge with 1MA plasma current and divertor configuration
July 11, 2023
1MA plasma current and divertor configuration

## Slide 31
Diverted plasma discharges (Ip ~ 1.1 MA) and k=1.5.
Flat-top q95 = 2.6 - 3.4.
1MA plasma current and divertor configuration

## Slide 32
Realization of H-mode 15 days after combined commissioning of NBI, ECRH and LHCD
First H-mode on HL-3
A solid foundation for high current H-mode operation

## Slide 33
H-mode operation achieved for the first time in HL-3
H-mode achieved with 0.5-1MA plasma current at total auxiliary heating power around 2.4 MW (NBI+EC+LHW)
1 MA H-mode discharge operated at q95 < 3 and qmin<1, with notable sawtooth and internal kink mode.
H-mode with plasma current>1MA

## Slide 34
H-mode Operation (Ip=0.5 MA)
H-mode Operation (Ip=1.0 MA)
Parameters | Shot 3331 | Shot 4077
Ip (MA) | 0.5 | 1.0
BT (T) | 1.7 | 1.6
R (m) | 1.75 | 1.79
a (m) | 0.54 | 0.62
ne (1019m-3) | 2.9 | 4.53
Poh (MW) | 0.22 | 0.45
Paux (MW) | 1.64 | 2.32
q95 | 4.6 | 2.8
H-mode with plasma current>1MA

## Slide 35
D-T operation plan
04

## Slide 36: D-T operation plan of HL-3 tokamak
Simulated by METIS
D：T=50:50
The JET DT operation experiment has been verified through METIS, and the experiment is basically consistent with the simulated fusion power.
Simulated by METIS, HL-3 has the feasibility to produce fusion power to 10 MW.
Fusion power produced by HL-3 has been simulated by METIS.
D-T operation of JET
Check the reliability of METIS
HL-3 3MA，3T
NBI power
ICRH power
Fusion power

## Slide 37
D-T operation plan of HL-3 tokamak
Ip>1MA，
Advanced divertor,
H mode
Ip~1.5MA ， Advanced divertor,
H mode
Pfus~1MW
Ip≥2.5MA
Bt≥2.2T
𝒏𝒊 𝑻𝒊 𝝉𝑬~ 1021
m-3·keV·s
Ti~10 keV
𝒏𝒊 𝑻𝒊 𝝉𝑬≥ 1×1020 m-3·keV·s；
βN>3
To demonstrate D-T plasma operation and advanced control with fusion power up to 10 MW on HL-3 tokamak.
Milestones
2025
Ti > 10keV
2027
First DT experiment
~2030
Fusion power up to 10 MW
Pfus~10MW
Dec
Dec
Dec
Dec
Dec
Dec
Dec
Dec

## Slide 38: Device upgrade plan of HL-3 tokamak
Heating and Current Drive power ：11MW--->44MW
Plasma current（Ip）and toroidal magnetic field(Bt ）：Ip≥2.5MA，Bt≥2.2T
Power supply system: 460MVA--->600MVA
Plasma control system：AI control
Diagnostics：diagnostics of fusion products, profiles, impurity, heat and particle flux
Tritium cycle and safety containment system
Radiation protection system
Divertor, first wall, cooling system, Cryogenic system，……

## Slide 39
Summary and outlook
05

## Slide 40
HL-3 Tokamak has the ability of burning plasma operation (ion temperature Ti>10KeV, plasma current Ip ~ 3MA). Various advanced divertor configurations can be tested, and high-performance plasma physics research can be done.
The installation of first wall, divertor, diagnostic systems, and auxiliary heating systems (ECRH, LHCD, NBI, total 11MW) is complete and commissioning is underway. The following milestones have been realized:
Divertor configuration with 1.2 MA plasma current
H mode confinement operation with 0.5-1.0 MA plasma current
snowflake divertor configuration
Next step: Further improve the heating power (to 44MW)and operation capability, achieve high performance plasma, and address critical physics and technology issues for ITER & fusion reactors .
Summary and outlook

## Slide 41
Experimental campaigns 2024-2025
1/3
20/6
31/10
30/4/2025
1st campaign
30/4
31/8
2nd campaign
3rd campaign
Experimental topics
Plasma control optimization
High Heating power commissioning
Advanced Scenarios and experiment
MHD control (Disruption, ELMs etc)
Divertor high heat flux control
Joint experiments are highly welcome!
1st campaign experimental conditions
Ip = 0.5~1.2MA, Bt =1.0~1.7T；ne=2~4 x1019/m3
ECRH ~1.2MW, NBI≥1.5 MW，LHCD ~0.5MW
Single null, snowflake divertor configuration
Ip≥1.6MA，Ti≥10 keV
Engineering
commissioning

## Slide 42
Thank you for your attention!
Lijun CAI
on behalf of HL-3 Team
Southwestern Institute of Physics, CNNC
Karlsruhe, Germany，Mar.19，2024