## Slide 1
Development of the DEMO plasma diagnostic and control system EU – China collaboration on CFETR and EU-DEMO Reactor Design
4th Technical Exchange Meeting
19-21 March 2024, KIT, Karlsruhe, Germany
Wolfgang Biel1,2 , M. Ariola3, F. Maviglia4 and contributors to EUROfusion WPDC and WPDES
1Institute of Energy- and Climate Research, Forschungszentrum Jülich GmbH, Germany
2Department of Applied Physics, Ghent University, Belgium
3Universita’ di Napoli “Parthenope”, Consorzio CREATE, Italy
4Eurofusion Technology Department
w.biel@fz-juelich.de, ariola@uniparthenope.it, Francesco.Maviglia@euro-fusion.org

## Slide 2: List of contributors
W. Biel1,2, E. Alessi3, M. Ariola4, M. de Baar5, C. Baumann1, M. van Berkel5, I. Bolshakova6, D. Borodin1, T. Bosman5, K. J. Brunner7,
M. Chernyshova8, P. David9, D. Dunai10, I. Duran11, S. Entler11, L. Giannone9, A. Gusarov12, S. B. Korsholm13, Y. Kost6, R. Luis14,
A. Malaquias14, O. Marchuk1, F. Maviglia18, E. Perelli Cippo3, A. Pironti15, A. Quercia15, J. Řeboun16, G. Renko17, N. Rispoli3, D. Sarajlic17, M. Siccinio9,18, A. Silva14, G. Tartaglione4, P. Turjanica16, W. Treutterer9, G. Verdoolaege2, S. Wiesen1,18, M. Zerbini19, H. Zohm9,18, et al.
1Institut für Energie- und Klimaforschung, Forschungszentrum Jülich GmbH, Germany
2Department of Applied Physics, Ghent University, Belgium
3ISTP-CNR, Istituto per la Scienza e Tecnologia dei Plasmi, Milano, Italy
4Universita’ di Napoli “Parthenope”, Consorzio CREATE, Italy
5DIFFER, Eindhoven, Netherlands
6Magnetic sensor laboratory, Lviv, Ukraine
7Max-Planck-Institut für Plasmaphysik, Greifswald, Germany
8IPPLM, Warsaw, Poland
9Max-Planck-Institut für Plasmaphysik, Garching, Germany
10EK-CER, Budapest, Hungary
11Institute of Plasma Physics, Czech Academy of Science, Praha, Czech Republic
12SCK CEN, Mol, Belgium
13DTU, Department of Physics, Lyngby, Denmark
14Instituto de Plasmas e Fusão Nuclear, IST, Universidade de Lisboa, Portugal
15Università degli Studi di Napoli Federico II, Consorzio CREATE, Italy
16University of West Bohemia, Research and Innovation Centre for Electrical Engineering (RICE), Czech Republic
17Cosylab, Ljubljana, Slovenia
18EUROfusion Power Plant Physics and Technology (PPPT) department, Garching, Germany
19ENEA, Fusion and Nuclear Safety Department, C. R. Frascati, Via E. Fermi 45, 00044 Frascati (Roma), Italy
EUROfusion work package “DEMO diagnostic and control” (WPDC)

## Slide 3: Main input assumptions for the development of the DEMO D&C system
  Pulsed DEMO tokamak as baseline
  Machine size ~ 1.5 times of ITER
  Plasma scenario with
    predominantly ohmic current drive
    confinement quality HH98y2 ~ 1
    high core radiation fraction but Psep ~ Pheat-Prad,core > PLH
    high plasma density with fully detached divertor plasma operation (lower single null)
    no ELMs / very small ELMs ( EELM/100)
  Vertical maintenance concept for blanket
    only limited access for diagnostics from the top side
  Large equatorial ports
    main access for diagnostics
Main DEMO parameters:
R0 ~ 9 m
a ~ 2.9 m
B0 ~ 5 T
Ptherm ~ 2 GW
Pel,net ~ 300…500 MW
tpulse > 2 h
See also C. Bachmann, ISFNT 2023; M. Siccinio et al. FED 2020

## Slide 4: Summary of the DEMO diagnostic and control concept
Control quantity | Operational limits | Diagnostics | Actuators + interactions
Plasma current / Edge safety factor q95 | safety factor limit (q95) | Magnetic diagnostics Faraday sensors | CS coils Auxiliary heating
Plasma position and shape, incl. vertical stability | Wall loads (FW and div.) Max. z / VDE disruption | Magnetic diagnostics MW reflectometry, ECE Neutron/gamma diagnostics IR polarimetry/interferometry Radiation power profile | PF + CS coils Auxiliary heating
Plasma edge density and temperature | Density limit Stable confinement Access for div. detachment | MW reflectometry, ECE IR polarimetry/interferometry Spectroscopy (pellet injection) | Pellet injection (fuel) Gas injection ECR heating
Fusion power | Wall loads (FW and div.) LH threshold | Neutron diagnostics Density and temp. measurement FW/blanket and div. power (for calibration only) | Auxiliary heating Pellet injection (DT ratio) Impurity gas injection PF+CS coils (shaping)
Power loss across the separatrix | Radiation limit LH threshold, divertor loads | Spectroscopy+radiation meas. Plasma heating power | Gas + Pellet injection Auxiliary heating
Divertor detachment and heat flux control | Divertor wall loads LH threshold | IR/VIS/UV spectroscopy Divertor thermo-currents Neutron flux, reflectometry | Gas injection (impurities + fuel) Pellet injection (fuel) PF coils
(MHD) plasma instabilities | Various | Reflectometry, ECE Radiation power measurements Neutron/gamma diagnostics IR polarimetry/interferometry Magnetic diagnostics | Auxiliary heating ECCD PF coils
Events (impurity ingress, component failure) | Various | All | All
Disruption mitigation | All | All | Matter injection
equilibr. control
kinetic control
Event control
See also W. Biel et al. FED 2022
Work in progress to define the
structuring and hierarchy of control
(supervisory control)
W. Treutterer, M de Baar, et al.
+ Collective Thomson Scattering

## Slide 5: Irradiation issues for diagnostic front-end components on DEMO
Typical fluence behind the blanket:
ITER: 1 GGy
0.1 dpa
DEMO: 1-10 GGy
0.5-5 dpa (for 5 fpy of operation)
(recent design iterations show smaller values)
Displacement damage / fpy
at inboard side
Neutron fluence behind the DEMO blanket may be 5…50 times larger than on ITER
 Move vulnerable components more away from the plasma / improve durability
(G. Vayakis,
ITER_D_26ZGC3)
Radiation effects on diagnostic components:
radiation-induced electromotive force (RIEMF)
temperature-induced electromotive force (TIEMF)
radiation-induced thermoelectric sensitivity (RITES)
radiation-induced absorption (RIA)
radio-luminescence
thermal conductivity decrease
volume changes (swelling)
…..
U. Fischer et al.,
FED 2016

## Slide 6: Durability of optical mirrors for DEMO: erosion/deposition due to CX neutrals (with gas target in the duct)
W. Biel et al. FED 2022, using the model by M. Z. Tokar, Nucl. Fusion 2018
Modelling of plasma-wall interaction
near a diagnostic duct (cylindr. geometry):
Elongated ducts with gas target (nD2 = 3e19 m-3) for 1st mirror protection
h/d > 20 for IR diagnostics (interferometry, thermography)
h/d > 28 for VIS spectroscopy
h/d > 30 for VUV spectroscopy
duct diametre d
duct length h
Mirror surface deposition per full power year:
Refined modeling started in 2022 using the ERO code
(C. Baumann et al., FZJ)

## Slide 7: WPDC concept for implementation of diagnostic front-end: Limitation of the design towards durable components; set back mounting positions
In front of blanket and divertor:
  No diagnostic components
Within blanket area/port area:
  Diagnostic ducts for spectroscopy, Prad, interferometry/polarimetry, neutron+gamma diagnostics
Diagnostic slim cassette (DSC):
  Metallic microwave antennae+waveguides within „diagnostic slim cassettes“
Behind the blanket/magnetic strips (MS):
  Magnetic sensors (metal+ceramic) & cabling within „magnetic strips“
Port plugs:
  Optical mirrors (metallic) and beam paths
  signal routing, penetrations (cables, tubes) and/or windows
Behind the divertor target:
  Implementation of sheath voltage or thermo-current measurement
  „Magnetic strip“ with some magnetic sensors
Ex vessel
  Detectors, cabling, fibres, …
equatorial
ports
vertical ports
lower ports
DSC
MS

## Slide 8: Equilibrium control
Main requirements:
Horizontal and vertical position of the current centroid remain within +/- 15 cm around nominal position
Minimum distance between separatrix and first wall in all poloidal locations always remains larger than 8 cm
Subsystem | No. sectors/ no. per sector
Inner vessel tangential pick-up coil | 4-8/30
Inner vessel normal pick-up coil | 4-8/30
Inner vessel flux loops | -/6
Inner vessel saddle coils | T.B.D./24
Diamagnetic loops | 4/1
Diamagnetic loop compensation coils | 4/1
Diamagnetic loop compensation saddles | 4/2
Fig.: Combined inductive+Hall sensor
Error estimation for centroid position:
∆B ~ 8 mT, ∆r = ∆Z ~ 1 cm
Main open issue:
Irradiation hardness of magnetic sensors
 Major R&D issue for the future
M. Ariola, A. Quercia, A. Pironti, I. Duran, I. Bolshakova, et al.
A. Quercia et al. NF 2022

## Slide 9: ‘Magnetic strip’ concept for integration of magnetics
Cable
looms
Cable structures
Cable
looms
Probe + cables detail
BB keys
(constraint)
VV attachment bosses
BB: 10-12 cm radial carving required
Cable routing
(limited space)
Divertor
11 probes
IB
25-26
probes
OB
22-23
probes
Full flux loops
Cable structures (UP)
25 cm (toroidal) x 8cm (radial)
Magnetics sensors
~60 probes (strip)
+ 6 full flux loops
to be integrated with
24 saddle loops
4+4 sectors
(redundancy included)

## Slide 10: Hall sensor development
Chart: Temperature [°C]
| 40 | 60 | 80 | 100 | 120 | 140 | 160 | 180 | 200 | 220 | 240 | 260
Bi | 329.4667 | 291.4417 | 256.8583 | 226.8583 | 200.6833 | 177.575 | 157.1917 | 139.4 | 123.4833 | 109.05 | 95.3917 | 83.1433
Sb2 | 113.05 | 111.38 | 107.27 | 102.97 | 98.48 | 93.863 | 89.096 | 84.235 | 79.27 | 74.237 | 69.211 | 64.161 | 59.179 | 54.245 | 49.427 | 44.766 | 40.311 | 36.126 | 32.125 | 28.521 | 25.186 | 22.14 | 19.43
Sb1 | 21.9158 | 21.0874 | 20.3347 | 19.5726 | 18.7979 | 18.0189 | 17.2253 | 16.4221 | 15.6011 | 14.7947 | 13.98 | 13.1884 | 12.3463 | 11.4726 | 10.6021 | 9.7366 | 8.9625 | 8.1882 | 7.3595 | 6.5911 | 5.8363 | 5.0911 | 4.3475 | 3.5905
Cr | 6.0366 | 5.9243 | 5.7497 | 5.5028 | 5.1842 | 4.8735 | 4.6699 | 4.5425 | 4.4714 | 4.4417 | 4.4373 | 4.45 | 4.4668 | 4.4852 | 4.505 | 4.5244 | 4.5483 | 4.5676 | 4.5818 | 4.5946 | 4.5967 | 4.6142 | 4.6153 | 4.619 | 4.6226 | 4.6262
Dia | 1.34 | 1.21
Au | 1.2234 | 1.1778
Mo2 | 0.91689 | 0.95005
Mo1 | 0.25224 | 0.23953
Ta | 0.13675 | 0.13413
Cu | 0.065714 | 0.067233
Antimony Hall sensor prototypes
Hall materials under investigation
18 mm
I. Duran, I. Bolshakova, et al.
DEMO in vessel
See also S. Entler et al. FED 2020
See also I. Bolshakova et al. NF 2017
Neutron fluence n/m2
Sensitivity [V/AT]
6.5 mm

## Slide 11: Equilibrium control simulations: loss of power event
Main requirements (repeated):
Horizontal and vertical position of the current centroid remain within +/- 15 cm around nominal position
Minimum distance between separatrix and first wall in all poloidal locations always remains larger than 8 cm
M. Ariola, A. Pironti, G. Tartaglione, et al.
Numerical simulation of equilibrium control
with and without in vessel control coils (CREATE)
See also
M. Ariola et al. FED 2019
G. Tartaglione et al. 2023 (submitted)
Feasibility of in vessel control coils under investigation
Controller | Minimum distance from wall | Maximum power
w/o fast radial circuit | 5.7 cm | //
w fast radial circuit | 10.8 cm | 26 MW

## Slide 12: Equilibrium control: microwave reflectometry
Main requirements (repeated):
Horizontal and vertical position of the current centroid remain within +/- 15 cm around nominal position
Minimum distance between separatrix and first wall in all poloidal locations always remains larger than 8 cm
A. Silva, R. Luis, et al.
Simulation of reflec-tometry performance
using the REFMUL* family codes 
Accuracy for gap determination better than 1 cm in most poloidal locations
F. da Silva et al 2022 JINST 17 C01017
F. da Silva et al, ISFNT 2023
J. Santos et al., ISFNT 2023

## Slide 13: Diagnostic slim cassette (DSC) integration with the Breeding Blanket (BB)
Waveguide extensions (routed through BB chimneys)
25 cm (toroidal)
DSC inboard and outboard segments in different vertical planes
Interfaces with the BB
  Sharing the BB First Wall (FW) and Back Support Structure (BSS)
  DSC integrated/attached to the BB segments
R. Luis, A. Malaquias, et al.
See also J. Belo et al. NF 2021

## Slide 14: Burn control: neutron camera for fusion power measurement
Main requirements:
Pedestal top density should remain at a level of 85% +/- 5% of the Greenwald density limit
Fusion power should remain within +/- 20% of the nominal value; variations above +/- 10% for < 20 seconds.
Separatrix power Psep should be controlled at a level of 20% above the LH threshold (to be refined)
Psep = P + Paux – Prad
Two instruments (n and g) to be located into the same structure with a camera (i.e. multiple LOS) structure (horizontal and vertical).
Active parts (i.e. detectors) to be placed outside the bioshield.
Detailed design work ongoing; main features include:
Gamma-ray detectors positioned behind neutron detectors
Neutron attenuator positioned in the LOS between n and g detectors
Easy access required for n detectors
Detector R&D started: stability of calibration to be validated
See also M. Cecconello et al. JINST 2019; L. Giacomelli et al. JINST 2022

## Slide 15: Burn control: Radiation power (Prad) measurement
Psep = P + Paux – Prad (scenario control and divertor control)
Plasma core radiation in the range of E > 1 keV
Detector R&D in preparation (GEM detectors)
Main requirements (repeated):
Pedestal top density should remain at a level of 85% +/- 5% of the Greenwald density limit
Fusion power should remain within +/- 20% of the nominal value; variations above +/- 10% for < 20 seconds.
Separatrix power Psep should be controlled at a level of 20% above the LH threshold (to be refined)
M. Chernyshova et al.
See also
M. Chernyshova et al.
JINST 2022

## Slide 16: Burn control: VUV spectroscopy and X-ray spectroscopy
VUV spectroscopy
Injected impurities concentration feedback for control (Ar, Xe, Kr)
Edge channels: Early detection of transient impurity ingress
X-ray spectroscopy
Impurity concentrations and ion temperature in core plasma
Crystals for Xe, (Kr) and W
Neutron streaming issue to be solved (caused by large duct diametre)
O. Marchuk, A. Krimmer, W. Biel, et al.
Spectrometers with gratings and detectors
Vacuum extensions
In-port mirrors (edge channels)
VUV spectroscopy

## Slide 17: Core density control: IR interferometry
Measurement of the line integrated plasma density, and vertical position during startup
Features:
Laser wavelength of 10/5 µm, (currently) dispersion interferometer
4 cm x 1 m beam ducts with gas target for protection of the plasma facing mirrors
Active environmental phase drift compensation and beam steering
Two variants under investigation:
Double-pass design with retro-reflectors
Single pass design with more windows
  much lower risk option
Major issues:
Mirror lifetime
Window lifetime
Long-term Laser stability
Alignment stability
Lifetime of beam steering components
See also
K. J. Brunner et al.; 2022; JINST 17 C04001
K. J. Brunner, G. Jereb et al.
n+3 port
n+4 port
n+5 port

## Slide 18: Burn control simulations under development
Main requirements (repeated):
Pedestal top density should remain at a level of 85% +/- 5% of the Greenwald density limit
Fusion power should remain within +/- 20% of the nominal value; variations above +/- 10% for < 20 seconds.
Separatrix power Psep should be controlled at a level of 20% above the LH threshold (to be refined)
FENIX tokamak flight simulator
code under development
ASTRA code coupled with model
for controllers, actuators and
diagnostics in Simulink
Shown here:
Plasma and control reaction on
missing pellets (MP)
Specific DEMO diagnostic and
actuator properties to be included
Integration of kinetic and magnetic
Control under way
E. Fable, P. David, F. Janky, et al.
See also:
F. Janky et al. FED 2017
C Wu et al. FST 2023

## Slide 19: Divertor (detachment) control
Main requirements (repeated):
Plasma at strike point should be strongly detached (T < 2 eV)
Pedestal top density should remain at a level of 85% +/- 5% of the Greenwald density limit
Separatrix power Psep should be controlled at a level of 20% above the LH threshold (to be refined)
IR/VIS/UV divertor spectroscopy is designed to provide signals for detachment control (power exhaust and burn control).
Main approach is the measurement of line intensity ratios of hydrogen or helium spectral lines
Optical design studies, CAD, first mirror lifetime studies and spectra modelling are ongoing.
SOLPS + collisional radiative modelling (CRM)  S. Wiesen et al.
Feasibility of these lines of sight has to be checked when changing the DEMO baseline
D. Dunai, C. Pastor, M. Cavedon,
Ch. Baumann, D. Borodin, T. Bosman, et al.

## Slide 20: Divertor (detachment) control (2)
Main requirements (repeated):
Plasma at strike point should be strongly detached (T < 2 eV)
Pedestal top density should remain at a level of 85% +/- 5% of the Greenwald density limit
Separatrix power Psep should be controlled at a level of 20% above the LH threshold (to be refined)
D. Dunai, C. Pastor, M. Cavedon,
Ch. Baumann, D. Borodin, T. Bosman, et al.
Modelling (SOLPS, CRM) and experimental investigations (on TCV) are ongoing to identify radiation features sensitive to detachment and viable for DEMO real-time control
SOLPS runs after
F. Subba et al. NF 2021
Te /eV
Te /eV
Emissivity / ph/sm2sr

## Slide 21: Divertor thermo-current measurement
Principle:
sheath voltage at divertor target depends on plasma temperature
Study on implementation on DEMO:
isolate coolant tubes against vacuum vessel
use coolant tubes as shunt resistor
implementation in each divertor target
Feasibility depends on durability of insulators against neutron irradiation and limit of current in water cooling pipes.
Low signal levels are expected.
A. Kallenbach et al., J. Nucl. Mat. 2001
L. Giannone,
G. Renko, et al.
See also S. El-Shawish FED 2020

## Slide 22: Power exhaust w-monoblock technology limits including sweeping
HF to coolant: In SS the CHF (pipe burn out) is reached in 5s, while the 10cm-1Hz sweeping is marginal, and the 20cm-1Hz allows 50% margin.
W armor temp.: In SS the W surface melt at ≈6s the CHF time, while in the sweeping cases it does not reach melting. In the 20cm-1Hz the temp. reaches 2000°C(> W-recrystallization: issue if kept too long).
CuCrZr pipe temp.: The pipe softening temperature of 350°C is reached in 2.7s in SS, and 8.6s in 10cm-1Hz seeping, while it is not reached for 20cm-1Hz.
tsurf (°C)
tpipe (°C)
HF (W/m2)
Critical Heat Flux
1)
2)
3)
melting
recryst.
soft./aging
Heat flux ramp from 10MW/m2 to 70MW/m2 in 10s (to mimic reattachment):
Experiment carried out in GLADIS shows unirradiated PFC functional integrity after 5000 pulses (≥1h at 1Hz) at equivalent 70MW/m2 (JH. You submitted to JNM)
No Sweep
Sweep 10 cm 1 Hz
Sweep 20 cm 1 Hz

## Slide 23: Summary of the DEMO diagnostic and control concept
Control quantity | Operational limits | Diagnostics | Actuators + interactions
Plasma current / Edge safety factor q95 | safety factor limit (q95) | Magnetic diagnostics Faraday sensors | CS coils Auxiliary heating
Plasma position and shape, incl. vertical stability | Wall loads (FW and div.) Max. z / VDE disruption | Magnetic diagnostics MW reflectometry, ECE Neutron/gamma diagnostics IR polarimetry/interferometry Radiation power profile | PF + CS coils Auxiliary heating
Plasma edge density and temperature | Density limit Stable confinement Access for div. detachment | MW reflectometry, ECE IR polarimetry/interferometry Spectroscopy (pellet injection) | Pellet injection (fuel) Gas injection ECR heating
Fusion power | Wall loads (FW and div.) LH threshold | Neutron diagnostics Density and temp. measurement FW/blanket and div. power (for calibration only) | Auxiliary heating Pellet injection (DT ratio) Impurity gas injection PF+CS coils (shaping)
Power loss across the separatrix | Radiation limit LH threshold, divertor loads | Spectroscopy+radiation meas. Plasma heating power | Gas + Pellet injection Auxiliary heating
Divertor detachment and heat flux control | Divertor wall loads LH threshold | IR/VIS/UV spectroscopy Divertor thermo-currents Neutron flux, reflectometry | Gas injection (impurities + fuel) Pellet injection (fuel) PF coils
(MHD) plasma instabilities | Various | Reflectometry, ECE Radiation power measurements Neutron/gamma diagnostics IR polarimetry/interferometry Magnetic diagnostics | Auxiliary heating ECCD PF coils
Events (impurity ingress, component failure) | Various | All | All
Disruption mitigation | All | All | Matter injection
equilibr. control
kinetic control
Event control
See also W. Biel et al. FED 2022
+ Collective Thomson Scattering

## Slide 24: Summary and conclusions
An initial concept for the DEMO plasma diagnostic and control (D&C) system has been developed
List of the main control issues and their allocation to measurements and actuators has been set up; structuring ongoing
Diagnostics were selected according to their robustness and coverage of control issues
Feasibility and performance of control procedures are being explored by means of simulations
Aiming to achieve reliable plasma operation on DEMO with high performance near operational limits
Key issues for the further development and diagnostic integration are:
  In vessel components are subject to extreme loads
  Allocation and plasma access are constrained by the needs for first wall integrity and optimization of tritium breeding
  Remaining uncertainties in the definition of plasma scenario and machine design