## Slide 1: Artificial Intelligence Application for DEMO Plasma Control
1Institute of Plasma Physics, Chinese Academy of Sciences, Hefei, China
2School of Nuclear Science & Technology, University of Science & Technology of China
3Shenzhen University, Shenzhen, China
4Massachusetts Institute of Technology, Plasma Science and Fusion Center
5Università degli Studi di Napoli Federico II
6Consorzio CREATE
*E-mail: bjxiao@ipp.ac.cn
Presented at 4th Technical Exchange Meeting
EU — China collaboration on CFETR and EU-DEMO Reactor Design
B.J. Xiao1,2,*
W.Y. Rui1,2, B.H.Guo1.3, Z.J. Liu1,3, C.G. Wan1, W.H. Hu1, C. Rea4, J. X. Zhu4, G. De Tommasi5,6, Y.H. Wang1, Y. Huang1, D.L. Chen1, Q.P. Yuan1, and EAST Team

## Slide 2
Outline
Conclusion and Discussion
03
Specific requirements for DEMO plasma control
01
Demonstration of AI solution in EAST
02
Plasma parameter/state estimation
Disruption prediction
Controller optimization

## Slide 3: Specific requirements for DEMO Plasma Operation Control
Ip
IPf
Magnetization
BD
Rampup shaping
Heating, CD and Flattop, fueling
Termination
Shaping
Event handling: Disruption prediction & mitigation, Stability control, Actuator/Diag. degradation
For DEMO:
Events must be avoided
Controllers must be robust enough with limited experiment time
Diagnostic may not as many as today or may be degraded
Control Solutions:
1. Events must be predicted, prevented, or soft-landing
2. Sufficient modeling to have good controllers before being tested in actual experiment
3. Reconstruction must be accurate enough in real-time under any cases.

## Slide 4: 研究方案
010101110101
SCALER
INPUT/Target
OUTPUT
Controller
Object
IP
RZ
Shape
profile
P
q”
MHD
Reconstruction
DAQ
Ip
B
Spectra
Te
ne
dB/dt
q”
Actuator
CD
Heating
PS
Fueling…
Challenges in plasma control
Limited, sharing
Indirect
limited
mm, sub-ms
coupling
3D structure,
non-linear,
MHD
Event handling, branching

## Slide 5: How to get physics quantities? An Example, eQ reconstruction
Diagnostics: Bps+ Fls + Ne.
G-S Solver by using GPU
Limitations: under limited or degraded diags? Consistency with more other diags? RT behavior?
1 full iteration: 300 us for 129*129 grids

## Slide 6: Controllers need complicated modeling
Controllers design: FF + Feedback
Maxwell + N+S
or F-P Eqs
+BI=CV
Y=CI+DV
For EM control,
I: Plasma current and its distribution
Coil currents (12 and more?)
Vessel currents and distribution
V: Commands to the coil power supply
An Example：Complexity of 3D passive structures
Simplified
Still gaps between the state space and the real world, controllers always need to be adjusted by experiments

## Slide 7
AI – a new way for tokamak control
Cross machine disruption predication, AL plasma shape control, plasma surrogate model
Data-driven plasma modelling
Surrogate model of simulator, control response, PDE solver
Advanced control algorithms
Reinforcement learning models
Self-adaptive control
Plasma state/parameter estimation
Disruption prediction
MHD mode recognition

## Slide 8: 研究方案
010101110101
INPUT/Target
OUTPUT
Controller
Object
IP
RZ
Shape
profile
P
q”
MHD
DAQ
Ip
B
Spectra
Te
ne
dB/dt
q”
Actuator
CD
Heating
PS
Fueling…
Ideal AI/ML for plasma control
Reconstruction
Controller

## Slide 9
Outline
Conclusion and Discussion
03
Specific requirements for DEMO plasma control
Demonstration of AI solution on EAST
02
Plasma parameter/state estimation
Disruption prediction
Controller optimization
01

## Slide 10
Surrogate NN Z model do well in REAL time
10
Magnetic measurement
Vertical displacement
Vertical instability growth rate
Equilibrium parameters
Motivation: Fast and accurate Z estimation for Z control
Method: BP neural network model was trained using magnetic probe measurement, offline EFIT calculated Z and TOK-SYS calculated Z growth rate
Surrogate models provide more reliable results than simplified linear physics model.
The surrogate models are deployed in the plasma control system to meet real-time computing demands.
The validation is obtained in EAST experiments.
Song H H, et al. [J]. Journal of Plasma Physics, 2023, 89(1): 895890104.
Liu B. N. et al., [J]. IEEE Transactions on Plasma Science, 2023.

## Slide 11
Integrated MHD modes recognizer using deep learning
The integrated MHD modes recognizer has been developed using deep learning on EAST
Accuracy rate > 98%
Identify MHD information：time, frequency & intensity
Recognizer Input
Dataset

## Slide 12
Outline
Conclusion and Discussion
03
Specific requirements for DEMO plasma control
01
Demonstration of AI solution on EAST
02
Plasma parameter/state estimation
Disruption prediction
Controller optimization

## Slide 13
CNN+LSTM predicted EAST disruption w/ TPR 95%
Feature extraction module(CNN) + Characteristic time learning module(LSTM)
1-D convolution: 1-D diagnostic features
2-D convolution: array diagnostic features (2-D features)
LSTM：time evolution information
The performance better than single algorithm (CNN，LSTM)
Testing Result: TPR (95.3%), FPR (8%)

## Slide 14
EAST plasma disruption prediction: transfer learning improves model extensibility
2019
2021
The lower C divertor has been replaced by W since 2021, some diagnostics have also been changed.
Previous model performance decreases (AUC~0.79)
Convolution attention module: channel attention module & spatial attention module
Transfer learning with a small amount of new data
The performance of all-metal wall is improved（AUC~0.93）
B.H. Guo, et al. Nucl. Fusion 63 (2023) 094001 (12pp)

## Slide 15
Cross-device plasma disruption prediction (EAST、DIII-D、C-Mod) (China-U.S. collaboration)
J.X. Zhu et al 2021 Nucl. Fusion 61 026007
hybrid deep-learning (HDL) disruption warning model developed based on convolutional and recurrent neural networks
Transfer learning：
Database of existing devices + new device L-mode --> New device H-mode discharges
Abnormal event detection

## Slide 16
EAST Density Limit Disruption Prediction and Experimental Validation based on Random Forest (China-U.S. collaboration)
W.H. Hu et al 2021 Nucl. Fusion 61 066034
Random Forest Disruption Predictor (DPRF)
Calculation time of DPRF is 200~300μs and satisfy the real-time disruption prediction.
Real-time disruption warning triggers the MGI system, effectively reduces the damage caused by disruptions.

## Slide 17
Outline
Conclusion and Discussion
03
Specific requirements for DEMO plasma control
01
Demonstration of AI solution on EAST
02
Plasma parameter/state estimation
Disruption prediction
Controller optimization

## Slide 18
Plasma Z instability characteristic may change during a shot => AI Z self-adaptive control
  Adaptive-LQR optimal controller for alternative plasma configuration (LSN/USN/DN/Limiter)
  State-space model calculation by using neural network surrogate model（1s->0.1ms）trained by rigid model calculation datasets
Z self-adaptive control with NN enhanced controllability
      Real-time self-adaptive control verified in EAST experiment with half in-vessel coil turns.
        Maximum κ~1.87 (#126611)
        Maximum γ~750/s (#126625)

## Slide 19
Data-driven approach proved robust in scenarios simulation
RL vertical position controller decoupled with plasma shape control
A RL-based Vertical Stabilization System for the EAST tokamak (China-Italy cooperation): better decoupling with shape
G. De Tommasi, American Control Conference, 2022
Reward：
A model-free agent trained with the Q-learning algorithm and interact with a state-space linearized model of the plasma and the surrounding coils dynamics
Blue： Exp. #92141 Red: RL model

## Slide 20: VS with Robust Adversarial Reinforcement Learning（RARL）
Vertical stabilization controller must avoid overcurrent with PF perturbations
12 PF coils with different amplitudes and frequencies: Impossible to exhaust
Adding adversarial during training to enhance the robustness
  RL-based adversarial (): Automatic Attempts to Attack Weaknesses
Env
PF controller
EAST
VS controller
observation
disturbance source
Agent
Adversarial
Environment Configuration
High amp. turb.
High freq. turb.
Adv. try different types of attacks during training

## Slide 21
RL-based feedback control of βp traces the target accurately in EAST experiment
  Profile response model by system identification
  Error integral and error model are included in reward function and training procedure
RL-based βp controlled well on EAST tokamak
#128847
#128849

## Slide 22
Outline
Conclusion and Discussion
03
How AI Benefits Plasma Control
01
AI Application in EAST Plasma Control
02
Plasma parameter/state estimation
Disruption prediction
Controller optimization

## Slide 23
Conclusion and Discussion
AI/ML approaches have been applied on EAST for establishing plasma simulation, estimation, control response models and optimizing controllers,
  Plasma parameter recognition surrogate model: equilibrium/MHD mode
  Implications to DEMO: more reliable and RT state/parameters recognition.
  Advanced control algorithms: RL/self-adaptive based vertical instability and profile control
  Implications to DEMO: Simplified/Sys identification model can train RL AI model to have better controllability with less requirements to actuators
  Event handling: Cross-device disruption prediction and mitigation
  Implications to DEMO: more confidence for disruption predication and thus avoidance/mitigations
More physics-oriented modeling database/codes to train AI model for control
More cross machine AI train for disruption avoidance and robust plasma control