## Slide 1
Evaluation of heat loads on the first wall in BEST
R. Ding, C.J. Li, M.Z. Lei, B.F. Gao, Y.F. Zheng, G.Q. Li, X.B. Peng, the BEST team

## Slide 2
Design of the first wall (FW) as shielding blanket
Outline of the FW design
  Poloidal contour profile fitting the magnetic configuration
  Blanket modules (BMs) as the FW: shaping design
  Radial location of the FW: heat loads Vs RF coupling
Heat loads on the FW
  SOL plasmas
  Charge-exchange neutrals
  Radiation
  Fast ion loss
  Transient heat loads
  Nuclear heating

## Slide 3
now
before
Poloidal blanket modules (BMs): 913
BMs design: one panel  two wings with 6cm slot
Radius of the FW (@OMP LFS): 4.95m  4.85m
Magnetic configuration optimization: gap between LCFS and FW @OMP: ~15cm
Slight change on the FW poloidal contour
Ripple: 1.5% 0.75% (ferromagnetic inserts)
Updates of the first wall (FW) design in BEST

## Slide 4
Shaping Design of the FW Panels
4
P.C. Stangeby Nucl. Fusion 51 (2011) 033008
The FW panels need to be shaped to protect the leading edges caused by radial misalignment (inter-BM 10 mm, intra-BM 0.3mm) and gaps (inter-BM 10 mm, intra-BM 60mm)
  Both toroidal (inter-BMs and intra-BM) and poloidal chamfering have been considered, respectively
  Initial chamfering dimensions: theoretical calculation (Nucl. Fusion 51 (2011) 103015) 10% rule:
  Iterative optimization: 3D models  field line tracing (PFCFlux) for shadowing poloidal and toroidal leading edges

## Slide 5
BEST FW shaping design
  Poloidal: 13 blanket modules (each has 2 wings/panels)
  Toroidal: 16 modules(BM 1#-7#, 8#&9#-up port, 11#&12-equatorial port); 32 modules(BM 10#,13#)
  RIW=2.45m; ROW=4.85m
  Toroidal circular arc surface and poloidal chamfer
5
Current Shaping Design of the FW Panels in BEST

## Slide 6
Contact point
3#
2#
4#
FW heat fluxes during limiter start-up phase
The inner FW is used as limiter during start-up and ramp-down stage
  Start-up (<4s)  as limiter
  With 10mm radial misalignment
  Heat flux distribution from PFCFlux code
  q// defined by a double exponential radial profile
  (Nucl. Fusion 60 (2020) 036011):
+
  Peak surface heat load ~3.07 MW/m2 on panel 3# during start-up phase （at 3s）
6
 | 1.58
 | 22.22
(mm) | 5.17
(MW/m2) | 20.01
(MW/m2) | 80.04
ROMP(m) | 4.3533
 | 1.58
 | 22.22
 | 5.17
 | 20.01
 | 80.04
ROMP(m) | 4.3533

## Slide 7
FW heat loads during flat-top phase(Q=1)
7
Main contributions of heat flux:
  SOL (SOLPS-ITER+PFCFlux)
  Near SOL (r-rsep<2.184 cm): SOLPS
  Far SOL:
  Radiation and CX particles (SOLPS-ITER)
  Ripple loss of fast ions (ISSDE)
Field line tracing taking into account 10 mm radial misalignment
  Maximum surface heat load from SOL ~0.51 MW/m2 on panel 12#
12#

## Slide 8
FW heat loads during flat-top phase(Q=5)
Main contributions of heat flux:
  SOL (SOLPS-ITER+PFCFlux)
  Near SOL (r-rsep<2.184 cm): SOLPS
  Far SOL:
  Radiation and CX particles (SOLPS-ITER)
  Ripple loss of fast ions (ISSDE)
Field line tracing taking into account 10 mm radial misalignment
  Maximum surface heat load from SOL ~0.60 MW/m2 on panel 12#
12#

## Slide 9
Fast ion loss calculation
  Alpha particles ; NBI fast ions
  Prompt loss; Pitch angle scattering loss; Ripple well loss and stochastic ripple diffusion loss
  NUBEAM : initial distribution
  ISSDE: fast ion loss (Ripple field and Coulomb collision, first wall chamfering)
  Ripple decrease from 1.5% to 0.75% @OMP of separatrix due to ferromagnetic inserts (FIs)
Main results
  Pfusion=44MW(Q=1); 168MW(Q=5) (20% for α particles)
  Maximum heat load on FW: 0.83MW/m2(Q=1@12#); 0.76MW/m2(Q=5@11#)
  The fast ion loss fraction of Q>1 is greater than that of Q=5 case, due to the lower Ip.
9
Ripple field distribution (with and without FIs)
Q=1
Q=5
FW heat loads from fast ion loss

## Slide 10
FW heat loads during flat-top phase （Q=1）
10
Panel number | SOL (MW/m2) | Ripple loss of fast ions (MW/m2) | Radiation and CX particles (MW/m2) | Total Heat flux
1 | 0.07 | 0 | 0.11 | 0.18
2 | 0.09 | 0 | 0.11 | 0.20
3 | 0.12 | 0 | 0.11 | 0.23
4 | 0.09 | 0 | 0.10 | 0.19
5 | 0.05 | 0 | 0.08 | 0.13
6 | 0.05 | 0 | 0.08 | 0.13
7 | 0.04 | 0 | 0.08 | 0.12
8 | 0.11 | 0 | 0.07 | 0.18
9 | 0.16 | 0 | 0.07 | 0.23
10 | 0.21 | 0 | 0.08 | 0.29
11 | 0.42 | 0.71 | 0.08 | 1.21
12 | 0.51 | 0.83 | 0.07 | 1.41
13 | 0.15 | 0.10 | 0.07 | 0.32
~59% of total heat flux on panel 11 and 12 contributed by ripple loss of fast ions
Radiation and CX particles ~0.07-0.11 MW/m2

## Slide 11
FW heat loads during flat-top phase （Q=5）
11
Panel number | SOL (MW/m2) | Ripple loss of fast ions (MW/m2) | Radiation and CX particles (MW/m2) | Total Heat flux
1 | 0.15 | 0 | 0.19 | 0.34
2 | 0.22 | 0 | 0.13 | 0.35
3 | 0.25 | 0 | 0.12 | 0.37
4 | 0.17 | 0 | 0.10 | 0.27
5 | 0.08 | 0 | 0.09 | 0.17
6 | 0.03 | 0 | 0.10 | 0.13
7 | 0.12 | 0 | 0.09 | 0.21
8 | 0.12 | 0 | 0.09 | 0.21
9 | 0 | 0 | 0.09 | 0.09
10 | 0.25 | 0 | 0.11 | 0.36
11 | 0.50 | 0.76 | 0.11 | 1.37
12 | 0.60 | 0.47 | 0.09 | 1.16
13 | 0.17 | 0.06 | 0.09 | 0.32
41%-55% of total heat flux on panel 11 and 12 contributed by ripple loss of fast ions
Radiation and CX particles ~0.09-0.19 MW/m2

## Slide 12
Summary
Stationary heat loads on FW have been evaluated
  Shaping design of the FW panel and radial misalignment is taken into account
  3D heat flux is obtained with mapping of magnetic flux surface and local pitch angle
  Fast ion loss dominates the heat loads on the LFS FW panels
New optimization and iteration being carried out to further reduce the fast ion losses
Heat load due to major disruption and VDE is under evaluation

## Slide 13
Thank You for Your Attention!