## Slide 1: In-Vessel Components Integration Design of BEST
X. PENG, M. Lei, X. Huang, Z. Wang, P. Liu,
K. Chen and BEST Team
with fruitful discussion with EU-DEMO Team
pengxb@ipp.ac.cn

## Slide 2
CONTENTS
IVC layout and design requirements
Divertor
Shielding blanket
Vertical stabilization system
In-vessel diagnostic integration
Assembly procedure
Summary

## Slide 3
IVC Layout and Design Requirements
Part 01

## Slide 4
Functions required and Poloidal layout
Functions | Engineering
Heat and particle exhaust: 10MW/m2, 63Pam3/s in SS | Divertor (in blue) (PFU~15MW/m2), 8 cyropumps in the lower ports
Neutron shielding for VV and TF coils | Shielding blanket (in yellow), passive stabilization plate and shielding structure below the divertor
Plasma vertical stabilization control: m_s≥0.2 | Vertical stabilization coil (in brown) and passive stabilization plate (in green)
Diagnostics for machine safety, operation and physics study | 28 sets for measuring 43 physical parameters Dozens of in-vessel diagnostics need to be integrated with IVC
Divertor
Vertical stabilization system
In-vessel diagnostic
Shielding blanket

## Slide 5
Main design requirements / guidelines
Utilize mutual and reliable technologies for IVC, to realize the functions required from physics.
Fast implementation in 3-4 years into BEST .
Robust to sustain various loads in fusion power of SS 20 MW and 5-10 s 200 MW, the Ip of 7.3 MA.
Baking @ 190 °C (divertor @ 240 °C ).
Vacuum quality class 1, quality control class 1.
Remote handling compatible from plasma side for Divertor PFCs, First Wall in shield blanket and passive stabilization plate.
Other components are design for life in BEST

## Slide 6
Divertor
Part 02

## Slide 7
Divertor overall design
48 divertors in toroidal, 7.5° for one module.
RH maintenance for PFCs.
PFU: monoblock (strike zone) combined with flat-type，heat flux removal capability of 15 MW/m2 .
3 SS supports to connect VV with bolts.
DOME
Inner Target
Outer Target
Cassette
Support
Main parameters for one module | 
Toroidal | 7.5°
L/W/H | 2.01×(0.28-0.53)×1.02 m
Weight | ~1.6t
Design heat flux | 15 MW/m2
One PFU
Divertor module

## Slide 8
Divertor supports
Assembly and installation
  3 supports;
  CB fixed to supports by bolts;
  Customed compensation.
Divertor and supports
2xM30
2xM36
M45
Surface machining
Surface machining
Bolt M36
Surface machining
VV supprot
Compensation
M20x4
M24x6
VV
Compensation

## Slide 9
Pipe cutting
Bolts removal
PFC Grabbing
Guide slot
Guide block
10°
Guide slot
90°
8mm
Grabbing feature
A
B
C
TIG
Welding
position
Welding
position
Tube cap
Tube
Pipe welding
Divertor RH compactible features
9
85
U shape pipe
315
70
mm

## Slide 10
Divertor RH procedure
M30
M36
IVT&Dome
IVT&Dome move
160mm
Unbolt
（4xM30）
Cut pipe（Φ51x3）
85
116
193
120
IVT&Dome lift
Remote Handling maintenance:
  Cut the coolant pipe end cover;
  Internal pipe cutting;
  Remove the bolt;
  Move horizontally to the right;
  Vertical lift.

## Slide 11
Shielding Blanket
Part 03

## Slide 12
Overall Configuration
Poloidal: 13 modules (inboard – BM 1#-5#; upper – BM 6# - 9#; outboard – BM 10#-13# )
Toroidal (FW): 16 modules(FW 1#-9#, 11&12#-equatorial port); 32 modules(FW 10#,13#)
Toroidal (SB): 8 modules(SB 1#-5#); 16 modules (SB 7#-9#, 11#-13#); 32 modules(SB 10#)
Layout of shielding blanket modules
The gaps between blanket modules are 10 mm both poloidally and toroidally for installation and disassembly.
176 SB +240 FW
#1
#2
#3
#4
#5
#6
#7
#8
#9
#10
#11
#12
#13
1 SB+2 FW
1 SB+1 FW

## Slide 13
Manifold Configuration

## Slide 14
Manifold Configuration
Three bunches of manifolds and water flow chart for 45° shielding blanket

## Slide 15
First Wall Design
Cooling channels
Mechanical connection
Coolant pipe connection
RH Positioning/ grabbing holes
W tiles
Cu foils
CuCrZr plate
CuCrZr covers
Coolant distribution
Inlet from beam
Coolant back to beam
Slots ↓ EM load/ Thermal stress
Cooling of PFU
FW= Left/Right Fingers + Beam + Connection Pipes

## Slide 16
Shielding block design
From FW1
From FW2
To Manifold
Φ42.2
Φ15
Φ24
From FW2
From FW1
To Manifold
Peak T 227℃
Peak stress 339MPa
Preliminary design of one shield block has two first wall.
Nuclear heating <0.3W/cc, mass flow rate 2.0114kg/s，inlet temperature 143.3℃, coolant pressure 4MPa

## Slide 17
Connection with VV
Inboard SB Module
VV
SB Support Structure
Housing
Housing
Key pad
M50 bolt
Direction of thermal expansion
The Key pad is arranged in a direction parallel to the expansion direction of the SB. The key pad supports the SB without preventing thermal deformation

## Slide 18
Vertical Stabilization System
Part 04

## Slide 19
Vertical Stabilization System
Maximum controllable vertical drift of 11 cm;
Vertical displacement growth rate <100/s.
Upper support structure bolted
Lower passive plate bolted on the support
Support bolted on VV
VS coils clamp bolted on Upper support structure and Lower passive plate
Welded on VV

## Slide 20
Vertical Stabilization System
Type | Unit: MPa | SS jacket | Cu conductor | Brackets | Bolts
Baking | Stress results | 158 | 58 | 304 | 274
 | Allowable | 381 | 90 | 381 | 381
 | result | √ | √ | √ | √
Lorentz + Thermal | Stress results | 218 | 70 | 322 | 207
 | Allowable | 411 | 100 | 411 | 411
 | result | √ | √ | √ | √
VS coils
two coils, each with 4 turns, 2 feeders X 2 ports.
200 brackets bolted to upper support structure and lower passive plate.
In-port brackets welded to VV
VS coils conductor | 
Max Current per turn (kA) | 26.2
Current per turn effective(kA) | 2.2
Turns effective | 4
Length per turn（m） | 44
Neutron heating rate(W/cc) | <0.3
Rated voltage(V) | 1200
Jacket OD (mm) | 38
Jacket ID (mm) | 33
Insulation thickness (mm) | 3.5
Conductor OD (mm) | 26
Conductor ID (mm) | 16
Flow velocity (m/s) | 3
Water Inlet Temperature (℃) | 70
Coil delta_T (℃) | 10
Jacket: 316L
Insulation: MgO
Conductor: Cu
VS Design-Basis Current Waveform
VS Bracket Design
（SS316L）
In Port Bracket Design
（SS316L）

## Slide 21
Vertical Stabilization System
Contact resistance test on passive plate
Passive stabilization plate
Passive structure resistivity coefficient | 4.82
ms | 0.19
gamma | 100.0/s
ndecay | -1.0983
ncrit | -1.3054
ndecay/ncrit | 0.8414
Imax(kA) | 24.3
Umax(V) | 1740
Pmax(MW) | 42.3
Lower passive plate
Upper support structure
X16
X16
Tungsten first wall
1MW/m2
Water cooled body:316L
Water cooled body:316L
The minimum contact resistance of a single contact surface is 0.1μΩ, totally 3.2μΩ for all 32 contacts.

## Slide 22
In-Vessel Diagnostic Integration
Part 05

## Slide 23
Magnetics
D loop
Flux loop
Saddle coil
Toroidal cable tray
Outlet cable
Feedthrough
Partial Rogowski Coil
  11 D-shaped loops: continuous coils or a set of probes/cables on support, including Rogowski+FOCS, pickup coils, Mirnov coil, diamagnetic coil. (slotting needed in blanket)
  Pickup coils to measure toroidal mode number (one for each of 16 sectors. slotting needed in blanket)
  Flux loop (for a total of 95, i.e. 45 groups, mounted on VV inner wall)
  Saddle loop (mounted on VV inner wall, for total of 16 - every equatorial port)
  Partial Rogowski coil (16 toroidal location divertor leg×3; port A, E, I and M lower passive plate leg×4)
  Toroidal cable tray (between LFS blanket and PS plate)
  Flux loop centralized outlet cable（mounted on VV between A-B, slotting in blanket needed)
  Feedthrough (lower port B, F, J and N for outlet cables)

## Slide 24
Other In-VV Diagnostics
NAS&MFC in section O, DNFM in section O&G
NAS&MFC
NAS&MFC
NAS&MFC
NAS&MFC
NAS
DNFM
NAS pipe & MFC cable
NAS&MFC
NAS&MFC
DUMP
CCR
Faraday Cup
HFS bolometer in sector A
A DDMS pipe below divertor for each lower port
TS dump in sector G
POINT CCR in section J
Faraday cup in section I
NAS & MFC & DNFM
  NAS and MFC: located between O-P, 7 for NAS and 6 for MFC, shared slotting in blanket.
  DNFM: located in sectors O and G. Space reservation in divertor area.
Faraday Cup: 2 detectors in LFS blanket I.
CCR: mounted in HFS blanket J.
TS DUMP: mounted in HFS blanket G.
Bolometer: detector and LoS in the front, and cable in the back and bottom of HFS blanket A.
DDMS: A Φ50 tube for each lower port, below divertor.
Slotting and cooling needed

## Slide 25
Assembly procedure
Part 06

## Slide 26
Assembly procedure
Assembly Strategy:
With the updating of VV and shielding blanket design, the IVCs can be assembled starting from 3/8 VV completed (for some shield blocks).
After the VV torus formed, (3-4) multi-construction workstations would be set up to transfer the IVCs from equatorial ports into VV for final assembly.
Assembly Sequence:
#6
#5
#4
#3
#2
#1
#7
#8
#9
#10
#11
#12
#13
Start
Close
1
3
4
2
Diagnostic Integration
BM #6, #7, #8, #9
BM #5, #4, #3
BM #10, #11, #12
Divertors
Lower Vertical Stabilization System
BM #13
Upper Vertical Stabilization System
BM #2, #1

## Slide 27
Assembly procedure
②
③
④
①
Establish ①assemble platform in VV, which is fixed onto the divertor supports.
Establish ②transport frame from port cells to equatorial ports , to transfer the IVCs and tools into VV.
Use purpose-build ③lifting tools, ④upending and adjusting tools (series of tools under design to adapt the special structure blankets and VS) to assemble BM #3 to BM#12 and upper VS system.
Key steps:

## Slide 28
Assembly procedure
⑤
⑧
⑦
⑥
Disassemble the platform and transport frame used in previous steps.
Establish ⑤transports hanging rail system and ⑥bottom circular rails.
Use ⑦lifting hooks to transfer the left IVCs into VV.
Use the ⑧assembly trolley (can move on the circular rails) to assemble the IVCs to final positions.
During divertors assembly, the bottom circular rails will be removed gradually to expose the supports.
Beams support on TFCs
Slings

## Slide 29
Summary
Part 07

## Slide 30
Summary
BEST In-Vessel Components (IVC) have the functions of heat and particle exhaust, neutron shielding, plasma vertical stabilization, and in-vessel diagnostic integration.
The IVC includes divertor, shielding blanket, VS coil, passive stabilization plate and in-vessel relevant diagnostics.
The IVC integration has being progressed well with the focus on the overall design, interfaces, and supporting structure.
The shielding blanket and the plasma vertical stabilization system need more effort to detail the engineering design.
More R&D will be carried out to verify the critical interface design, such as the RH interface of the cooling pipes for divertor and shielding blanket.
All your comments are appreciated!

## Slide 31
Thanks for Your Attention!