## Slide 1: Integration concepts of VNS in-vessel components
C. Bachmann
21/03/2024

## Slide 2: VNS Vacuum vessel
Design: ITER-like
Double-wall structure: stainless steel XM-19, 316(L)N
Shell thickness (tentative): 20 mm
Mechanical supports of in-vessel components to the VV:
Inboard side: Interference with VV ribs to be considered.
Outboard side: Only areas available outside the VV ports (which are irregular).

## Slide 3: DEMO-like RH-compatible machine architecture
Blanket cooling pipes integrated and accessible inside the 12 upper ports.
Divertor cooling pipes:
In lower RH ports: direct access.
In lower pumping ports: Separate access hatch for pipe tools above cryopump flange.
Cooling pipes inside ports (no access required from plasma side through first wall, reduced gamma radiation, no bolts – tbd.).
Divertor cassettes, vertical blanket segments (integration studies only for inboard segments so far).
Lower horizontal, vertical upper ports.
[C. Bachmann et al., Fus. Eng. Des. 136 (2018), 87-95]

## Slide 4: Electrical connections
Design: Small thermal expansions.
Inboard blanket: Radial electrical connections guaranteed by ferromagnetic force. (Currents in pipes to be verified.)
Outboard blankets: electrical connections possibly guaranteed by bolts (not decided yet).
Divertor: electrical contacts guaranteed by preloaded cassette.
EM Loads:
Asymmetric electrical connections cause large asymmetric EM loads  electrical connections in the center of the blanket, see also [I. Maione et al., Fus. Eng. Des. 166 (2021) 112285]
Phenomenon not fully understood, will be studied this year.
2.1
2.2
2.3
1.0
Radial loads during plasma disruption on left/right inboard segment:
±512 kN ±444 kN ±79 kN ±424 kN
Electrical connections to VV
Chosen concept

## Slide 5: Identification of design loads acting on in-vessel components
Loads considered in the concept definition phase (currently estimates) | Divertor cassette | Inboard blanket segment | Outboard blanket segment
Dead weight | Fz = -12 kN (1.2 tons) | Fz = -30 kN (3 tons) | Fz = -70 kN (7 tons)
Ferromagnetic force | Tbd. | Frad = -200 … -600 kN (tbd) | Tbd.
EM loads due to TF coil fast discharge | Fz = -600 kN | Frad = -1200 kN | Frad = 400 kN
EM loads in disruptions (Lorentz forces) (current quench time: 4.7 ms, based on review of ITER Physics basis and other relevant literature) | Fz = -100 kN Ftor = 40 kN Mrad = 60 kNm Mz = 110 kNm | Ftor = 90 kN Mrad = 550 kNm Mz = 150 kNm | Tbd.
Halo current loads (halo current magnitudes defined based on ITER Physics basis, to be revisited.) | Tbd. | Fz = ±100 kN (25 kA / BLK) | Fz = ±60 kN (20 kA / BLK)

## Slide 6: Mechanical attachments - blankets
Inboard blankets:
Design:
Ferromagnetic (radial) force replaces the preload of radial bolts.
Pre-compressed radial supports on both sides of the blanket provide support against Mz.
Pair of toroidal shear keys react the large radial moment due to disruptions.
Outboard blankets: design tbd.

## Slide 7: Alignment of first wall
Prior to in-vessel component installation:
VV assembly and survey of VV shape.
Customization of support structures on VV  correct VV shape tolerances.
Customization of support structures on in-vessel components  correct shape tolerances of blankets/divertor cassettes.
 Must foresee excess material for machining.
 Good FW alignment at the support locations.
 Misalignment of the wall in-between support locations due to manufacturing imperfections and thermal deformations.

## Slide 8: Summary
 | Inboard blankets | Outboard blankets | Divertor cassette
RH approach | 12 upper vertical RH ports |  | 4 lower RH ports
Service of cooling pipes | 12 upper vertical RH ports |  | 4 lower RH ports 8 lower pumping ports access without removing pumps
Electrical integration | Contact on radial supports ensured by ferromagnetic force | Tbd. | Contact on radial supports ensured by cassette preload
Mechanical integration | Shear keys and contact pads, no bolts | Tbd. | Shear keys, pins, contact pads, no bolts (ITER-like)
Design to be developed in 2024!

## Slide 9
Thank you for your attention