## Slide 1: DIVGAS modelling of neutral particle gas dynamics and exhaust for DEMO
S. Varoutis, C. Tantos, Y. Igitkhanov, C. Day
WPPWIE Midterm Meeting 2024, VTT Finland, 9-11 Apr. 2024

## Slide 2: Outline
  Objective of the work – DEMO particle exhaust
  Description of the DIVGAS code
  WPPWIE activities within 2021, 2022 and 2023
    Electric and magnetic effects – Benchmark
    Gas-surface interaction – Benchmark
    Atomic & molecular processes
    GPU acceleration
  Exploitation of DIVGAS for building up the SN and XD albedo database
  Comparison between SN and XD divertor
  WPPWIE 2024 activities
  Summary

## Slide 3: Objective – DEMO particle exhaust
  Description of the gas flow in the divertor and vacuum systems  Challenging task, flow covers a wide range of Knudsen number.
  Consider more relevant physics, which influence the divertor conditions and consequently the pumping requirements.
  For DEMO, a reliable tool, which can predict overall quantities, the neutral recirculation and improve the exhaust pumping efficiency, is required.
  Elaborate a self-consistent matrix of albedo values for a DEMO divertor. Albedo is a “hand-shake” parameter, which links plasma performance and pumping capability.
  Often, albedo is considered as a “knob” having no real physics basis – Only for stability and convergence purposes.
  Due to the high geometrical complexity the computational effort could be reduced by exploiting advanced parallelization techniques (MPI, CUDA etc) as well as large HPC clusters.

## Slide 4: Particle Exhaust parameters
Divertor
Pump
duct
Pumps
CORE
SOL
re-circulation
Limited Conductance
Sreq (noble gases)
Sreq (D,T)
  At which pumping speed can the machine gas throughput be pumped?
  Competition against recycling and conductance losses
Γin
Γpump
Γoutflux
Γpump
Γpuff
Throughput = pressure x pumping speed
ξ
Pumping probability
Throughput = pressure x pumping speed

## Slide 5: DIVertor GAs Simulator
  DIVGAS is based on the deterministic (Discrete Velocity Method) and stochastic (Direct Simulation Monte Carlo) numerical methods.
  The solution of the Boltzmann equation is reproduced.
  Conservation of momentum and energy.
  Correct estimation of transport coefficients.
Ludwig
Boltzmann
1872 Boltzmann equation
  DIVGAS 3-step workflow

## Slide 6: Objective of DIVGAS
  The main objective of the DIVGAS code is to develop a multi-machine platform for divertor gas flows
  Validate the code with experimental results in JET and AUG.
  Benchmark the code with the extensive ITER divertor database.
  Apply the code for the design of particle exhaust in fusion devices.
DEMO

## Slide 7: Work plan 2021-2024
  Introduction of atomic and molecular processes (2021 activities)
  Introduction of the CLL advanced gas-surface interaction model (2021 activities)
  Introduction of the electric-magnetic field effects (2021 activities)
  Acceleration of the DIVGAS code using GPUs for reducing the computational time (2021 activities)
  Study the influence of the liner in the overall pumping efficiency of the divertor (2021 activities)
  DIVGAS enhancements and studies within WPPWIE
  Exploitation of the improved DIVGAS code within WPPWIE
  Apply the improved DIVGAS code in order to elaborate a self-consistent matrix of albedo values for a DEMO SN divertor (IDM: 2P57HS) (2022 activities)
  Apply of the improved DIVGAS code in order to elaborate a self-consistent matrix of albedo values for a DEMO XD divertor (IDM: 2NNVBJ) (2023 activities)
  Apply of the improved DIVGAS code in order to study the influence of the poloidal/toroidal leakages in the 3D DEMO SN divertor (2024 activities) – Ongoing work

## Slide 8: Electric and magnetic effects
  The computational kernel of the DIVGAS code demonstrates the numerical solution of the Boltzmann equation using the DSMC method:
  Within WPPWIE, the DIVGAS code was extended to include the modeling of charged particles (ions and electrons) in presence of magnetic field or/and electric field, by replacing F by the Lorentz force as follows:
  F: is an external force which generally acts to any particle
  The free motion of the DSMC particles is performed using the explicit Boris scheme (phase space volume conserving and simulated particles typically remain along the correct trajectory)

## Slide 9: Benchmark
  Numerical requirements/assumptions:
  Cell sizes must resolve Debye length λD to avoid numerical heating, i.e. Δx< λD
  Time step must resolve plasma frequency ωp, i.e. Δt< 2/ ωp
  Should satisfy Courant-Friedrichs-Lewy (CFL) condition similar to continuum CFD, i.e. Δt< Δx/umax, where umax is the thermal velocity
  Cell size must resolve the collision mean free path λ (and other vdf gradient length scales)
  The computational cells should be sufficiently populated in order to preserve good statistics
  The validity of the updated DIVGAS code has been confirmed by performing comparisons using some simplified examples with known analytical solutions:
Blue: DIVGAS
Black: Analytical

## Slide 10: Gas-surface interaction
  The particle collisions with the solid walls are modeled using the advanced CLL kernel:
  Where RCLL is a complex kernel which depends on two coefficients (at, an), one for the tangential momentum and another for the kinetic energy
  Data for these coefficients for deuterium and impurities (Ne, Ar, He) were determined experimentally and are available in the literature
  Typical values for (at, an) extracted from experimental data are: He (0.9,0.1), Ar (0.96, 1.0), D2 (0.95,0.1)
CLL
at: 0.5
an: 0.5
at: 0.0
an: 0.0
specular
at: 1.0
an: 1.0
diffuse
at: 2.0
an: 0.0
back-scattering

## Slide 11: Benchmark
  The classical Fourier problem (see the flow set-up shown below) is considered as benchmark in order to validate the accuracy of the CLL implementation in the DIVGAS code (one of the KIT tasks under WPPWIE) by performing comparison with existing data in the literature
  Very good agreement is observed in a wide range of the coefficients an and at – Maximum relative deviation less than 0.9%
[1] M. Vargas et al., AIP Conference Proceedings 1333, 354 (2011)

## Slide 12: Atomic & Molecular processes
The rate of change in the number density of species A due to the bimolecular reaction , with reaction rate coefficient , can be expressed as
where and are the total cross-section and relative velocity for the A-B collision. Note the reaction probability can also be written in terms of the reaction cross-section, .
The TCE reaction probability can be expressed as:
PR=
Total Collision Energy (TCE) Model [2]
[2] I. Boyd and T. Schwarzentruber, Nonequilibrium gas dynamics and molecular simulations, Cambridge University Press, (2017).
Gas-phase Reactions | Surface Reactions
D2+ee+2D | D+D
D2+e2e+D+D+ | D+D2
D+e2e+D+ | D2+D2
D2+e2e+D2+ | D2+D
D2++ee+D+D+ | DD2
D+D2+D2 + D+ | DD
D2 + D+D2+ + D | D2D2
D2++eD+D | 
  The TCE formulation can reproduce ionization, dissociation/recombination and exchange reaction rates described in terms of
  Deuterium atomic and molecular processes have been implemented in the DIVGAS code considering a set of volumetric and surface reactions.

## Slide 13: GPU acceleration – MPI, CUDA
Source: https://www.hpc.cineca.it/
https://www.hpc.cineca.it/hardware/marconi
Source: https://www.nvidia.com
Source: https://www.nvidia.com
  NVIDIA Tesla K80 - 4992 NVIDIA CUDA cores with a dual-GPU design (2 x 12 GB of GDDR5 ) - Up to 2.91 teraflops double-precision performance
  NVIDIA Tesla V100 - 5376 NVIDIA CUDA cores (32 GB HBM2) - Up to 7 teraflops double-precision performance
  MARCONI A-3 partition – Nodes: 3188
    CPUs/Node: 2 x 24-cores Intel Xeon 8160 (SkyLake) at 2.10 GHz
    RAM: 196 GB/Node
    Peak Performance: ~8 PFlop/s

## Slide 14: SN and XD DIVGAS model
Γpump
Γ-
Γ+
Γ-
Liner
Pumping opening
Neutron radiation shields
HFS inlet of neutrals
LFS inlet of neutrals
Γ+
  Particle balance:
  Species: D2, D, He, Ar and corresponding ions
  Parametric analysis: 0.2Γ+, Γ +, 2Γ + and 5Γ +
  A pumping probability 0.05 ≤ ξ ≤ 0.3 is imposed on the pumping opening. The liner is included.
Γpump
Γ+
Γ-
Γ+
Γ -
Liner
Pumping opening
HFS inlet of neutrals
LFS inlet of neutrals
  Albedo:
2019 XD baseline DEMO
2022 SN baseline DEMO

## Slide 15: ITER-SOLPS plasma BCs
 | P+ (Pa) |  | T+ (eV) |  | Γ+ (s-1 m-1) | 
 | LFS | HFS | LFS | HFS | LFS | HFS
D | 3.77 | 1.5 | 0.87 | 0.79 | 1.64E+22 | 6.86E+21
D2 | 5.35 | 4.0 | 0.88 | 0.63 | 1.64E+22 | 1.62E+22
He | 0.5 | 0.3 | 0.9 | 0.99 | 1.48E+21 | 7.90E+20
Ar | 0.085 | 0.04 | 2.74 | 2.66 | 2.81E+19 | 2.08E+19
Albedo | 0.994 (for all neutrals) |  |  |  |  | 
 | P+ (Pa) |  | T+ (eV) |  | Γ+ (s-1 m-1) | 
 | LFS | HFS | LFS | HFS | LFS | HFS
D | 0.33 | 1.17 | 0.15 | 0.81 | 4.98E+21 | 5.46E+21
D2 | 2.88 | 4.86 | 0.15 | 0.81 | 3.04E+22 | 1.59E+22
He | 0.011 | 0.21 | 0.15 | 0.81 | 1.17E+20 | 6.96E+20
Ar | 0.008 | 0.004 | 0.15 | 0.81 | 2.66E+19 | 4.47E+18
Albedo | 0.45 (for all neutrals) |  |  |  |  | 
  SN Divertor
  X Divertor
  The SN plasma simulation is based on the „kinetic“, while the XD is based on the „fluid“approximation.
  The MARCONI HPC fusion cluster has been exploited.

## Slide 16: Effect of A&M processes
  It has been observed that in the case with the liner and plasma temperature 10 eV, the influence of A&M processes on neutral pumped flux and outflux is negligible (within ~2% difference). As the temperature increases to 20 eV the neutral outflux increases by ~22%, while pumped flux increases only by ~2%.
  In the case without the liner the influence of A&M processes on neutral pumped flux and outflux is more significant and by increasing from 10 eV to 20 eV the outflux and the pumped flux are increased by 16% and 22% respectively.
  The average neutral pressure below the liner (i.e in the pumping port) has a weak dependence on the considered A&M processes as well as on the plasma temperature.
  In the case with liner, the gas-surface reactions related to the atomic deuterium (D) recombination have a higher impact compared to the gas-phase recombination on the particle exhaust, resulting to large production of molecular deuterium (D2) close to the walls. Upon convergence, D2 number density is one order of magnitude higher than atomic deuterium D.

## Slide 17: Effect of external fields
  By considering the magnetic field in the DIVGAS code the results for a divertor w/o liner are affected significantly, while for the cases with liner the effect of the magnetic field on both pressure and pumped fluxes becomes weak.
  The simulations have been performed assuming DEMO relevant magnetic field and boundary conditions (P+D=10 Pa, T +D =1 eV, ne=1019 m-3, Te=10 eV).
  In the cases w/o liner, the presence of the magnetic field leads to lower pumped fluxes and pressures at the pumping opening (about 80% in pumped fluxes and 90% in pressure).

## Slide 18: Computing performance
  Since the DIVGAS simulations are time consuming, the parallelization optimization had to be completed initially – this task has been completed showing that the hybrid version CPU/GPU of the DIVGAS code can significantly reduce the required computational cost
  The GPU simulations have a speed-up of ~60 compared with the serial case
  The GPU simulations have a similar speed-up compared with ~96 CPUs
  This part of the work has been already published in the Plasma Physics and Controlled Fusion journal: https://doi.org/10.1088/1361-6587/ac172b

## Slide 19: Comparison SN vs XD for Γ+ (1)
  It has been confirmed that as the pumping probability ξ increases, the albedo decreases for both SN and XD divertor configurations.
  It is deduced that the albedo is not the same for the gas species D2, He and Ar.
  For the same pumping probability ξ, the required albedo is lower → Results to lower neutral outflux.
  The reason of having D2 albedos higher than unity is due to the contribution of D to the D2 outflux through the wall recombination process.
SN
XD

## Slide 20: Comparison SN vs XD for Γ+ (2)
  The presence of the neutron radiation shields results to a reduction ~40% of the pumped flux.
  The XD divertor performs slightly better (following the total incoming flux behavior) in terms of pumping efficiency (considering the negative effect of the neutron shields) for deuterium, while for helium the SN performs better, owing to the higher helium incoming flux for SN case.
For reference Γ+

## Slide 21: Comparison SN vs XD for Γ+ (3)
ξ=0.3
ξ=0.3
ξ=0.05
ξ=0.05
  For the case of SN, as ξ increases by x6 the helium and deuterium pressure in the sub-divertor decreases by ~x4 and ~x3 respectively. For XD the corresponding values are ~x4 and ~x2 respectively.
  At the pumping port, the XD deuterium pressure is ~x1.2-1.7 higher compared to SN.
ξ=0.05
ξ=0.3
ξ=0.05
ξ=0.3

## Slide 22: Work for 2024 (PWIE-SP D.4.T-T004-D001)
  For 2024, the DIVGAS code will be applied to study the 3D effects (poloidal/toroidal leakages) on the pumping efficiency of the latest DEMO divertor design.
  The above study will be based on a reference plasma scenario of SN magnetic configuration, which has been provided by Fabio Subba (email 14/07/2022).
  A parametric analysis will be performed assuming different pumping speed scenarios, based on the current pumping system design (the range of pumping probability will be narrowed down in order to reduce the computational effort).
  Ongoing work on the simplification of the original 3D CAD model.
  After contacting the responsible officer of WPDIV for the divertor configuration (Jeong-Ha You), the latest SN divertor geometry has been provided and is available under the IDM link: https://idm.euro-fusion.org/?uid=2PPMQB

## Slide 23: Summary
  The DIVGAS code has been upgraded in terms of physics, considering the A&M processes, magnetic field and advance gas-surface interaction models. The DIVGAS code has been accelerated using GPUs.
  The new DIVGAS code has been exploited for building-up the albedo database for SN and XD divertors. All the DIVGAS simulations are based on corresponding ITER-SOLPS plasma simulations.
  The main outcome from the comparison between SN and XD divertors is that XD performs better in terms of pumping efficiency (considering the negative effect of the neutron shields). Lower albedos should be considered in plasma simulations, compared to the SN case.
  For a given pumping probability ξ, the albedo for each specie varies significantly. We confirm that the assumption of having the same albedo for all species, is not realistic. Thus, the albedo values should be extracted from the provided database.