## Slide 1
EUROfusion Science Meeting
12th June 2024
P. Mantica(1), M.V. Falessi (2), G.Vlad(2)
on behalf of DTT Plasma Scenarios, MHD stability and Theory groups
(1) CNR-ISTP Milano (2) ENEA C.R. Frascati
DTT Consortium (DTT S.C.a r.l. Via E. Fermi 45 I-00044 Frascati (Roma) Italy)
DTT plasma scenarios, MHD stability and energetic particle physics

## Slide 2: DTT at full power, field and current
Integrated modelling performed with both ASTRA and JINTRAC with TGLF or QLK transport models, solving for Te, Ti, ne, J, rotation and 2 impurities, heating and equilibrium self-consistent. See I.Casiraghi et al, PPCF 2023, N.Bonanomi et al, EPS 2023 to be submitted.
Standard baseline H-mode
High density but low collisionality
Mainly external electron heating but large collisional coupling
Issue:q=1 ~mid radius

## Slide 3: DTT at full power, field and current
 | DTT | ITER | EU DEMO
R [m] / a [m] | 2.19/0.70 = 3.1 | 6.2/2.0 = 3.1 | 9.07/2.92=3.1
Ipl [MA] / Btor [T] /q95 | 5.5/5.85/3 | 15/5.3/3.2 | 17.75/5.86/3.9
Psep/R [MW/m] | 15 | 14 | 19
Ptot [MW] | 45 | 150 | 450
Pulse length [s] | 95 | 400 | 7200
βN [%] | 1.6 | 2.1 | 2.5
𝜏E [s] | 0.42 | 2.9 | 6.9
ρ*at r/a=0.5 [10–3] | 3.8 | 2.0 | 1.5
𝜈* at r/a=0.5 [10–2] | 1.2 | 1.4 | 0.8
ρ*ped [10–3] | 2.7 | 0.3 | 0.3
𝜈*ped [10-2] | 5 | 2.2 | 8
nGW [E20 m-3] | 3.6 | 1.2 | 0.66

## Slide 4
High BT and Ip and high power wrt plasma size
High neGW--> high ne : reactor relevant n*ped and r*ped and within local approximation, but high n*sep for divertor studiesIntegration of edge/core reactor relevant parameters, in presence of W wall
Low edge neutral penetration: reactor relevant fuelling studies
Transport studies of intrinsic (W) and seeded impurities in reactor relevant conditions
ELM mitigation studies with reactor relevant parameters
Strong variation of Ip, BT, q95 : test of scaling laws and integrated modelling
Wide spectrum of accessible scenarios, operation with both favourable and unfavourable gradB drift (for L-mode, I-mode, negative triangularity), strong shaping for ELM-free scenarios (EDA, QCE, XPR)
NBI/ICRH fast ions allow studies of energetic particles as mediators of cross-scale couplings in reactor relevant plasmas
Unique DTT characteristics within EU devices
(indicated as indispensable in Facility Review)

## Slide 5: Time dependent simulations
Using ASTRA/IMEP/TGLF
Flux consumption at the end of ramp-up allows discharge duration ~30-40 sec at full performance.

## Slide 6: Time dependent simulations

## Slide 7: Weak coupling
Weak coupling with CREATE-NL to check consistency of scenarios with magnetic controls
Weak coupling with the edge code SOLEDGE2D-Eirene
Particle and power fluxes derived from core modelling are input to SOLEDGE2D-Eirene
Separatrix density, temperatures and impurity concentration for sustainable power exhaust at the divertor targets and the neutral penetration are input to core modelling

## Slide 8: Scenarios accessible in DTT during the various phases
L-mode
Baseline H-mode
High bN
Negative d
Hybrid
EDA/QCE
XPR-CRD
I-mode
WPQH
Phase 1
Half RF
Phase 2
Half RF+NBI
Phase 3
Full RF+NBI

## Slide 9: DTT single null baseline scenarios in various phases
Scenarios can be performed also in Negative Triangularity configuration, since the early phase
DTT negative triangularity scenarios
Full power NT
PT
PT
PT
NT
NT
NT
Full power NT vs PT

## Slide 10: MHD stability
linear stability code [A. Bondeson, G. Vlad, and H. Lütjens, 92]
it solves full MHD linear, resistive equations [ A. Bondeson, G. Vlad, and H. Lütjens [4]].
It considers an axisymmetric general toroidal equilibrium.
MARS
HYMAGYC
nonlinear gyrokinetic hybrid code [G. Vlad et al., 2009, G. Fogaccia, et al., 2013]
two modules:
the fluid module describes the bulk plasma solving the full MHD linear resistive equations (evolutive MARS)
the kinetic module solves the Vlasov equations with a PIC (particle in cell) tecnique
The two modules are coupled by means of the pressure tensor of the energetic particles added to the fluid momentum equation.

## Slide 11: Linear stability analysis with MARS for Full Power Scenario SN from low to intermediate n
Input data and profiles for Full Power at flat-top from JINTRAC integrated modelling [I. Casiraghi et al, Nucl. Fusion 61, 2021, 116068]. No sawtooth model included.
Unstable internal kink (q0 <1) . The q=1 surface is located around s=rpol≈0.64.
the infernal modes are observed where q rational surfaces lie in the zone of low shear and high-pressure gradient
Sensitivity studies have been carried out showing that the appearance of external modes occurs for parameters far from the nominal scenario [V. Fusco et al. 2022, 48th EPS Conference on Plasma Physics]
Internal kink n=1
vsm,n
q
s
n
𝛄τA0
Infernal mode (n≤10): pressure driven modes excited in a region of low shear and high-pressure gradient.
s
n=7

## Slide 12
Input data and profiles for Full Power at flat-top from JINTRAC integrated modelling [I. Casiraghi et al, Nucl. Fusion 61, 2021, 116068]. No sawtooth model included.
Unstable internal kink (q0 <1) . The q=1 surface is located around s≈0.54.
Infernal modes are stable indeed pressure has a low gradient in the flat q region
vsm,n
q
s
Internal kink n=1
Full Power
Day0
s
q
p/B02/μ0
Linear stability analysis with MARS for scenario A (day0) SN from low to intermediate n

## Slide 13
Prediction of 2/1 (N)TM control
EC power requirements for the control and suppression of (Neoclassical)Tearing Modes, (N)TM
in the DTT full power scenario at 5.5 MA, 5.85T with sawteeth the 2/1 mode is located at very off-axis positions rtor2/1=0.82
EC power up to 7.2 MW can be injected in continuous (CW) and modulated 50% duty cycle (mod) from the upper launcher
mode width = 0.023 m: ECH-ON stabilizes with 4 MW modulated for TM and 1.5 MW CW or modulated for NTM
mode width=0.04 m: ECH-ON stabilizes with 6 MW CW or modulated for TM

## Slide 14: Linear MHD stability and Alfvénic modes with HYMAGYC (no EPs): Negative vs Positive triangularity
n=1, Internal kink and Global Alfvénic modes
n=3, Infernal mode
(q(s)=2/3)
|𝜙(s, 𝜔)|2
𝜔/𝜔A0
s
|𝜙(s, 𝜔)|2
𝜔/𝜔A0
s
|𝜙(s, 𝜔)|2
𝜔/𝜔A0
s
s
n=2, Global Alfvénic modes
MHD stability for Negative Triangularity (”flipped”) equilibria is considered for two different cases:
“Flipped” boundary and fixed p’, I* profiles, or
“Flipped” boundary and p’, q profiles.
Internal kink stability of NT equilibria is always worst, Infernal modes are always less unstable for NT with fixed p’, q profiles.
Frequency spectra of the perturbed electrostatic potential

## Slide 15: EP studies on DTT
DTT has been designed with reactor-relevant dimensionless parameters;
In particular, EPs dimensionless parameters preserve cross-scale couplings: /;
Integrated simulations are required to address plasma as a complex self-organized system;

## Slide 16: Self-organization

## Slide 17: Self-organization
NL wave-particle
NL wave-wave
Importance of EPs as mediators of cross-scale couplings;
A description of transport processes in the phase space is crucial because of non Maxwellian features of EPs

## Slide 18: Hierarchy of reduced transport models

## Slide 19: Alfvénic modes driven by EPs: linear dinamics using HYMAGYC
t𝜔A0=72
t𝜔A0=100
Alfvénic modes driven by EPs using a model DTT equilibrium:
Mawellian distribution function of EPs, ITER-like EP density profile
purely MHD (infernal modes)
Infernal modes modified by EPs
Purely EP driven modes

## Slide 20: Phase Space Zonal Structures
  ORB5 simulation Courtesy of Thomas Hayward-Schneider
M.V. Falessi & FZ, NJP 25 123035 2023
EP transport can be calculated in ORB5 global non-linear EM simulations
Constant of motion space : Pf, E, m
Resonant transport induces small scale phase space zonal structures in the distribution function (PSZS)
 Can be used in building reduced models for transport in presence of EPs
This distribution function can be evolved in phase space according to:

## Slide 21: Advanced transport models for EPs (ATEP)

## Slide 22: Advanced transport models (ATEP)
PF
F