## Slide 1: Observation of FMM-like behaviour in MMG configuration
C. Killer, D. Cipciar, J. Geiger

## Slide 2: Recap: interesting observations in FMM configuration
FMM configuration(s) have 5/5 islands just inside LCFS, SOL is “limited”
[T. Andreeva et al 2022 Nucl. Fusion 62 026032]
[G. Wurden, T. Andreeva, N. Chaudhary, D. Cipciar, A. Krämer-Flecken, …]
improved energy confinement (including adjustment for plasma volume)
intermittent crashes of Wdia, associated with mode activity in many diagnostics
[A. Krämer-Flecken]
phenomenology is limited to a certain iota range
island size plays a role
 how universal is this behavior for W7-X?

## Slide 3: MMG000 island position
MMG000: vacuum field line tracing, Icc=0 , no accounting for iota offset from coil deformation
almost a limited configuration!
very long but still finite (>1000m) connection lengths surrounding the islands
Lc difference plot shows that this is still an island divertor configuration

## Slide 4: MMG000 island compensation via control coils
all configurations with negative Icc appear to be limited configurations (islands inside LCFS)
attempt 5/5 compensation for low beta  seems already overcompensated, with “flipped” 5/5 islands appearing
attempt over-compensation of 5/5 islands  large flipped islands
Icc=--1100A
Icc=--1700A
Icc=--2500A
attempt 5/5 compensation for high beta  again seems over-compensated

## Slide 5: 2MW , 3.5e19 plasmas: comparison of Icc settings
Icc=0A
240kJ
quiet
Icc=++1500A
230kJ
quiet
Icc=--1100A
280kJ
bursts

## Slide 6: limited configurations have worse density control  compare programs with higher density (~5e19)
Icc=--1100A
Icc=--2500A
290kJ
bursts
320kJ
massive bursts

## Slide 7: bursty mode activity in MMG000 with Icc=--2500A is quite similar to FMM002
intermittent bursts with repetition of some 10Hz
associated with fast drops / “crashes” of Wdia
strong signature in magnetic (and many other) diagnostics
[D Cipciar]

## Slide 8: close-up view of one burst event
[D Cipciar]
MPM poloidal array of Vf probes
extremely high positive Vf associated to Wdia loss
temporal substructure of event
poloidal gradient of event

## Slide 9: side remark on weirdness regarding density control
these two programs were run with completely identical settings, except for control coils
Icc=++1500A
(divertor configuration)
Icc=--1100A
(limited configuration)
good density control
density overshoots and stays high without fueling
(this is just He beam, no effect on general plasma)
density control strongly depends edge topology!

## Slide 10: MMG000 with increased island size (Icc=++1500A)
regular island divertor configuration
interesting SOL physics: potential maps and poloidal Te gradients from MPM probes
MMG000+2520
Icc=+1500A
[Killer EPS2023/PSI2024]

## Slide 11: Summary
MMG configuration was run in OP2.1 in limited configurations with 5/5 islands inside LCFS
similar phenomenology to FMM: increased Wdia and strong intermittent bursty mode activity (Wdia crashes)
confinement improvement and crash intensity depend on detailed island geometry (via control coils)
 for the first time it has been shown that the “FMM phenomena” are not restricted to that configuration but appear also in other settings with 5/5 islands being inside the LCFS
more difficult density control in limited configurations
To do:
          check IR loads (transition from divertor to limited configuration)
          check beta effects for reconstruction (MMG is more susceptible to beta effects)
          assess role of iota offset by coil deformation in MMG (not known for this configuration)