## Slide 1: On Intensity, Relativity, Shift & Compression – Video data archiving at W7-X
S.Fischer1, L.Vandevenne2, P.Perusek3, M.Grün1, A.Holtz1, M.Grahl1, J.Pribošek3, J.Alakuijala2 and the W7-X team1
1 Max Planck Institute for Plasma Physics, Greifswald, DE - 2 Google Research, Zurich, CH - 3 Cosylab, d. d., Control System Laboratory, Ljubljana, SI
Credit: MPI for Plasma Physics 3rd party images used in this presentation without specific credit are sourced from http://pixabay.com and used under the terms of their content license / CC0

## Slide 2: Wendelstein 7-X
Credit: MPI for Plasma Physics, Photo: Ben Peters
Stellarator type experimental fusion device
400+ physicists, engineers, technicians & personnel
70+ diagnostic systems
1.3+ Petabyte of archived data
OP2.2 upcoming end of Q3
1 campaign / year from now on
E5-CoDaC Software Development
13 Software Engineers
1 long term external contributor
1 intern
We are hiring! (on premise in beautiful Greifswald)

## Slide 3: Agenda
  Video compression
    Basics
        Digital images
        Compression schemes
    State of the art
    Challenges @W7-X
    Fusion Power Video
        History
        Algorithm
        Implementation @W7-X
    Outlook
    Call for standardization
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization

## Slide 4: Basics – Digital images: 2D/3D arrays of relative intensity
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
…
…
…
8 bit / channel (component, e.g. [r, g, b])
R0
B0
G0
(A0)
G1
R1
B1
(A1)
…
0 8 16 24 32 40 48 56 64 72 80 88
32 bit / pixel (int / 32 bit aligned)
R0
B0
G0
R1
B1
G1
…
0 8 16 24 32 40 48 56 64 72 80 88
24 bit / pixel (interlaced)
…
R0
R2
R1
G1
G0
G2
B0
B1
B2
…
0 8 16 24 W*H*8+0 +8 +16 2*W*H*8 +8 +16 +24
24 bit / pixel (de-/non interlaced)
…
…
…
…
P0
P1
…
0 8 16 24 32 40 48 56 64 72 80 88
8 bit / pixel
P0
P1
…
0 8 16 24 32 40 48 56 64 72 80 88
16 bit / pixel
P0
P1
…
0 8 16 24 32 40 48 56 64 72 80 88
12 bit / pixel (short / 16 bit aligned)
P0
P1
P0P1
P2
P3
P2P3
P4
P5
P4P5
P6
P7
P6P7
…
0 8 16 24 32 40 48 56 64 72 80 88
12 bit / pixel (bit packed)
Its all relative
Its all relative
180
200
180
200
212
200
175
120
175
intensity aperture
exposure

## Slide 5: Basics – Compression schemes – bit stream level
Compression = transport the same information with less data
Reliance on patterns & their frequency
Þ
randomness/noise is the enemy
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
Bit packing •
Run length encoding •
Dictionary encoding •
Variable length encoding •
A
A
A
A
b
b
C
C
C
d
e
e
4
2
A
b
C
3
1
2
d
e
P0
P1
P0P1
P2
P3
P2P3
P4
P5
P4P5
P0
P1
P0
P1
P2
P2
P3
P4
P3
P4
P5
P5
A
c
b
A
c
b
a
A
b
b
D
c
0
1
0
0
2
0=Abc 1=ab 2=D
0
0
0
0
1
0
0
1
0
0
0
1
0
0
1
0
1
0
0=Abc 10=ab 110=D
Compute
Space/Bandwidth

## Slide 6: Basics – Compression schemes – predictive encoding
Predict the next value based on previous one(s)
Subtract the predicted from the actual value
Þ
Good prediction: Variable length encoding (maybe even RLE) is very effective
(bad prediction Ü encoding effect low/negative)
In images, predictions can utilize spatial coherence – in video also temporal
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
Prediction: Each value is equal to its predecessor
Good prediction: values of/around 0 are dominant
Bad prediction: values vary a lot
4
5
4
6
5
5
3
4
4
3
5
4
13
15
14
16
17
16
18
20
20
21
21
22
4
23
42
6
-7
15
8
9
9
27
5
-4
4
1
0
1
0
-1
-2
0
1
-1
1
1
13
1
1
1
1
0
1
0
2
1
-1
1
4
-19
38
-17
-22
9
15
0
1
18
9
-31

## Slide 7: Basics – Compression schemes – loss & progress
Credit: Imagecon 2019 - Jon Sneyers
Lossless – visually lossless – lossy compression
(lossy: the original cannot be identically reconstructed from the compressed)
(visually lossless: apply the above, limited to a level not perceivable to the human eye)
Progressive encoding
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
original
►
Com-pressed
►
Decom-pressed
≠ ? =
Reduce bit depth
Reduce resolution
Reduce high frequencies
Encode high level details first
Progressively add more details later in the bit stream
0,0
1,0
2,0
0,1
1,1
2,1
0,2
1,2
2,2
0,3
1,3
2,3
3,0
3,1
3,2
3,3
0,0
1,0
2,0
0,1
1,1
2,1
0,2
1,2
2,2
0,3
1,3
2,3
3,0
3,1
3,2
3,3
0,0
2,2
0,0
1,1
2,2
3,3
0,0
1,1
2,1
1,2
2,2
0,3
3,0
3,3
0,0
1,0
2,0
0,1
1,1
2,1
0,2
1,2
2,2
0,3
1,3
2,3
3,0
3,1
3,2
3,3

## Slide 8: State of the art
How do people archive images / videos for scientific use?
  They don’t (archive them)
  Throw most away (after selecting an important few)
  Store them uncompressed (aren’t that many & storage is cheap)
  Compress utilizing general bit stream compressors (or compressing FS)
  Store lossy/visually lossless, utilizing (HW supported) standard video compressors
  Get creative with lossless H264
    Cut bit depths down to 8-10 bpp grayscale
    (Mis-)use chroma planes of YUV
    And you?
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization

## Slide 9: Challenges at Wendelstein 7-X – machine level
Long Pulses & lots of Cameras
  Stellarators (in theory) support continuous operation
    Goal of W7-X: 30 minutes
  Archiving/compression required in (near) real time
  Present: ~100 cameras – .8 to 5.5 MP – 25 to 400 FPS (+ analyzed data)
  Example OP2.1: Divertor thermography + Halpha + EDICAM:
          35 cameras + 12x thermal: ~.8PByte raw data
Data swamp
  Risk: relevant potions are hard to find -> a lot of archived data is rarely/never read
  Fast (overview) access needed to support filtering
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization

## Slide 10: Challenges at Wendelstein 7-X – camera level
White noise
  Some cameras are very noisy
  White noise is incompressible
(Non-)Alignment of pixel data
  You need to know
  Complicates finding the non-noisy part & assess the relativity
Requirement for lossless
  Lossly compression not only looses scientific data, but changes it
  There also could be a Nobel Prize hidden in those bits we loose…
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
15 14 13 12 11 10 9 8 7 6 5 4 3 2 1 0

## Slide 11: Fusion Power Video – A short history (I)
We need to compress losslessly – what options do we have?
  Bit stream compressors: ZSTD on fast – 60% of RT, 60% compression
  JPEG lossless: 8 bpp only
  H264: >10 bpp only with expensive commercial solutions (not tested)
  H265/VP9: (max. 12 bpp) – 550% of RT, 25% compression
  FFV1: 300% of RT, 50% compression
  FFVHUFF/Dirac: < 90% of RT, >90% compression
  What about HW support? (Nvidia CUDA – Intel QSV lossy only)
  JPEG2000 CUDA: ~100% of RT, 77% compression (commercial codec, expensive)
  H264/265 CUDA: only <= 10bpp
    8/10 MSB in Y, remainder in U plane: 80% of RT, 36% compression
    8/10 MSB in grayscale, remainder in separate stream (bit packing): 60% of RT, 33% compression (~6% MSB)
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
Reference: Intel Xeon, 3.4GHz, 24 cores; 128GB RAM, Geforce GTX 2060 6GB X% compression  compressed size is X% of raw size data from 2020

## Slide 12: Fusion Power Video – A short history (II)
New upcoming, promising standard: JPEG XL
  Contacts to JPEG XL developers lead to cooperation with Google Research, Zurich
  Supported with in depth domain knowledge
  Analyzed samples of real world W7-X videos
  Identified, implemented & open sourced low compute, high impact W7-X specific compression scheme
  Collaboratively evolved the C++ implementation
    https://github.com/google/fusion-power-video
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
pro:
Support for lossless & 16+bpp
Moderate compute resources
(upcoming) open standard & open source
con:
not yet finalized (2020)
Reference implementation not ready for reference testing

## Slide 13: Fusion Power Video – Algorithm Details
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
Raw input image
Preview
¼ x ¼, 7bpp
High plane (8 MSB)
Low plane (0-8 MSB)
Left aligned input
High plane
Low plane
Preview
High plane
compressed
Preview
compressed
High plane
compressed
Low plane
Left Shift to Alignment
Plane Splitting
Delta Frame
⊝
⊝
Delta Prediction
brotli Stream Compression
Clamped Gradient Prediction
? = clamp(
min(N,E),
N + E - NE,
max(N,E))
N
NE
?
E

## Slide 14: Fusion Power Video – Implementation at Wendelstein 7-X
Where did we go from there?
  Java wrapper around the C++ library
    Performance issues at JNI boundary: copy ops & incompatible asynchrony frameworks
  Full reimplementation in native Java
    Exception: brotli compression (uses brotli4j JNA wrapper of libbrotli)
  Columnar serialization format
    Batches of e.g. 100 frames, non-interlaced planes => efficient extraction
    For now: duplicates schema & delta frame with each batch
  Example results from OP2.1:
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
Savings: 0.5 Petabytes of Archive storage

## Slide 15: Fusion Power Video – Implementation at Wendelstein 7-X
How to work with FPV data from W7-X ArchiveDB?
  Decompression is fully transparent to the reader
  SignalAccess and WebAPI offer 4 separate signals:
    full: left aligned 16 bpp (values 0 – 65535)
    highbits: left aligned 8 bpp MSBs (values 0 – 255)
    preview: left aligned 8 bpp, 4x4 subsampled (values 0 – 254)
    denormalized: reconstructed original alignment, 16 bpp (values camera dependent)
  Current limitations:
    Client side decompression using Java API (SignalAccess) – including full data download even for preview
    MultiSignalReader cannot read more than one signal from n FPV stream at a time
    No public API offering the amount of alignment shift between full & denormalized
    With compression, we pay space savings with compute: reading is slower than on raw data
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization

## Slide 16: Outlook
Try to go open source
Implement read optimizations for preview & high planes
Prevent delta frame duplication
Directly use FPV preview in W7X DataMonitor
Allow WebAPI Archive uploads with compression / of compressed data
Since it is standardized these days: evaluate jpegXL
    Would offer colored images, maybe multispectral, maybe float images, more generalized image compression
    Compare performance of FPV preview and progressive jpegXL
    Compare performance of FPV high byte only extraction and progressive jpegXL
    maybe combine approaches for future jpegXL based lossless video compression scheme
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization

## Slide 17: From first principles – a call for standardization
Let all be aligned to the left!
    When working with relative intensity images, normalize everything to 65,535
Don’t stuff your tummy with waste!
    Before compressing images, remove what’s of no value
All power to the little people!
    Almost all compute hardware today (for integers) is Little Endian – use it
All types are not created equal!
    Generally, IEEE floating point does more harm than help – prefer fixed point == integer
Digital images | Compression | S.o.t. Art | Challenges | FPV History | FPV Algorithm | FPV@W7X | Outlook | Standardization
Credit: Uy Nguyen
0.1 + 0.2 != 0.3 0/0 != 0/0 -0 == +0

## Slide 18: Questions?
Thank you very much for your attention!
Simon Fischer
simon.fischer@ipp.mpg.de
@simon-fischer-24255a109
@percurious
*