## Slide 1: Extending enhanced-performance scenarios after pellet injection in TJ-II stellarator. I. García Cortés, K. McCarthy & TJ-II team
CIEMAT, Madrid (Spain): D. Medina-Roque, T. Estrada, B. van Milligen, N. Panadero, A. Baciero, A. Cappa, R. Carrasco, J. M. Fontdecaba, R. García, J. Hernández-Sánchez, F. J. Hernanz, B. López Miranda, F. Medina, M. Navarro, J. L. de Pablos, I. Pastor, P. Pons, J. de la Riva, M. C. Rodríguez, D. Tafalla, and TJ-II team.
UC3M, Madrid (Spain): V. Tribaldos, L. García, B. Carreras.
NSC KIPT Kharkiv (Ukraine): O. O. Chmyga and O. S. Kozachok,
This work has been partially financed by grants PID2020-116599RB-I00 and PID2022-137869OB-I00 funded by MCIN/AEI/10.13039/501100011033.
50th EPS Conference on Plasma Physics, Salamanca, Spain 8-12 July 2024

## Slide 2
The TJ-II Stellarator
4-period flexible heliac-type stellarator
R = 1.5 m, a = 0.19 m,
V =~1 m3, t ≤300 ms, B0 = 0.98 T.
i0/2π = 1.2 to 2.2
~500 kW ECRH (53.2 GHz)
ne0 ≤1.7x1019 m-3
Te0 ≤1.5 keV
~1 MW of through-port NBI (30 keV)
ne0 ≤1.2x1020 m-3
Te0 ≤ 400 eV
Ti0 ≤ 200 eV
I. García-Cortés et al. 50th EPS Conference on Plasma Physics, Salamanca, Spain 8-12 July 2024

## Slide 3
S. K. Combs et al., Fusion Sci. Tech. 64 (2013) 513.
K. J. McCarthy et al, Proc. Sci (ECPD2015) 134.
N. Tamura et al., Rev. Sci. Instrum. 87 (2016) 11D619
K. J. McCarthy et al, EPL 120 (2017) 25001.
TJ-II Pellet Injector
4 H Pellets per shot.
Typical sizes:
2.4 x 1019 H
1.4 x 1019 H
0.8 x 1019 H
0.5 x 1019 H
2.2×1019 H atoms
Vp = 710 m/s
<ne> = 1.9x1019 m-3
HPI2
N. Panadero et al., Nucl. Fusion 58 (2018) 026025.
K. J. McCarthy et al, Nucl. Fusion 61 (2021) 076014.
I. García-Cortés et al. 50th EPS Conference on Plasma Physics, Salamanca, Spain 8-12 July 2024
Notes: The pellet injector is a pipe-gun type injector that can provide up to 4 hydrogen pellets per discharge.These are delivered to the plasma outer edge through straight guide tubes that have in-line diagnostics for velocity and mass measurement. Two of the lines direct pellet through the magnetic axis while the nearest approach for the other guide tubes is at rho = 0.35. Pellet ablation is followed using Halfa filterscopes.
In NBI heated plasmas pellets can penetrate well beyond the magnetic axis. Since detaching plasmoids drift outwards and downwards, the pellet deposition profile is peaked near the centre, as shown here.
Pellets injection times are pre-programmed, thus we can adjust time delays between them as required.

## Slide 4
Extending operational regime of TJ-II plasmas
H. Yamada et al., Nucl. Fusion 45 (2005) 1684. Scaling Law ISS04
M. A. Ochando et al. 41EPS (2014) Norm. factor TJ-II (NBI) 0.5
I. García-Cortés et al., PoP 30 (2023) 072506.
K. J. McCarthy et al., Nucl. Fus. 64 (2024) 066019.
τE = Wdia / (Pabs − dWdia/dt)
τEISS04= 0.5 · (0.134 · a2.28 · R0.64 · Pabs−0.61 · <ne>0.54 · B0.84 · ι2/30.41)
NBI PLASMAS
Heating power (400 - 900 kW, Co/CNTR)
Plasma wall conditioning (Boron plus lithium coating)
Mag. configuration 100_HX_65: 42,44,48
τEISS04 (ms)
τE (ms)
Notes: On the left, black and purple data points are representative plasma confinement times when fuelling is by gas-puff or wall recycling. Red, blue and green points are for NBI plasmas with pellet injection. The selected plasmas have different heating powers, different magnetic configurations (3) and for boron-lithium wall conditions.
The main difference between points above, below or on the diagonal line is the type of plasma fuelling. In TJ-II core fuelling is a key parameter to enter this enhanced phase. This is achieved using pellet injection.

## Slide 5
τEISS04 (ms)
Extending operational regime of TJ-II plasmas
PI: target density: (1 - 2) x1019 m-3
Pellet time sequence: Δt ⩬ τE
Deep core fuelling induces enhanced performance in NBI plasmas in TJ-II.
Best confinement observed to date.
τE (ms)
NBI PLASMAS
Heating power (400 - 900 kW, Co/CNTR)
Plasma wall conditioning (Boron plus lithium coating)
Mag. configuration 100_HX_65: 42,44,48
H. Yamada et al., Nucl. Fusion 45 (2005) 1684. Scaling Law ISS04
M. A. Ochando et al. 41EPS (2014) Norm. factor TJ-II (NBI) 0.5
I. García-Cortés et al., PoP 30 (2023) 072506.
K. J. McCarthy et al., Nucl. Fus. 64 (2024) 066019.
τE = Wdia / (Pabs − dWdia/dt)
τEISS04= 0.5 · (0.134 · a2.28 · R0.64 · Pabs−0.61 · <ne>0.54 · B0.84 · ι2/30.41)
Notes: On the left, black and purple data points are representative plasma confinement times when fuelling is by gas-puff or wall recycling. Red, blue and green points are for NBI plasmas with pellet injection. The selected plasmas have different heating powers, different magnetic configurations (3) and for boron-lithium wall conditions.
The main difference between points above, below or on the diagonal line is the type of plasma fuelling. In TJ-II core fuelling is a key parameter to enter this enhanced phase. This is achieved using pellet injection.

## Slide 6
Multi-pellet injection into NBI-phase
K. J. McCarthy, I. García-Cortés et al., Nucl. Fus. 64 (2024) 066019.
w/ PI
w/3 PI
NBI 400kW
w/o PI
τEISS04
τE
Wdia
<ne>

## Slide 7
Multi-pellet injection into NBI-phase
K. J. McCarthy, I. García-Cortés et al., Nucl. Fus. 64 (2024) 066019.
w/ PI
w/3 PI
Injection of a single pellet (>1019 H) causes a Pellet-induced Enhanced Confinement (PiEC) phase.
Significant increase of WE and τE
NBI 400kW
w/o PI
τEISS04
τE
Wdia
<ne>
Wdia
Pellet: 1.4x1019 H
Target density: 1.5 - 2x1019 m-3
τEISS04
τE

## Slide 8
Multi-pellet injection into NBI-phase
K. J. McCarthy, I. García-Cortés et al., Nucl. Fus. 64 (2024) 066019.
w/ PI
w/3 PI
w/o PI
Additional pellets further increase the stored energy and confinement quality f = τE / τEISS04 > 1
NBI 400kW
τEISS04
τE
Wdia
<ne>
Wdia
P1: 1.4x1019 H
P2: 0.5x1019 H
P3: 0.5x1019 H
PI: target density 1.5 - 2 x1019 m-3
Pellet time sequence Δt ⩬ τE
τEISS04
τE
τEISS04
τE

## Slide 9
Multi-pellet injection into NBI-phase
NBI 400kW
τEISS04
τE
electron density
electron temperature
Peaking ne0/ne ON/OFF
1.28 for #52580 (no PI)
1.72 for #52588 (1 PI)
1.4 for #52586 (3 PIs)
τEISS04
τE
τEISS04
τE
Notes: When we look at TS profile we see than single pellet increases the core density profile while additional small pellets broaden it. In contrast pellets have a minor effect on the Te profile.

## Slide 10
Highest TJ-II densities achieved by largest PI
NBI (480kW)
Three large pellets induce a very high density peaking factor, ne(0)/<ne> = 2
By controlling pellet settings and plasma target conditions is possible to shape density profiles and achieve record values
P1: 3.5x1019 H
P2: 1.7x1019 H
P3: 1.4x1019 H
PI: low target <ne> (1019 m-3)
I. García-Cortés et al. 50th EPS Conference on Plasma Physics, Salamanca, Spain 8-12 July 2024

## Slide 11
NBI (450kW)
PI: low target density (1019 m-3)
2 large pellets
P1: 2.0x1019 H particles
P2: 1.4x1019 H particles
PiEC: Te is similar for reference and PI plasmas, ne & Ti show clear rises after PI.
Better coupling between thermal electrons and ions
Significant ion contribution to plasma energy during PiEC
Density and temperature profiles (TS, CXRS)
ion temp. (CXRS)
electron temp. (TS)
density (TS)
Wdia
<ne>
I. García-Cortés et al. 50th EPS Conference on Plasma Physics, Salamanca, Spain 8-12 July 2024

## Slide 12
Er gradient is measured at 2 DR channels: rho = 0.8, and rho = 0.7.
Er shear (dEr / dr) at rho= 0.75 increases after each PI.
The maximum lasts about 10 ms before tending towards the reference level after 20 - 30 ms
Multi-pellets keep this Er shear at maximum level, this being coincident with longer energy confinement times.
In these experiments, there exists a clear relationship between observed improvement and the evolution of Er shear.
Effect of pellets on Er shear
dEr/dr (kV/m2)
Wdia (kJ)
#53666 REF
#53662 1 PI
#53664 2PI
#53665 3PI
100_48_65
#53666 REF
#53662 1PI
#53664 2PI
#53665 3PI
I. García-Cortés et al. 50th EPS Conference on Plasma Physics, Salamanca, Spain 8-12 July 2024

## Slide 13
PiEC
P2
PiEC
P2
PiEC
P2
Effect of pellets on plasma turbulence
More negative Er after PIs in gradient region.
Maximum energy when minimum turbulence.
DR (ρ = 0.85)
Repeated suppression of turbulence after PI
ñ and φ
∼
HIBP (ρ = 0.5)

## Slide 14
Simulations
V. Tribaldos et al. P3-071, Thursday 11th July
Role of magnetic configuration is studied by
Resistive interchange MHD code.
MHD activity associated with edge rational surface (here: 5/3) could facilitate the formation of zonal flows / transport barriers in the gradient region.
L. García et al. P3-074, Thursday 11th July
NC simulations indicate that from #55511 to #55300 there is a reduction of collisionality and an change from the Pfirsch-Schlüter to the Plateau regime.
Integrated NC heat fluxes of 55 kW for #55511 (no PI) and 122 kW for #55300 (1 PI) represent a small fraction of the 350 kW NBI power. Turbulence may play a role in PiEC.

## Slide 15
Best TJ-II performance has been achieved after pellet injection(s) (>1019 H) into its NBI-heated phase (PiEC). WEdiag and τE increase after PI, τE / τEISS04 >> 1
PiEC is characterized by increased ne(ρ) & Ti(ρ) but similar Te(ρ) and by a more negative density gradient around ρ = 0.6.
A Bifurcation is observed in performance trajectory. Interesting for intermachine comparison.
Shaping density gradient by tailoring pellet settings and plasma target conditions.
Density and ϕ fluctuations reduced by PI.
Multi-pellets keep the Er shear at maximum level, near the gradient region.
NC simulations agree qualitatively, but not quantitatively, with experimental results.
The mechanisms that lead to PiEC require further study – turbulence.
Summary
I. García-Cortés et al. 50th EPS Conference on Plasma Physics, Salamanca, Spain 8-12 July 2024

## Slide 16
Backup slides
I. García-Cortés 50th EPS Conference on Plasma Physics, Salamanca, Spain 8-12 July 2024

## Slide 17
Discharge | ne0 (x1019 m-3) | Te0 (eV) | Ti0 (eV) | WEmax (kJ) | τEdiag (ms) | τISS04 (ms) | τE / τISS04 | βnorm* (%) | β0* (%)
55300++ | 9.0 | 285 | 185 | 4.4 | 13.9 | 12.4 | 1.12 | 0.94 | 1.88
55313+ | 6.2 | 325 | 160 | 3.8 | 11.8 | 10.7 | 1.11 | 0.68 | 1.4
55511 | 5.8 | 325 | 15 | 3.0 | 8.5 | 10 | 0.85 | 0.54 | 1.12
55308 | 3.2 | 300 | 130 | 2.0 | 9.0 | 9.8 | 0.92 | 0.32 | 0.6
+ = 1 PI, ++ = 2 PIs, * = at WEmax
450 kW through-port counter NBI power
Summary of reference and pellet-injection plasmas
S. Sudo et al., Nucl. Fusion 30 (1990) 11.
A. Varias et al., Nucl. Fusion 30 (1990) 2597.
βSudo(%) = 0.55 Pabs0.77 B−0.82 a−0.69 R−0.6 = ∼0.56% [S. Sudo]
Predicted βnorm(%) for 100_44_64 is 3% [A. Varias]

## Slide 18
Clear bifurcation in triple product, ne · Ti · τΕ, towards an improved confinement branch when compared to branch product predicted by ISS04 scaling law.
Transition phase (5-10 ms) previous to PiEC phase
I. García-Cortés, K. McCarthy et al., PoP 30 (2023) 072506.
Pellet fuelling enhances the triple product
ne · Ti · τΕ (x 1019 m-3 keV s)
ne · Ti · τΕ (x 1019 m-3 keV s)

## Slide 19
Inter-machine performance comparison
A. Dinklage et al., to be sent to NF (2024).