## Slide 1: WP PWIE
Sebastijan Brezinsek, Michael Reinhart
Forschungszentrum Jülich
JT60SA – transition to full-W

## Slide 2: Input up to know …
WPPWIE has exposed a pre-series W sample from Japanese origin provided by R. Neu
WPPWIE was in discussion to support WPDIV regarding W divertor in the following topics:
  Divertor optimisation with SOLPS-based algorithm from KU-Leuven: optimisation on heat flux reduction, target temperature: standard SN solution with variation of curvature targets, strike-line position, leg distance
    At that time, it was unclear if actively cooled C divertor design has to prevail at what freedom exists
    Problem now – responsible person at KU Leuven left and one need to provide additional resources to recover
  W divertor PFC qualification and characterisation under steady-state loads expected in JT60-SA
    Exposure in MAGNUM-PSI or PSI-2 to divertor-like plasma conditions under steady-state load
    As no PFC material was available to load with plasma, no tests have been done
    Note, pure heat load tests are done in WPDIV => combined plasma and heat load tests and characterisation in WPPWIE
  W erosion modelling of divertor PFCs
    Not followed up due to uncertainties in time scale, plasma backgrounds, divertor types etc.
    Note, principle data about “typical conditions and impact of magnetic field” already exists

## Slide 3: Where we could help ….
WPPWIE can support in the qualification of divertor and first wall PFC
  Power and plasma handling: transients and steady state in portfolio of WPPWIE devices
  Erosion and retention properties, material properties etc. prior and post exposure
  This can be included in the present program for 2025 within budget (priority change)
  Support in analysis if samples are exposed in WPTE facilities (manipulators)
  Note, several material solutions for the W divertor and first-wall W coatings schemes have already been qualified for
  other facilities and purposes => synergies
WPPWIE can support in the PWIE simulation of W sources and W migration
  Workflow in TSVV-6 (SOLEDGE3X + ERO, EMC3-EIRENE + ERO) and TSVV-7 (SOLPS-ITER + ERO) exists
  Might require additional resources for plasma-background and PWIE modelling
  Dedicated input to required W PFC thickness and potential W influx from divertor and main chamber (ITER-like?)
WPPWIE can in principle support in divertor design optimisation
WPPWIE can in principle support neutral particle modelling (EIRENE or DIVGAS)
WPPWIE can in principle support in area of wall conditioning related to B
WPPWIE can in principle support in spectroscopic diagnostics related to W
Important: One team approach with WPSA, WPTE, WPDIV, WPPWIE, WPMAT
F4E and clear defintion and hand-over points