## Slide 1: Neutral pressure and compression in LHD 2020-04-20 U. Wenzel, G. Motojima, V. Haak, S. Masuzaki

## Slide 2: Motivation -> Test of LaB6 emitters in a neutron environment 20 % 10B, 10B is very sensitive to neutron capture
9kura
Subject of the master thesis of Victoria Haak, not reported here.

## Slide 3: Helical divertor in LHD
Fully closed, not pumped.
Works in the inboard shifted
Configuration only
Divertor slit in front
Of the 8i

## Slide 4: Pressure gauge positions
8I
8.5U
9kura
Morisaki et al. First results of closed
helical divertor experiment in LHD

## Slide 7: LHD 156883 – 2 LaB6 pressure gauges are operational
Delay between 9k and 8i
of almost 1 s
Recombination
peak
The pressure in 9k follows the
density and the energy Wdia
Particle confinement
P is in the 10-4 mbar range
ne = 2e19 m-3

## Slide 8: Data Set 2020-01-15 - All Pressures over Density
Reduced
data
set
8.5u
8i
9kura
High pressure in 9kura
is unexpected!
Will not be used as a reference
for the in vessel pressure
Instead 8.5u position will be used
which is in the vessel on top

## Slide 9: Comparison of 8.5u position from 2020-01-15 and 2020-01-29
On 2020-01-15 in-vessel
pressure follows density
2020-01-29 large scatter
3 data sets
Outward shifted cryopump on
Inward shifted cryopump on
Inward shifted cryopump off
Do not use 9kura, but 8.5u

## Slide 10: Data Set 2020-01-29 - Divertor Pressure 8i over Density
Inward shifted config. pdiv ~ ne
Outward shifted config. pdiv saturates

## Slide 11: Data Set 2020-01-29 – In-Vessel Pressures over Density
Outboard shifted configuration pressure increases (it is more isotropic)

## Slide 12: Data Set 20-01-29 – correlation p 8.5U – p 8i - compression
R= 3.8m outboard shifted
No neutral compression
R= 3.6m inboard shifted
Neutral compression about 6
No influence of cryo pumping on
the neutral compression in the
inboard shifted configuration

## Slide 13: Data Set 20-01-29 – Correlation Divertor-Outboard Pressures
Divertor pressure 8i is always smaller
Particle source from the 9kura position is not „seen“ by the divertor in 8i position.
Compression
>1
Compression
< 1

## Slide 14: Summary
Both LaB6 pressure gauges are functional. We got some information about the performance with neutrons  Victorias master thesis.
Results
  Outboard pressure (9kura position) is very high – was not used up to now because it contradicts modeling
Neutral compression is typically 6 in the inward shifted configuration when related to the pressure on top, no influence of the cryopumps on neutral compression in the data set 2020-01-2
Influence of magnetic configuration:
  Lower in-vessel pressure in the inboard shifted configuration (reasonable)
  Higher neutral compression in the inboard shifted configuration (about 6) compared to the outboard shifted configuration (no significant compression)

## Slide 15: Comparison to W7-X
Similar maximum divertor pressures of 2e-3 mbar obtained in W7-X and in LHD  exhaust would be similar
The neutral compression of 6 in the inward shifted configuration in LHD is comparable to W7-X OP1.2a
In general in LHD the pressure in the vacuum vessel is higher to W7-X  lower compression ratios in LHD.
LHD -- 2020-01-29
P 8.5U 4e-5 mbar
P 8i 2.5-e4 mbar