## Slide 1: IJCLab and its contribution to HerHEA project In situ TEM with He ion implantation of HEA at IJCLab Stéphanie Jublot-Leclerc, Aurélie Gentils + new postdoc : Antoine Combrisson Université Paris-Saclay, CNRS/IN2P3, IJCLab, Orsay, France Meeting #2, 14/11/2024
EUROfusion, ENR-MAT.02.VTT-T001
2024-2025
https://indico.euro-fusion.org/event/3309/

## Slide 2: Our task : observing the bubbles nucleation and growth by in situ ion TEM
- which compositions of alloys for the
in situ exp. ?
- thin foil preparation dev. / optimization
- ions parameters (similar as for some ex situ experiments ?)
Helium, 10-20 keV
One condition: influence of a coupled few MeV irradiation ?
- implantation temperature : RT and 500°C
- Observation of He bubbles nucleation and growth vs fluence
10 – 500 keV ions
IRMA
ARAMIS
0.5 – 6 MeV ions
Orsay
M3.1 In situ TEM experiments performed (Links to D3.1) June 2025
« The evolution of created defects (and, in particular, the size and density of cavities, voids and bubbles) will be monitored in different compositions vs the fluence at room temperature and 500°C), for selected parameters chosen with the help of simulations. »
To be chosen : binary -WMo, WTa, WV, ternary –WTaV- or WTaMoNbV ? and W ?
https://mosaic.ijclab.in2p3.fr
From MF Barthe
HerHEA project, EUROfusion, ENR-MAT.02.VTT-T001, 2024-2025
In situ TEM coupled to 190 kV IRMA ion implanter and 2 MV ARAMIS accelerator
https://indico.euro-fusion.org/event/3309/

## Slide 3: Literature – He ion implantation in W-based HEA
https://doi.org/10.1016/j.nme.2023.101513
W-Ta-Cr-V thin film, 200 keV He+ at RT
HerHEA project, EUROfusion, ENR-MAT.02.VTT-T001, 2024-2025
https://indico.euro-fusion.org/event/3309/

## Slide 4: Future work
Select the material(s) to be studied (depending on availability)
Prepare TEM thin foils (to be optimized)
Check the initial microstructure
Select the He ion implantation conditions (based on the literature data + simulations ?)
energy, temperature, range of fluence (+ coupled to irradiation ?)
Ex situ + in situ TEM ?
to follow the nucleation and growth of bubbles
Analyse the data
Interpretation + publication
HerHEA project, EUROfusion, ENR-MAT.02.VTT-T001, 2024-2025
https://indico.euro-fusion.org/event/3309/
We found a subcontractor in France for the EDM to cut the specimens as requested for the characterization techniques.
The delay is short (less than a week), and the price is 25 € per sample (square of 7*7*0.5 mm).
As there is 4 compositions (W, W-Ta, W-Mo and W-V), and we need 12 samples of each (10 for CEMHTI, and 2 for IJCLab), the total cost is 25 x 4 x 12 = 1300 €

## Slide 5
ARAMIS
IRMA
TEM
Ion modification and analysis of materials, in situ TEM
Home-made ion accelerators
In situ dual ion beam Transmission Electron Microscope
since 1980 Updated in 1994, 2007
M.-O. Ruault et al., J. Mater. Res. 20 (2005) 1758
A. Gentils et al., NIMB 447 (2019) 107
IRMA since 1979
  190 kV ion implanter
  10 - 570 keV, up to 20 mA
  Bernas-Nier source
J. Chaumont et al., NIMB 198 (1981) 193
ARAMIS since 1987
2 MV Tandem – Van de Graaff
SNICS negative ion source:
500 keV < E < 11 MeV ; 10 nA < i < 10 mA
Penning source @ HV : i < 20 mA
200 keV < He < 3.6 MeV ; 200 keV < H < 1.8 MeV
E. Cottereau et al., NIMB 45 (1990) 293
H. Bernas et al., NIMB 62 (1992) 416
Ion implantation Ion irradiation
LN2 –> 1000°C
Available elements
Ion Beam Analysis
RBS, RBS/C, ERDA, PIXE, mPIXE, PIGE
XRD
in construction (SIXPAC project)
Ion implantation and in situ RBS/C
LN2 –> 600°C
The JANNuS-Orsay experimental hall :
ARAMIS, IRMA, in situ TEM
https://mosaic.ijclab.in2p3.fr