## Slide 1: Meeting to identify Digital Twin Pilot projects: Breeding Blanket
S. D’Amico on behalf of the BB design Team and the DEMO Central Team
Identification of Digital Twins projects
16 December 2024

## Slide 2
Breeding blanket technology is crucial for the development of fusion power
  Heat removal for electrical production: (~300-500 MWe) predictably and safely, with minimal environmental impact
    use Reduced Activation Ferritic-Martensitic ‘RAFM’ steel  EUROFER
    minimization of tritium permeation, dust and corrosion products generation
  Breed tritium: “a 2 GWth fusion power DEMO will consume around 111 kg T/FPY, and this clearly underscore the indispensable requirement to achieve T-self-sufficiency”
  Radiation Shielding of the Vacuum Vessel and Coils
    Absorb plasma radiation on the first wall
    Dose in epoxy / 10 fpys - Limit: 50 MGy
    N-heating - Limit: ~444 W/m³ (TF cond.)
Breeding Blanket R&D Programme: Background
M. Kovari et al, (2018) Tritium resources available for fusion reactors, Nuclear Fusion, 58, 026010, DOI: 10.1088/1741-4326/aa9d25
  The main BB Loads and boundary conditions are:
    Inertial (dead weight and earthquake)
    Thermal (nuclear heating and heat fluxes)
    Pressure and Electromagnetic loads
    Material damage

## Slide 3: Current BB design variants: the HCPB concept
Helium Cooled Pebble Bed Concept (HCPB)
Structural Material: EUROFER (RAFM steel), ~3000 t
Breeder: ACB-KALOS (Li4SiO4 + 35 mol% Li2TiO3 ) in form of a pebble bed, 6Li at 60%, ~165 t
Neutron multiplier: Beryllide (TiBe12) hexagonal rods, 612 t
Coolant: helium 300-520°C @ 8 MPa, ~ 4.2 t
Plasma protection: 2 mm W layer (wo Limiters)
T extraction with purge Helium: 0.1% H2 (%H2O) @ ~8 MPa, ~ 137 m3
G. Zhou et al, (2023) The European DEMO Helium Cooled Pebble Bed Breeding Blanket: Design Status at the Conclusion of the Pre-Concept Design Phase, Energies, 16, 5377 , DOI: 10.3390/en16145377

## Slide 4: Current BB design variants: the WCLL concept
Water Cooled Lead Lithium Concept (WCLL)
Structural Material: EUROFER (RAFM steel), ~3500 t
Breeder/neutron multiplier: PbLi (6Li at 90%) liquid (~330 °C @ 0.25-1.55 MPa), ~10,000 t,
Coolant: Water (295-328°C @ 15.5 MPa), ~520 t
Plasma protection: 2 mm W layer (wo Limiters)
T extraction from recirculating PbLi
P. Arena et al, (2023) Design and Integration of the EU-DEMO Water-Cooled Lead Lithium Breeding Blanket, Energies, 16, 2069 , DOI: 10.3390/en16042069

## Slide 5: Exploring variants: the WLCB concept
    Water-cooled Lead Ceramic-Breeder Concept (WLCB)
    Structural Material: EUROFER (RAFM steel)
    Coolant: Water at PWR conditions (285-325 °C @155 bar)
      cooling scheme: BZ and FW in series
      radial cooling plates (acting as stiffeners)
    Breeder: ACB (Li4SiO4 + 35 mol% Li2TiO3 ) in form of a pebble bed, 6Li at 60% and Li8XO6, X=Pb, Zr…) in cassettes
    Purge gas: He + %H2 @2bar
    Neutron multiplier: molten Pb in cassettes
    Neutron spectra shifter: metal hydride such as ZrHx (?) or YHx (?) in cassettes
    Cassettes (cladding): SiC (?) ~2 mm thick

## Slide 6: Important points and possible problems around the topic: BB modelling (for minimum design)

## Slide 7
Water activation analysis
Tritium transport analysis
Electromagnetic analysis
Etc. (e.g. MHD, activation, …).
Important points and possible problems around the topic: BB modelling (for extended design)

## Slide 8: Toward a Breeding Blanket Digital Twin?
V. Badalassi et al, (2023) FERMI: Fusion Energy Reactor Models Integrator, Fusion Science and Technology, 79, 345-379 , DOI: 10.1080/15361055.2022.2151818
Near term objective: identification of a common simulation framework plus workplan for its development
No integrated or component tests in a relevant environment available
Digital Database
Uncertainties Evaluation

## Slide 9
… for your kind attention!

## Slide 10: Neutronic analysis
Neutronics workflows for system design and plant radiological protection analyses
HCPB Blanket MCNP model
Nuclear responses (heat, flux, etc.)
Courtesy of D. Leichtle

## Slide 11: Thermal-hydraulic analysis
Local model
Implementation of material properties, correlations (e.g. contact resistance, etc.)
Power density on the whole volume;
Non-uniform heat flux on the FW (max 0.1-0.5 MW/m2);
Temperature and mass flow rate of the working fluid;
Adiabatic conditions on the sides and back of the BB;
Symmetry conditions in the poloidal direction.
Segment model
Use of porous domains.
Courtesy of G. Zhou

## Slide 12: Structural analysis
Courtesy of A. Retheesh
Courtesy of I. Catanzaro
Shift channels 2mm inwards