## Slide 1: Digital Twin Pilot Project brainstorming Flight Simulator 16/12/2024
F. Imbeaux
Acknowledgements to E. Fable, R. Nouailletas, P. David, J.F. Artaud

## Slide 2: Why a Flight Simulator ?
A Flight Simulator is a fast but comprehensive simulator of the plasma + actuators + diagnostics + control system
Function: used to check that a Pulse Schedule will result in a successful plasma when programmed on the real experiment
  Physics targets reached
  Within the operational limits of the machine
  Using the actual controllers of the experiment
Systematic use of a Flight Simulator is foreseen in ITER before authorizing any real experiment
Flight Simulator tools already exist, for instance:
  FENIX for AUG and DEMO, being also tested in TCV and starting to implement external IMAS interfaces under TSVV15
  NICE+METIS for JT-60SA
  NICE only for WEST, coupling to METIS is ongoing under MUSCLE3 framework
  It would be nice to get applications and validation on more than one of the present EUROfusion devices, as well as more modular tools to test different equilibrium solvers

## Slide 3: Possible improvements of existing Flight Simulators
Make the Plant simulation part (plasma+actuators+diagnostic) machine generic  IMAS interfaces
  Internal IMAS interfaces allow testing also different equilibrium reconstruction methods on the same platform
More realistic description of diagnostics (synthetic diagnostics) and actuators (system response time), test of robustness to noise, missing sensors, parameters of the Real Time equilibrium reconstruction
Performance optimisation / use of NN surrogate models  covered by TSVV15
Coupling with automated optimisation of Feed Forward waveforms, controller parameters, physics model parameters
Integration of discharge forecasting to control algorithms seems too much exploratory for a 1 year project
Different teams have different interests in the items listed here
Connection/application to other WPs: WPTE, WPPrIO
1 year pilot project, limited to 2025, challenging to hire additional manpower on so short a time scale