## Slide 1: SP-F Update and Plans & Discussion
Andrei Goriaev
LPP-ERM/KMS
WP PWIE Meeting 2025

## Slide 2: Outline
SP F3:
Activities at TOMAS with test of ITER conditions and needs: ECWC, ICWC, GDC
Cleaning activities of B-layers from lab or tokamaks in TOMAS
Application of in-situ LID-QMS or LIBS in those systems
SP F2:
(In-situ) laboratory experiments with B layers (PSI-2, MAGNUM, GYM) focus on B erosion, deposition, retention within capabilities
Generic wall conditioning studies
SP F1:
Coordination of activities related to wall conditioning and boronisation with strong links to activities of machines in TE/W7-X
Recapitulation of existing knowledge
Benchmark in TE/W7-X experiments: manipulator / full device
SP F / Wall conditioning & Boronization

## Slide 3: SP F1: Coordination of wall conditioning and boronisation activities
Deliverable Owner | Beneficiary | PM | Deliverable (Team)
A. Gallo | CEA | 3 | D001
T. Dittmar | FZJ | 3 | D002
V. Rode | MPG | 3 | D003
Total |  | 9 | 
Tasks to be performed:
Review of boronization procedures, experimental settings, and efficiency of boronization in toroidal devices.
Define new experiments in collaboration with TE and W7X and assessment of improved diagnostic access.
As for 2025
W7-X -> ?
CEA -> only WP TE contribution
Other devices -> ?
As for 2024

## Slide 4: SP F1: Recapitulation of existing knowledge
Knowledge structuring
equipment for boronization
  Pumps, diborane injectors, sensors, decomposers, GD anodes, ...
parameters of boronization procedures
  GD pressure and current, injection, duration, gas composition, ...
diagnostics (in-situ & post-mortem)
  Quartz Micro Balance (QMB), Residual Gas Analyzer (RGA), ...
boronization frequencies and need for boronization
  time of boron layer deterioration, special needs (plasma start-up, ...)
experimental data and results of boronization
  Effect on the consequent plasma performance
dedicated PWIE studies (-> SP F2: Benchmark in TE/W7-X experiments: manipulator / full device)
  post-mortem PFC analysis, sample exposures, etc.
ITER modeling of spatial distribution of diborane reactions with respect to GD anode position (green) and injection points (red) in H2 GD. T. Wauters et al., NME 42, 2025).

## Slide 5: SP F2: (In-situ) laboratory experiments with B layers
Main focus on
Reference boron coated sample production and analysis for wall conditioning needs
Studies of fuel removal and retention in reference samples by laboratory wall conditioning – relevant plasmas
Studies of erosion and redeposition of mixed boron layers from reference samples by laboratory wall conditioning – relevant plasmas
A lot of overlapping activities with SP B -> strong coordination required!
Characterization of H2-GDC and corresponding erosion rates estimation in TOMAS
Pressure, *10-3 mbar

## Slide 6: SP F2: (In-situ) laboratory experiments with B layers
Laboratory investigations on hydrogen/deuterium retention behavior in boron films
  CEA, MPG, VR, CIEMAT, ...
Boron layer production set-ups/tools
  Magnetron sputtering, plasma-enhanced chemical vapor deposition, Pulsed Laser Deposition
Available diagnostics
  XPS, TDS, NRA, ...
Responsible people
Human resources involved
What we need to define is

## Slide 7: SP F2: (In-situ) laboratory experiments with B layers
IAP experiments. Boron plasma coatings and boronization studies
Speakers: Dr Corneliu Porosnicu (IAP), Sorin Vizireanu (IAP)
In-situ ion beam analysis of deuterium retention in W-B layers: effects of composition and incorporation pathway
Speaker: Eduardo Pitthan Filho (VR)
Example of sample preparation and characterization in FZJ
Manufacturing, polishing, annealing
  Boron coating by physical vapor deposition (PVD) using RF magnetron sputter device
  Deuterium insertion close to substrate during deposition process
Sample pre-characterization and post-mortem analysis
  Boron layer characterization (crystal phase, microstructure, thickness and elemental composition)
  -> XRD, FIB/SEM, EDX
  Deuterium content -> NRA, TDS

## Slide 8: SP F2: Generic wall conditioning studies
Standard wall conditioning methods
Initial wall conditioning (after venting)
  Baking
  Glow Discharge Cleaning
Regular wall conditioning (during plasma operation phase)
  Glow Discharge Cleaning
  Electron Cyclotron Wall Conditioning
  Ion Cyclotron Wall Conditioning
  Wall coating (Boronization)
Real-time wall conditioning
  Boron dropper
  Operation with elevated wall temperature
We need to define what generic wall conditioning is!

## Slide 9: SP F3: TOMAS
Deliverable Owner | Beneficiary | PM | Deliverable (Team)
S. Möller | FZJ | 6 | D001
Y. Kovtun | KIPT | 6 | D002
A. Goriaev | LPP-ERM-KMS | 16 | D003
P. Petersson | VR | 4 | D004
Total |  | 32 | 
Tasks to be performed:
Optimize and characterize wall conditions cleaning schemes in TOMAS and beyond
Laser-based analysis system
Assess efficiency of cleaning of boron-containing samples

## Slide 10: SP F3: Activities at TOMAS with test of ITER conditions and needs
A highlight talk of TOMAS results and plans
Speaker: Luis Daniel Lopez Rodriguez (LPP-ERM-KMS)
Current plasma-based wall conditioning studies
Glow Discharge Cleaning (GDC)
  Characterization of plasma parameters, input for GD modelling, input for sample exposure experiments
Electron Cyclotron Wall Conditioning (ECWC)
  Studies of wave absorption and propagation for model (e.g. TOMATOR-1D) validation
Ion Cyclotron Wall Conditioning (ICWC)
  Characterization of plasma parameters, charge-exchange neutrals generation
Mixed ECWC+ICWC, GDC + EC
  Behavior of plasma parameters, optimization of existing schemes
Diagnostics for wall conditioning studies
  Residual Field Energy Analyzer (RFEA)
  Time-of-Flight Neutral Particle Analyzer (ToF NPA)
  LID QMS development

## Slide 11: SP F3: Cleaning activities of B-layers from lab or tokamaks in TOMAS
ITER-relevant activities
  Erosion and deuterium removal from D-dopped boron layers on tungsten substrates by GDC and ICWC at elevated wall temperatures
Contribution to W7-X boronization studies
  Studies of boron layer erosion from graphite and tungsten substrates by GDC and ICWC
Near-surface composition of TEXTOR samples
  Impurity and fuel removal from mixed C-B layers on Graphite substrates
SEM (FIB)
B
Pt
W
TEXTOR co-deposits
Boron-coated W samples for ITER-relevant studies