## Slide 1: Plasma background and impurity migration modelling for COMPASS-U
D. Tskhakaya1, D. ŠvorC1, S. Lukeš1, H. Kumpulainen2, P. Tamain3, I. Borodkina1, O. Shyshkin1, ERO2.0 and IPP T@M Department teams
1Institute of Plasma Physics of the Czech Academy of Sciences, Prague, Czech Republic
2Institute of Fusion Energy and Nuclear Waste Management, 52425 Jülich, Germany
3IRFM/CEA, Cadarache, 13108, St-Paul-Lez-Durance, France

## Slide 2
COMPASS-U
R= 0.894 m, a = 0.275 m
High magnetic field (BT ≤ 5 T) and high-current (Ip ≤ 2MA)
ITER and DEMO relevant geometry;
advanced plasma configurations
nsep ~ 1020 [m-3]
Hot-wall operation (up to 500°C)
High power fluxes in the divertor (λq ~ 0.7 - 1 mm)
Metallic first wall and/or liquid metal divertor
Optimized for plasma edge study

## Slide 3
Numerical / analytical tools (plasma edge)
Field line SOL codes
SOLPS-ITER
Impurity transport
ERO2.0, Aurora
Kinetic (PIC MC) modelling of SOL and plasma sheath
BIT1, SPICE2,3
Edge turbulence codes
GBS, …
PWI codes
SDTRIM, …
In near future
Equilibrium + core transport
FIESTA, METIS, ASTRA, …
External (PWIE)
SOLEDGE3X
The main toolbox
Plasma profiles

## Slide 4
Outline
  Field line simulations
  SOLPS-ITER
  SOLEDGE2X
  ERO2.0 modelling of impurity transport in COMPASS-U
  Kinetic models of the COMPASS-U SOL

## Slide 5
SOLPS-ITER modelling 2024
[K. Krieger, et al., Nucl. Fusion 65 (2025)]
METIS / FIESTA (CUDB)
Shot | Ip (MA) | Bt (T) | Pin (MW) | PSOL (MW ) | Ne,sep (1020 m-3) | Λq (mm)
#24300 | 1.2 | 4.3 | 3+1 | 3.0 | 1.72 | 0.79
#5400 | 1.6 | 4.9 | 4+2 | 4.6 | 1.90 | 0.65
λq ~ 0.6 - 1 mm
[F. Jaulmes, et al.]

## Slide 6
Matching core profiles and lq
  #24300
  #5400
[I.Borodkina, et al., PSI (2024)]

## Slide 7
Divertor profiles

## Slide 8
Identifying the problem (i)
#5400
OMP
Te
OMP
ne
λ
λ
Narrow gap
[D. ŠvorC / O. Shyshkin]
Divertor baffle
SOLPS-ITER version 3.0.9
Good match with METIS core profiles
B2.5 mesh extent limited by outer divertor baffle

## Slide 9
SOLPS-ITER non wide-grid for #5400
~ 45% of input power leaving through the outer B2.5 boundary
SOLPS-ITER wide grids version required
Identifying the problem (ii)
[D. ŠvorC / O. Shyshkin]
fhe,i - electron, ion thermal energy flux
fnt - convective heat flux - viscous correction terms for ions
fhm - kinetic energy flux
fhp - ionization energy flux
fhj - electrostatic energy flux
fht - total energy flux

## Slide 10
SOLPS-ITER wide-grid (wg-3.2.0-alpha)
OMP
Te
OMP
ne
#5400
Full vessel mesh, fluid neutrals
Good match with METIS separatrix values
SOL decay length (lq) not matched: adjustments to SOL transport coefficients needed
[D. ŠvorC / O. Shyshkin]

## Slide 11
SOLPS-ITER modelling: future plans
Development/adoption of better analysis tools for the wide-grids unstructured mesh
Adjustment of transport to match lq
Move from fluid neutrals to kinetics (EIRENE)
Include impurities and drifts
Updates in manpower (SOLPS-ITER - COMPASS-U)
I. Borodkina (maternity leave)
O. Shyshkin (left)
Daniel ŠvorC

## Slide 12: SOLEDGE3X COMPASS-U simulations
Objective: produce SOLEDGE3X up-to-the-wall backgrounds for COMPASS-U to
  compare with SOLPS-ITER solutions
  evaluate fluxes and conditions on the wall
SOLEDGE3X mesh
Wall mask function
EIRENE
mesh
Simulation set-up:
  scenario #5400
  pure D plasma, no impurities
  no drifts, no current
  W wall, no sputtering, R=1
  no gas puff & pump
  Input power: 2MW (e-) + 2.7MW (D+)
  at core boundary

## Slide 13: Preliminary results (not converged))
WIP - not converged
WIP - not converged
WIP - not converged
Simulations up and running, not converged, but already:
  Plasma could detached at strike-point
  Significant flux and ion temperature at shoulder of outer target
  Power load to the wall << divertor + fuffle power loads
Shoulder of outer target
WIP - not converged

## Slide 14
ERO2.0 simulations (LM)
First Li & Sn simulations [S. Lukes et al., PSI (2024)]
HeatLMD
SOLPS
ERO2.0
Aurora
q⊥
2D plasma
LM erosion
rate
LM density
near separatrix
Core radiation
Li density profile for #5400
FACIT transport coefficients for Sn (Li: the same anomalous coefficients as for D)

## Slide 15
ERO2.0 simulations (updated approach)
Additions from SOLPS-ITER
global electric field
global thermal force: Fth ~ q||
increased time & spatial resolution,
Sheath is prescribed analytically
[simulations by S. Lukes]

## Slide 16
Outer Divertor Baffle can be the dominant source of W (lower prompt redeposition and higher anomalous diffusion than at the strike-points)
Average W core concentration < 10-3 %:
below the critical limit.
To be addressed in future runs:
updated background plasma
effects of core poloidal asymmetries & ELMs [H. A. Kumpulainen et al., Plasma Phys. Control. Fusion 66 (2024) 055007]
[simulations by S. Lukes]
ERO2.0 simulations (W)
W density (#5400)

## Slide 17
Kinetic (BIT1) simulations
Outer wall
Plasma and heat source
Outer
divertor
Inner
divertor
Fueling, impurity seeding
e, D+
D recycling
W sputtering
Be/W sputtering
synthetic diagnostic
No seeded impurity
Simulation “price”: ~200 M CPU hours

## Slide 18
 | Sheath | ne,div [1021 m-3] | Te,div [eV] | Ti,div [eV] | qpl, div [MW /m2] | Fdiv [1024 /m2s] | FW, gr [1019 /m2s] | FW, net [1019 /m2s]
#5400 | col. / col. | 6.0 / 3.3 | 6.5 / 11.3 | 5.6 / 7.1 | 25 / 68 + neutrals (<10) | 4.47 / 4.66 | 6.0 / 10 | 4.0 / 5.0
Low n | clas. / clas. | 0.32 / 0.15 | 4.8 / 13.7 | 5.1 / 6.6 | 5.3 / 10.1 | 0.47 / 0.35 | 5.3 / 5.6 | 0.0 / 1.3
Kinetic simulations: results
Parallel Mach number profiles at the ID
Angular DF of D+ ions absorbed at the ID

## Slide 19
Electron VDF at the divertor plate
Collision effect
Reduced sheath potential drop
ID
Nonclassical VI characteristics?

## Slide 20
Conclusions
  First set of field line code modelling of COMPASS-U has been completed. Simulations predict partial plasma detachment in high performance scenarios even without impurity seeding. Some results need revision, e.g. high wall heat loads.
  Updated models are under preparation / or started: SOLPS-ITER-wg, seeded impurity and drifts.
  ERO2.0 modelling: no W accumulation for #24300, #5400 (cases without ELMs, impurity and drifts); next steps: to use updated plasma background, include ELMs and core poloidal asymmetries.
  Kinetic models of the COMPASS-U predict formation of collisional sheath.
  New simulations are running /or under preparation (ELMs, seeded impurities). We have new BIT1 modelers at the IPP CAS: Jakub Hromadka and Simon Vrba.
  In one week we will host BIT1 Hackathon with more than 30 registered participants.

## Slide 21
EDF of plasma particles during ELMs
ELM
Thermal
EDFs are far from the Maxwellian at any time  kinetic modelling is required
EDF for electrons and ions from ELMy SOL modelling of ASDEX-tokamak SOL with Type-I 60 kJ ELM (from PIC simulations)