## Slide 1
Training on the use of
IDS2CPO & CPO2IDS
translation tools from IDSs to CPOs and back again
Adapted from: ETS training – October 2019, MP-IPP, Garching , Germany

## Slide 2: Data workflow
IDS / IMAS
Mapping tools
1 to 1 : WEST Imasgo! : JET & MAST
Trview : AUG
tcv2ids : TCV
JET
Data server
ETS in CPOs
CPO / ITM
ids2cpo/ cpo2ids

## Slide 3
IDS / IMAS
CPO / ITM
ids2cpo
ids2cpo
this tool is written in python and translates IDSs into CPOs, making experimental data on IDSs available to ETS v.5 which relies on CPOs.
can be extended easily by the user for use cases that rely on data that is not translated by default
it is available to users on the ITM environment (module load itmenv), and can be found in $KEPLER/kplots/ids2cpo for every new release of ETS
options are available for particular use cases, which can be learned during ETS training sessions or WPCD code camps
typical use case: $KEPLER/kplots/ids2cpo --user <username> <device> <pulse> <run>
for help on usage do: $KEPLER/kplots/ids2cpo -h
ids2cpo – translation between data formats

## Slide 4
ids2cpo – typical use cases
To get help run:
$KEPLER/kplots/ids2cpo -h
$KEPLER/kplots/ids2cpo -h
usage: ids2cpo [-h] [--toRun TORUN] [--user USER]
[--forceImpurities FORCEIMPURITIES [FORCEIMPURITIES ...]]
[--ignoreIons IGNOREIONS [IGNOREIONS ...]]
[--addMD ADDMD [ADDMD ...]] [--AUGMD] [--no23] [--filterNBI]
[--useOldAL] [--verbose] [--flipEC]
machine pulse run
ids2cpo translator
positional arguments:
machine tokamak (database) where the IDSs are stored
pulse pulse number
run run number
optional arguments:
-h, --help show this help message and exit
--toRun TORUN write CPOS to a given run
--user USER owner of the database where the IDSs are stored (…)
--forceImpurities FORCEIMPURITIES [FORCEIMPURITIES ...]
listed ions are initialised as impurities
--ignoreIons IGNOREIONS [IGNOREIONS ...]
listed ions are ignored during the translation
--addMD ADDMD [ADDMD ...] (…)
to add machine description of supported devices from (…)
local MDdb in CPOs. Supported devices: jet, mast,
mast-u
--AUGMD Augment AUG NBI with MD
--no23 set to zero the half and third (NBI) beam current and
energies
--filterNBI set NBI power to zero if beam energy is lower than 20
KeV
--useOldAL use old UAL(Access Layer) and IMAS/DD 3.20.0
--verbose increase log verbosity
--flipEC flip EC launching poloidal angles

## Slide 5
ids2cpo – typical use cases
To convert IDSs from AUG to CPOs run:
$KEPLER/kplots/ids2cpo --user g2dpc aug 36440 3 --AUGMD
Translating IDSs to CPOs
creating ITM/cpo pulse:36440 run:3 machine:aug version:4.10b user:g2jofe
translating equilibrium IDS
found 73 timeslices in equilibrium
saving equilibrium data into CPO
translating core_profiles IDS
found 300 timeslices in core_profiles
core_profiles has 2 ions, 2 will be translated to CPOs,
ion 1: A=2.00, Zn=1.00
ion 2: A=12.00, Zn=6.00
and 0 will be translated to impurity ions.
saving coreprof data into CPO
saving coreimpur data into CPO
(…)
translating wall IDS
found 1 timeslices in wall with 2 2d description(s)
saving wall data into CPO
translating nbi IDS
augmenting AUG NBI with data from MD
found up to 100 timeslices in nbi units
saving nbi data into CPO
translating EC and IC antennas IDS
found 225 timeslices in ec_antennas with 8 antennas each
found 195 timeslices in ic_antennas with 4 antennas each
saving antennas data into CPO
done!

## Slide 6
ids2cpo – typical use cases
To convert IDSs from TCV to CPOs run:
$KEPLER/kplots/ids2cpo --user g2ferik tcv 61021 3
translating wall IDS
wall with 1 2d description(s)
saving wall data into CPO
translating nbi IDS
found up to 20095 timeslices in nbi units
saving nbi data into CPO
translating EC and IC antennas IDS
found 11060 timeslices in ec_antennas with 9 antennas each
Warning! p.ec_antennas.antenna[0].beam.spot.size.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[1].beam.spot.size.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[2].beam.spot.size.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[3].beam.spot.size.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[4].beam.spot.size.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[5].beam.spot.size.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[0].beam.phase.curvature.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[1].beam.phase.curvature.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[2].beam.phase.curvature.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[3].beam.phase.curvature.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[4].beam.phase.curvature.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
Warning! p.ec_antennas.antenna[5].beam.phase.curvature.data is empty or inconsistent. Please update this leaf
the leaf will be filled with zeros
saving antennas data into CPO
c
done!

## Slide 7
ids2cpo – typical use cases
typical use
$KEPLER/kplots/ids2cpo
--user <username where imas are>
<machine> <shot> <run>
--AUGMD. (option needed for AUG)
--toRun <run out>
--no23. (zero half and third NBI energy/current fractions, useful for TCV)
--useOldAL ( if you IDS data was stored using the use old UAL 3 )
--filterNBI ( set NBI power to zero if beam energy is lower than 20 keV)

## Slide 8
cpo2ids
Key differences
Runs from IMAS environment
> module load imasenv
Translates data in the other direction
Maps data from:
equilibrium, coreprof, corescource, coretransp, distsource, wall, nbi
Please ask for more mappings. Alternatively, those that are able are more then welcome to add mappings themselves!

## Slide 9
cpo2ids
Very similar use
> python <path>/kplots/cpo2ids/cpo2ids.py <machine> <shot> <run>
or
> ./<path>/cpo2ids.py <machine> <shot> <run>
Options
--user <username where CPOs are>
--toMachine <database where you wish to store the IDSs>
--toRun <run out>

## Slide 10
ion_mix
One more thing…
ion_mix change the ratio of hydrogenic species in core_profiles
You can (inconsistently) add He3 and He4 to core_profiles
Need to build this functionality so as to not break quasineutrality

## Slide 11
DEMO