## Slide 1: Overview of WEST platform: achievements and possible upgrades
Lionel Meunier
March 17th 2025

## Slide 2: WEST Capabilities
1

## Slide 3: WEST: a MA class superconducting tokamak
Full tungsten actively cooled PFC
Flexible magnetic configuration (LSN, USN, DN)
Large current drive capability
Long pulse operation >1000 s
Ip (q95~2.5) | 1.0 MA
Bj | 3.7 T
R | 2.5 m
a | 0.5 m
A | 5-6
k | 1.35
d | Up to 0.5
Vp | 15 m3
nGW (1MA) | 1.5 1020 m-3
PRF_Steady state | 12MW (2025)
Tflattop | 1000 s
3

## Slide 4: WEST auxiliary systems ready for 10MW-1000s
Magnets
  18 TF Superconducting NbTi magnets
  9 CS/PF water cooled Copper Coils
  Upper and Lower water cooled Copper Divertor Coils
Cryoplant to cool down magnets
  300W @ 1.8K, 1kW @ 4.5K
  3.5 tons of helium inventory
Water cooling system
  Recently upgraded to 15MW steady-state (third cooling tower)
  Dedicated high pressure and temperature water loop (PFC 200°C-40bars, LHCD, ICRH, ECRH)
New cooling water tower
10MW cooling water
towers
Electrical Power Supplies
  400kV direct connection
400kV
2 x 15kV
Heating systems
  Lower Hybrid: 6MW steady-state available
  ICRH: 3MW steady-state available
  ECRH: 3MW steady-state being installed
4
~ 8m

## Slide 5: WEST: ITER-grade divertor and W limiters First Wall
ITER divertor cassette
ITER-like WEST divertor
WEST in 2025
Upper divertor W coating/CuCrZr
Vessel protection panels Stainless steel
Baffle
W coating /CuCrZr
VDE/Ripple protection
W coating / CuCrZr
Inner limiters
Bulk W
Antenna protections
W coating / CFC
Outer limiters
Bulk W
ITER like PFU
bulk W
Phase 1 (Dec 2016 – Jan. 2021) | Phase 2 (2021)
Actively cooled + W coated inertial divertor elements | Fully actively cooled ITER grade divertor
5

## Slide 6
6
WEST real time wall protection key tool for Long pulse operation
IR diagnostics installed on the WEST tokamak covering 52% of the 1st wall, 85% of the lower divertor
Real time feedback control of the injected power on apparent temperature of multiple regions of interest
Interlock: temperature threshold leading to plasma soft landing
Advanced RT processing to address reflection and emissivity issues (IA)
Additional diagnostics for wall protection
VUV (Vacuum Ultra Violet) on cooper wavelength: Real time feedback control acting on the injected power
Calorimetry diagnostic (~200 sensors & flow meters implemented) with automatic Data processing tool

## Slide 7: Wide range of diagnostics

## Slide 8: WEST Achievements
2

## Slide 9
WEST plasma campaigns
Plasma pulses
Number of pulses/day
  30 pulses/day (shift up to 9:00pm)
  22 pulses/day (shift up to 6:00pm)
  WEST availability > 70% since 2019 during plasma campaigns
Year | Total | Failed | Commissioning plasmas | Physics program
2023 | 1420 | 13% | 15% | 72%
2024 | 1478 | 9% | 14% | 77%
Up to 45 pulses per day

## Slide 10: Long pulse operations
2023 plasma campaign was partly dedicated to high fluence
  1 months of repeated long pulses of 60s target
  3h of cumulated plasmas over 300 pulses
  111 pulses >50s
  145 stopped by UFO (W influx)  increasing over campaign
  55 stopped by IR (hot spot/deposit) or LHCD system (klystrons)
2024-25 : 11 sessions dedicated to long pulse operations :
79 plasma shots over 60s
40 plasma shots over 100s
7 plasma shots over 500s
Reaching 4h10 of plasma
Record pulse with 1337s and 2,6 GJ injected power
Repetition of long pulses on a single day (>2300s)
Paving the way towards high fluence operation  several hours of plasma per day (terra incognita!)
JET C30-C
1 shot
ITER PFPO
(200s)
PCS CODAC issue
Slower slope
Chart: High Fluence Campaign
| <10s | <10s Tech. | <20s | <20s Tech. | <30s | <30s Tech. | <40s | <40s Tech. | <50s | <50s Tech. | <60s | <60s Tech. | >60s | >60s Tech.
 | 82 | 5 | 46 | 25 | 27 | 18 | 22 | 6 | 13 | 1 | 46 | 15 | 67 | 17

## Slide 11: Very long pulse operations limitation
Outgassing observed after 100’s with conditioning effect
Around 2% of the VV is not perfectly protected (~1m2)
  Gaps between lower/upper divertor and first wall (to allow easy removal of the divertor PFUs)
  Few centimeters gaps in the ports
  Steel temperature of gap protections reaches at least 300°C on long pulses
  Cause outgassing limiting long pulses for specific scenario
Thermal radiation on VV

## Slide 12
Gap protections: welded SS plates

## Slide 13: Issues with inner limiters
A phenomenon occurring on new Bulk W tiles of the inner limiters installed in 2024:
Components are 25mm thick bulk W, bolted on a Copper cooled support
30mm x 30mm castellations
Several castellations broke during C10/11 campaigns
Cause is under investigation
  Twisting effect?
  EM forces?
  Machining?
Experience of components in real Tokamak environment provides information on load cases to consider and engineering rules to apply

## Slide 14: WEST proposed upgrades
Towards 10MW / 1000s
3

## Slide 15: Full Tungsten Jacket
Modify WEST inner configuration
  10MW radiated - 1000s objective for all components
  Overcome component thermal limitations with 100% water cooled systems
ITER like wall
  Removed
    Baffle
    Inner and outer bumpers
    VDE and ripple protections
    Stainless Steel protection panels
  Full Tungsten Jacket
    W wall
    ITER relevant plasma / wall gap (6-10cm ?)
    Conform wall ? – Limiters ?
    Antennas integrated in the W wall
Cryopumps
  Gap between new wall and VV will allow installation of cryopumps
  Improved pumping mode

## Slide 16: Full Tungsten Jacket
Modularity of FW
  Test ITER and DEMO relevant technologies / design
  Test advanced FW technologies
  Install and maintain FW diagnostics
  Maintenance of Lower and Upper divertor and inner components

## Slide 17: Ripple
Ripple Correction Coils
WEST ripple causes energy losses, warming up the Upper Divertor water pipes
Ripple correction with Ferromagnetic inserts installed in the VV has been studied:
Would divide ripple by a factor of 2 with 130mm inserts
Chart: K1
| 0 | 2.6019E-2 | 5.2039000000000002E-2 | 7.8058000000000002E-2 | 0.10408000000000001 | 0.13009999999999999 | 0.15612000000000001 | 0.18214 | 0.20815 | 0.23416999999999999 | 0.26018999999999998 | 0.28621000000000002 | 0.31223000000000001 | 0.33825 | 0.36426999999999998 | 0.39029000000000003 | 0.41631000000000001 | 0.44233 | 0.46834999999999999 | 0.49436999999999998 | 0.52039000000000002
vacuum | 3.1552 | 3.1528 | 3.1505 | 3.1435 | 3.1368 | 3.126 | 3.1156 | 3.1022 | 3.0892 | 3.0746 | 3.0604 | 3.046 | 3.032 | 3.0191 | 3.0068 | 2.9965 | 2.987 | 2.9803 | 2.9744 | 2.9718 | 2.9701
with 8 cm thick insert | 3.1342 | 3.1323 | 3.1307 | 3.1254 | 3.1204 | 3.1122 | 3.1043 | 3.094 | 3.0841 | 3.0726 | 3.0616 | 3.05 | 3.0389 | 3.0284 | 3.0184 | 3.0099 | 3.0021 | 2.9965 | 2.9915 | 2.9894 | 2.9879
with13 cm thick insert | 3.1151 | 3.1138 | 3.1127 | 3.1091 | 3.1058 | 3.1002 | 3.0948 | 3.0873 | 3.0803 | 3.0716 | 3.0634 | 3.0542 | 3.0456 | 3.037 | 3.0289 | 3.0217 | 3.0151 | 3.0103 | 3.0061 | 3.0041 | 3.0029

## Slide 18: Stabilizing plates
Copper plates (Thickness: 2cm, width: 36cm) connected with resistances to get the desired total resistance

## Slide 20: Torus hall configuration
Space available all around the tokamak
  Flexibility for integration of new systems
  Easy maintenance
Services available on all equatorial, upper and lower ports
  Water cooling: B30 loop (70°C in operation / 200°C baking) – STEFFI loop (20-30°C)
  Pressurized air / Electrical power / vacuum pumping

## Slide 21: Gap protections limitation
Chart: Inertial components limits
| 170 | 320 | 500 | 1000 | 4000
UHFS | 7.32 | 4.86 | 3.66 | 2.52 | 2.5
Divertor feet | 6 | 4.98 | 4.02 | 3 | 2.76 | 2.52 | 2.28 | 2.22 | 2.22
Bellow protections | 6 | 4.98 | 4.02 | 3 | 1.98 | 1.74 | 1.5 | 1.26 | 1.2 | 1.2
LLFS | 5.64 | 3.96 | 2.28 | 1.8 | 1.8
70 328 1000 4000 | 6 | 3 | 1.5 | 1.4
Sacrificial protection panels have been included where possible
Adding actively cooled protections has been studied and would impose significant modification of internal components
 Record WEST pulse already close to the limits
Objective is to overcome these limits towards long pulses with high power and high fluence