## Slide 1: JT-60SA W divertor modeling: Status of SOLPS-ITER modelling
6/5/2025
Wouter Dekeyser
Sander Van den Kerkhof
Wim Van Uytven

## Slide 2: Content
Benchmark 3.0.8 vs WG
Narrow grid kinetic cases (with 9-point stencil)
Extended grids – SOLPS progress
Extended grids – alternative geometries

## Slide 3: Motivation
After conversion to WG format, a benchmark run (turning off 9-point stencil in WG) was performed
  Densities and parallel velocities OK
  Upstream temperature profiles OK
  Divertor temperatures: more substantial differences
  → Deeper investigation performed

## Slide 4: Four differences found
Sheath boundary conditions
Flux limiter thermo-electric conductivity
Parallel electron velocity around X-point
EIRENE sources (on fixed BG)

## Slide 5: 1. Sheath boundary conditions
In WG, BCPOT = 3, BCON = 3, BCMOM = 3, BCENE = 3 and BCENI = 3 are automatically converted to “new” SpB sheath BCs BCPOT = 11, BCCON = 14, BCMOM = 13, BCENE = 15, BCENE = 15
These should be identical up to interpolation, if GAMMAE = 0 and enepar = 1.0 Otherwise there is a difference due to (1+GAMMAE)/(1-GAMMAE) vs enepar. In the original case, GAMMAE was 0.5

## Slide 6: 2. Flux limiters thermo-electric conductivity
Discovered a bug in 3.0.8 (which was also still present in 3.0.9), whereby the flux limit value for was a factor 4 wrong due to an erroneous local computation of . This error was not present in WG due to the use of the centralized routines for gradient computation.
Note: the activation/deactivation of these flux limiters has quite a large effect on the solution. What value to choose for remainder of work? Based on what was it selected?

## Slide 7: 3. Parallel electron velocity around X-point
In WG, the parallel electron velocity does not depend on b2sigp_style.
In 3.0.8, b2sigp_style leads to local differences in ue around X-point.
The combination 3.0.8 + b2sigp_style = 2 is the one that differs from the other three
This is assumed to be due inferior discretization in 3.0.8

## Slide 10: 4. EIRENE sources on fixed BG
One timestep with 1M particles / stratum
Good agreement, but small differences due to minor updates in EIRENE and B2.5-EIRENE coupling (didn’t investiage further which changes)

## Slide 11: EIRENE sources: ix = 2

## Slide 12: EIRENE sources: ix = 60

## Slide 13: EIRENE sources: ix = 97 (nx-1)

## Slide 14: Fluxes and non-EIRENE sources on fixed BG
After adressing these issues it was possible to get perfect agreement for all fluxes and non-EIRENE sources on fixed plasma background. Some examples:
ix = 40
Total ion particle flux
Electron heat flux

## Slide 15
Inner target boundary conditions sources

## Slide 16: Dedicated benchmark run
Re-ran an adapted benchmark case in both WG and 3.0.8
  ‘New’ sheath BCs also in 3.0.8 (removing difference #1)
  Fixed puff instead of feedback (but I checked independently that feedback scheme works for the case in WG)
  Thermo-electric flux limit turned off in both cases (removing difference #2)
  Use b2sigp_style = 1 (removing difference #3)
  → Only differences in EIRENE remaining

## Slide 17: Results target temperatures dedicated benchmark runs
Differences are still not fully negligible, but small enough to conclude benchmark study

## Slide 18: Content
Benchmark 3.0.8 vs WG
Narrow grid kinetic cases (with 9-point stencil)
Extended grids – SOLPS progress
Extended grids – alternative geometries

## Slide 19: Narrow grid cases
Narrow-grid cases with kinetic neutrals run robustly in WG code version (with 9-point stencil)
Ready to be used for preliminary studies
Performed convergence scan on # EIRENE particles (see next slide)
Ne
D2

## Slide 20: Convergence assessment on EIRENE particles
EIRENE reference particle distrubtion P
→ Good statistics needed on outer target
 | D | Ne
IT | 25000 | 25000
OT | 25000 | 25000
IPF | 20000 | 20000
OPF | 20000 | 20000
MCW | 20000 | 20000
Puff | 10000 | 10000
Vol. Rec. | 7000 | 7000

## Slide 21: Narrow-grid cases with drifts
Started narrow-grid case with kinetic neutrals and drifts
For now, forced to reduce timestep to and
100k + iterations without crash with 100% drifts, but not yet converged
No analyis of physics impact of drifts yet

## Slide 22: Content
Benchmark 3.0.8 vs WG
Narrow grid kinetic cases (with 9-point stencil)
Extended grids – SOLPS progress
Extended grids – alternative geometries

## Slide 23: Extended grid cases
Technically running with both kinetic neutrals and advanced fluid neutrals
Remaining issues with parallel velocities and temperatures in specific areas

## Slide 24: Extended grid with kinetic neutrals
Anomalous numerical viscous heating? Currently under investigation

## Slide 25: Extended grids with fluid neutrals
Anomalous numerical viscous heating and high parallel velocities at tangency points
→ These issues must be resolved before starting physics interpretation

## Slide 26: Content
Benchmark 3.0.8 vs WG
Narrow grid kinetic cases (with 9-point stencil)
Extended grids – SOLPS progress
Extended grids – alternative geometries

## Slide 27: CAD geometry

## Slide 28: CAD geometry
This is actually a gap in rotated configurations!  chose to extend reflector plate to close gap
These are probably the PFUs you want the strike point on (actively cooled, MB)

## Slide 29: Baseline

## Slide 30: 10 degrees, extended RP

## Slide 31: 5 degree, extended RP

## Slide 32: Conclusion
Technical work performed to continue JT60-SA modelling in WG SOLPS-ITER
  Benchmark 3.0.8. vs WG: OK
  Narrow grid runs: OK
  Narrow grids + drifts: ± OK but slow
  Extended grids: runs without crashing but some anomalies to be resolved
Fully extended grids can be created for alternative geometries

## Slide 33: Input for next steps
Flux limiter thermo-electric conductivity
  Specific reason they were activated?
  Value?
Updates on what to aim for?
Which geometries to investigate?
  Target inclination?
  Dome?
  What to do with gap when inclination is changed?
Cost functions?