## Slide 1: Reducing turbulent transport in tokamaks by combining up-dwn asymmetry and the low momentum diffusivity regime
Haomin Sun1*, Justin Ball1, Stephan Brunner1, Anthony Field2, Bhavin Patel2, Alessandro Balestri1, Daniel Kennedy2 and Colin Roach2, Eleonora Viezzer3, Manuel Munoz3, Diego Zabala3
1Swiss Plasma Center, EPFL
2CCFE, Culham Science Centre, Abingdon, Oxon, UK
3University of Seville, Seville, Spain
October 2025
TSVV2 annual meeting, 16 October 2025

## Slide 2: Obtaining up-down asymmetry by changing upper and lower triangularity
[Happel et al. 2023]
[Camenen et al. 2010]

## Slide 3: Outline
Introduction
  Suppression of turbulence by flow shear
  Generating flow shear using up-down asymmetry
Results
  The Low Momentum Diffusivity (LMD) regime
  Turbulence stabilization using LMD and up-down asymmetry
  Practical applicability study using up-down asymmetric experimental geometries
  Recent progress on Prandtl number in electromagnetic turbulence
Conclusions

## Slide 4: Introduction

## Slide 5: Suppression of turbulence by flow shear
Flow shear twists turbulence eddies into smaller spatial scale, reducing their amplitude
[Highcock et al., PRL, 2010]
[Angioni et al., PRL, 2011]
Pressure gradient
Pressure gradient
ASDEX-U Experiments
Gyrokinetic Simulations
Heat Flux
Increasing flow shear
Pressure gradient
Heat Flux
Experiments and simulations have shown that flow shear can stabilize turbulence, improving tokamak performance
Notes: Blue arrows are velocity (mention during the talk!)

## Slide 6: Generating flow shear using neutral beam/radio frequency waves
Flow shear is usually generated from external momentum sources such as NBI or RF waves.
External injections does not scale well to large devices:
Alternatives?
ITER:
[Liu et al., Nuclear Fusion, 2004]
Notes: The best scenario is that we don’t have to do anything and we let the plasma itself generate a strong flow shear for us.

## Slide 7: Generate flow shear using up-down asymmetry
[Parra et al., 2011, Camenen et al. 2011, Happel et al. 2023, Ball et al., 2018]
Define Prandtl number:
Typical expression for momentum flux
In steady state: , assuming is small, we have
Most important source of intrinsic rotation in the core: up/down asymmetry of magnetic equilibrium.
Prandtl number estimate the rotation shear at a given turbulence level
People typically believed
Intrinsic momentum flux
Turbulent diffusion
Pinch term
Notes: Three things that I want to emphasize:
In the following parts of the talk, I’ll be mostly focusing on spherical tokamaks.
We will be focusing on momentum flux driven by turbulence, not neoclassical effects.
3. In ASDEX or other tokamaks, one can achieve this shape by making a negative top triangularity and a positive bottom triangularity
Flow: 1. strong intrinsic drive, already done
2. Need low momentum diffusivity: done by us
3. To find flow shear being generated is too expensive: QL model
4. Final answer and results of flow shear reduction of heat flux.
5. Mention how you find out in simulations
the most important source of intrinsic rotation is up/down asymmetry of magnetic equilibrium.
From the equation, we can see that if there is no up-down asymmetry or no flow, there is no momentum flux.
So in order to get strong flow shear, we can either increase the intrinsic momentum flux, or we can decrease the momentum diffusivity. So in order to find out the real flow shear being generated by the intrinsic rotation, in simulations, we typically tilt the geometry, and scan the flow shear value to find out the flow shear value that makes total momentum flux drop to zero.
However, in reality what we actually want to minimize is the so-called Prandtl number
Flow: 1. strong intrinsic drive, already done
2. Need low momentum diffusivity: done by us
3. To find flow shear being generated is too expensive: QL model
4. Final answer and results of flow shear reduction of heat flux.
5. Mention how you find out Π_𝑖=0 in simulations

## Slide 8: Results1: The Low Momentum Diffusivity (LMD) regime

## Slide 9: Low Momentum Diffusivity (LMD) regime: tight aspect ratio, low , normal to high
Our simulation results are not only consistent with previous works [Casson et al. 2009, McMillan et al. 2019], but going beyond them:
1. Flow shear in toroidal direction
2. Full toroidal angular momentum flux
Contours of constant at , , circular geometry, adiabatic electrons, ITG
Notes: All of these are nonlinear simulations
We choose to define the Pr<0.5 as the low momentum diffusivity regime!!!

## Slide 10: Low Momentum Diffusivity (LMD) manifold: tight aspect ratio, low safety factor , normal to high magnetic shear
Low momentum diffusivity manifold for adiabatic electrons: more than 500 nonlinear GENE simulations.
, circular geometry
Notes: The hat on the heat flux Q denotes that the heat flux is in the local gyroBohm unit.

## Slide 11: Results2: Turbulence stabilization using LMD and up-down asymmetry
Notes: Now we are moving on to the flux surface denoted by the red

## Slide 12
Using QL model to estimate flow shear at equilibrium
Using our QL model to predict the steady-state flow shear, which shows good agreements
Scan flow shear to find the value at which
QL model: [Sun et al., NF, 2024]
Notes: Transition between the different subsection needs to be added!
Elongation 1.5 add
Please note that the negative value of flow shear denotes only the direction of the flow!
Please note that the QL model is only used to predict the zero crossing point.

## Slide 13: Strong flow shear in LMD regime with up-down asymmetry
In the LMD: strong flow shear, significant suppression of turbulence especially near marginal stability
Out of the LMD: weak flow shear, nearly no effect on heat transport
In the LMD regime
Out of the LMD regime
Notes: 3D plot should be flipped left-right

## Slide 14: One question remains: what is the main effective parameter in determining the heat flux reduction?
LMD regime
Heat flux reduction
Heat flux reduction
Prandtl number is the main effective parameter in determining the flow shear stabilization

## Slide 15: Effect of pinch term on intrinsic rotation
We therefore have
Considering pinch term will only make the intrinsic rotation stronger
Important to note that both and are positive [Peeters et al., PRL, 2007]
Flip up-down symmetry changes its sign
Notes: Say flipping the sign of intrinsic by flipping the up-down symmetry of flux surface!

## Slide 16: Results3: Practical applicability study using experimental geometries

## Slide 17: Artificially tilt MAST geometry to study intrinsic flow shear
No triangularity
MAST #24600

## Slide 18: Predicting flow shear generated by up-down asymmetry
Errorbars come from rolling average
Theoretical Prediction (by up-down asymmetry) | Experimental Value (by NBI)
Theoretical Prediction (by up-down asymmetry) | Experimental Value (by NBI)
Notes: Flip the two figures, remove the left, add a momentum flux one.
Two implications of this figure: 1. If a spherical tokamak like MAST-U could tilt its flux surface, then the intrinsic rotation could potentially stabilize turbulence
2. This strategy can be combined with the external momentum injection, meaning that it could potentially drive flow shear that is twice as large.

## Slide 19
Preliminary simulation for SMART shows strong heat flux reduction with our strategy
Heat flux reduction
[Doyle S. et al. 2021 Fusion Eng. Des. 171 112706]
Notes: SMART is a new tokamak being built in Spain

## Slide 20: Results4: Recent progress on electromagnetic component of toroidal angular momentum flux

## Slide 21: Full expression of electromagnetic toroidal angular momentum flux driven by turbulence
[Sugama & Horton 1998, Parra et al. 2011, Abel et al. 2013, Ball 2016]

## Slide 22
Full expression of electromagnetic toroidal angular momentum flux driven by turbulence (continue)
[Ball 2016]

## Slide 23
Linear benchmark between GENE and CGYRO
Parameters: , , ,
, , ,

## Slide 24: Doubled
Parameters: , , ,
, , ,

## Slide 25: MTM scan , , , ,
Prandtl number is tiny and negligible for MTM
MTM dominated
Notes: Plot Prandtl number versus q

## Slide 26: Magnitude of different terms: MTM
Maxwell stress term cannot be neglected for MTM!
Notes: Current transport?

## Slide 27: KBM scan , , , , ,
KBM dominated
Prandtl number is relatively large for KBM

## Slide 28: Magnitude of different terms: KBM
Electromagnetic components are negligible for KBM with low

## Slide 29: Conclusions of results
We propose a new approach to reduce turbulent transport in future tokamak fusion power plants.
For tight aspect ratio, low , high , and low , the Prandtl number can be much smaller than , indicating LMD regime.
Combining the LMD regime with up-down asymmetry creates strong intrinsic flow shear that can significantly reduce the heat flux.
Verified that MAST discharges can exhibit LMD and artificially tilting the flux surfaces drives sufficient flow to stabilize turbulence.
Performed a preliminary study for a geometry that can eventually be achieved on SMART to test the predictions in this work.
Prandtl number in electromagnetic turbulence is studied, showing the importance of considering electromagnetic contributions to .
[H. Sun et al., Nucl. Fusion 64 (2024), 036026]
[H. Sun et al., Nucl. Fusion. 65 (2025), 076026]
Notes: Mention SUNIST-2 & HL-3

## Slide 30: References
[1] C. Angioni et al. “Intrinsic Toroidal Rotation, Density Peaking, and Turbulence Regimes in the Core of Tokamak Plasmas.” Phys. Rev. Lett. 107 (2011), 215003.
[2] E. G. Highcock et al. “Transport Bifurcation in a Rotating Tokamak Plasma.” Phys. Rev. Lett. 105.21 (2010), 215003.
[3] Y. Liu et al. “Stabilization of resistive wall modes in ITER by active feedback and toroidal rotation.” Nuclear Fusion 44.2 (2004), 232.
[4] J. Ball et al. “Optimized up–down asymmetry to drive fast intrinsic rotation in tokamaks.” Nucl. Fusion 58 (2018), 026003.
[5] H. Sun et al. “A new quasilinear model for turbulent momentum transport in tokamaks with flow shear and plasma shaping.” Nucl. Fusion 64 (2024) 036026.
[6] H. Sun et al. “Reducing turbulent transport in tokamaks by combining intrinsic rotation and the low momentum diffusivity regime.” Nucl. Fusion. 65 (2025), 076026.
[7] B. F. McMillan and J. Dominski. “Tokamak parameter regimes with low toroidal momentum diffusivity.” In: Journal of Plasma Physics 85.3 (2019), p. 175850301.

## Slide 31: Why LMD regime is beneficial (simple physics explanation)?
: Diffusive component
For ITG: maximizes at around
: Anti-diffusive component
With the increase of , the field line pitch angle is larger, meaning is becoming larger. This results in a larger and smaller

## Slide 32: Benchmark between GENE and CGYRO

## Slide 33: Microturbulence in tokamaks
Microturbulence causes most of the energy loss in tokamaks
Ion scale turbulence
4. Gyrokinetic simulation is needed to simulate such turbulence
1. Turbulence is highly anisotropic
2. Electromagnetic turbulence
3. Weakly collisional
[Ball et al., J. Plasma Phys., 2020]
[GYRO official website]
Notes: Kinetic modelling is necessary.
Turbulence is highly anisotropic (on the scale of ion gyroradius)
EM turbulence
Only consider turbulent diffusivity but neglecting the neoclassical diffusivity

## Slide 34: Magnetic confined fusion
: energy confinement time
Improve as much as possible
Energy transport
Producing Confinement
[Giacomin et al., Computer Phys. Comm.,2021]
Notes: Explain the figure
The plasma tends to escape from the confinement of the magnetic field.
Equilibrium->microinstability->turbulence being generated->turbulent transport
To achieve fusion energy: plasma: why tokamak: (get the attention of president for the first 5 minutes)

## Slide 35: Procedure of getting input parameters for GENE gyrokinetic simulations
Kinetic parameters
Fit experimental TS/CXRS data
Obtain density, temperature input for GENE
Geometry parameters
Obtain EQDSK file from experimentalists
Convert to Miller general input parameters in GENE
GENE needs

## Slide 36: Gyrokinetics and its coordinate system
: straight field line poloidal angle
For a coordinate, define
[Abel et al., Rep. Prog. Phys., 2013]
[Ball et al., J. Plasma Phys., 2020]
Gyro-average:
Notes: This figure is an illustration of this coordinate, a plot with respect to straight field line poloidal angle and toroidal angle. The red arrows are the direction of the magnetic field. It is an unorthogonal coordinate.

## Slide 37: MAST #24600 important parameters
parameter | value | parameter | value
q | 1.2824 | Omt_i | 4.5641
 | 1.1722 | Omn_i | 2.5803
amhd | 1.0637 | Omt_e | 4.0157
 | 1.4474 | Omn_e | 2.5803
 | 0.1814 | Lx | 157.364
 | 0.4188 | Ly | 125.664
 | 0.1586 | nexc | 16
 | -0.0194 |  | 0.05
 | 1.63% | Nakata collision | 0.0008428
parameter | value | parameter | value
q | 1.2824 | Omt_i | 4.5641
 | 1.1722 | Omn_i | 2.5803
amhd | 1.0637 | Omt_e | 4.0157
 | 1.4474 | Omn_e | 2.5803
 | 0.1814 | Lx | 157.364
 | 0.4188 | Ly | 125.664
 | 0.1586 | nexc | 16
 | -0.0194 |  | 0.05
 | 1.63% | Nakata collision | 0.0008428

## Slide 38: Linear Simulations
Exp value:

## Slide 39: Add flow shear, compare with experiments
Exp value:
Exp value:

## Slide 40
Converge grid:
Nonlinear Simulations, realistic geometry, no flow shear
Exp value:
Exp value:
Exp value:
Exp value:

## Slide 41: MAST #24600 important parameters
parameter | value | parameter | value
q | 1.4843 | Omt_i | 3.6615
 | 2.0902 | Omn_i | 2.3267
amhd | 1.0138 | Omt_e | 3.7291
 | 1.4525 | Omn_e | 2.3267
 | 0.1893 | Lx | 168.288
 | 0.4642 | Ly | 125.664
 | 0.2439 | nexc | 24
 | 0.0272 |  | 0.05
 | 1.09% | Nakata collision | 0.0009874
parameter | value | parameter | value
q | 1.4843 | Omt_i | 3.6615
 | 2.0902 | Omn_i | 2.3267
amhd | 1.0138 | Omt_e | 3.7291
 | 1.4525 | Omn_e | 2.3267
 | 0.1893 | Lx | 168.288
 | 0.4642 | Ly | 125.664
 | 0.2439 | nexc | 24
 | 0.0272 |  | 0.05
 | 1.09% | Nakata collision | 0.0009874

## Slide 42
Linear Simulations

## Slide 43
Converge grid:
Nonlinear Simulations

## Slide 45: MAST #24600 important parameters
parameter | value | parameter | value
q | 1.8560 | Omt_i | 3.5438
 | 3.2020 | Omn_i | 1.5932
amhd | 0.9969 | Omt_e | 5.1947
 | 1.4678 | Omn_e | 1.5932
 | 0.1922 | Lx | 146.4
 | 0.5119 | Ly | 125.664
 | 0.3730 | nexc | 48
 | 0.0899 |  | 0.05
 | 0.69% | Nakata collision | 0.001948
parameter | value | parameter | value
q | 1.8560 | Omt_i | 3.5438
 | 3.2020 | Omn_i | 1.5932
amhd | 0.9969 | Omt_e | 5.1947
 | 1.4678 | Omn_e | 1.5932
 | 0.1922 | Lx | 146.4
 | 0.5119 | Ly | 125.664
 | 0.3730 | nexc | 48
 | 0.0899 |  | 0.05
 | 0.69% | Nakata collision | 0.001948

## Slide 46
Linear Simulations

## Slide 47: Linear Simulations: including electron scale

## Slide 48
Converge grid:
Nonlinear Simulations

## Slide 49
Parameters
At , we have (LMD regime)
Use miller general geometry for GENE simulations