## Slide 1: OP2: L-H power threshold characterization in H and D
Proponents and contact person:
L. Aucone (CP), C. Angioni, G. Birkenmeier, M. Cavedon, F. D’Isa, E. Fable, A. Fil, C. Maggi, J. Morales, R. Pasqualotto, E.R. Solano E. Tomasina, P. Vincenzi
Scientific Background
PLH and PHL prediction determines size & heating needs of next step devices
Recent multimachine L-H scaling studies indicate both ne,min and PLH depend on divertor configuration & plasma content: H, D, T, He, mixtures
High ne branch PLH multi-machine scaling: better fits with Bpol than with Btor
Studies at AUG [Ryter NF2016] indicate Qi at the edge plays a key role in the L-H transition
Scientific Objectives, experiments
when H-NBI and D-NBI have reached reasonable values: experiments with only NBI (slow power ramp up) and mixed NBI+ECRH (low background NBI and ramp of ECRH), reaching the L-H transition
identify ne,min (at least 5 ne values per dataset) dependence on Ip, Bt
Once PLH is well documented up to high ne (near fGW~1), PLH vs. PHL
Study Qi vs. and in H and D plasmas & impact of Qi/Qe ratio.
Divertor configuration effect on PLH (factor of 2 on PLH)
Triangularity impact on
Impact of EFCCs on PLH in low and high ne branches. Resonances?
Parasitic: document M-mode, frequency scaling
JET 3T 2.5 MA Horizontal Target
HT
HT
JET
JT-60SA

## Slide 2: OP2: L-H power threshold characterization in H and D
The plot reports:
LH transition power from the ITPA2008 scaling [Martin 2008] for JT-60 SA at 2.25 Tesla (solid black line)
Minimum in density for for different values of according to AUG scaling [Ryter NF2014] (coloured diamonds)