## Slide 1: Pedestal structure, stability, transport and ELMs characterization
Limited by resistive MHD,
Strong ETG pedestal turbulence
[Maggi NF2015] and [Challis NF2015]
[Frassinetti NF2021]
Proponents and contact person:
  L. Frassinetti, S. Saarelma, O. Krutkin
Background
  In JET-ILW at high power and high gas rate (high nesep/neped) the pedestal is not limited by ideal MHD but by resistive MHD [Maggi NF2015, Frassinetti NF2021, Nyström NF2023] and ETGs play a major role in the pedestal transport [Chapman NF2022, Krutkin PPCF2025].
  Do we have and in which conditions similar phenomenology in JT-60SA?
  This will provide a more general understanding of resisistive MHD and pedestal transport, that can help us for extrapolation to future machines.
Objectives
  Direct objectives:
    measure pedestal structure and ELMs in different plasma conditions
    quantify the correlation of the pedestal with power and gas rate
    quantify pedestal stability and GK turbulent transport characteristics
    quantify the correlation between pedestal stability with nesep/neped
    Identify under which conditions resistive MHD and ETG pedestal transport start to be relevant in JT-60SA
    compare the JT-60SA results with JET-ILW and JET-C
  Indirect objectives (to be linked to other proposals):
    Identify the PLH threshold at different gas rates
    Identify transition from type III ELMs to type I ELMs
    Global confinement in H-mode and core transport

## Slide 2: Pedestal structure, stability, transport and ELMs characterization
Limited by resistive MHD,
Strong ETG pedestal turbulence
[Maggi NF2015] and [Challis NF2015]
[Frassinetti NF2021]
power
gas rate
medium gas
low gas
high gas
Proponents and contact person:
  L. Frassinetti, S. Saarelma, O. Krutkin
Background
  In JET-ILW at high power and high gas rate (high nesep/neped) the pedestal is not limited by ideal MHD but by resistive MHD [Maggi NF2015, Frassinetti NF2021, Nyström NF2023] and ETGs play a major role in the pedestal transport [Chapman NF2022, Krutkin PPCF2025].
  Do we have and in which conditions similar phenomenology in JT-60SA?
  This will provide a more general understanding of resisistive MHD and pedestal transport, that can help us for extrapolation to future machines.
Objectives
  Direct objectives:
    measure pedestal structure and ELMs in different plasma conditions
    quantify the correlation of the pedestal with power and gas rate
    quantify pedestal stability and GK turbulent transport characteristics
    quantify the correlation between pedestal stability with nesep/neped
    Identify under which conditions resistive MHD and ETG pedestal transport start to be relevant in JT-60SA
    compare the JT-60SA results with JET-ILW and JET-C
  Indirect objectives (to be linked to other proposals):
    Identify the PLH threshold at different gas rates
    Identify transition from type III ELMs to type I ELMs
    Global confinement in H-mode and core transport
Strategy:
  Perform power scans at constant gas rate
  Perform gas scan at constant power

## Slide 3: Pedestal structure, stability, transport and ELMs characterization
Limited by resistive MHD,
Strong ETG pedestal turbulence
[Maggi NF2015] and [Challis NF2015]
[Frassinetti NF2021]
power
gas rate
medium gas
low gas
high gas
subset at constant bN
Proponents and contact person:
  L. Frassinetti, S. Saarelma, O. Krutkin
Background
  In JET-ILW at high power and high gas rate (high nesep/neped) the pedestal is not limited by ideal MHD but by resistive MHD [Maggi NF2015, Frassinetti NF2021, Nyström NF2023] and ETGs play a major role in the pedestal transport [Chapman NF2022, Krutkin PPCF2025].
  Do we have and in which conditions similar phenomenology in JT-60SA?
  This will provide a more general understanding of resisistive MHD and pedestal transport, that can help us for extrapolation to future machines.
Objectives
  Direct objectives:
    measure pedestal structure and ELMs in different plasma conditions
    quantify the correlation of the pedestal with power and gas rate
    quantify pedestal stability and GK turbulent transport characteristics
    quantify the correlation between pedestal stability with nesep/neped
    Identify under which conditions resistive MHD and ETG pedestal transport start to be relevant in JT-60SA
    compare the JT-60SA results with JET-ILW and JET-C
  Indirect objectives (to be linked to other proposals):
    Identify the PLH threshold at different gas rates
    Identify transition from type III ELMs to type I ELMs
    Global confinement in H-mode and core transport
Strategy:
  Perform power scans at constant gas rate
  Perform gas scan at constant power
  Indirectly  subset at constant bN for pedestal stability studies

## Slide 4: Pedestal structure, stability, transport and ELMs characterization
Limited by resistive MHD,
Strong ETG pedestal turbulence
[Maggi NF2015] and [Challis NF2015]
[Frassinetti NF2021]
power
gas rate
medium gas
low gas
high gas
subset at constant bN
Proponents and contact person:
  L. Frassinetti, S. Saarelma, O. Krutkin
Background
  In JET-ILW at high power and high gas rate (high nesep/neped) the pedestal is not limited by ideal MHD but by resistive MHD [Maggi NF2015, Frassinetti NF2021, Nyström NF2023] and ETGs play a major role in the pedestal transport [Chapman NF2022, Krutkin PPCF2025].
  Do we have and in which conditions similar phenomenology in JT-60SA?
  This will provide a more general understanding of resisistive MHD and pedestal transport, that can help us for extrapolation to future machines.
Objectives
  Direct objectives:
    measure pedestal structure and ELMs in different plasma conditions
    quantify the correlation of the pedestal with power and gas rate
    quantify pedestal stability and GK turbulent transport characteristics
    quantify the correlation between pedestal stability with nesep/neped
    Identify under which conditions resistive MHD and ETG pedestal transport start to be relevant in JT-60SA
    compare the JT-60SA results with JET-ILW and JET-C
  Indirect objectives (to be linked to other proposals):
    Identify the PLH threshold at different gas rates
    Identify transition from type III ELMs to type I ELMs
    Global confinement in H-mode and core transport
Strategy:
  Perform power scans at constant gas rate
  Perform gas scan at constant power
  Indirectly  subset at constant bN for pedestal stability studies
Related OP2 scientific topics
Initial characterization of H-mode confinement
L-H power threshold characterization in H and D
Pedestal and ELMs generation studies in different plasma conditions