## Slide 1: Proposal title: Optimization of the ramp-down phase
Proponents and contact person:
edoardo.alessi@istp.cnr.it, carlo.sozzi@istp.cnr.it, luca.bonalumi@istp.cnr.it
Scientific Background & Objectives
  Topic: [MHD-2] Disruption studies at high current in L mode and creation of disruption databases (ITER RP A.4, B.1.2, B.1.3, B.1.4, B.1.5, B.1.6)
  Rationale for the proposal and main questions to be answered with respect to OP2 priorities: [Safe step-by-step increase of plasma current up to 5.5 MA in L-mode; Disruption and mitigation technique studies; Studies of L-H back-transition] - Development of an optimized soft-stop strategy depending on the flat-top conditions (Ip, Additional power, Density, Scenario, Impurity concentration,…)
  Construction of a reward function to classify successful ramp-down cases (eg: low disruption forces, low recycling, low thermal loads, related mhd activity…)
  Characterization of the ramp-down phase against (this may involve definition of kinetic profile parameters to classify the plasma behavior during termination)
    Gas fueling rate
    Ip rate
    Additional power ramp-down
    Shape control (elongation)
  Construction of a ramp-down database
  Tentative extrapolation to higher engineering parameters
WPTE | JT-60SA OP2 Proposal | 2026
Number of sessions or shots required
Use of the database of all the experiments
1 dedicated session (12 shots) for variation of the parameters defining the safe region
Threshold for TH and EC
Electron Temperature profile
D influx
IP
Electron Density
profile
Greenwald fraction
Density peaking

## Slide 2: Proposal title: Characterization of the ECH/ECCD effect on sawtooth activity
Proponents and contact person:
edoardo.alessi@istp.cnr.it, carlo.sozzi@istp.cnr.it, silvana.nowak@istp.cnr.it, luca.bonalumi@istp.cnr.it
Scientific Background & Objectives
  [MHD-4] Sawtooth activity and modification by ECH/ECCD
  Rationale for the proposal and main questions to be answered with respect to OP2 priorities: [Initial integrated scenarios development towards high confinement H-mode operation ] – Characterization of the ECH/ECCD effect on sawtooth activity in order to control the sawtooth period, inversion radius, amplitude of 1,1 mode, determination of the limit to avoid NTM triggering
  Variation of
    ECH/ECCD power level from 1.5 to 3 MW
    Radial power deposition via poloidal steering
    Inside/outside q=1
    ECCD effects via toroidal steering
    Ip, density and additional heating
    (S.Nowak, NF 2014)
  Modeling of the sawtooth dynamics
Number of sessions or shots required
2 sessions (12 shots each, one at Ip=3.5MA/Bt=1.7T, and one at Ip=4.6MA/Bt=2.2T)
  Changes on electron density, poloidal and toroidal steering
Low additional heating in piggy-back
Evaluation of ST triggering conditiond for plasma scenarios by METIS code.
S. Nowak et al., IAEA-FEC 2025