## Slide 1: Exploration of optimal breakdown conditions and magnetic configurations for ECWC on JT-60SA
Proponents and contact person:
johan.buermans@mil.be
kristel.crombe@ugent.be
laura.laguardia@istp.cnr.it
…
Scientific Background & Objectives
  Exploration of optimal breakdown conditions for ECWC4
    Fundamental wave @82GHz is optimal for breakdown, but encounters a density limit and possible parametric decay
    Second harmonic @138 GHz is optimal for increased plasma density, but can cause stray radiation and parametric decay
    => Combine both to mitigate the risks and increase the plasma flux
  Exploration of optimal magnetic configuration for ECWC1234
    Determine the most polluted areas (HFS Langmuir probes + cameras)
    Determine magnetic configurations to direct the particle flux (HFS Langmuir probes) 3
    Evaluate the ECWC efficiency by RGA (calibration needed)
  Determine efficient ECWC scenarios to increase the plasma performance
    Duty cycle and power requirements
Number of session or shots required ?
TCV experiments on ECWC3
1M. Fukumoto et al, Nucl. Mater. Energy, 2017
2D. Douai et al, Nucl. Fusion, 2018
3J. Buermans et al, EPS plasma conference, 2022
4M. Fukumoto et al, Nucl. Mater. Energy, 2025