## Slide 1: OP2 and/or OP3: QH-mode development
Proponents and contact person:
emilia.solano@ciemat.es, eviezzer@us.es, samui.Saarelma@ukaea.uk, +?…
Scientific Background of Quiescent H-mode (QH)
ELM-less regime with high Ti,ped, low *, good confinement
development best done in hot ion regimes, most easily obtained with a C wall and low initial density
Wall conditioning to reduce recycling is key
DIII-D and AUG-C cn-NBI easier. QH in DIII-D can reach high ne,sep, low Te,sep
DIII-D observed co-NBI QH and cn-NBI Hydrogen QH-mode
Scientific Objectives, experiments
Within Scenario Development? Initial integrated scenarios development towards high confinement H-mode operation
when 15-20 MW NBI reached in OP2 without shine-through problems at low ne & 2-3 MA, search for phases with EHOs. When found, initiate QH-mode development studies Gap scan.
Coordinated effort of many groups: ORD-4 (B9.8), TC-3 (B2.2), HEP-1(B11.2), PEP-2 (B2.5), DSOL-3 (B6.1-2)
EFCCs can contribute to induce QH-modes: systematic studies?
QH-modes compatible with ion ITBs, of interest to HEPB studies.
Possible summary figures
QH
JET-C
JET-C QH-mode (not optimized), 6kHz EHO
Bt=2.6 T, Ip=2.5 MA, 15 MW co-NBI
Density at start of EHO fGW= 0.42,
reaches 0.68 nGW at end.
Within OP2 capabilities?
EHO
(29/10/2008)

## Slide 2: QH-mode characteristics at JET, JT-60U
Record QH in JET-C: 1.4 s EHO duration, 2.1s ELM-free
Starts as Hot ion mode Ti=14keV, Te=9keV, ends with Ti=Te=7keV
Before NBI on: 0.9e19, 0.10 nGW
At L2H: 1.3e19, 0.14 nGW
At start of EHO: 4.0e19, 0.42 nGW
At end of EHO: 6.6e19, 0.68 nGW
Bt=2.6 T Ip=2.5 MA, 15 MW co-NBI, ~0.4
20.
15.
10.
5.
8.0
6.0
4.0
2.0
Dalpha
ne [1019m-3]
fGW
0.8
0.6
0.4
0.2
4.0
3.0
2.0
1.0
0.0
EHO
E.R. Solano et al., PRL 104, 185003 (2010)
QH-mode observed in JT-60U, with cn, co & mixed NBI
1MA, ne,ped=1.3e19, 0.28 nGW
EHO: 10 kHz, n=2 & n=4
Importance of plasma position: gap scan
N. Oyama et al Nucl. Fusion 45 871 (2005)
K. Kamiya, et al. Commun Phys 4, 141 (2021).
JET-C 75411
Transient EHOs and QH phases observed in AUG-W USN co-NBI, work ongoing in WPTE RT-02… E. Viezzer
Ongoing collaboration with DIII-D…
Optimal conditions for QH in JT-60SA tbd, ask N. Aiba
(29/10/2008)

## Slide 3: Profile evolutrion
In fact, hot ion regime lost with sawtooth at 54.2s