## Slide 1: Uncertainties impact on DEMO Design Status and Mitigation
Clarisse Bourdelle,
the plasma system division,
WPDES, WPRD, TSVV11 teams
PSD2 meeting, Oct 1st 2025

## Slide 2: outline
Uncertainties in system code and mitigation action
Going up the ladder of models for a better understanding of uncertainties impact: Scaling laws with ad-hoc heat transport coefficients
High fidelity integrated modelling using turbulent transport models: validation
Gaps between today’s tokamak plasmas and ITER/DEMO
Verification against even higher fidelity integrated modelling
Extrapolation towards DEMO: status and plans
Side note on VNS
Conclusion

## Slide 3: Definition of an EU-DEMO design point robust to epistemic plasma physics uncertainties
System code PROCESS
Design space for A=2.8, Ro=8.6 m
B=4.4 T Ip=18.8 Ma
Physics model choices
energy content based on IPB98(y,2) with H radiation-corrected factor=1.1 but… depending on database selection, weighting of points, the prediction for ITER varies by a factor 2. Nuclear Fusion, Vol. 39, No. 12 (1999) + many other scalings
For the density: Greenwald fraction at separatrix, pedestal + core peaking
For the temperature : Tped using a scaling derived at fixed B + peaking
Entry in H mode PLH from Martin 2008
Design constrains:
PsepBT/(q95AR0) ≤ 6.0 MW·Tm−1
βthermal ≤ 0.03 Ip/(aBT)
H mode: Psep≥ 1.1xPLH
Mitigation action to epistemic plasma physics uncertainties:
Design at q95>3.3 to be able to increase Ip to compensate confinement loss
Pfus=1.6 GW
[Coleman et al NF 2025]

## Slide 4: Using scaling laws in presence of Gaps
 | Pfus | Palpha/Paux | Q | b(core) | nC | r* | frad r<1 | Plasma energy
JET DT | 12.5 MW | 8 % | 0.4 | 2.2 % | 2.4e5 | 0.034 | ~20% | 9 MJ
ITER 15 MA | 500 MW | 200 % | 10 | 4-4.2 % | 1.3e5 | 0.021 | 4% | 300-400 MJ
DEMO A=2.8 | 1600 MW | 640 % | 32 | 4.9 % | 1.4e5 | 0.016 | ~60-70% | 600-1200 MJ
[M. Maslov NF2023]
[F. Eriksson NF2024]
scaling law IPB98(y,2)
DEMO/ITER similar dimensionless parameters
DEMO with H98(y,2) only, factor 2 uncertainty on tE
In PROCESS, optimization done using tE w/o uncertainty range
Prediction for ITER [NF 99]
inner box indicates a ‘95% log-linear’ interval, whereas the region enclosed by the wiskers is an estimate of a ‘95% log-non-linear’ interval

## Slide 5: Using scaling laws in presence of Gaps: Example for frad
 | Pfus | Palpha/Paux | Q | b(core) | nC | r* | frad r<1 | Plasma energy
JET DT | 12.5 MW | 8 % | 0.4 | 2.2 % | 2.4e5 | 0.034 | ~20% | 9 MJ
ITER 15 MA | 500 MW | 200 % | 10 | 4-4.2 % | 1.3e5 | 0.021 | 4% | 300-400 MJ
DEMO A=2.8 | 1600 MW | 640 % | 32 | 4.9 % | 1.4e5 | 0.016 | ~60-70% | 600-1200 MJ
[M. Maslov NF2023]
[F. Eriksson NF2024]
In DEMO if
with all radiation in the confined plasma removed: (if equivalent H=1.1)
no (then here equivalent to H=1.4)
Energy
scaling law IPB98(y,2)

## Slide 6: Going up the ladder of models for a better understanding of uncertainties impact: Scaling laws with ad-hoc heat transport coefficients
In PROCESS:
[Lux PPCF 2016]
In METIS: Same Ip=18.8 MA
Same H factor, scaling law, density peaking, fGr, same Tped etc
But here in METIS, cannot do
2 choices for Power:
1/
2/ max
Does it impact the design point?

## Slide 7: Going up the ladder of models for a better understanding of uncertainties impact: Scaling laws with ad-hoc heat transport coefficients
METIS:
Same Ip=18.8 MA, B, machine size
Same H factor, scaling law, density peaking, fGr, same Tped etc
2 choices for P:
1/ (dashed line)
2/ max() cannot find manually operation point 1.5< Pfus<1.7 and 100<Psep<140 MW
Very different T profiles when using ad-hoc c shape and self-consistent sources/radiations/heat exchange
PROCESS
Ti=Te
METIS Ti, Te
Same density

## Slide 8: Uncertainty impact in METIS, assuming machine built, and constraining on 1.5< Pfus<1.7 GW and 100<Psep<140 MW
The machine is assumed to be built, so the B and geometry are fixed.
1.5< Pfus<1.7 GW : hence scanning on Ip until Pfus is matched
100<Psep<140 MW or 1.1<Psep/PMartin<1.3: hence scanning Xe content
All the other parameters are fixed: H factor, fGr, scaling law choice, density peaking choice, etc.
Their impact on Ip hence the pulse length can be studied one by one.
NB: fixing Vloop and let Pfus vary is also planned, not shown here

## Slide 9: illustration 1/3: impact of Prad in P used in scaling law: from 18.4 to 21.8 MA
DEMO A=2.8 H98 scaling H=1.1 fGr=1.2 | Ip (MA) | Wth (MJ) | Vloop (mV) | li (3 ITER) | Pfus (GW) | q95 | bN | fboot | Zeff | Psep (MW) | Pulse length
1/ ref_H98v2_fixedfGr_iterPsep.mat | 18.4 | 1113 | 40 | 0.86 | 1.7 | 3.8 | 3.1 | 0.35 | 2.8 | 126 | 1h25
2/ max() ref_H98v2_fixedfGr_iterPsep_maxP_lowZeff_iterPsep.mat (copied as ref_H98_maxP.mat) | 21.8 | 1053 | 57 | 0.82 | 1.5 | 3.1 | 2.3 | 0.25 | 1.8 | 131 | 1h
DEMO A=2.8 H98 scaling H=1.1 fGr=1.2 | Ip (MA) | Wth (MJ) | Vloop (mV) | li (3 ITER) | Pfus (GW) | q95 | bN | fboot | Zeff | Psep (MW) | Pulse length
 | 18.4 | 1113 | 40 | 0.86 | 1.7 | 3.8 | 3.1 | 0.35 | 2.8 | 126 | 1h25
 | 21.8 | 1053 | 57 | 0.82 | 1.5 | 3.1 | 2.3 | 0.25 | 1.8 | 131 | 1h
Full line: Power w/o radiation subtracted
Dashed line: max power radially (as if radiation subtracted inside rho=0.6)

## Slide 10: illustration 2/3: impact of H factor, fGr and scaling law
DEMO A=2.8 max() | Ip (MA) | Wth (MJ) | Vloop (mV) | Pfus (GW) | q95 | bN | fboot | Zeff | Psep (MW) | Pulse length
Ref. case H98 scaling law H=1.1 fGr=1.2 ref_H98_maxP.mat | 21.8 | 1053 | 57 | 1.5 | 3.1 | 2.3 | 0.25 | 1.8 | 131 | 1h
H98 scaling law H=1.1 fGr=1.6 ref_H98_maxP_fGr1d6_iter.mat | 19.9 | 1085 | 55 | 1.7 | 3.4 | 2.5 | 0.23 | 1.6 | 148 | 1h
H98 scaling law H=1.5 fGr=1.2 ref_H98_maxP_H1p5_iter.mat | 19.6 |  | 36 |  | 3.5 |  |  |  |  | 1h35
DS03 scaling law H=1.1 fGr=1.2 ref_DS03_maxP_iter.mat | 19.6 |  | 33 |  | 3.5 |  |  | 2.4 | 127 | 1h45
 | Ip (MA) | Wth (MJ) | Vloop (mV) | Pfus (GW) | q95 | bN | fboot | Zeff | Psep (MW) | Pulse length
Ref. case H98 scaling law H=1.1 fGr=1.2 ref_H98_maxP.mat | 21.8 | 1053 | 57 | 1.5 | 3.1 | 2.3 | 0.25 | 1.8 | 131 | 1h
H98 scaling law H=1.1 fGr=1.6 ref_H98_maxP_fGr1d6_iter.mat | 19.9 | 1085 | 55 | 1.7 | 3.4 | 2.5 | 0.23 | 1.6 | 148 | 1h
H98 scaling law H=1.5 fGr=1.2 ref_H98_maxP_H1p5_iter.mat | 19.6 |  | 36 |  | 3.5 |  |  |  |  | 1h35
DS03 scaling law H=1.1 fGr=1.2 ref_DS03_maxP_iter.mat | 19.6 |  | 33 |  | 3.5 |  |  | 2.4 | 127 | 1h45

## Slide 11: illustration 3/3: impact of profile choices when constraining energy and density on resp. H98 and fGr
Easier than optimization loops in PROCESS
More physics at reach, can explore/understand one by one uncertainty impact
But… No profile stiffness, energy content constrained as well as line averaged density for more physical response : need turbulent transport model
DEMO A=2.8 max() | Ip (MA) | Wth (MJ) | Vloop (mV) | Pfus (GW) | q95 | bN | fboot | Zeff | Psep (MW) | Pulse length
Ref. case H98 scaling law H=1.1 fGr=1.2 Density peaking factor 1.2 ref_H98_maxP.mat | 21.8 | 1053 | 57 | 1.5 | 3.1 | 2.3 | 0.25 | 1.8 | 131 | 1h
H98 scaling law H=1.1 fGr=1.2 Density peaking factor 1.7 ref_H98_maxP_vane1d7_iter.mat | 21.8 | 1049 | 55 | 1.6 | 3.1 |  |  | 1.8 |  | 1h
H98 scaling law H=1.1 fGr=1.2 Tped/2 ref_H98_maxP_Tped0d5_iter.mat | 21.2 | 1085 | 57 | 1.7 | 3.1 | 2.5 | 0.26 | 1.9 | 119 | 1h
 | Ip (MA) | Wth (MJ) | Vloop (mV) | Pfus (GW) | q95 | bN | fboot | Zeff | Psep (MW) | Pulse length
Ref. case H98 scaling law H=1.1 fGr=1.2 Density peaking factor 1.2 ref_H98_maxP.mat | 21.8 | 1053 | 57 | 1.5 | 3.1 | 2.3 | 0.25 | 1.8 | 131 | 1h
H98 scaling law H=1.1 fGr=1.2 Density peaking factor 1.7 ref_H98_maxP_vane1d7_iter.mat | 21.8 | 1049 | 55 | 1.6 | 3.1 |  |  | 1.8 |  | 1h
H98 scaling law H=1.1 fGr=1.2 Tped/2 ref_H98_maxP_Tped0d5_iter.mat | 21.2 | 1085 | 57 | 1.7 | 3.1 | 2.5 | 0.26 | 1.9 | 119 | 1h

## Slide 12: outline
Uncertainties in system code and mitigation action
Going up the ladder of models for a better understanding of uncertainties impact: Scaling laws with ad-hoc heat transport coefficients
High fidelity integrated modelling using turbulent transport models: validation
Gaps between today’s tokamak plasmas and ITER/DEMO
Verification against even higher fidelity integrated modelling
Extrapolation towards DEMO: status and plans
Side note on VNS
Conclusion

## Slide 13: Instead of extrapolating with scaling laws and guessing profile shapes, need to use flux driven profile prediction
transport PDE solver
Sources: ECRH, NBI,fusion power
Sinks: radiation
Turbulent transport fluxes
reduced models: TGLFsat2
2D magnetic eq
Initial profiles
Predicted Ti, density, profiles up to r=1
√
√
√ in today’s tokamaks
X in high b, 3.5 MeV alphas
ASTRA, HFPS …
Reduced turbulent transport models fast enough to be iterated with source and sink calculations as well as magnetic equilibrium reconstruction successfully validated against density and temperature profiles evolution in AUG, JET, WEST, TCV etc doing better than scaling laws, explaining ICRH/ECRH impact of radiative collapse, explaining the ‘cold pulse’ etc see for a review [Bourdelle PPCF 2025]

## Slide 14: high fidelity integrated modelling: towards large scale validation
User independent: need automated validation (software support)
Quantification: need synthetic diagnostics vs measurements
Large amount of data manipulation, need support from UQ techniques and hardware for storage (LTSF)
8 plasma phases in WEST, 4 settings
[Vergnaud TTF 2025]
4 TCV Ip ramps, 6 settings
[Marin NF 2025]
Full radius prediction, input are engineering parameters and BC at separatrix
test of various settings. quantification prediction vs measure

## Slide 15: high fidelity integrated modelling: better than scaling laws
On ~50 L [C. Angioni NF 2022] & H modes on AUG, [T. Luda NF 2022],
ASTRA+TGLF up to separatrix in L mode, with IMEP pedestal model in H mode
better than scaling laws
see for a review [Bourdelle PPCF 2025]

## Slide 16: high fidelity integrated modelling: ready to use IMAS compatible toolboxes AND REPLACE SCALING LAWS
Metrics on Te, Ti and ne
JET
3936 predicted
0.5 s HFPS time
windows
[A. Ho EPS/TTF 2023, C. Bourdelle PPCF 2025]
Need to test various simulation settings:
Codes, BC etc
And quantify using synthetic diags
[Azizi ArXiv 2024]
Ex. Anna Glasser TWINTOK
universal diagnostics digital twin
Here bolometry
From a few to 1000s of plasma phases
Technically ready at least to get started: need manpower to work on such large scale validation project (TSVVH WP4) + support on soft/hardware and UQ
Data Management Plan: all machine data accessible in IMAS
QLKNN
Surrogate models for turbulence, pedestal and SOL
Now: TGLFNN, MISHKANN, SOLPSNN, HPI2NN ready to go

## Slide 17: Back to the Gaps in parameters from today’s tokamak to Burning Plasmas
 | Pfus | Palpha/Paux | Q | b(core) | nC | r* | frad r<1 | Plasma energy
JET DT | 12.5 MW | 8 % | 0.4 | 2.2 % | 2.4e5 | 0.034 | ~20% | 9 MJ
ITER 15 MA | 500 MW | 200 % | 10 | 4-4.2 % | 1.3e5 | 0.021 | 4% | 300-400 MJ
DEMO A=2.8 | 1600 MW | 640 % | 32 | 4.9 % | 1.4e5 | 0.016 | 90% | 600-1200 MJ
high b means more electromagnetic turbulence vs electrostatic turbulence
large fraction of Alphas at 3.5 MeV drive MHD modes which interplay with turbulence
[M. Maslov NF2023]
[F. Eriksson NF2024]
ITER
Q=16
DEMO
Q=34
Similar electron heat in MW/m3 from alpha power and ECRH in ITER and DEMO

## Slide 18: Reduced turbulent model, validated, not ready for high beta/ burning plasmas
Need higher fidelity code guidance

## Slide 19: At high b, with energetic particles, no validated reduced turbulent transport model. Need to go up the fidelity ladder of turbulent transport models
transport PDE solver
Sources: ECRH, NBI, fusion power
Sinks: radiation
Turbulent transport fluxes: GENE, CGYRO,..
Global, electromagnetic, non-linear gyrokinetic
2D magnetic eq
Initial profiles
Predicted Ti, density, profiles
TANGO, PORTALS,…
Frontier of what can be achieved presently using GPU acceleration
Being validated against high b, with fast ions experiments on AUG and JET
And used to predict ITER 15 MA
GENE-Tango [A. Di Siena et al, NF 2024]
CGYRO-PORTALS P. Rodriguez-Fernandez

## Slide 20: First global gyrokinetic profile predictions of ITER burning plasma inside rtor=0.6 [A. Di Siena et al, submitted]
GENE-Tango: global, electromagnetic, nonlinear, flux matching 8 million CPUh for convergence tests + 70k node hours on GPU [A. Di Siena et al, submitted]
TGLFsat2-HFPS: TGLFsat2 settings optimized to handle electromagnetic KBM inside r=0.5 see E. Fransson’s poster for more details and [Najlaoui PPCF 2025] for verification TGLFsat2 / GKW on JET high β plasma
kygridmodel = 4, alphazf = −1, width = 3, filter =−0.1, minwidth = −0.3, nbasis = 6, useMHDrule = true,
usebperp = true and usebpar = false ~1000 CPUh
GENE-Tango - ES
GENE-Tango – EM
QuaLiKiz-HFPS
TGLFsat2-HFPS – ES
TGLFsat2-HFPS - EM

## Slide 21: First global gyrokinetic profile predictions of ITER burning plasma [A. Di Siena et al, submitted]
GENE-Tango: with electromagnetic fluctuations, Ti is more peaked (as expected [Citrin, Mantica PPCF 2023], ne flatter (as expected [Hein et al PoP 2010]), Te unchanged. In TGLFsat2-HFPS only a slight density flattening is reported.
Good agreement between GENE-Tango electromagnetic and TGLFsat2-HFPS electromagnetic. For good or bad reasons? On-going verification GENE-GKW-TGLF on this ITER case
Next steps: adding alphas’impact on MHD/turbulence in GENE-Tango and improve physics of reduced models. Key to prepare JT60-SA operation, ITER, VNS, DEMO, etc
GENE-Tango - ES
GENE-Tango – EM
QuaLiKiz-HFPS
TGLFsat2-HFPS – ES
TGLFsat2-HFPS - EM

## Slide 22: ITER benchmark case
On same case, highest fidelity modelling (GENE-Tango CGYRO-Portals) and ASTRA/HFPS-TGLF
ASTRA/HFPS-TGLF will be used to test impact of uncertainties: q, Vtor, W content etc on performance (D. Fajardo)
The most impacting parameters will be verified in GENE-Tango CGYRO-Portals
HFPS
ASTRA
[T. Luda et al sub. NF 2025]

## Slide 23: outline
Uncertainties in system code and mitigation action
Going up the ladder of models for a better understanding of uncertainties impact: Scaling laws with ad-hoc heat transport coefficients
High fidelity integrated modelling using turbulent transport models: validation
Gaps between today’s tokamak plasmas and ITER/DEMO
Verification against even higher fidelity integrated modelling
Extrapolation towards DEMO: status and plans
Side note on VNS
Conclusion

## Slide 24: Impact of TGLFsat2 settings importance of resolving correctly the electromagnetic modes
TGLFsat2 | Electrostatic, default | Optimized, being verified [E. Fransson poster]
Min ky | 0.05 (grid 4) | 0.05 (grid 4)
filter | 2 | -0.1
width | 1.65 | 3
Alpha_zf | 1 | -1
Min width | 0.3 | -0.3
dBerp | off | on
dBparallel | off | off
Use_mhd-rule | false | true
ne at 360s
Ti at 360s
Pfus in W
750 MW due to TGLFsat2 settings
! ne flatter in electrostatic TGLFsat2 unlike expectation [Hein et al PoP 2010]) and unlike GENE-Tango

## Slide 25: pedestal pressure impacts Pfus due to ci stiffness
IMEP
+9%, +140 MW
Pped in Pa
Pfus in W
+10%, +9kPa
at 360 s
Pedestal in HFPS based on ITER-EPED scaling [Polevoi NF 2015] multiplied by 0.55 and 0.50
Stiff TGLF turbulent heat flux, Ti(core) responds linearly to Ti(ped) hence
Dedicated DEMO at A=2.8, 4.4 T, 18.8 MA Pedestal pressure prediction using IMEP : MISHKA MHD stability + empirical relation on the electron temperature gradient [Luda NF 2021] in ASTRA predicts Pped=92 kPa. In agreement with IPED based scaling [Puchmayr, Dunne 2020]

## Slide 26: Physics based HFPS-TGLFsat2 profiles very different from assumed profiles in PROCESS for DEMO design
ne in 1019m-3
Ti in keV
HFPS-TGLFsat2
HFPS-TGLFsat2
METIS-scaling on energy + ad-hoc shape
METIS-scaling on energy + ad-hoc shape
 | Wth (MJ) | Vloop (mV) | li | Pfus (GW) | q95 | bN | Zeff | fboot
METIS profiles | 1113 | 40 | 0.86 | 1.7 | 3.8 | 3.1 | 2.8 | 38%
HFPS | 1055 | ~50 | 0.71 | 1.7 | 3.9 | 2.6 | 1.7 | 40%
PROCESS

## Slide 27: DEMO predictive modelling: what comes next?
Next:
Explore the impact of Ip on DEMO performance (with IMEP for pedestal). Verify scaling law based mitigation action to epistemic plasma physics uncertainties: Design at q95>3.3 to be able to increase Ip to compensate confinement loss
Test other actuators: ECRH, density, fuel mix, etc
Add more nonlinear couplings (TSVV-H support):
  Pellet ablation model (HPI2)
  Alpha transport based on alpha driven MHD (ATEP)
Test impact of uncertain BC such as W content, of Vtor etc as done for SPARC [Muraca ArXiv 2025]
Ultimate goals:
Guide flight simulator physics content requirement. Prepare control schemes and adjust design accordingly
Guide DEMO design by reducing ad-hoc parameters in system code: energy, density, profiles, radiation
Synergies/collaborations tbd
Strong synergy with ITER 15 MA: ITPA T&C ITER 15 MA ref. case (EU-US, Spring 2026 report), more?
Possibly more with MIT team on SPARC
And STEP team at UKAEA

## Slide 28: outline
Uncertainties in system code and mitigation action
Going up the ladder of models for a better understanding of uncertainties impact: Scaling laws with ad-hoc heat transport coefficients
High fidelity integrated modelling using turbulent transport models: validation
Gaps between today’s tokamak plasmas and ITER/DEMO
Verification against even higher fidelity integrated modelling
Extrapolation towards DEMO: status and plans
Side note on VNS
Conclusion

## Slide 29: VNS predictive modelling
High fidelity integrated modeling settings as validated on JET/AUG NBI+EC/IC
TGLFsat2 for turbulent transport & FACIT for W neoclassical transport in ASTRA
E. Bray’s PhD U. Torino + C. Angioni, M. Siccinio, C. Bourdelle et al
Ib. Validation on JET beam-target, to reduce range of uncertainnties
Which is what ITER is to DEMO.
Momentum transport and W content at separatrix
Time of radiative collapse
Inside r/a<0.3
Power on electrons OH+NBI+ECRH+Alpha
Radiative power
[Maslov NF2023]
Ia. Prediction of time evolution in VNS
Understand actuators: NBI torque/particle source, ECRH impact. Optimize machine design to delay radiative collapses
II. After validation, explore uncertainties impact on time of radiative collapse and other key performances
Likely W content at separatrix
Pedestal transport hypothesis
Neutral particle source choices
Momentum transport etc

## Slide 30: Conclusions: high fidelity modelling validation, getting ready for ITER, designing DEMO
Uncertainties in validation of High Fidelity Integrated Modelling in today's devices. Both on 1000s of plasmas and testing 10s of BC/code settings. Technically ready to go (including surrogates on main models)
  Need to support (HiFi modelers, soft/hardware, data management plan, UQ) large scale automated validation of High Fidelity integrated modeling. All the IMAS interfaced tool boxes are available.
  Compare to scaling law prediction capabilities, towards replacement of scaling laws
VNS: High Fidelity integrated modeling guiding the design. Validation on JET beam-target, then uncertainties impact on performances
Towards burning plasmas, gap between today’s tokamaks and ITER/DEMO : beta, fast particle fraction. But similarities between ITER/DEMO
  Need verification of reduced models against GPU accelerated nonlinear global gyrokinetic codes. Need to join forces EU/US (and more) ITPA T&C TC33 on ITER 15MA ref case, on-going + SPARC?
  On High Fidelity Integrated modeling: need to complexify coupling: pellet model, pedestal, EP transport
  Yearly feedback on
    flight simulator physics content requirement. Prepare control schemes and adjust design accordingly
    Guide DEMO design by reducing ad-hoc parameters in system code: energy, density, profiles, radiation
  Be ready for validation (STEP/SPARC/ITER), with a hierarchy of models. The fastest accurate validation on a burning plasma is the best way to accelerate DEMO.

## Slide 31: Brainstorming ideas for on-site week
Hierarchy of models going up and down the ladder key to understand and mitigate uncertainties.
Quantifying the results against measurements when available as well
With EUROfusion whole device modelling spread in : WPTM (TSVV-H), Digital Solutions for fusion Office, DEMO Central team /WPDES.
Therefore on-site week could focus on activities aiming at whole device modelling, towards better than scaling laws.
Benchmark cases could be proposed to compare various fidelity levels.
Use and verify surrogates
Training/sharing UQ tools for large scale validation (e.g. in PROCESSFailure severity, probabilistic approach, Uncertainty theory )
IMAS experimental database made available, support for uniformizing IMAS input/output
Should be repeated yearly, ideal coordination platform
Physics understanding |  | Prepare operation |  | Design future devices | 
1st principle codes | High Fidelity Integrated Modeling |  | Pulse Design Tools Full pulse, testing controllers |  | System codes in/out are engineering parameters only
Validation against tokamak experiments |  |  |  |  |