## Slide 1: WP PWIE: SP D Reporting 2025
Andreas Kirschner & SP D task holders
Notes: Please Indicate your subproject

## Slide 2: SP D Deliverables 2025
SP D.1 Plasma Boundary Modelling
D001: Plasma background parameters of WEST for modelling of impurity migration experiments (focus on long-pulse, high fluence discharges, impact of magnetic field ripple and drifts). (CEA) 2PM
D002: Plasma background parameters of MAGNUM-PSI and UPP for modelling of impurity migration experiments (improvement of boundary conditions in particular for UPP). (DIFFER) 2PM
D003: Plasma background parameters of GyM for modelling of impurity migration experiments (focus on Ar plasmas, validation against cross-machine experiments under SP B). (ENEA) 2PM
D004: Plasma background parameters of W7-X (based on OP2.2 and OP2.3) and linear device PSI-2 (plasma source, fluid runs, neutral kinetics) for modelling of impurity migration experiments. (FZJ) 4PM
D005: PIC modelling: sheath for collisional boundary conditions, study of inverse sheath. (IPP.CR) 5PM
D006: Plasma background parameters for JET for impurity migration experiments (consideration of limiter configurations, characterisation of ELMs and SOL flows e.g. for Ni/W migration). (VTT) 3PM
D007: Parametric SOLPS-ITER simulations, optimised divertor operation point (magnetic field arrangement, geometry, and divertor leg length), and exhaust capabilities compared with reference single null divertor (JT-60SA full-C) arrangement. (LPP-ERM/KMS) 12PM

## Slide 3: SP D Deliverables 2025
SP D.2 Production of Atomic/Molecular and Surface Data
D001: Dust production from anomalous events and detached divertor conditions, identify possible dust formation mechanisms like nucleation in fusion-relevant plasmas. Cross section determination for neutral and charged W clusters. Connection to exp. data (e.g. dust studies in WEST). (CEA) 2PM
D002: Sputtering and reflection data for surface systems including boron (e.g. W-B, B-O, and other combinations also containing D), including seeding projectiles (e.g. Ar, Kr, Xe). Development of according interaction potentials. (ÖAW) 3PM
D003: Erosion information (SPRAY code, SDTrimSP-3D) of surfaces including morphology, roughness, fuzz. Influence of structure (oriented vs. random) and porosity. Comparison to experiments (e.g. PSI-2) and MD results. (ÖAW) 2PM
D004: Modelling of tungsten gap melting and bridging including comparison to experiments (e.g. from AUG and WEST). Gap melt scenarios for ITER. (VR) 6PM
D005: Sputtering and reflection yields from MD for W, W-D(H, T) and W-B surfaces. Application of more advanced (accurate) (ML, AI) interaction potential for tungsten and boron sputtering/reflection modelling. Comparison to BCA. (VTT) 5PM

## Slide 4: SP D Deliverables 2025
SP D.2 Production of Atomic/Molecular and Surface Data … cont´d
D006: Reflection/erosion information of 2D/3D surfaces with focus on lattice effects, comparison to MD simulations and/or experiments. (MPG) 2PM
D007: Sputtering of W-D(H, T) surfaces, release of W-D molecules (study of impact energy and surface temperature). Study of interaction potentials: gauge, which is most reliable. Analyse the effect of electronic energy losses. (VTT) 3PM

## Slide 5: SP D Deliverables 2025
SP D.3 Impurity Migration Modelling
D001: SOLEDGE3X-ERO2.0 simulations of tungsten transport in WEST. Determination of main tungsten sources and core contamination in WEST. Comparison with spectroscopy and post-mortem data. One focus on long-pulse, high-fluence discharges and full 3D treatment (antennae, magnetic field ripple). (CEA) 2PM
D002: ERO2.0 simulations of tungsten dynamic morphology studies in GyM with Ar (see also SP B). Global ERO2.0 migration simulations in GyM, also for the design of diagnostics. ERO2.0 modelling of global erosion/deposition experiments in AUG He H-mode scenarios (connected to WP TE SOLPS modelling). (ENEA) 5PM
D003: ERO modelling of 13C injection experiments (local) in comparison to post-mortem data in W7-X and steady-state simulations. ERO2.0 predictive modelling for full W environment in W7-X (inclusive role of CX neutrals). ERO and ERO2.0 modelling of W prompt redeposition (focus on JET experiment with varying B field), in combination with sheath characteristics from PIC. Initial simulations of ITER with full-W plasma-facing components and Ne seeding. Modelling of tungsten (prompt) redeposition at inner wall during ITER ramp-up phases. (FZJ) 17PM

## Slide 6: SP D Deliverables 2025
SP D.3 Impurity Migration Modelling … cont´d
D004: Predictive material migration in full-W ITER including B transport resulting from boronisation using new SOL plasma solution with self-consistent far SOL. (MPG) 2PM
D005: ERO2.0 simulations of AUG erosion and migration experiments in L- and H-mode D plasma and comparison with experimental data and former simulations. Assess impact of uncertainty of OSP position and plasma conditions. (VTT) 4PM
D006: Self-charging properties for (tritiated) boron dust. (VR) 3PM
D007: ERO2.0 of Ni/W migration modelling in JET. (VTT) 2PM

## Slide 7: SP D Deliverables 2025
SP D.4 Neutral Particles Modelling
D001: DIVGAS modelling: effect of 3D poloidal and toroidal leakages for the DEMO baseline SN divertor case including impurities, pVT characteristics (KIT) 4PM
D002: Atomic and molecular fluxes spatially resolved to the wall surfaces (including divertor) in JET. Explore pressure range, sub-divertor geometry and conclusions for effective pumping speed in JET. (VTT) 2PM
SP D.5 Plasma Background and PWI Modelling for COMPASS-U
D001: SOLPS-ITER plasma backgrounds for full-W COMPASS-U H-mode scenarios (gradual consideration of drifts, currents, pump feedback and Ne seeding). Sheath characteristics from PIC simulations, strike-line plasmas. (IPP.CR) 12 PM
D002: Supervision of ERO2.0 modelling. (FZJ) 1PM
D003: SOLEDGE3X plasma backgrounds in comparison to SOLPS-ITER. (CEA) 3 PM

## Slide 8: SP D.1 Plasma Boundary Modelling

## Slide 9: SP D.1 Plasma Boundary Modelling: CEA
G. Ciraolo
D001
More details: talk by D. Sales de Oliveira
SOLPS-ITER modelling for WEST
3D plasma backgrounds: ripple effect correctly recovered with SOLEDGE3X
  New plasma and wall mesh generated
  Power and density scans performed → results close to the experimental values with ripple effect
  Similar values for Te,max in both SP → feature found in experiments but not present in previous SOLEDGE3X simulations with ripples
  ERO2.0 data analysis on going → post-processing tools generating artifacts with the new meshes

## Slide 10: SP D.1 Plasma Boundary Modelling: DIFFER
E. Westerhof,
H.J. de Blank
D002
SOLPS-ITER modelling of relevant range of UPP and Magnum-PSI discharges are continuing
Still: SOLPS-ITER modelling of UPP relies on the existence of measurements of radial density and temperature profiles in the Magnum-PSI beam at same source parameters (gas flow and current) and magnetic field …
… or adjusting boundary conditions of UPP-simulations iteratively to fit UPP's profile measurements which are halfway the beam, not at the boundary of the computational domain.
Aim: these two approaches should lead to a parametrization of UPP source boundary conditions based on the source parameters and magnetic field.
SOLPS-ITER modelling for UPP and MAGNUM-PSI

## Slide 11: SP D.1 Plasma Boundary Modelling: ENEA
M. Passoni
D003
SOLPS-ITER modelling of Ar plasmas in GyM
Approach
Optimise SOLPS-ITER simulation setup for Ar plasma investigation in GyM
Validate SOLPS-ITER against experimental plasma profiles
Exploit validated SOLPS-ITER simulations as a testbed for 0D models
Results
Parametric scan performed: absorbed power identified as main driver for electron density and ionization degree. Pumping speed set to reproduce neutral pressure at baratron position.
Post processing: low-ionized plasma (α ≃ 0.02), dominant ionic species is Ar+, complete thermal decoupling between electrons and ions/neutrals.
Tested 0D plasma models provided good agreement against optimised SOLPS-ITER simulations for electron and neutral densities, electron temperature and ionisation degree (deviations < 30%) over a wide parametric scan.
More details: talk by G. Alberti

## Slide 12: SP D.1 Plasma Boundary Modelling: ENEA
M. Passoni
More details: talk by G. Alberti
SOLPS-ITER modelling of Ar plasmas in GyM
Comparison betweeen Langmuir probe and optimised SOLPS-ITER radial plasma profiles
F. Mombelli, A. Uccello, M. Passoni
D003

## Slide 13: SP D.1 Plasma Boundary Modelling: FZJ
S. Xu
D004
EMC3-EIRENE plasma backgrounds of W7-X
EMC3-EIRENE modeling with Nitrogen seeding based on experiments in OP2.3. (#XP_20250522.*)
Input:
Pin = 3.5 MW
D⊥ = 0.5 m2/s
χ⊥ =1.5 m2/s
nLCFS= 2.7E13 cm-3
Impurity:
C from divertor: sputtering yield 4%
N from seeding: P_imp_N= 0 MW, 0.5 MW, 1.0 MW

## Slide 14: SP D.1 Plasma Boundary Modelling: FZJ
S. Xu
D004
EMC3-EIRENE plasma backgrounds of W7-X
Heat flux distribution at divertor
depending on N seeding flux

## Slide 15: SP D.1 Plasma Boundary Modelling: FZJ
D. Reiser
D004
More details: talk by D. Reiser
PSI-2 simulations using SOLPS-ITER
Basic Steps to a Running System for PSI-2 Simulations:
Installation of Code Package
Preparing Geometry Input
Test Run B2.5 Standalone
Preparing Visualization Tools
Preparing Source Input Files
Adjustment of Physics Parameters
B2.5 Standalone Runs
B2.5-Eirene Runs
Examples for starting guesses for sheath:
Densities vary only about a factor of 2, exception: run3 with negative biasing

## Slide 16: SP D.1 Plasma Boundary Modelling: IPP.CR
D. Tskhakaya
D005
Simulations of emissive sheaths in SPICE2
Simulations of ITER-relevant intra-ELM plasmas at hot W PFCs including electron thermionic emission (TE), secondary electron emission (SEE) and electron back-scattering (EBS)
The objective: characterize the magnitude of escaping electron current, which is an important input to MEMENTO code and better understanding of the emissive sheath
At grazing angles the electron prompt re-deposition is essential; from [Costin SciRep 2021]
M. Komm, S. Ratynskaia, P. Tolias, A. Podolnik
Outcomes:
We have validated the Costin formula
We found a semi-empirical relation between the net electron yield Y and the surface E field

## Slide 17: SP D.1 Plasma Boundary Modelling: VTT / Aalto U
M. Groth
D006
JET He plasmas
Horiz. and vert. target configuration, 1-5 MW → ERO2.0 for W sputtering, transport
SOLPS-ITER underpredicts the total radiation (helium emission) by 2x, consequentially, overpredicts total heat flux to low-field side plate by 2-3x
D. Rees

## Slide 18: SP D.1 Plasma Boundary Modelling: VTT / Aalto U
M. Groth
D006
JET He plasmas
D. Rees
Performed first comparison of measured He+ Lyman-alpha emission (dominant radiator) from VUV spectroscopy to SOLPS-ITER / Cherab for helium plasma
Observed same issue as for hydrogenic plasmas: divertor plasma too hot, too sparse?
Discrepancy in total heat to LFS plate is in part due to lack of radiation and more peaked heat flux profiles in simulations
Modification to radial transport for addressing heat flux profiles, analyses to be presented at PSI 2026
SOLPS-ITER underpredicts the total radiation (helium emission) by 2x, consequentially, overpredicts total heat flux to low-field side plate by 2-3x

## Slide 19: SP D.1 Plasma Boundary Modelling: LPP-ERM/KMS
W. Dekeyser
D007
SOLPS-ITER modelling for JT-60SA W divertor
W. Van Uytven, S. Van den Kerkhof, W. Dekeyser
Provide support for the possible transition to W divertor through SOLPS-ITER exhaust scenario assessment
Previous work (G. Rubino, L. Balbinot): high temperatures at OT restrictive for current baseline scenario
Refine predictions through simulations with drifts, and extending grid up to the full vessel wall (extended grid: technically running but not converged yet …)
Explore whether divertor shape modifications can mitigate this problem
Note: successful backwards compatibility testing with structured code version; small bugs in structured version and model discrepancies identified.

## Slide 20: SP D.1 Plasma Boundary Modelling: LPP-ERM/KMS
W. Dekeyser
D007
SOLPS-ITER modelling for JT-60SA W divertor
W. Van Uytven, S. Van den Kerkhof, W. Dekeyser
Results from drift simulations: non extended grid, 3 MW input, ne,sep = 2E19m-3
Drifts aggravate situation w.r.t. W sputtering at OT: even higher Ti at outer baffle
To be repeated with feedback on ne,sep to recover exact density from reference case

## Slide 21: SP D.1 Plasma Boundary Modelling: LPP-ERM/KMS
W. Dekeyser
D007
SOLPS-ITER modelling for JT-60SA W divertor
W. Van Uytven, S. Van den Kerkhof, W. Dekeyser
Results from drift simulations: non extended grid, density scan
Pushing separatrix density of reference scenario up to 3.5e19 m-3 at fixed Ne puff of 4.1e20 s-1 still leads to (unacceptably) high OT temperatures
Compatibility with core to be investigated for these higher-density cases

## Slide 22: SP D.1 Plasma Boundary Modelling: LPP-ERM/KMS
W. Dekeyser
D007
SOLPS-ITER modelling for JT-60SA W divertor
W. Van Uytven, S. Van den Kerkhof, W. Dekeyser
Results from drift simulations: alternative geometries
Need new equilibrium in order to rotate target plate around ‘upper hinge point’ at baffle without moving strike point onto reflector plates

## Slide 23: SP D.2 Production of Atomic/Molecular and Surface Data

## Slide 24: SP D.2 Production of Atomic/Molecular and Surface Data: CEA
A. Michau
D001
Molecular Dynamics of Neutral Tungsten Cluster Growth
Structure of cluster formed by the growth via the reaction: Wn + W → Wn+1
Computed up to n=40 using Molecular Dynamics (Lammps, EAM potential)
plateau after n=20 atoms
=> Interpolation possible for larger size

## Slide 25: SP D.2 Production of Atomic/Molecular and Surface Data: CEA
A. Michau
D001
Thousands of trajectories simulated with
different potentials: case of W-W5
How likely two clusters are to coalesce under collision conditions?
Molecular Dynamics of Neutral Tungsten Cluster Growth

## Slide 26: SP D.2 Production of Atomic/Molecular and Surface Data: CEA
A. Michau
D001
DFT Investigation of collision between charged tungsten clusters
Thousand trajectories:
highly time-consuming

## Slide 27: SP D.2 Production of Atomic/Molecular and Surface Data: ÖAW
M. Probst, S. Shermukhamedov
D002
MD for B surface: sputtering of B by D and B
D on B
B on B

## Slide 28: SP D.2 Production of Atomic/Molecular and Surface Data: ÖAW
M. Probst, S. Shermukhamedov
D002
MD for B2O3 surface: sputtering by D
Sputtering of B
Sputtering of O
Differences between B and O can be attributed to the energy transfer factor 4M1M2/(M1 +M2)2
Yields of oxygen atoms increase monotonously with the energies and angles

## Slide 29: SP D.2 Production of Atomic/Molecular and Surface Data: ÖAW
M. Probst, S. Shermukhamedov
D002
MD for B2O3 surface: chemical sputtering by D
Ony B-O radicals were detected, no O-D
Different from B surfaces where B-D is formed (however, here B₂O₃ was sputtered)
The result might therefore be different for cumulative MD simulations where a coating of adsorbed D might already be present on the surface

## Slide 30: SP D.2 Production of Atomic/Molecular and Surface Data: ÖAW
F. Aumayr, J. Brötzner
D003
Influence of morphology & porosity on erosion
Generation of fuzzy model surfaces after SEM input data. Variation of the fuzz porosity/volume filling factor. Simulations with SDTrimSP-3D for Ar and D projectiles.
Suppression of the angular dependence of the sputter yield.
Decrease in sputter yield over wide range of incidence angles.
Stronger effect for more porous samples, i.e. lower volume filling factor.
Observed for all studied projectiles and energies.
Example: 1 keV Ar -> W

## Slide 31: SP D.2 Production of Atomic/Molecular and Surface Data: ÖAW
F. Aumayr, J. Brötzner
D003
Influence of morphology & porosity on erosion
Sputter yield is a linear function of porosity/volume filling.
Intercept with a solid target is not given by the flat sample sputter yield, but rather the rough sample sputter yield when hollows are not considered.
Results in line with measured and simulated data for nano-columnar tungsten.

## Slide 32: SP D.2 Production of Atomic/Molecular and Surface Data: VR
S. Ratynskaia
D004
Completed
Compared Fluent simulations of in-place gap filling scenarios (melt produced symmetrically on both sides of a castellation gap) in JET with experimental observations (see pinboard manuscript #120517)
Implementation and testing of volume forces from surface-integrated thermionic emission current in Fluent (necessary for in-place W gap filling scenarios)
Carried out first in-place gap filling simulations for an ITER W monoblock gap during unmitigated current quenches, with a large B field inclination angle (i.e. strong driving force from thermionic emission)
Ongoing until the end of 2025
Repeat ITER-like simulations with shallower B field inclinations to sample the relation between driving force and time required to bridge the gap during a single exposure
Gap melting simulations

## Slide 33: SP D.2 Production of Atomic/Molecular and Surface Data: VR
S. Ratynskaia
D004
W gap bridging predictions for ITER
500 um wide gap, computed at every time step from total thermionic current emitted from PFC surface.
B field inclination angle varied between 5° (typical value) and 20° (edge of ITER divertor cassettes) while maintaining the normal plasma heat flux at 250 MW/m2.
Results
For shallower inclination angles, bridges take longer to form but are thicker, hence more likely to subsist.
Characteristic bridge thickness is consistently larger than typical melt depth, as in Be simulations.
When 20°, the bridge is unstable because its thickness is comparable to the amplitude of “falling-film” free-surface waves.
aB = 5°
aB = 20°

## Slide 34: SP D.2 Production of Atomic/Molecular and Surface Data: VTT
K. Nordlund / F. Granberg
D005
More details: talk by F. Granberg
Development and testing of W-B ML interatomic potential
Initial sputtering and B deposition simulations successfully done
W-O-H potential finished within TSVV-7
It seems that D decoration will increase slightly sputtering of W (D weakens bonds)
Sputtering of alloys (HEAs): preferential sputtering and surface enrichment observed, some increased sputtering for alloys compared to elemental W
MD for W surfaces including B, O, H and for alloys

## Slide 35: SP D.2 Production of Atomic/Molecular and Surface Data: MPG
U. von Toussaint
D006
Erosion of surfaces with SDTrimSP: amorphization
  Status: SDTrimSP capable of handling crystalline structures (calc. erosion yields validated): code diseminated and in production use
  Enhancement: Amorphization of crystalline structures by irradiation (in non-channeling regime) (see Fig.)
  Implemented (but still waiting for TD-DFT data on electron density): reduced stopping in channels

## Slide 36: SP D.2 Production of Atomic/Molecular and Surface Data: MPG
U. von Toussaint
D006
Erosion of surfaces with SDTrimSP: improved potentials
  Status: SDTrimSP provides several (semi-) empirical binary collision potentials (KrC, ZBL etc.)
  Enhancement : Recently complete set of DFT-based pair potentials (NLH, Nordlund et al.) have been published with promise of improved accuracy
  These ‚ab-initio‘ potentials have been implemented and partly evaluated (ie. with respect to sputtering)
Example: sputtering of Cu

## Slide 37: SP D.2 Production of Atomic/Molecular and Surface Data: VTT
A. Sand, N. Fakhrayi Mofrad
D007
More details: talk by N. Fakhrayi Mofrad
MD modelling of W surfaces
Study of interaction potentials and molecular sputtering
Results of MD sputtering simulations significantly dependent on interatomic potential.
Compared three potentials capable of describing W-H/D/T molecules:
  Dimer bond strength and distance, surface binding energies, surface energies, cohesive energy elastic constants
  Tersoff bond-order potential (BOP-1) performs best
Molecular sputtering of W surfaces depends on impact energy and surface temperature

## Slide 38: SP D.2 Production of Atomic/Molecular and Surface Data: VTT
A. Sand, N. Fakhrayi Mofrad
D007
More details: talk by N. Fakhrayi Mofrad
MD modelling of W surfaces
Molecular sputtering of W surfaces depends on impact energy and surface temperature

## Slide 39: SP D.2 Production of Atomic/Molecular and Surface Data: VTT
A. Sand, N. Fakhrayi Mofrad
D007
More details: talk by N. Fakhrayi Mofrad
MD modelling of W surfaces
Effect of electronic energy losses
Using electronic stopping dependent on local electron density (b(ρ)) gives a higher sputtering yield compared to SRIM stopping.
b(ρ) model fitted to TDDFT, generally enhances agreement with experiments.
Reason: SRIM overestimates the energy losses for channeling ions.

## Slide 40: SP D.3 Impurity Migration Modelling

## Slide 41: SP D.3 Impurity Migration Modelling: CEA
G. Ciraolo
D001
More details: talk by D. Sales de Oliveira
SOLEDGE3X + ERO2.0 for WEST erosion/deposition data
  Both location and magnitude of the ISP erosion matching the post-mortem analysis
  Large region with re-deposited W in the ISP far-SOL → weakly predicted in the simulations

## Slide 42: SP D.3 Impurity Migration Modelling: ENEA
M. Passoni
D002
Approach
Migration experiment: erosion of the exposed target and re-deposition on Si wafers (catchers)
Preliminary simulations using background plasma from SOLPS-ITER SP D.1 activity to optimize the experimental setup (target material choice, exposure time, biasing voltage, catchers positioning...)
Experiment performed under SP B.1 and produced erosion/ deposition data are compared to ERO2.0
Results
Final experimental setup: two Cr coatings exposed for 5 hours in total at –70V, with catchers in different positions in proximity of sample-holder (SH)
Factor ~1.5 higher erosion rate of Cr target in modelling compared to exp, due to higher ion flux on target surface computed by ERO2.0
Good agreement between exp and ERO2.0 deposited thickness on catcher surface (30-40 nm)
Migration experiment design and ERO2.0 code validation in GyM Ar plasma
ERO2.0 morphology modelling of Ar plasma exposed W samples
Results
Good agreement with exp -> lower dynamic retention effect wrt He plasma
G. Alberti, C. Tuccari, A. Uccello, M. Passoni
More details: talk by G. Alberti

## Slide 43: SP D.3 Impurity Migration Modelling: ENEA
M. Passoni
D002
More details: talk by G. Alberti
Modelling of H-mode He plasma discharges in AUG
Approach
SOLPS-ITER background plasma produced under WP TE and imported in ERO2.0
Estimate of the impact of He+/2+ fraction, H+ (as a result of NBI) and O concentration on divertor erosion in inter-ELM conditions
Modelling of ELMs as 1 keV D+ ions impacting in OSP region as a function of impact angle
Results
No significant effect on erosion profile of He+ and H+ inclusion
Important impact of O6+ inclusion but far from OSP and lower erosion than experiments (150-250 nm net erosion close to OSP, net deposition in private flux region)
Good match with experiments considering 85° ELM impact in OSP area
G. Alberti, C. Tuccari, A. Uccello, M. Passoni

## Slide 44: SP D.3 Impurity Migration Modelling: FZJ
J. Romazanov
D003
W7-X: predictive modelling for full W environment in Ne-seeded plasma.
ITER: erosion and deposition on mirrors in remote areas: updated simulations for full-W, boronized ITER.
JET: simulation of tungsten erosion and edge-to-core transport in Ne-seeded JET plasmas.
ITER full-W simulations performed with Ne seeded SOLPS-ITER wide-grid plasma backgrounds.
ITER ramp-up simulations.
ERO2.0 (ERO) modelling for W7-X, ITER, JET …
C. Baumann, S. Rode, H. Kumpulainen, A. Kirschner

## Slide 45: SP D.3 Impurity Migration Modelling: FZJ
D003
ERO2.0 (ERO) modelling for W7-X, ITER, JET …
J. Romazanov
Work has been presented at various conferences in 2025

## Slide 46: SP D.3 Impurity Migration Modelling: FZJ
A. Kirschner
D003
ERO modelling: W prompt redeposition at inner wall during ITER ramp-up
Accepted NME
Example: W redeposition profiles for medium density case – influence of Dperp

## Slide 47: SP D.3 Impurity Migration Modelling: MPG
K. Schmid
D004
WallDYN3D modelling of B layer lifetime in ITER
First lifetime estimates were presented in PSI-2024 contribution:
Lifetime of boronization layers will determine frequency of boronizations in ITER
How long does a 100 nm B layer survive in ITER?
First predictions based on surface concentration but no closed material balance because of simple WallDYN3D surface model
New surface model with reservoir layer allows to close material balance

## Slide 48: SP D.3 Impurity Migration Modelling: MPG
K. Schmid
D004
WallDYN3D modelling of B layer lifetime in ITER
New surface model with reservoir layer allows to close material balance
Surface concentration result qualitatively the same…
…but now with closed material balance
B ends up at inner target but is covered by W once main chamber B source depletes
submitted to NME

## Slide 49: SP D.3 Impurity Migration Modelling: VTT
A. Hakola, J. Karhunen, S. Saari
D005
ERO2.0 for AUG marker experiments

## Slide 50: SP D.3 Impurity Migration Modelling: VTT
A. Hakola, J. Karhunen, S. Saari
D005
ERO2.0 for AUG marker experiments

## Slide 51: SP D.3 Impurity Migration Modelling: VR
S. Ratynskaia
D006
Self charging properties of tritiated dust
Completed: Results for W dust (W is already embedded in MicroElec)
Tuned the surface barrier model so that experimental results on secondary electron emission and electron backscattering from W are accurately reproduced.
Added physics list transition from 10 to 20keV, since MicroElec cannot be employed above 10keV.
Performed extensive simulations including the beta electron angular distribution, the beta electron energy distribution, the depth of implantation and the dust size.
For each dust size, obtained simple analytical formulas that perfectly fit simulation results for depth resolved β−electron induced emission yields.
Derived a general expression for the self-charging rate that is expressed as a radial integral of the depth resolved β−electron induced emission yields.
Performed comparison between new MicroElec results and previous EMOpt4 results, which reveal that EmOpt4 results strongly underestimate W dust self-charging rate
Ongoing: Results for B dust which is not included in the material library of MicroElec.
More details: talk by P. Tolias

## Slide 52: SP D.3 Impurity Migration Modelling: VR
S. Ratynskaia
D006
Self charging properties of tritiated dust
Basic physics:
Tritium radioactivity implies that tritiated dust will self-charge positively due to the continuous loss of fast internal electrons that are generated by the beta-decay.
Methodology:
The MicroElec package of Geant4 (Monte Carlo simulations) is the most appropriate being based on single scattering implementations, following the dielectric formalism that well captures secondary electron production and including a surface barrier model.
More details: talk by P. Tolias

## Slide 53: SP D.3 Impurity Migration Modelling: VTT
M. Groth
D007
P. Virtanen
JET-ILW scenario simulations for Ni → limiter plasmas
For HFS limited plasmas, the ERO2.0 predicted Ni erosion peaks at LFS vessel wall at a rate of 1.12x1020/s, similar to low-power diverted scenarios
Ni erosion and deposition in JET – Ni density in limited plasma

## Slide 54: SP D.3 Impurity Migration Modelling: VTT
M. Groth
D007
P. Virtanen
Ni erosion and deposition in JET – net deposition in divertor
For HFS limited plasmas, the net deposition of Ni into the divertor HFS default scenario is negligible compared to diverted phase

## Slide 55: SP D.4 Neutral Particles Modelling

## Slide 56: SP D.4 Neutral Particles Modelling: KIT
Ch. Tantos,
Th. Giegerich
D001
DIVGAS modelling: effect of 3D poloidal and toroidal leakages for 2022 DEMO baseline SN divertor case including impurities (He)
  DIVGAS used to simulate flow of helium-deuterium mixture in DEMO sub-divertor region
  At divertor entrances, the neutral inlet pressure ranged from 1 to 4 Pa, pumping probability (ξ) from 1% to 10%, and helium mole fraction from 5% to 10%.
  As with deuterium, poloidal gaps have stronger effect than toroidal gaps, with pumped flux (for inlet divertor pressures up to 10 Pa) expected to remain well below 20% of incoming flux.
  Helium’s albedo are similar to deuterium’s: 0.78 and 0.72 for weak (ξ=1%) and strong (ξ=10%) pumping at 4 Pa.
  The change in helium mole fraction was minor, likely due to similar mass, same pumping probability and most probable speed of helium and deuterium.
  The helium partial pressure was found to range from 0.04 Pa to 0.17 Pa when the overall inlet pressure is 4 Pa and the mole fraction varies from 5% to 10%.

## Slide 57: SP D.4 Neutral Particles Modelling: KIT
Ch. Tantos,
Th. Giegerich
D001
DIVGAS modelling: effect of 3D poloidal and toroidal leakages for 2022 DEMO baseline SN divertor case including impurities (He)
  Distribution of the overall incoming flux across various gaps and leakages

## Slide 58: SP D.4 Neutral Particles Modelling: KIT
Ch. Tantos,
Th. Giegerich
D001
DIVGAS modelling: gas distribution in JET vessel
Aim: support accurate interpretation of the in-vessel pVT calibration.
  DIVGAS was applied to study neutral gas dynamics in JET, including the sub-divertor and vessel. The effect of the thermal accommodation coefficient was analyzed for three pressures (1 Pa, 2.5 Pa, 5 Pa) and two reference temperature conditions.
  Macroscopic distributions were found to be insensitive to the thermal accommodation coefficient, due to low Knudsen numbers.
  Density increases by a factor of 1.5 from the vacuum vessel to the pipes, with a much larger increase—about fivefold—near the cryopump surface.
  Macroscopic distributions remain uniform in lower sub-divertor region and L-shaped pipe.

## Slide 59: SP D.4 Neutral Particles Modelling: KIT
Ch. Tantos,
Th. Giegerich
D001
DIVGAS modelling: gas distribution in JET vessel
Aim: support accurate interpretation of the in-vessel pVT calibration.
DIVGAS JET model, with temperatures indicated by different colours
Temperature conditions (°C)
case A case B
(standard) (baking)
(nom. 200) (nom. 320)
----------------------------------------------------------------------
180 280
----------------------------------------------------------------------
80 140
----------------------------------------------------------------------
55 100
----------------------------------------------------------------------
45 45
----------------------------------------------------------------------
20 20
  Density for 1 Pa

## Slide 60: SP D.4 Neutral Particles Modelling: VTT / Aalto U
M. Groth
D002
JET neutral dynamics using EIRENE – isotope effect
Explore pressure range, sub-divertor geometry
→ effective pumping speed
→ DIVGAS comparison for simplified geometry
A. Vesa

## Slide 61: SP D.4 Neutral Particles Modelling: VTT / Aalto U
M. Groth
D002
JET neutral dynamics using EIRENE – isotope effect
A. Vesa
Time-dependent EIRENE simulations of pumping speed for H2, D2, T2 injection into JET empty vessel are within a factor of 2 of the measurements
Adjust conductance at sub-divertor entrance to force agreement w/ exp.
⇒ next: replace sub-divertor with calibrated pump surface in divertor corner

## Slide 62: SP D.5 Plasma background and PWI Modelling for COMPASS-U

## Slide 63: SP D.5 Plasma background and PWI Modelling for COMPASS-U: IPP.CR
D. Tskhakaya
D001
Strike point sheath simulations for COMPASS-U
(i) Simulations of strike-line plasma w/rt divertor design and sheath physics
Simulations with reduced parameters finalized in Q3/2025, full parameters. starting soon (new SOLPS profiles necessary).
To be done: new SOLPS profiles upcoming – re-run few cases
Conclusions: reduction of parameters is too restricting – wider simulations necessary to reduce periodic boundary effects, code updates were performed to enable this strategy (2025).
SPICE2 w/nonuniform injection scheme (2D PIC), inputs: BIT1 (injection VDF, Tskhakaya) + SOLPS-ITER (target profiles, Shyshkin / Švorc)
(ii) Evaluation of simulated results, possible code updates for full-scale simulations
A. Podolnik

## Slide 64: SP D.5 Plasma background and PWI Modelling for COMPASS-U: IPP.CR
D. Tskhakaya
D001
Kinetic model of the COMPASS-U flux tube in the SOL
Two sets of simulations have been performed #3210 (Ne seeded) and #5400 moderate and high density shots (H-mode)
#3210: completed; Ne seeded ID and OD are (partially) detached, with strong reduction of Gw, net.
#5400: w/o Ne seeding – completed; formation of the collisional sheath at the ID; significant W outflux, Gw, net ~ 1020 m-2s-1. Ne seeded – ongoing (2025 – 2026?)
Future plans (2026/2027): ELM modeling (started); different injection rates of Ne and Ar

## Slide 65: SP D.5 Plasma background and PWI Modelling for COMPASS-U: IPP.CR
D. Tskhakaya
D001
SOLPS-ITER wide-grid modelling of the background plasma
#5400
(high density / performance shot)
Full vessel mesh
Fluid neutrals, no currents and drifts, no impurities
Good matching of PSOL (Tped), nped from core model (METIS) and e-folding lengths based on lq scaling
Example:
radial profiles of ne at the OMP
#24300
(H mode with moderate density)
Ongoing, convergence problems …
D. Svorc

## Slide 66: SP D.5 Plasma background and PWI Modelling for COMPASS-U: IPP.CR
D. Tskhakaya
D001
S. Lukes
ERO2.0 modelling of the W transport COMPASS-U
Q1: A preliminary ERO2.0 parametric study and an investigation of basic dependencies and phenomena ✔ (presented at PET-20)
Q2: ERO2.0 simulations with liquid metals and their influence on W erosion ✔ (presented at PSI-26)
Addition of global electric field and thermal force from SOLPS-ITER background plasma✔
Q3: W erosion and transport modelling using SOLPS ITER-ext. background plasma ✘ (some delay in SOLPS ITER-ext results)
We expect all tasks to be finished till the end of 2025

## Slide 67: SP D.5 Plasma background and PWI Modelling for COMPASS-U: IPP.CR
D. Tskhakaya
D001
S. Lukes
ERO2.0 modelling of the W transport COMPASS-U

## Slide 68: SP D.5 Plasma background and PWI Modelling for COMPASS-U: FZJ
J. Romazanov
D002
Has been done !
ERO2.0 support to IPP.CR

## Slide 69: SP D.5 Plasma background and PWI Modelling for COMPASS-U: CEA
P. Tamain
D003
Simulation of COMPASS-U in L-mode conditions with SOLEDGE3X
R. Düll

## Slide 70: SP D.5 Plasma background and PWI Modelling for COMPASS-U: CEA
P. Tamain
D003
Simulation of COMPASS-U in H-mode conditions with SOLEDGE3X
R. Düll

## Slide 71: WP PWIE SP D: Plans for 2026/27

## Slide 72: WP PWIE SP D: Plans for 2026/27
SP D1 Plasma background modelling
SOLPS-ITER, SOLEDGE3X, PIC codes, …
WEST, AUG, JET, COMAPSS-U, ITER
W7-X
GYM, PSI-2, MAGNUM, UPP
CEA, DIFFER, ENEA, FZJ, IPP.CR, IPP.LM, VTT
SP D2 Production of surface data
MD, SDTrimSP, SPRAY, …
Sputtering, reflection, morphology
W, B, steel, D, seeding species, O, He, …
CIEMAT, ENEA, MPG, ÖAW, VTT, UKAEA
SP D3 Atomic/molecular data
CRM, neutrals
ENEA, FZJ
SP D4 Impurity migration modelling
WallDYN, ERO2.0, core modelling
WEST, AUG, JET, COMAPSS-U, ITER
W7-X
GYM, PSI-2, MAGNUM, UPP
CEA, ENEA, FZJ, IPP.CR, IPP.LM, MPG, VTT
Strong connection to:
ITER, TSVV, SP B, WP TE, WP W7X, …
37PM
15PM
+3PM
32PM
4PM
PMs per year …

## Slide 73: WP PWIE SP D: Agenda – SP D Highlight Talks
Tue Nov. 18th
Thu Nov. 20th

## Slide 74: WP PWIE: SP D Reporting 2025
Thank you very much for your patience !!!