## Slide 1: TSVV 9: Dynamics of runaway electrons during tokamak disruptions
E. Nardon, EUROfusion Science Meeting – TSVV final reports, 14/01/2026

## Slide 2: Outline
Introduction to disruptions and Runaway Electrons (REs)
TSVV 9 team, tools, activities – with selected highlights:
  Self-consistent MHD + kinetic REs in JOREK
  Validation of RE generation models
  Predictions on RE avoidance in ITER
  Trying to understand RE beam benign terminations
Summary and perspectives
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 2

## Slide 3: Disruptions
[Courtesy M. Lehnen]
Current Quench (CQ):
  Very resistive post-TQ plasma
  Ip decay
  Electromagnetic loads
  Thermal flash on PFCs
  Large electric field Eφ, typically >> Ec
  → Sometimes, RE beam
[Nardon PPCF 2021]

Thermal Quench (TQ):
  MHD instability, stochastic B field
  Ip spike
  Radiative collapse
  Thermal flash on PFCs
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 3

## Slide 4: RE beam impact: often harmful… but can also be benign
Recent PPCF roadmap paper: [Ratynskaia PPCF 2026]
Impacts can be benign under specific conditions
  Background plasma needs to be recombined
  Accessible only inside a certain range of neutral pressure
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 4

## Slide 5: What are runaway electrons?
eE
eEc
Force on an electron from collisional friction + synchrotron radiation
Electrons may run away whenever E > Ec
(‘critical electric field’)
When E > Ec, electrons faster than the
‘critical velocity’ v1 will run away
RE energy is limited (typically to ~10-20 MeV)
by radiation reaction forces
Review papers: [Breizman NF 2019] [Boozer PoP 2015]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 5

## Slide 6: Primary (‘seed’) RE generation mechanisms (1/2)
Dreicer: collisional diffusion into RE domain [Connor NF 1975]
  Typically negligible in ITER
Hot-tail:
  In case of fast cooling, e- distribution function F deviates from a Maxwellian
  Strong RE production if E rises faster than collision time at critical velocity [Smith PoP 2007]
  Hard to predict but potentially by far largest seed in ITER
F
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 6

## Slide 7: Primary (‘seed’) RE generation mechanisms (2/2)
Tritium β decay
Compton scattering by wall-emitted γ’s
Eγ (MeV)
Γ(Eγ) (MeV)
‘Nuclear’ seeds:
[Martín-Solís NF 2017]
E (keV)
ν(E) (a.u.)
Small but active throughout the CQ
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 7

## Slide 8: Secondary RE generation mechanism: the avalanche
Close (‘knock-on’) collisions can generate 2 REs from 1
→ Exponential growth in RE population
Initial theory by Rosenbluth and Putvinsky [Rosenbluth NF 1997]
→ When E|| >> Ec, log(Gav) ∝ Δψ ∝ ΔIp
→ Avalanche gain Gav scales exponentially with Ip!
E.g. Gav = 1.9 × 1016 in ITER (15 MA) vs. 1.8 × 103 in JET (3 MA) [Hender NF 2007]
(note: E|| ≈ ∂tψ/R)
Theory extended to account for bound electrons
  Additional targets for knock-on collisions, not fully compensated by additional friction (because of charge screening)
  → Can strongly boost Gav [Hesslow NF 2019]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 8

## Slide 9: RE-handling strategies
ITER: Shattered Pellet Injection (SPI) [Lehnen JNM 2015]
One or several Ne+H pellets (flexible mixture ratio)
Aim: RE avoidance and/or mitigation
Also in charge of thermal and electromagnetic loads mitigation
SPARC: RE Mitigation Coil (REMC)
Passive system
Induced current from dIp/dt → B stochasticity
→ RE avoidance
[Tinguely PPCF 2023]
EU-DEMO:
sacrificial limiters
[Maviglia FED 2022]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 9

## Slide 10: The TSVV 9 project
≈ 6 ppy/year over 2021-2025
Labs.: IRFM, Chalmers U., KTH, IPP Garching, EPFL, ACH VTT
≈ 15 funded contributors + many unfunded collaborators
Important synergies with TSVV 8, WPTE, ITER DMS Task Force, …
Group picture from the 12th Runaway Electron Modelling meeting, Lausanne, June 2025
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 10

## Slide 11: Simulation tools: 2 main ‘workhorses’
DREAM
  Designed specifically to model REs during disruptions
  1D (flux surface averaged, fixed geometry), 2P
  Self-consistently evolves e- distribution function using bounce-averaged kinetic equation
    Different possible levels of description, from fully kinetic to fluid-like
JOREK
  Originally an MHD code, later extended to model REs
  2D or 3D, self-consistently evolved geometry
  Fluid REs [Bandaru PRE 2019]
  Kinetic REs [Bergström PPCF 2025] [Särkimäki NF 2022] [Sommariva NF 2018]
Good complementarity and synergy between the 2 codes
  Simplifying a bit, DREAM is faster but contains less physics
[Hoelzl NF 2021]
[Hoppe CPC 2021]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 11

## Slide 12: Model/code developments
Pellet models (essential to study disruption mitigation with SPI)
  Self-consistent ablation plasmoid drift model [Vallhagen JPP 2023] implemented in DREAM
  Physics of pellet ablation plasmoid drifts also investigated with JOREK [Kong NF 2025]
  Ad hoc ablation plasmoid teleportation model in JOREK [Kong NF 2024]
  Pellet rocket effect model [Guth PRL 2025] [Guth JPP accepted]
Kinetic REs in JOREK
  Self-consistent coupling to the MHD equations via PiC method [Bergström PPCF 2025]
  Hot tail (test particles) [Puel NF 2025]
  Avalanche [Wouters EFTC 2025]
Effect of vertical plasma motion implemented in DREAM [Vallhagen JPP 2025] based on key input from JOREK [Wang NF 2025]
Reduced model to predict RE generation in activated tokamaks [Zaar JPP submitted]
Model for upper neutral pressure limit to access benign RE beam termination [Hoppe PPCF 2025]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 12

## Slide 13: Validation
Validation of DREAM SPI simulations for ASDEX Upgrade [Halldestam JPP 2025] [Vallhagen PPCF 2025]
  (Similar effort for JOREK SPI simulations on ASDEX Upgrade, JET, …, but mainly outside TSVV 9)
Validation and investigation of 3D MHD aspects of disruptions with JOREK
  Ip spike, magnetic stochasticity, impurity mixing [Nardon PPCF 2021] [Nardon NF 2023]
Validation of RE beam formation simulations with JOREK and DREAM [Järvinen JPP 2022] [Nardon REM 2024]
  Using Bayesian framework (ACH VTT)
RE benign termination
  JOREK simulations for JET [Bergström PPCF 2025] [Singh REM 2024] [Sommariva NF 2024]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 13

## Slide 14: Predictions
ITER
  RE generation
    Extensive predictions for SPI-mitigated disruptions with DREAM [Vallhagen NF 2024] [Vallhagen JPP 2025] [Votta, in prep.]
    Compared fluid and kinetic DREAM predictions [Ekmark JPP 2024]
    Optimised mitigation through Bayesian framework [Ekmark JPP 2024]
    Started assessing hot tail generation with JOREK [Puel NF 2025]
    Investigated 3D MHD effects during the CQ with JOREK [Särkimäki NF 2022] [Wang, in prep.]
  RE termination
    First predictions with JOREK [Bergström PPCF 2024] [Bandaru NF 2024]
    Investigation of the role of background plasma resistivity [Nardon PoP 2023]
Other machines
  Predicted RE beam generation and termination in EU-DEMO with JOREK [Vannini NF 2025]
  Predicted RE generation in DTT with JOREK [Emanuelli FED 2026] [Emanuelli, submitted]
  Predicted RE beam generation in ≈STEP with DREAM [Berger JPP 2022]
  SPARC:
    Predicted effect of REMC with DREAM [Tinguely PPCF 2023]
    Predicted RE generation in MGI-mitigated disruptions with DREAM (w/o REMC) [Ekmark JPP 2025]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 14

## Slide 15: Summary
DREAM and JOREK have been developed massively to improve the modelling of RE dynamics during tokamak disruptions
  This is highly complex integrated modelling
  Good complementarity and synergy between the 2 codes
Validation has progressed but is a complex task, to be pursued
  Avalanche model partly validated using Bayesian framework
  Other models (RE impact, hot tail) started but difficult
Avoiding RE beams in large future machines like ITER remains a major challenge
  Enormous avalanche gain + nuclear seeds + possibly large hot tail seed
  It is critical to capture the mechanisms that impact the avalanche gain (e.g. vertical motion during CQ, j profile flattening during TQ)
Some aspects of RE beam terminations have been modelled and understood, but a lot remains to be investigated
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 15

## Slide 16: Perspectives
Essential to maintain a strong activity
  Partly covered by TSVV-F in 2026-2027
Key topics:
  TQ physics (in particular in SPI-mitigated disruptions): trigger condition, transport, current density profile flattening, hot tail RE generation
  Impact of 3D MHD activity during the CQ on RE beam dynamics
  RE beam termination and PFC damage
  Access conditions to benign terminations
    ⚠ Might be in conflict with current RE avoidance strategy in ITER
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 16

## Slide 17
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 17

## Slide 18: Self-consistent MHD + kinetic REs in JOREK
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 18
JOREK electron pusher evolves a population of kinetic electrons
Moments of this population used in the fluid equations
Pressure coupling scheme
  [Bergström PPCF 2025]
Benchmarks on, e.g.:
  Impact of RE energy on major radius of magnetic axis
  Linear tearing mode growth rates
First applications to RE beam terminations

## Slide 19: Validation of RE generation models
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 19
Validation is made difficult by the existence of “free parameters”
Typical example: validation of the avalanche model
  Aim: reproduce the RE plateau current IRE
  Issue: RE seed is “free” → Can be used as a knob to match IRE → “Fancy fitting” instead of validation
Solution?
  1) Automatize fancy fitting through Bayesian optimisation framework → Speed, objectivity
  2) Try to match more experimental observations, e.g.
  synchrotron radiation, detailed shape of Ip(t) curve, …
  3) Show that fancy fitting is not possible with
  a falsified model
[Järvinen JPP 2022]
[Nardon REM 2024]
Falsifying Γav: true / x 2 / x 0.5
  (JOREK data lost in Marconi flooding )

## Slide 20: Predictions on RE avoidance in ITER
Extensive predictions for SPI-mitigated disruptions with DREAM [Vallhagen NF 2024] [Vallhagen JPP 2025] [Votta, in prep.]
  Cover a wide range of plasma scenarios and SPI parameters
The model includes ‘ad hoc’ ingredients, informed e.g. by JOREK simulations
  TQ: trigger condition, duration, transport, j profile flattening
  Effect of vertical motion during CQ
Avoiding multi-MA RE beams in ITER disruptions is challenging
  Enormous avalanche gain + unavoidable nuclear seeds
  In addition, hot tail generation can also be a major concern
Strategy: use SPI to dilute the plasma as much as possible before the TQ
  Suppresses hot tail generation by increasing the collisionality
  (Moderately) reduces the avalanche gain Gav by raising Ec
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 20

## Slide 21
15 MA L-mode plasma, no nuclear seeds
15 MA H-mode plasma, with nuclear seeds
Multi-MA RE beam cannot be avoided because of unavoidable nuclear seeds combined with very large avalanche gain
But these predictions may be pessimistic…
RE beam can be avoided by suppressing the hot tail (+ Dreicer) seeds
Most effective method: staggered injection, i.e. pure H SPI followed by H+Ne SPI
[Votta, in prep.]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 21

## Slide 22
15 MA H-mode plasma, with nuclear seeds
Including a j profile flattening during the TQ improves prospects
  Related to the Ip spike – a common feature of disruptions
  Modelled in DREAM through a hyper-resistivity term (Λm)
  Reduces the avalanche gain Gav by reducing Δψ
RE avoidance may not be hopeless, even with nuclear seeds
[Votta, in prep.]
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 22

## Slide 23: Trying to understand RE beam benign terminations
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 23
Typical chronology of benign terminations:
  1) Injection of D2 into the RE beam → Recombination of the background plasma
  2) At some point, violent instability → Complete loss of the REs
Background plasma recombination seems essential. Why?
Here, we propose a tentative partial interpretation, which certainly does not cover the whole story.
[Reux PRL 2021]
RE beam terminations in JET, including a benign one

## Slide 24
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 24
Poincaré plot (dots) + nRE (color)
ITER simulation using JOREK with the RE fluid model
[Bandaru NF 2024]
(Time progressing from left to right and top to bottom)
Dominantly m/n = 2/1 instability related to qa approaching 2
As the instability grows, magnetic stochasticity develops, deconfining the REs.
The stochastic region expands radially in time. Let’s call its radial extent Δrstoch.

## Slide 25
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 25
RE heat load on the wall in the previous ITER simulation
[Bergström PPCF 2024]
The deconfined REs distribute on the wall inside the “magnetic footprint”, whose area Afootprint increases in time.
Afootprint is largely determined by the amplitude of the dominant (i.e. 2/1) mode.

## Slide 26
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 26
Afootprint
Δrstoch
0
a
Benign
Non-benign
A key factor determining the severity of the impact may be the ratio Δrstoch/Afootprint.
Experimentally, benign impacts have a larger Afootprint. Why?
This may be related to the background plasma resistivity η.
  Note: Instability dynamics largely determined by η, even though the current is initially fully carried by REs [Helander PoP 2007].

## Slide 27
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 27
η = η0
η = 10 η0
[Bandaru NF 2024]
At lower η, Δrstoch is larger for a given 2/1 mode amplitude.
  This is because of stronger secondary modes, as detailed in [Nardon PoP 2023].
Since Afootprint is determined by the amplitude of the 2/1 mode, Δrstoch/Afootprint is larger at lower η.
Low η promotes larger heat fluxes.
The increased η resulting from recombination may be a key factor in benign terminations.
Comparing 2 simulations at different background plasma resistivity η

## Slide 28
E. Nardon | EUROfusion Science Meeting | 14 Jan. 2026 | Page 28
Some key open points:
  JOREK simulations so far were initialized from an unstable state. How does the picture change when evolving across the instability boundary?
  Kinetic + orbit shift effects? → Simulations with the JOREK kinetic RE model [Bergström PPCF 2025].
  Self-consistent modelling of the (recombined) background plasma and its re-ionization during the termination
  Access conditions to benign terminations
    ⚠ Might be in conflict with current RE avoidance
    strategy in ITER
    Model for upper neutral pressure limit [Hoppe PPCF 2025]