## Slide 1: Contributions from Aalto University
Ray Chandra, Timo Kiviniemi, Mathias Groth
Aalto University, Espoo, Finland
TSVV-5 : Report 2025
Dec 12, 2025

## Slide 2: TSVV-5 deliverables 2025: development and application of EIRENE photon model & EIRENE validation in JET
Full photon-gas-plasma coupling enabled in SOLPS-ITER and validation with JET-ILW Ohmic plasmas
Evaluation of isotope effect on (H,D,T) gas pumping with time-dependent EIRENE simulations of JET-ILW

## Slide 3: Full photon-gas-plasma coupling enabled in SOLPS-ITER and used for JET-ILW Ohmic plasma simulations
R. Chandra et al., PET 2025
Feature in the SOLPS-ITER/EIRENE git branch feature/photon_transport
Applied to SOLPS-ITER JET-ILW Ohmic D plasma in varying midplane separatrix density  Prediction of ILFS-plate peak values improved by ~30% and increased qLFS-plate by 10-80% at high-recycling

## Slide 4: Full photon-gas-plasma coupling enabled in SOLPS-ITER and used for JET-ILW Ohmic plasma simulations
R. Chandra et al., PET 2025
Use PESDT-Cherab on SOLPS-ITER result to produce synthetic diagnostic
Increased Ba-α emission by 3x with Lyman trapping but Ba-γ overestimated at deep detachment  not the complete picture
Current results summarized to a Nuclear Fusion publication

## Slide 5: Evaluation of isotope effect on (H,D,T) gas pumping with time-dependent EIRENE simulations of JET-ILW
[1] C. Day, Fusion Sci. Technol., 2005
Seff (H2) = 192 m3/s
Seff (D2) = 112 m3/s
Seff (T2) = 66 m3/s
KT5P Bar. 1
Pumping speeds as measured by the subdivertor Baratron pressure gauge
The differences between isotopes are caused by their masses and sticking coefficients
Sticking coefficients [1]: α(H2) = 0.6, α(D2) = 0.9 and α(T2) = 1.0
JPN 104589
Seff (H2) = 216 m3/s
Seff (D2) = 150 m3/s
Seff (T2) = 124 m3/s
EIRENE
(prior to 2D geometry calibration)

## Slide 6: Evaluation of isotope effect on (H,D,T) gas pumping with time-dependent EIRENE simulations of JET-ILW
Adjustment on the LFS entrance obstruction matched measured and simulated effective pumping speeds of D2 (112 m3/s vs. 119 m3/s)
Matching all isotopes simultaneously requires modifying sticking coefficients [similarly as in A.Scarabosio & A. Zito works]
Isotope | Measured Seff | Simulated Seff (unobstructed) | Simulated Seff (obstructed)
Protium (H2) | 192 m3/s | 216 m3/s | 160 m3/s
Deuterium (D2) | 112 m3/s | 150 m3/s | 119 m3/s
Tritium (T2) | 66 m3/s | 124 m3/s | 98 m3/s