## Slide 1: KDII#8 Final Meeting Solps DEMO Simulations
F. Subba

## Slide 2: Outline
Task specification/status
Low/density attached case
Scans towards high density/detachment
Current status: target loads, sputtering, pumping
Future developments

## Slide 3: Task Specifications
Deliverable | Status
Strongly attached case (no evidence of momentum loss in the plasma flow to the target) | 
Barely detached case (evidence of momentum loss but electron temperature still above 5 eV on the divertor plate) | 
Fully detached case (electron temperature below 5 eV and heat flux below 10 MW/m2 on the divertor plate) | 
Overly detached case (larger impurity concentration than in case 3 – radiation front moving towards the X-point) | 
The first two objectives are available now, the last two are still to be completed

## Slide 4: Attached Case
First attached case: end 2019
Target heat flux barely tolerable
BUT
Temperature unrealistic
Upstream density: < 2e19 m-3
Pin = 150 MW
Particles:
  D Pellet = 3.0e22 s-1
  D puff = 4.6e21 s-1
  Ar puff = 3.0e19 s-1
  He 7.1e20 s-1
Heat flux density
Density and temperature

## Slide 5: Increase Upstream Density: Dead End?
Pull D puff up
Push Ar Puff down
Increase Dpuff shows little effect
  Probably need (at least) to be more aggressive
  But puff would be no more a “correction”
Decrease Ar puff has more significant effect
  Possible explanation from S. Krasheninnikov, Phys. of Plasmas, 2016
  But we still want a high-radiative divertor
Try both ways together!
Upstream density
Upstream density

## Slide 6: Explore a Different Setup (Pilot Case)
Change substantially the setup
Particle fuelling:
  Dpuff: 1e23 s-1
  Pellets: 7e21 s-1
  Arpuff: 1.5e19 s-1
Pcore: 150 MW (unchanged)
Consequences:
  Worsen the T burn-up
  Put more stress on the fuel recycle system
  Still doable

## Slide 7: Approach to Steady State
Upstream density
Int. energy content
nup  ~3e19 m-3?
Pilot case not steady state yet, but not terribly far
Energy content: increase rate ~4 MW (vs. 150 Pin)
Electron content increase rate: ~4e22 s-1 (vs. Dpuff 1.e23 s-1)
Range of “acceptable” upstream densities: 3-4 e19 m-3
Probably still more room to improve target conditions

## Slide 8: Core Plasma Pollution
Core Zeff
Zeff profile
Core Zeff decreasing noticeably
  Now slightly les than 2 at the separatrix
  Large changes no more expected
  Almost uniform across the core

## Slide 9: Core Plasma Pollution
Zeff profile
Ionic species profiles
Core Zeff decreasing noticeably
  Now slightly les than 2 at the separatrix
  Large changes no more expected
  Almost uniform across the core
Helium core content
  Measure concentration as cHe = nHe/nD
  At the moment cHe = 20%-25%
  Space for improvement if nup can increase further

## Slide 10: Target Profiles: HFS
HFS target is markedly high-recycling / detached
Large max. density: ~1.3e21
Tsep < 1 eV
Ptarg/Pup ~ 0.3
T increases away from strike point but:
  Max value still ~5 eV
  About 0.5 m far from strike point
Not a big surprise on the HFS
Target density
Target temperature

## Slide 11: Target Profiles: LFS
LFS more critical
Higher density: ~2e21
Reduced pressure drop: Ptarg/Pup~0.6
Higher max temperature: ~19 eV
Target density
Target temperature

## Slide 12: Target Profiles: LFS
LFS more critical
Higher density: ~2e21
Reduced pressure drop: Ptarg/Pup~0.6
Higher max temperature: ~19 eV
Luckily enough Tmax is still going down...
Target density
Target temperature

## Slide 13: Target Profiles: LFS
LFS more critical
Higher density: ~2e21
Reduced pressure drop: Ptarg/Pup~0.6
Higher max temperature: ~19 eV
Luckily enough Tmax is still going down...
Now check:
  Heat flux
  Sputtering
  Neutrals in the divertor
Target temperature
Target density

## Slide 14: Target Heat Flux
Heat flux density
Peak heat flux less than 2 MW m-2
Does not include radiation, but no dramatic changes expected

## Slide 15: Sputtering
Sputtered flux density
Preliminary estimate of target W sputtering
  Use TRIM database
  Python routines courtesy of D. Coster
Literature reported limit: 1.5e19 m2s-1 (R. Wenninger, Nuclear Fusion, 2014)
Wall damage also to be evaluated
Input can be given to other codes (e.g. ERO)
Wall neutral flux

## Slide 16: Neutrals in the Divertor
Pump
Pump
Pump
Pump
Neutrals accumulate close to the pump ... But not so much!

## Slide 17: Neutrals in the Divertor
Estimated pumping speed: several 1e3 m3s-1  too much
Neutral species | Pressure close to pump opening (Pa) | Density close to pump opening (m-3)
 | 1.2 | 1.3×1019
 | 2.8 | 3.8×1019
 | 0.26 | 1.3×1018
 | 0.025 | 9.6×1016
Neutral species | Pressure close to pump opening (Pa) | Density close to pump opening (m-3)
 | 1.2 | 1.3×1019
 | 2.8 | 3.8×1019
 | 0.26 | 1.3×1018
 | 0.025 | 9.6×1016

## Slide 18: Improving Neutral / Divertor Conditions
At a first look, neutral conditions in the divertor seems the most critical parameter feature
Possible mitigating actions:
  Explore higher upstream density
  Should we include the liner in our modeling?

## Slide 19: Future Developments (Proposal)
Higher upstream density
  Always beneficial
  Complete the desired detachment scan
Include the liner in simulations
  More accurate divertor description
  Hope for better pumping conditions
Consider species-dependent albedos
  Not sure if a major difference might arise
  But it could improve the simulation accuracy/reliability
Code upgrade: from 3.0.6 to 3.0.7
  New version just released
  Second half of 2020 seems a reasonable time to upgrade

## Slide 20: Thank you For Attention