## Slide 1: Improved feedback control of the radiated power in Wendelstein 7-X using system identification
A. Tsikouras, F. Reimold, G. Partesotti, M. Krychowiak, M. van Berkel, and the W7-X Team

## Slide 2: Content
Motivation
Control approach
  Perturbative experiments
  Frequency Analysis
Results
Summary
Future Work
System Identification

## Slide 3: Motivation
Radiated power () control : essential for the operation of W7-X
Impurity seeding from the gas divertor inlet system
Safe divertor operation
Plasma studies in different steady-state radiation regimes

## Slide 4: Motivation
Radiated power () control : essential for the operation of W7-X
Impurity seeding from the gas divertor inlet system
Safe divertor operation
Plasma studies in different steady-state radiation regimes
Until now: seeding pulses (feedforward approach)
Frequency of the pulses and valve opening times are experimentally defined
Different operating parameters require different pulse parameters
Oscillatory behaviour not suitable for clean physics studies
Unexpected response  discharge termination
Example feedforward control discharge (Argon seeding)

## Slide 5: Motivation
Feedback control:
Accuratelly following of different setpoints during discharges
Steady state
Reaction to unexpected events and drifts
Same controller can be used for different parameters

## Slide 6: Motivation
M. Krychowiak et al. Nuclear Materials and Energy 34 (2023)
Feedback control:
Accuratelly following of different setpoints during discharges
Steady state
Reaction to unexpected events and drifts
Same controller can be used for different parameters
Previous feedback system
Oscillatory behaviour due to unoptimized controller

## Slide 7: Motivation
Establish a systematic framework for designing controllers for the using System identification techniques
Perform perturbative experiments
Acquire the dynamics information of the system
Design controller based on the identified dynamics

## Slide 8: Control approach
The H block represents the system under investigation
 the relation between input and output signals
  Differential equation
Perturbative signal
Observed response
H
Τ. Ravensberger, et al. Nature communications 12 (2021)
R. Pintelon et al. System Identification: a frequency domain approach (2012)

## Slide 9: Control approach
The H block represents the system under investigation
 the relation between input and output signals
  Differential equation
Perturbative signal
Observed response
H
Τ. Ravensberger, et al. Nature communications 12 (2021)
R. Pintelon et al. System Identification: a frequency domain approach (2012)
Transfer function: the Laplace transform of
Main advantage of Laplace domain:

## Slide 10: Control approach
R. Pintelon et al. System Identification: a frequency domain approach (2012)
Frequency Response Function obtained for (transfer function in the frequency domain)
Experimentally acquired from the perturbative experiments
Cross-power spectral density
Auto power spectral density

## Slide 11: Control approach
R. Pintelon et al. System Identification: a frequency domain approach (2012)
Frequency Response Function obtained for (transfer function in the frequency domain)
Experimentally acquired from the perturbative experiments
Condition: high coherence (analysis assumes linear system around the operating point)
Cross-power spectral density
Auto power spectral density

## Slide 12: Control approach
Actuator (gas valves)
W7-X
Sensor (bolometer camera)
input
output
H

## Slide 13: Actuator (input)
Piezo-electric valve
Locations: 1 valve per divertor target
Maximum operating frequency:
Pressure dependence on the flowrate
Non-linear flowrate with respect to the valve voltage
  Focus on the linear valve regime
M. Griener et al. Rev. Of Scientific Instrumements 87 (2017)
upper divertor location
lower divertor location
input ()  valve voltage

## Slide 14: Sensor (output)
Compact Bolometer Camera (CBC)
Wide angle resistive bolometer
Triangular cross-section of module 3
Update interval of in between samples to the controller (Zero-Order-Hold implementation)
Noise level: (pre-discharge)
G. Partesotti et al. Rev. Of Scientific Instrumements 95 (2024)
output ()  calculated proxy from CBC

## Slide 15: Perturbative experiment
Multi-sinusoidal signal
Designed input signal with frequency components

## Slide 16: Perturbative experiment
Parameters for the experiment
Seeding onset:
Excited frequencies: all harmonics from
Density:
ECRH power:
Configuration: Standard
Gas box pressure:

## Slide 17: Perturbative experiment
Multi-sinusoidal signal
Designed input signal with frequency components
Bolometer signal
Clean reaction to the input
Visible delay ()
Filtering
Avoid high frequency artifacts

## Slide 18: Frequency domain analysis
Discrete Fourier Transform (excitation quality)
Dominant excitation of the input frequencies
High coherence for the input frequencies

## Slide 19: Frequency domain analysis
Transfer function representation: Bode plot
Magnitude:  relative magnitude of output in respect to the input
Phase:  phase difference between input and output

## Slide 20: Frequency domain analysis
Transfer function representation: Bode plot
Magnitude:  relative magnitude of output in respect to the input
Phase:  phase difference between input and output
System exhibits pure delay behaviour
Characteristics of pure delay
  Constant magnitude
  Descending phase as frequency increases
Expected a frequency-dependent behaviour

## Slide 21: Frequency domain analysis
Investigation of pure delay behaviour
Impulse-like experiment under investigation
3 different bolometer signals
  Real-Time CBC signal (RT)
  Post-Processed CBC signal (PP)
  Core Bolometer signal (QSB)

## Slide 22: Frequency domain analysis
Investigation of pure delay behaviour
Impulse-like experiment under investigation
3 different bolometer signals
  Real-Time CBC signal (RT)
  Post-Processed CBC signal (PP)
  Core Bolometer signal (QSB)
All signals exhibit similar amplitude behaviour
Small amplitude change for the high coherence frequencies
Low coherence
Transfer function behaviour  part of the system
Low coherence

## Slide 23: Transfer function modelling
Modelling of experimental transfer function
Different models can exhibit the same behaviour for a specified frequency region
Simplest model able to match the experimental data: pure delay
how strong the output will respond to an input
how fast the decay is
Higher order model: double exponential decay + delay
delay

## Slide 24: Transfer function modelling
Modelling of experimental transfer function
Different models can exhibit the same behaviour for a specified frequency region
Simplest model able to match the experimental data: pure delay
how strong the output will respond to an input
how fast the decay is
Higher order model: double exponential decay + delay
delay

## Slide 25: Transfer function modelling
Modelling of experimental transfer function (time domain)
Behaviour is captured by model
Missmatches in the amplitude due to non-linearities (valve operating in non-linear regimes)
Non-linearities

## Slide 26: Transfer function modelling
Modelling of experimental transfer function (time domain)
Behaviour is captured by model
Missmatches in the amplitude due to non-linearities (valve operating in non-linear regimes)
Correlation with the amplitude decreases in the bode plot
Non-linearities

## Slide 27: Controller designed:
response simulated based on model
Use of synthetic model to acquire the controller parameters
PI Controller:
Bandwidth
Satisfactory synthetic response

## Slide 28: Controller designed:
response simulated based on model
Use of synthetic model to acquire the controller parameters
PI Controller:
Bandwidth
Experimental vs Synthetic response:
Faster response
overshoot compared to
Longer settling time
Non-linearities present (valve sticking)
Satisfactory synthetic response

## Slide 29: Summary
Established framework for identifying the dynamics of the system
Perturbative experiments provide with the dynamics of the system
        Multisinusoidal and impulse-like signals provide with transfer function estimations
        Pure delay behaviour for the investigated frequency regime: only the steady state of the system is captured
Modelling of the experimental transfer function is possible with simple models
PI gains can be further optimized
        Main obstacle: the delay of the system

## Slide 30: Future work
Optimize perturbative experiment
        Smaller voltage span: operate only at the linear regime of the valve
        Include higher frequency components to investigate higher frequency dynamics
Optimize modeling of the transfer function for performing simulations
        Physics based transfer function model
Identify dynamics using as an input the seeding rate and not the valve voltage
        Controller independent of the gas box pressure
Include feedforward part for faster response