## Slide 1: Instabilities at the edge of NT TCV plasmas and geometric proxies to predict the impact of plasma shaping on turbulence
A. Balestri1,2, J. Ball1, S. Coda1, O. Sauter1, A. Mariani3, P. Mantica3 ,B. Vanovac4,B. Labit1
1Ecole Polytechnique Fédérale de Lausanne (EPFL), Swiss Plasma Center (SPC), 1015 Lausanne, Switzerland,
2Max-Planck-Institut für Plasmaphysik, Garching, Germany
3Istituto per la Scienza e la Tecnologia dei Plasmi, CNR, Milan, Italy
4Plasma Science and Fusion Center, Massachusetts Institute of Technology, Cambridge, MA 02139, United States ofAmerica
TSVV-A annual workshop07.10.2026

## Slide 2: Negative Triangularity plasmas: H-mode performance without H-mode
Experiments (TCV, DIII-D, AUG) and simulations showed that Negative Triangularity (NT):
Robustly inhibits access to H-mode [1,2,3]
Intrinsically ELM-free
Reduction of turbulent transport [4,5,6,7,8,9,10]
Recover H-mode performance
[1] A. Merle et al., 2017 PPCF 59 104001
[2] A. O. Nelson et al., 2024 PPCF 66 105014
[3] O. Sauter et al., 66th APS 2024
[4] A. Marinoni et al., 2009 PPCF 51 055016
[5] G. Merlo et al, 2023 PoP 30 102302
[7] A. Balestri et al., 2024 PPCF 66 075012
[6] G. Di Giannatale et al., 2024 PPCF 66 095003
[8] A. Mariani et al., 2024 NF 64 106024
[9] M. Bécoulet et al., 2026 PPCF 68 035031
[10] L. De Gianni et al., 2026 PPCF 64 106024

## Slide 3: Negative Triangularity plasmas: H-mode performance without H-mode
Experiments (TCV, DIII-D, AUG) and simulations showed that Negative Triangularity (NT):
Robustly inhibits access to H-mode [1,2,3]
Intrinsically ELM-free
Reduction of turbulent transport [4,5,6,7,8]
Recover H-mode performance
[1] A. Merle et al., 2017 PPCF 59 104001
[2] A. O. Nelson et al., 2024 PPCF 66 105014
[3] O. Sauter et al., 66th APS 2024
[4] A. Marinoni et al., 2009 PPCF 51 055016
[5] G. Merlo et al, 2023 PoP 30 102302
[7] A. Balestri et al., 2024 PPCF 66 075012
[6] G. Di Giannatale et al., 2024 PPCF 66 095003
[8] A. Mariani et al., 2024 NF 64 106024
[9] M. Bécoulet et al., 2026 PPCF 68 035031
[10] L. De Gianni et al., 2026 PPCF 64 106024
[7] A. Balestri et al., 2024 PPCF 66 065031
[2] A. O. Nelson et al., 2024 PPCF 66 105014
TCV
DIII-D

## Slide 4: Reduction of turbulence at the edge plays a crucial role in NT plasmas
Steepening of pressure logarithmic gradients is observed at the very edge of NT plasmas in TCV and DIII-D
[1] A. O. Nelson et al., 2024 PPCF 66 105014
[2] A. Balestri et al., 2024 PPCF 66 065031
[2]
[1]
TCV
DIII-D
Clear sign of turbulence stabilization

## Slide 5: H-mode-like performance in NT only if turbulence is reduced
NT beneficial effect might change depending on turbulence regime [1,2]
Important to characterize the dominant type of microinstabilities that dominate the NT edge
Understanding how geometry plays a role in this reduction of turbulent transport is key to design and optimize a NT scenario
NT beneficial effect might change depending on other geometrical parameters [1-3]
Can we find metrics that describe well the effect of shaping on turbulence and go beyond the definition of elongation, triangularity, etc.?
[1] A. Balestri et al., 2025 PPCF 67 105025
[2] A. Balestri et al., 2024 PPCF 66 075012
[3] G. Merlo et al, 2023 PoP 30 102302

## Slide 6: Database of TCV and DIIID [1] NT shots
All the NT datasets consist of ELM-free diverted NT scenarios.
[1] DIIID data courtesy of A. O. Nelson

## Slide 7: Database of TCV and DIIID [1] NT shots
All the NT datasets consist of ELM-free diverted NT scenarios.
At sufficiently large H-mode-like confinement can be achieved.
[1] DIIID data courtesy of A. O. Nelson

## Slide 8: Database of TCV and DIIID [1] NT shots
All the NT datasets consist of ELM-free diverted NT scenarios.
At sufficiently large H-mode-like confinement can be achieved.
Performance similar to ELMy PT H-modes [2]
[1] DIIID data courtesy of A. O. Nelson
[2] B. Labit et al.,2020 28th IAEA FEC

## Slide 9: Database of TCV and DIIID [1] NT shots
Perform linear GK simulations of high performing TCV NT shots to characterize turbulence
Most of the discharges are well above the LH power threshold
Full physics simulations at
Realistic geometry

## Slide 10: GK linear simulations of TCV NT database
Simulations of 35 TCV NT discharges show “standard” TEMs dominating transport
QL estimate predict maximum contribution to NL fluxes around

## Slide 11: GK linear simulations of TCV NT database
Simulations of 35 TCV NT discharges show “standard” TEMs dominating transport
QL estimate predict maximum contribution to NL fluxes around
Turbulence seems standard, so we can try to apply and extend a previously developed model that predicts the impact of shaping on turbulence [1]
[1] A. Balestri et al., 2024 PPCF 66 075012

## Slide 12: Where does geometry enter the gyrokinetic equation?
Parallel advection term
Trapping term
Curvature terms
FLR effects from gyroaverage operator
GK Maxwell’s equations
Pressure term
Drive term
Collisions

## Slide 13: Where does geometry enter the gyrokinetic equation?
Curvature terms
FLR effects from gyroaverage operator
GK Maxwell’s equations

## Slide 14
Geometric dependence of magnetic drifts and FLR effects
FLR effects
NT makes the FLR effects stronger
Weaker turbulence [1]
[1] A. Balestri et al., 2024 PPCF 66 075012

## Slide 15
Geometric dependence of magnetic drifts and FLR effects
Poloidal variation of magnetic drift
Magnetic drift
NT causes faster magnetic drifts that change more rapidly along the poloidal angle
Weaker turbulence [1] [1]
[1] A. Balestri et al., 2024 PPCF 66 075012

## Slide 16: I know, it was a lot to digest… let me summarize
To reduce effectively ITG and TEM turbulence we want:
as negative as possible to be away from the resonant condition
, i.e. how much changes along the flux surface, to be as large as possible to push the modes away from the resonance
to be as large as possible to increase the FLR effects and suppress turbulence
Parallel dynamics is still complicated to assess, but it seems that if we optimize the above metrics, the parallel dynamics will follow
Tested on simplified scenarios [1]. We can test it on more realistic scenarios
[1] A. Balestri et al., 2024 PPCF 66 075012

## Slide 17: Testing importance of magnetic drift and FLR effects
Proxies predict a substantial beneficial effect of NT on transport in
Let’s consider an experimental NT/PT couple from TCV [1,2]
[1] A. Balestri et al., 2024 PPCF 66 065031
[2] A. Mariani et al., 2024 NF 64 106024

## Slide 18: Testing importance of magnetic drift and FLR effects
Linear simulations at of two TCV discharges with equal and fixed gradients [1]
Consistently with previous results, we have TEM dominated regimes.
NT shows the usual linear stabilization of modes wrt PT
[1] A. Balestri et al., 2024 PPCF 66 065031
[2] A. Mariani et al., 2024 NF 64 106024

## Slide 19: Testing importance of magnetic drift and FLR effects
Nonlinear simulations show substantial reduction of turbulence from PT to NT shape.
Swapping magnetic drift velocity and FLR effects between geometry allows to recover a good part of the difference between NT and PT.
Adapted from A. Mariani et al. (submitted to PPCF)

## Slide 20: Further validation in realistic ITG scenarios from different tokamaks (DIII-D, AUG, JET)
DIII-D
NT shot #171241 [1]
PT produced with CHEASE flipping LCFS
DIII-D
AUG
JET
AUG
NT shot #43493 [2]
PT shot #36157 [3]
JET
NT shot #105835 [4]
PT produced with CHEASE flipping LCFS
[1] A. Marinoni et al., 2024 NF 64 086045
[2] B. Vanovac et al., 2026 NF, 66 106040
[3] L. Aucone et al., 2024 PPCF 66 075013
[4] O. Sauter et al., 2024 APS-DPP meeting

## Slide 21: Proxies predict stabilization of turbulence in AUG-NT scenario at
Poloidal averages performed in
Similar trends observed for DIII-D and JET
Proxies predict a substantial beneficial effect of NT on transport

## Slide 22: Importance of magnetic drift and FLR effects confirmed in realistic ITG scenarios
Nonlinear simulations show substantial reduction of turbulence from PT to NT shape.
Swapping magnetic drift velocity and FLR effects between geometry allows to recover most of the difference between NT and PT.

## Slide 23: Can we find a scenario where the proxies predict NT to be worse than PT?
Performing an artificial elongation scan starting from a TCV equilibrium, we predict that at NT should be worse than PT
NT good
NT bad

## Slide 24: Gyrokinetic simulations seem to confirm this prediction
Local gradient-driven gyrokinetic simulations of TCV
Elongation artificially changed
As expected at , in both ITG and TEM turbulence NT more stable than PT
As expected at , in both ITG and TEM turbulence NT more unstable than PT

## Slide 25: Experimental results on TCV confirm predictions
Ohmic
Ohmic
Inner limited NT and PT discharges with same magnitude of triangularity and heated with different levels of ECRH power

## Slide 26: Experimental results on TCV confirm predictions
The experimental results is well captured by the proxies

## Slide 27: Conclusions

## Slide 28: Summary
Edge linear simulations of the NT-TCV database show standard TEM dominating transport
Developed and extended simple model based on geometry dependence of magnetic drift velocity and FLR effects to predict impact of shaping on turbulence
The model seems to hold well for edge simulations of TCV TEM-dominated scenarios
The model seems to hold well for simulations of ITG-dominated scenarios in different machines (DIII-D, JET and AUG)
Predictive capabilities of geometric proxies successfully tested experimentally on TCV with and elongation scan

## Slide 29: Thank you!

## Slide 30: Backup

## Slide 31: ITG linear theory
The wave travels with a velocity:
When we add curvature and gradient of B, the ions will also drift with a velocity:
Because of different temperatures, the ions will drift at different speed. This cause an accumulation/depletion of charge
An electric field is consequently generated. This causes the appearance of a ExB drift that makes the wave’s amplitude grow
This is a resonant process.
From [1], we found that the optimal point for the growth of ITG is:
[1] M. Beer, Gyrofluid models of turbulent transport in tokamaks”, Ph.D. Thesis (1994)
where
If 0

## Slide 32: Magnetic drift scan (methodology)
To understand the impact of magnetic drifts, we have modified artificially the original NT magnetic drift profile:

## Slide 33: Magnetic drift scan in pure-ITG regime
Existence of a “rollover” point.
Growth rates decrease with increasing variation of .
Faster magnetic drifts wrt. the rollover point imply more stable modes
In agreement with [1], where the maximum growth rate can be found when:
[1] M. Beer, Ph.D. Thesis (1994)

## Slide 34: Magnetic drift scan in pITG regime
Resonant condition
NT makes the ions drift faster, causing a mismatch between and . This pushes the ITG away from the resonant condition

## Slide 35: Nonlinear simulations at conventional A in pure-ITG
We can try to see what role faster magnetic drifts and stronger FLR effects play in a conventional A case. In this context, the physical processes involved could be more complex.

## Slide 36: Nonlinear simulations at conventional A in pure-ITG
The same picture holds for the conventional A case. However, depending on the scenario, parallel dynamics could play some role

## Slide 37: We tested the same physical picture in a pure-TEM scenario
Heat flux [gB]
In a TEM scenario, the same physical picture holds, but parallel dynamics and geometry/dependent terms in collisional operator become more important