## Slide 1
A multi-machine study on turbulence suppression by density peaking in stellarators
D. Carralero1, B. Stefanoska2, K. Tanaka3, H. Thienpondt1, J.M. García-Regaña1, E. Maragkoudakis4, A. González1 , K. Aleynikova4, A. Alonso1, A. Cappa1, T. Estrada1, A. Knieps5, H. Okawada, E. Sánchez1, J. L. Velasco1, T. Windisch4, W7-X team and LHD team
1 Laboratorio Nacional de Fusión. CIEMAT, 28040 Madrid, Spain. 2Max-Planck-Institut für Plasmaphysik, 85748, Garching, 3National Institute for Fusion Science. 322-6 Oroshi-cho, Toki, Gifu 509-5292, Japan. 4Max-Planck-Institut für Plasmaphysik, D-17491 Greifswald, Germany. 5Forschungszentrum Jülich GmbH, 52425 Jülich, Germany
This work has been funded by the Spanish Ministry of Science, Innovation and Universities under grant PID2021-125607NB-I00 and PID2021-123175NB-I00 financed by MICIU/AEI /10.13039/501100011033 and FEDER, UE; and was carried out within the framework of the EUROfusion Consortium, funded by the European Union via the Euratom Research and Training Programme (Grant Agreement No 101052200 - EUROfusion). Views and opinions expressed are however those of the authors only and do not necessarily reflect those of the European Union or the European Commission. Neither the European Union nor the European Commission can be held responsible for them.

## Slide 2
A. Alonso NF 2022, D. Carralero PPCF 2022
N. Panadero, see I27 tomorrow
Scaled W7-X reactor
J.M. García-Regaña NF 2025,
see E. Sánchez P2.51 this afternoon
  Model validation is critical for the design of a stellarator reactor
Turbulence suppression is essential for achieving sufficient confinement in a stellarator reactor. BUT:
Density gradient stabilization is not obviously applicable in a reactor scenario.
Turbulence optimization is possible, but as of yet, not validated experimentally.
In order to design a reactor based on this optimization, sufficient validation is required.
1
HPI2
Recent works have provided substantial advances towards self-consistent transport simulations (D.L.C. Agapito PoP 2025). However, no experimental validation of the predicted stabilizing role of the density gradient has been carried out yet.

## Slide 3
H. Thienpondt et al., NF 2025
  Validating the effect of the density gradient: an experimental approach
2
From the theory side, this work is already well advanced:
Extensive flux tube, non-linear simulations have been carried out with code stella regarding the effect of a/Ln on turbulent transport (H. Thiendpondt et al., NF 25).
These simulations show qualitative differences between different magnetic configurations, which should be outstanding in experimental data.

## Slide 4
  Validating the effect of the density gradient: an experimental approach
2
H. Thienpondt et al., NF 2025
From the theory side, this work is already well advanced:
Extensive flux tube, non-linear simulations have been carried out with code stella regarding the effect of a/Ln on turbulent transport (H. Thiendpondt et al., NF 25).
These simulations show qualitative differences between different magnetic configurations, which should be outstanding in experimental data.

## Slide 5
  Validating the effect of the density gradient: an experimental approach
From the theory side, this work is already well advanced:
Extensive flux tube, non-linear simulations have been carried out with code stella regarding the effect of a/Ln on turbulent transport (H. Thiendpondt et al., NF 25).
These simulations show qualitative differences between different magnetic configurations, which should be outstanding in experimental data.
2
H. Thienpondt et al., NF 2025
In this work, we set out to validate experimentally these predictions at two levels:
Verify the quantitative behavior of transport among different configurations
Carry out a quantitative comparison between code predictions and experiments
 Develop comparable scenarios in W7-X, LHD and TJ-II
 Carry out a systematic comparison between simulations and power balance observations in these scenarios

## Slide 6
Introduction
W7-X results
  Baseline density gradient suppression of turbulence
  A low density scenario
  Transport evaluation
LHD results
    LHD experimental scenarios
    Transport evaluation
Multi-machine comparison and preliminary validation results
Summary
Outline

## Slide 7
  Turbulence suppression by ∇n – Baseline scenario in W7-X
3
NBI
ECRH
ECRH + NBI
ECRH
ne (1019 m-3)
Te (keV)
Ti (keV)
B. Stefanoska, in preparation
Baseline turbulence suppression scenarios in W7-X are well documented [1,2,3]:
A ∇ne is created by NBI/pellets, suppressing turbulence and increasing tE/tISS04
Then, additional heating can be used to bring up Ti,core, neTitE
With the improved gradients, a strong NC Er appears at the core [4].
[1] S. Bozhenkov, NF 20 [2] D. Carralero PPCF 22 [3] O. Ford NF 24 [4] T. Estrada, NF, 20

## Slide 8
  Turbulence suppression by ∇n – Baseline scenario in W7-X
3
NBI
ECRH
ECRH + NBI
ECRH
∇ne (1019 m-4)
∇Ti (keV/m)
∇Te (keV/m)
B. Stefanoska, in preparation
Baseline turbulence suppression scenarios in W7-X are well documented [1,2,3]:
A ∇ne is created by NBI/pellets, suppressing turbulence and increasing tE/tISS04
Then, additional heating can be used to bring up Ti,core, neTitE
With the improved gradients, a strong NC Er appears at the core [4].
Recent studies have shown that this Er plays a further role in turbulence suppression. Effects on transport are currently being analyzed.
[1] S. Bozhenkov, NF 20 [2] D. Carralero PPCF 22 [3] O. Ford NF 24 [4] T. Estrada, NF, 20
This scenario presents two problems for code validation:
It introduces a large variation in density along that of ∇ne
Much higher density than in comparable scenarios in LHD

## Slide 9
  A low density high performance regime in W7-X
4
A dedicated low density HP scenario was developed in the 2024-2025 campaigns:
During a short NBI pulse, ECRH power is halved
Clean wall, no puff lead to strong ne reduction at the edge
A stable ∇ne emerges at the edge, increasing performance
With additional heating, this scenario yields record confinement levels, with tE/tISS04 ~ 1.25
tE/tISS04

## Slide 10
  Low edge density leads to higher performance!
5
While the basic turbulence suppression mechanism is the same, there are some relevant differences with baseline scenarios:
Density gradient appears at the edge, rather than at the mid-radius
As a result, Ti gradient is also radially displaced, leading to higher “HP volume”, thus improving performance
Rho
Rho
Rho
a/Lne, a/LTe, a/LTi

## Slide 11
  Low edge density leads to higher performance!
5
While the basic turbulence suppression mechanism is the same, there are some relevant differences with baseline scenarios:
Density gradient appears at the edge, rather than at the mid-radius
As a result, Ti gradient is also radially displaced, leading to higher “HP volume”, thus improving performance
Same differences can be observed in DR measurements of Er and fluctuations.
Rho
HP phase
HP phase
Kick et al., PPCF 1999
This regime is reminiscent of the “Optimum Confinement” regime in W7-AS, which produced tE/tISS95 ~ 2-2.5, record Ti, neTitE.

## Slide 12
  Transport in the LDHP regime
6
Power balance (electrons+ions)
Power balance was used to calculate transport. Some caveats in order:
No Prad included (see D. Zhang PPCF 23)
No NBI deposition
Only Qe+i is reliable
M. Wappl, PPCF 25
Usual a/Ln effect on core transport!

## Slide 13
  Transport in the LDHP regime
6
Power balance (electrons+ions)
NC transport becomes dominant at mid-radius:
During LDHP, Qturb ~ QNC
During ECRH ramp, Qturb < QNC
Coherent experimental picture, consistent with NC simulations:
Very strong suppression of density fluctuations
Radial position consistent with cturb/cGB
Radial position aligned with maximum Er gradient?
Connection to Adrian, Andreas K-F?
Power balance was used to calculate transport. Some caveats in order:
No Prad included (see D. Zhang PPCF 23)
No NBI deposition
Only Qe+i is reliable

## Slide 14
Introduction
W7-X results
  Baseline density gradient suppression of turbulence
  A low density scenario
  Transport evaluation
LHD results
    LHD experimental scenarios
    Transport evaluation
Multi-machine comparison and preliminary validation results
Summary
Outline

## Slide 15
Two kinds of scenarios were carried out in the 2025 LHD campaign.
Step down scenario:
  Direct repetition of W7-X LDHP, aimed at reproducing original profiles.
  PNB is used to increase a/Ln during ECRH phase.
Power scan scenario:
  Low collisionality to ensure IC stability and ITG-dominated transport.
  Core ∇ne was scanned by means of different ratios of positive and negative NBI.
  LHD experimental scenarios
Step down
Power scan
In LHD, PNB tends to create peaked profiles, while NNB tends to flat ones
ECRH
back to ECRH
ECRH +PNB
NNB
PNB
PNB + NNB
7

## Slide 16
ECRH
NBI+ECRH
back to ECRH
LHD, Step Down
  LHD scenarios – profiles and gradients
LHD/W7-X agreement is remarkable in the Step Down scenario:
Initially, profiles and normalized gradients are almost equal
No transition to LDHP is observed in LHD.
a/Lne, a/LTe, a/LTi
W7-X
ECRH
NBI+ECRH
Early HP
Late HP
ne, Te, Ti
ne, Te, Ti
a/Lne, a/LTe, a/LTi
8

## Slide 17
NNB
PNB+NNB
PNB
Power scan
ne, Te, Ti
a/Lne, a/LTe, a/LTi
ECRH
NBI+ECRH
back to ECRH
Step down
ne, Te, Ti
a/Lne, a/LTe, a/LTi
8
  LHD scenarios – profiles and gradients
The Power Scan scenario introduces lower density discharges:
A similar range of core a/Ln is covered with substantially lower density/collisionality
No transition to LDHP is observed in these discharges either.

## Slide 18
Power Scan
  Transport in LHD scenarios
Transport is evaluated by power balance. Two clearly different trends appear, depending on the scenarios:
In the Step Down scenario (similar to W7-X), a/Ln increases transport and does not improve confinement.
Density (thus collisionality) reduces transport and improves confinement.
In the Power Scan scenario, a/Ln causes a moderate, but clear reduction of transport and confinement improvement.
In this case, density/collisionality have no effect on performance.
IC-like
ITG-like
9
Step down (W7X-like)
At first sight, these results are consistent with previous studies:
T. Kinoshita PRL 2024
IC-like
ITG-like
Low density data are better suited for inter-machine comparison!

## Slide 19
Outline
Introduction
W7-X results
  Baseline density gradient suppression of turbulence
  A low density scenario
  Transport evaluation
LHD results
    LHD experimental scenarios
    Transport evaluation
Multi-machine comparison and preliminary validation results
Summary

## Slide 20
  Multi-machine transport comparison
We recover the main qualitative features of the model for LHD and W7-X:
Transport falls around one order of magnitude within 0 < a/Ln < 2. Same in stella for 0.5 < a/Ln < 2.5
Instead, LHD transport decays around 30% 0.3 < a/Ln < 1. The code shows a similar decay for 0.5 < a/Ln < 2
LHD
W7-X
10
H. Thienpondt et al., NF 2025

## Slide 21
  Preliminary validation attempts
A more quantitative comparison of transport is being developed using interpolation of “academic scans” (see J.M. García-Regaña I07):
Comparison of normalized Qe+i at r = 0.7 produces rather good quantitative agreement with code predictions.
11
stella
Qturb
Qtotal

## Slide 22
  Preliminary validation attempts
11
stella
Qturb
Qtotal
A more quantitative comparison of transport is being developed using interpolation of “academic scans” (see J.M. García-Regaña I07):
Comparison of normalized Qe+i at r = 0.7 produces rather good quantitative agreement with code predictions.
Unfortunately, this result could not be reproduced generally. More detailed analysis is ongoing.

## Slide 23
  Summary and outlook
12
Experimental validation of predictive codes is essential to determine the operation point of a stellarator reactor
We have created a multi-machine transport database allowing:
  Evaluation of the singled-out effect of density gradient
  Comparison of equivalent scenarios in W7-X and LHD
In W7-X, this also also led to a promising low density HP regime, reminiscent of the W7-AS “Optimum confinement“
First results show qualitative agreement with GK predictions in W7-X and LHD.
A quantitative validation of transport predictions is still ongoing:
  Detailed comparison, including additional ingredients (several gradients, Te/Ti, potential influence of radial position, etc.)
  TJ-II results still to be included in the multi-machine database. Experiments in the spring campaign!
  Evaluation of path dependence
W7-X low density HP scenario will be further explored in the next experimental campaigns, with the aim of rising the achieved triple product.