## Slide 1
WP-PWIE SP B kick-off meeting 2026
SP B.1 & 2 - Plans for BiGyM and PWI experiments therein
Andrea Uccello
CNR-ISTP
G. Alberti, A. Cremona, M. De Angeli, D. Dellasega, F. Gaspari,
F. Ghezzi, M. Passoni, M. Pedroni, D. Ripamonti
Beneficiary: ENEA
Linked Third Parties: CNR-ISTP Milano and Politecnico di Milano

## Slide 2: SP B.1 & 2 - Plans for BiGyM and PWI experiments therein
Fiber optics
Beam guide
New plasma sources
New sample exposure system
Picosecond-laser induced
breakdown spectroscopy (ps-LIBS)
Infrared camera
Upgrade of vacuum system:
pumps
pressure gauges
isolation valves
pressure control valves
New CODAS and storage system
New sample exposure system
Birdcage antennas
Ps-LIBS
Helicon wave plasma
 | GyM | BiGyM
ne [m-3] | 1015 – 1017 | 1018 – 1019
Γ [m-2s-1] | 1021 | 1022 – 1023
Sources | 2 magnetrons @2.45 GHz | 2 RF antennas @13.56 MHz
Pin [kW] | 4.5 | 20
τ = 29 ps
Ep,max = 70 mJ
High-resolution monochromator
λ = 200 –1000 nm, Δλ = 0.06 nm
PI-MAX 4 ICCD camera w/ Gen II SR intensifier
Sample temperature
up to 1500 K
First plasma is expected by June 2026. PWI experiments planned for the second half of 2026
SP F.1 2026 - Commissioning on BiGyM and first tests with B-coated samples

## Slide 3: SP B.1 & 2 - Plans for BiGyM and PWI experiments therein
Upgrade Status
  Disassembly of GyM ✔
  Assembly of BiGyM vacuum vessel and repositioning of coils ✔
  Vacuum leak testing of the vessel (down to 1e-7 mbar) ✔
  Installation of sample exposure system on BiGyM support structure ✔
  Installation of pumping lines, including gate valves (safety) and butterfly valves (pressure control) ✔
  System-wide vacuum leak testing
  First plasma (in collaboration with SPC–EPFL): by June 2026
  Characterization of plasma parameters using optical emission spectroscopy and interferometry
  Connection of sample exposure system to BiGyM vacuum vessel: by September 2026
  First SP B.1 BiGyM PMI experiments on W/B reference layers like those exposed in GyM
  D plasma exposure of ns-PLD 100 nm-thick compact B films
  Eion =76 eV according to PSI-2 experiments [M. Sackers, et al., Nucl. Mater. Energy 45 (2025) 102003]
  Φ =4e23 D+m-2 to avoid full layer erosion

## Slide 4: SP B.1 & 2 - Plans for BiGyM and PWI experiments therein
Analysis programme
In-house at CNR-ISTP and PoliMi
  Semi-micro balance  mass loss (sputtering yield)
  AFM, SEM  surface morphology
  XPS, LEIS  surface chemistry
  SIMS, TDS  deuterium retention
EUROfusion partner laboratories
(aiming to follow the same analysis chain as B layers exposed to D plasma of GyM in 2025)
ToF-ERDA, EBS+NRA+PIXE, ToF-MEIS - Uppsala University
SIMS - CIEMAT
Raman and XPS - Aix Marseille Université
Analysis of B layers exposed to D plasma of GyM in 2025
  Completion of the analysis with SEM investigation of surface structure changes
  (in-house or EUROfusion partner laboratories)