## Slide 1: Explaining observed potential and drift phenomena in Wendelstein 7-X with the mean-field Braginskii model
T. Tork1,2, F. Reimold1, D. Bold1, B. Dudson3, A. Stegmeir4, V. Perseo1, D.M. Kriete5, A. Bonciarelli1, C. Killer1, F. Scharmer1, A. von Stechow1, B. Shanahan6, P. Manz2,1 and the W7–X Team
1Max Planck Institute for Plasma Physics, Wendelsteinstr. 1, 17491 Greifswald, Germany
2Institute of Physics, University of Greifswald, 17489 Greifswald, Germany
3Lawrence Livermore National Laboratory, 7000 East Avenue, Livermore CA 94550,USA
4Max Planck Institute for Plasma Physics, Boltzmannstr. 2, 85748 Garching, Germany
5Auburn University, Auburn, Alabama 36849, USA
6Plasma Science and Fusion Center, Massachusetts Institute of Technology, Cambridge, MA, USA
Prepared in part by LLNL under Contract DE-AC52-07NA27344 and supported by the HiFiStell SciDAC.

## Slide 2: Motivation
Divertor heat loads
Drifts are expected to play an elevated role in the SOL of island diverted stellarators
        Increased importance of perpendicular transport [1]
        Experimental observations support the expectations [2-4]
Self-consistent modelling drifts has been absent in 3D mean-field simulations of stellarators
        Challenging to implement in state-of-the-art code, EMC3 [5]
        Self-consistent description of the electrostatic potential needed
[1] Y Feng et al 2011 Plasma Phys. Control. Fusion 53 024009
[2] K C Hammond et al 2019 Plasma Phys. Control. Fusion 61 125001
[3] Carsten Killer et al 2026 Nucl. Fusion 66 056031
[4] D.M. Kriete et al 2023 Nucl. Fusion 63 026022
[5] R. De Wolf et al 2024 Contrib. Plasma Phys. 2024, 64(7-8)
[3]
Langmuir profiles
[4]
Ion flows

## Slide 3: Outline
Simulation setup
Experimental comparison
      Langmuir probe measurements
      Gas puff imaging
      Coherence imaging diagnostics
Physics implications
      ExB fluxes between SOL regions
      Redistribution of trace densities by the ExB vortex

## Slide 4: Simulation setup
does:
Provides e/i-density, e/i-velocities, e/i-pressures and the electrostatic potential
Diamagnetic/ExB drifts
        Impact on profiles
Self-consistent description of the balance of currents
        Evolve vorticity from which we infer the potential
does not:
Neutral physics
        Limits simulations to low densities/powers to stay closer to the experiment
Impurity physics
        No radiation etc.
Turbulence
        Turbulent fluxes are closed by heuristic diffusion coefficients (inputs)
Implemented in BOUT++ [1]
First simulated geometries include simplified island divertors, TCV X-21 and now W7-X
What the simulation
[1] B Dudson et al 2009 Computer Physics Communications 180 (2009) 1467–1480

## Slide 5: Simulation setup
does:
Provides e/i-density, e/i-velocities, e/i-pressures and the electrostatic potential
Diamagnetic/ExB drifts
        Impact on profiles
Self-consistent description of the balance of currents
        Evolve vorticity from which we infer the potential
does not:
Neutral physics
        Limits simulations to low densities/powers to stay closer to the experiment
Impurity physics
        No radiation etc.
Turbulence
        Turbulent fluxes are closed by heuristic diffusion coefficients (inputs)
Implemented in BOUT++ [1]
First simulated geometries include simplified island divertors, TCV X-21 and now W7-X
What the simulation
Carry out W7-X simulations of one module
Standard configuration
Forward and reverse field simulation
[1] B Dudson et al 2009 Computer Physics Communications 180 (2009) 1467–1480

## Slide 6: Electrostatic potential and ExB flows
Electrostatic potential is mostly aligned with LCFS
Maxima close to the separatrix
LCFS

## Slide 7: Electrostatic potential and ExB flows
Electrostatic potential is mostly aligned with LCFS
Maxima close to the separatrix
ExB vortex
    Clockwise in the core, counter-clockwise in the SOL
    in the main SOL mainly poloidal
    Highest (~500 m/s) in regions of densely packed flux surfaces
ExB vortex

## Slide 8: Experimental comparison – Langmuir probes
W7-X provides Langmuir probe measurements of the floating potential and the electron temperature [1]
[1] C. Killer et al 2022 JINST 17 P03018
Plasma potential inferred from temperature and floating potential
Simulation provides plasma potential immediately
[1]

## Slide 9: Experimental comparison – Langmuir probes
W7-X provides Langmuir probe measurements of the floating potential and the electron temperature [1]
[1] C. Killer et al 2022 JINST 17 P03018
Plasma potential inferred from temperature and floating potential
Simulation provides plasma potential immediately
Comparison between simulation and experiment
Simulation and experiment agree within error bars
Finer structure not fully resolved, but overall gradient are mostly recovered
Simulation
LCFS
[1]
20231126.23

## Slide 10: Experimental comparison – Gas puff imaging
[1] J. L. Terry et al, Rev. Sci. Instrum. 95, 093517 (2024)
W7-X provides poloidal velocity estimations based on the gas puff imaging diagnostic [1]
[1]
Velocity estimations based on the movement of brightness fluctuations

## Slide 11: Experimental comparison – Gas puff imaging
LCFS
[1] J. L. Terry et al, Rev. Sci. Instrum. 95, 093517 (2024)
Comparison between simulation and experiment
Dominant upwards velocity recovered
Smaller shear layers are not resolved
GPI velocities generally a factor 2-4 higher
W7-X provides poloidal velocity estimations based on the gas puff imaging diagnostic [1]
[1]
Velocity estimations based on the movement of brightness fluctuations

## Slide 12: Experimental comparison – Coherence imaging spectroscopy
[1] V. Perseo et al 2021 Nucl. Fusion 61 116039
Coherence imaging spectroscopy provides C2+ impurity flow measurements [1]
Implementation of synthetic diagnostic that infers emissivity from local parameters in the simulation
2D image of ion flows
Divertor

## Slide 13: Experimental comparison – Coherence imaging spectroscopy
[3]
[1] V. Perseo et al 2021 Nucl. Fusion 61 116039
[2] D.M. Kriete et al 2023 Nucl. Fusion 63 026022
[3] V. Perseo et al 2022 PSI 2022
Coherence imaging spectroscopy provides C2+ impurity flow measurements [1]
Implementation of synthetic diagnostic that infers emissivity from local parameters in the simulation
2D image of ion flows
Divertor
Starting point
Previous EMC3-EIRENE simulations show strong alignment of stagnation points with X- and O-points [3]
[2]
Previous simplified model predicts movement of stagnation points at O-points due to poloidal drift [2]

## Slide 14: Experimental comparison – Coherence imaging spectroscopy
[1] V. Perseo et al 2021 Nucl. Fusion 61 116039
Coherence imaging spectroscopy provides C2+ impurity flow measurements [1]
Implementation of synthetic diagnostic that infers emissivity from local parameters in the simulation
2D image of ion flows
Divertor
With drifts

## Slide 15: Experimental comparison – Coherence imaging spectroscopy
[1] V. Perseo et al 2021 Nucl. Fusion 61 116039
Comparison between simulation and experiment
Reproduce shift of stagnation points and dominant flow velocity
Due to movement of gradients and poloidal momentum transport
Coherence imaging spectroscopy provides C2+ impurity flow measurements [1]
Implementation of synthetic diagnostic that infers emissivity from local parameters in the simulation
2D image of ion flows
Divertor
With drifts

## Slide 16: Physics implications

## Slide 17: ExB fluxes across SOL region boundaries
V. Perseo, 2025 IAEA TM Divertor
PFR
TSR
Main SOL
ExB drift is suggested to be main driver of asymmetries in the SOL of low density W7-X discharges [1]
Depending on field direction, regions experience different heat loads
Does the simulation see ExB fluxes into the different SOL regions ?
[1] K C Hammond et al 2019 Plasma Phys. Control. Fusion 61 125001
Lower target shadow

## Slide 18: ExB fluxes across SOL region boundaries
Particle fluxes perpendicular to the main SOL contour
PFR fluxes connect different magnetic islands
          2 - 10 ( magnitude in terms of diffusion)
          Similar to the tokamak drift picture [1]
TSR fluxes lead to transport between main SOL
          Depend on field direction
          0.2 - 4 (magnitude in terms of diffusion)
Forward field
Reverse field
Main SOL
PFR
TSR
[1] A.V. Chankin 1997
PFR
TSR

## Slide 19: Redistribution of trace densities by the ExB vortex
Impurity seeding
Islands are topologically separated*
Cross-field transport required to exchange particles
*In standard configuration
Boundary

## Slide 20: Redistribution of trace densities by the ExB vortex
Impurity seeding
Islands are topologically separated*
Cross-field transport required to exchange particles
Diffusion
*In standard configuration
Without drifts
Boundary

## Slide 21: Redistribution of trace densities by the ExB vortex
Impurity seeding
Islands are topologically separated*
Cross-field transport required to exchange particles
ExB
*In standard configuration
Without drifts
With drifts
Boundary

## Slide 22: Redistribution of trace densities by the ExB vortex
Impurity seeding
Islands are topologically separated*
Cross-field transport required to exchange particles
ExB
*In standard configuration
With drifts
Boundary
Drifts facilitate fast poloidal redistribution
No gradients needed
W7-X can detach in all islands even though seeding is happening in just one island [1]
[1] M Krychowiak et al Nuclear Materials and Energy 34, 101363 (2023).

## Slide 23: Summary and Outlook
Summary
Implementation of transport model with drifts and current balance
LCFS aligned potential and ExB vortex structure
Comparison to probe measurements shows agreement of plasma potential within uncertainties
GPI shows poloidal velocities close to LCFS
Synthetic CIS reproduces impact of drifts on the ion flow in the SOL
ExB fluxes between main SOL and PFR/TSR
Capabilities of ExB vortex to redistribute trace densities with fast ExB flows
[1] Threlfall, E. et al. (2023). Software for fusion reactor design: ExCALIBUR project NEPTUNE, 29th IAEA Fusion Energy Conference

## Slide 24: Summary and Outlook
Summary
Implementation of transport model with drifts and current balance
LCFS aligned potential and ExB vortex structure
Comparison to probe measurements shows agreement of plasma potential within uncertainties
GPI shows poloidal velocities close to LCFS
Synthetic CIS reproduces impact of drifts on the ion flow in the SOL
ExB fluxes between main SOL and PFR/TSR
Capabilities of ExB vortex to redistribute trace densities with fast ExB flows
Outlook
Implemented in Hermes-3 now
    https://github.com/boutproject/hermes-3
Neutral physics
    Fluid neutral model
    Kinetic neutrals (VANTAGE framework [1])
Impurity model
    Density, momentum and pressure
  Turbulence
  Fundamental tool to investigate physics in the SOL of island divertors
  Increase predictive capabilities for current and future experiments
[1] Threlfall, E. et al. (2023). Software for fusion reactor design: ExCALIBUR project NEPTUNE, 29th IAEA Fusion Energy Conference

## Slide 25: Appendix

## Slide 26
[1] K C Hammond et al 2019 Plasma Phys. Control. Fusion 61 125001
[1]

## Slide 27: Parallel electric field
Ohm‘s law
Parallel gradients dominate local form
Parallel current is adding constant offsets, especially in the SOL
  Neglecting this leads to deviations of ~5-10 V

## Slide 28: Radial electric field
On closed flux surfaces, the radial electric field follows the ion pressure gradient
In the scrape-off layer, the radial electric field follows the electron temperature gradient

## Slide 29: Simulation results
Without ExB drifts
Trace density diffuses from the right island into the core
From the core, it redistributes to the adjacent islands first
Opposite island experiences isolation from trace density
Still one order of magnitude differences after 10 ms
Atleast 15 ms expected until distribution
With ExB drifts
Counter clockwise distribution of trace density
2 Poloidal turns (~4ms) until full distribution
Overall lower trace densiy in islands
Strong divergences in PFR/TSR can constitute additional sinks (?)
Simplified geometry
4/4 Island chain with island divertor
Seeding begins at the outer island

## Slide 30: Forward and reverse field simulations
Forward
Reverse

## Slide 31
P. Hill et al, CPP Volume 213, April 2017, Pages 9-18
FCI mapping of parallel derivatives

## Slide 32: Curvilinear grids for W7-X

## Slide 33: The mean-field Braginskii model
  Implementation in BOUT++ [1], derivative of Hermes-2 [2] and using FCI [3]
  Starting point: Drift reduced Braginskii model
  2 Key adaptions:
[4] B. Gui et al 2018 Nucl. Fusion 58 026027
[5] N. M. Li et al 2018, Comput. Phys. Comm. 228 (2018)
Diamagnetic
ExB
Parallel current
Parallel flow
Conduction
Sources
Diffusion
Par. gradients
[1] B. Dudson et al, Computer Physics Communications 180 (2009), pp. 1467-1480
[2] P. Huslage et al 2024, Plasma Phys. Control. Fusion 66 015006
[3] Shanahan B W, Hill P and Dudson B D 2016 J. Phys:.Conf. Series 775 012012

## Slide 34: The mean-field Braginskii model
  Implementation in BOUT++ [1], derivative of Hermes-2 [2] and using FCI [3]
  Starting point: Drift reduced Braginskii model
  2 Key adaptions:
  Anomalous transport coefficients
        Turbulence is too expensive
Diamagnetic
ExB
Parallel current
Parallel flow
Conduction
Sources
Diffusion
Par. gradients
[4] B. Gui et al 2018 Nucl. Fusion 58 026027
[5] N. M. Li et al 2018, Comput. Phys. Comm. 228 (2018)
[1] B. Dudson et al, Computer Physics Communications 180 (2009), pp. 1467-1480
[2] P. Huslage et al 2024, Plasma Phys. Control. Fusion 66 015006
[3] Shanahan B W, Hill P and Dudson B D 2016 J. Phys:.Conf. Series 775 012012

## Slide 35: The mean-field Braginskii model
  Implementation in BOUT++ [1], derivative of Hermes-2 [2] and using FCI [3]
  Starting point: Drift reduced Braginskii model
  2 Key adaptions:
  Anomalous transport coefficients
        Turbulence is too expensive
  Elec. Potential not obtained via inversion:
      Inspired by approach already used in BOUT++ [4,5]
      Potential is modelled as diffusion equation:
      Shift convergence of potential to longer time scales
Diamagnetic
ExB
Parallel current
Parallel flow
Conduction
Sources
Diffusion
Par. gradients
[4] B. Gui et al 2018 Nucl. Fusion 58 026027
[5] N. M. Li et al 2018, Comput. Phys. Comm. 228 (2018)
[1] B. Dudson et al, Computer Physics Communications 180 (2009), pp. 1467-1480
[2] P. Huslage et al 2024, Plasma Phys. Control. Fusion 66 015006
[3] Shanahan B W, Hill P and Dudson B D 2016 J. Phys:.Conf. Series 775 012012

## Slide 36: The mean-field Braginskii model
  Implementation in BOUT++ [1], derivative of Hermes-2 [2] and using FCI [3]
  Starting point: Drift reduced Braginskii model
  2 Key adaptions:
  Anomalous transport coefficients
        Turbulence is too expensive
  Elec. Potential not obtained via inversion:
      Inspired by approach already used in BOUT++ [4,5]
      Potential is modelled as diffusion equation:
      Shift convergence of potential to longer time scales
  Simulations reach steady-state and include drift effects
Diamagnetic
ExB
Parallel current
Parallel flow
Conduction
Sources
Diffusion
Par. gradients
[4] B. Gui et al 2018 Nucl. Fusion 58 026027
[5] N. M. Li et al 2018, Comput. Phys. Comm. 228 (2018)
[1] B. Dudson et al, Computer Physics Communications 180 (2009), pp. 1467-1480
[2] P. Huslage et al 2024, Plasma Phys. Control. Fusion 66 015006
[3] Shanahan B W, Hill P and Dudson B D 2016 J. Phys:.Conf. Series 775 012012