## Slide 1: ETS-6: Comparing solvers in the ETS-6
Thomas Jonsson

## Slide 2: Overview
Three solvers used to solver the transport equations in the ETS-6 have been compared:
  solver4 – finite difference solver
  FEM – finite element on Kolmogorov backward equation; numerical derivatives of D.
  FEM2 – finite element on diffusion equation; numerical derivatives avoided
Compare JET #92436 with modified edge profiles; more smooth.
  g2tjohns/jet_reference/92436/849
Times:
  Simulation domain: 49.0 – 49.5 s
  dt = 0.01, 0.05, 0.1
  n_rho = 50, 100, 200, 400

## Slide 3: Four test cases; diffusion and convection
Test1
Test2
Test3
Test4
Diffusion
Diffusion
Diffusion
Diffusion
Convection
Convection
Convection
Convection

## Slide 4: Four test cases; temperature evolution
Test1
Test2
Test3
Test4
49.01: After first step
49.41: End of run
Evolution changes Te by up to ~600 eV

## Slide 5: Test 1, FEM and FEM2 give the same results!
FEM
FEM2
In FEM is correct, then errors in FEM2 are large

## Slide 6: Test2, Progonka4 and SolverFEM converge to the same result
Progonka4 (ref: FEM)
FEM (ref: Progonka4)
Not converging towards solution from Progonka-4, but only ~ 5eV difference!
Smaller error in FEM
CONCLUSION: FEM is more accurate

## Slide 7: Test 2, Errors due to using finite time-step
FEM
(ref. FEM)
Progonka4 (ref. Progonka4)
CONCLUSION: Error due to finite dt are small

## Slide 8: Test 2, FEM and FEM2 are very different!
FEM
FEM2
Diverging!!
CONCLUSION: Suspicious FEM2 results PROPOSE: Check the implementation
In FEM is correct, then errors in FEM2 are large

## Slide 9: Test 3, Smallest error with FEM; different result with FEM2
FEM
FEM2
Progonka4
CONCLUSION: Similar to Test2

## Slide 10: Test 4, Smallest error with FEM; different result with FEM2
FEM
FEM2
Progonka4
CONCLUSION: Similar to Test2

## Slide 11: Conclusions
Compare Progonka4 and FEM:
  FEM has smaller error than Progonka4 (in this parameter range)
  Table show errors at n_rho=100 (independent of dt)
  The errors can be compared with a total change in Te due to evolution ~ 600 eV
Compare FEM2 with FEM:
  Identical for D=1
  For non-uniform D, FEM2 converges to a different results.
 | Error from finite nrho (eV) | Error from finite dt (eV)
FEM | 15 | 4
Progonka4 | 100 | ~4