## Slide 1: Large Scale Validation of TCV discharges
Viacheslav (Slava) BOCHKARV PhD student SPC EPFL viacheslav.bochkarev@epfl.ch
Supervisor: Michele Marin
16/06/2026

## Slide 2: Disclaimer
All presented work was conducted only for Ohmic TCV discharges !

## Slide 3: Overview
run_HFPS_pipeline
Validation and Verification pipeline
Demo: run HFPS  V&V (5 min)
Ohmic TCV discharges validation results
Q&A + how to (install/configure/start using)

## Slide 4
run_HFPS_pipeline
input IDS → HFPS run
TCV shots
65000–65200
(IMAS format)
SCAN & FILTER
Shot Explorer
Time window selection
CONFIGURE
build jetto.jset /.in /.sin
(via jetto-tools)
BC · ne-fb · imp-fb
SUBMIT & TRACK
SLURM
100 jobs / click
HFPS / JINTRAC
runs on efgw
→ sim output IDS
jetto-tools helpers
(version 2.2.0 - old)
NO RESTARTS !
Core functionality
Tested with Jintrac 37.0.0

## Slide 5
vv_pipeline
Sim + Exp IDS → error statistics
Experiment IDS
HFPS input
Simulation IDS
HFPS output
compare()
Calculate errors with weights over ρ, t grids
RMS@ρ
errbars-weighted
…
OUTPUTS
(per comparison)
report.json
report_detail.html
STATISTICS
error metrics across ~100s shots
shot number
Validation = sim vs experiment · Verification = sim vs sim
report_detail.html = detailed profiles + eq comparison
(self-contained – can be downloaded or emailed)
report.json = global comparison metrics over time and rho

## Slide 6: Demonstration
run HFPS pipeline:
Specify the path to your personal imasdb
Choose the shot range
Choose filters you want to apply for the shot/time-window selection
Choose template and sim options
SUBMIT
V&V pipeline:
Specify the path to your sim storage (e.g. jetto/runs)
Choose the shot range / run names
Choose comparison metrics
Run comparison
Comparison report
HFPS output

## Slide 7: TCV validation exercice results: 120 ohmic discharges
Configuration:
Time-evolving plasma state
– 10s of tau_current_diffusion (but Ip flattop only)
Full radius from separatrix to the core
Transport:
  tglfnn + nclass + sawteeth
W/ and w/o impurities
imp vs no_imp: 89172 <= shot <= 89175
98
completed successfully
19
mid-sim
3
Failed mid-simulation 19 · 16% → try restarts?
Failed at first Δt 3 · 2.5%
Completed successfully 98 · 82%

## Slide 8: Future plans
Near term:
Ohmic ramp-up simulations are undergoing
Adopt restart, H&CD, and error indexing from jetto-toolsw
Fix TCV simulations with SANCO+TGLFNN (any ideas?)
Start H&CD runs (ASCOT, TORAY/TORBEAM)
Add templates for H-mode and NT plasma simulations
Later:
Benchmark ASTRA / RAPTOR / TORAX with JINTRAC on 1000 TCV shots
Extend pipeline to other machines: JET, JT60, AUG

## Slide 9: Thank you!
any questions?

## Slide 10: How to
You can run all apps from both
  local browser through ssh
  Or noMachine
Install: clone THIS repo for run_HFPS_pipeline
and THIS repo for V&V pipeline
Specify the path to your personal imasdb
Choose the shot range
Click Scan
Choose filters you want to apply for the shot/time-window selection

## Slide 11: TCV validation exercice results: 120 ohmic discharges
Configuration:
Time-evolving plasma state
From separatrix to the core
No heating (for now)
Transport: tglfnn + nclass(?) + sawteeth
W/ and w/o impurities
imp vs no_imp: 89172 <= shot <= 89175
Success rate:
120 simulations submitted
98 completed succesfully
19 failed mid-simulation (try restarts?)
3 failed at the first dt