## Slide 1
TSVV-H in-person meeting
June 18th 2026
Preliminary integration of SOLPS-NN into JINTRAC: lessons learned and outlook
R.C. van Schaik1, S. Dasbach1, R. Futtersack2, D. vander Mijnsbrugge3, J. Simpson2, L. Zanisi2, S. Wiesen1,4
1 DIFFER - Dutch Institute for Fundamental Energy Research, De Zaale 20, 5612 AJ Eindhoven, The Netherlands
2 UKAEA – United Kingdom Atomic Energy Authority, Culham Campus, Abingdon, Oxfordshire, UK
3 University of Ghent, Sint-Pietersnieuwstraat 33, 9000 Gent, Belgium
4 EUROfusion, Boltzmannstr. 2, Garching 85748, Bavaria, Germany

## Slide 2: Motivation and Introduction
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
K. Krieger et al., Nucl. Fusion 65 (2025)
Optimal tokamak design and operation
Need fast and accurate tools to evaluate machine performance
Core-SOL-Wall Integrated modelling for full picture
Prohibitively expensive to scope large operational space (for optimisation, validation and UQ)
SOL model = bottleneck
Aim: Replace SOL model by fast, accurate surrogate
Proof of concept: Integrate SOLPS-NN (“off-the-shelf”) into JINTRAC (focused primarily on the coupling approach and behaviour)

## Slide 3: Outline
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Introduction to models:
  JINTRAC, SOLPS-NN, core-edge connector model
JINTRAC-SOLPS-NN coupling implementation
  Desired & current implementation, how I use it
JINTRAC-SOLPS-NN investigation
  Objectives, what I learned (summary), example case study
Proof of concept: D puff scan
Summary & next steps

## Slide 4: Outline
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Introduction to models:
  JINTRAC, SOLPS-NN, core-edge connector model
JINTRAC-SOLPS-NN coupling implementation
  Desired & current implementation, how I use it
JINTRAC-SOLPS-NN investigation
  Objectives, what I learned (summary), example case study
Proof of concept: D puff scan
Summary & next steps

## Slide 5: JINTRAC / HFPS
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
JETTO
1.5D core CFD:
ni, Ti, Te ,…
Transport models
Magnetic Equilibrium
Impurities
MHD
Heating and current drive
Fuelling
Plasma performance
Core dynamics
EDGE2D-EIRENE
2D Edge/SOL model
S. Wiesen, IIS Slides (2025)
M. Romanelli et al., Plasma Fusion Res. 9 (2014)
Communication at coupling interface

## Slide 6: JINTRAC-SOLPS-NN
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
JETTO
1.5D core CFD:
ni, Ti, Te ,…
Transport models
Magnetic Equilibrium
Impurities
MHD
Heating and current drive
Fuelling
Plasma performance
Core dynamics
SOLPS-NN
Communication at coupling interface
S. Wiesen, IIS Slides (2025)
M. Romanelli et al., Plasma Fusion Res. 9 (2014)
S. Dasbach, S. Wiesen, Nucl. Mater. Energy 34 (2023)

## Slide 7: What is SOLPS-NN “off-the-shelf”?
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Core input power [10 – 200 MW]
Core D+ Flux [1e19 – 1e24 s-1]
D gas puff rate [1e20 – 1e24 s-1]
N gas puff rate [1e18 – 1e23 s-1]
Density transport coefficient [0.1 – 2.0 m2/s]
Major Radius [1 – 10 m]
Toroidal magnetic field [1 – 10 T]
Heat transport coefficient [0.1 – 2.0 m2/s]
Just a sketch, the true network is much bigger
Fixed JET geometry, size scaled
5756 standard Fluid Neutral SOLPS-ITER simulations (~steady state)
Spatially homogeneous cross-field transp. coeff.
Deuterium + Nitrogen seeding
S. Dasbach, S. Wiesen, Nucl. Mater. Energy 34 (2023)
2D profiles*:
nD+
Ti
Te
nN(L)+
etc…
* Separate NN for each quantity

## Slide 8: SOLPS-NN connector model for core-edge coupling
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Separatrix heat flux [0.1 – 200 MW]
Separatrix D+ Flux [1e19 – 1e25 s-1]
D gas puff rate [1e20 – 1e24 s-1]
N gas puff rate [1e18 – 1e23 s-1]
Density transport coefficient [0.1 – 2.0 m2/s]
Major Radius [1 – 10 m]
Toroidal magnetic field [1 – 10 T]
Heat transport coefficient [0.1 – 2.0 m2/s]
Just a sketch, the true network is much bigger
Quickly created model for testing
Same dataset
core fluxes  separatrix fluxes
Outputs  0D quantities (required for coupling)
NN not optimised
0D quantities: total flux or LCFS volume averaged
Inputs clamped to training range

## Slide 9: Outline
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Introduction to models:
  JINTRAC, SOLPS-NN, core-edge connector model
JINTRAC-SOLPS-NN coupling implementation
  Desired & current implementation, how I use it
JINTRAC-SOLPS-NN investigation
  Objectives, what I learned (summary), example case study
Proof of concept: D puff scan
Summary & next steps

## Slide 10: JINTRAC-SOLPS-NN implementation
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Calling NN file within Fortran: how?  realised with FTorch*
Currently: explicit scheme
Important points for coupling consistency (where?):
Magnetic equilibrium (fixed by SOLPS-NN training set)
Coupling interface: separatrix (JETTO boundary location = chosen SOLPS-NN location)
Torchscript file (.pt)
via JAMS
fixed for one simulation
Full desired implementation
*
*
*
*
*
* Volume averaged
*Atkinson et al., Journal of Open Source Software, 10(107), 7602 (2025)

## Slide 11: JINTRAC-SOLPS-NN implementation
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Calling NN file within Fortran: how?  realised with FTorch*
Currently: explicit scheme
Important points for coupling consistency (where?):
Magnetic equilibrium (fixed by SOLPS-NN training set)
Coupling interface: separatrix (JETTO boundary location = chosen SOLPS-NN location)
Torchscript file (.pt)
via JAMS
fixed for one simulation
Current implementation
*
*
*
*
*
* Volume averaged
This work
*Atkinson et al., Journal of Open Source Software, 10(107), 7602 (2025)

## Slide 12: JINTRAC-SOLPS-NN implementation: How I use it
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
SOL_NN settings:
model: SOLPS-NN
BCs to update: ni, Ti, Te
torchscript file path (where NN lives)
SOLPS-NN user inputs
SOLNN_STARTUP_DELAY_TIME (time after simulation start when SOL surrogate is ‘activated’)
  Gives additional control and sim. time to start up
  JAMS prescribed boundary conditions used before update
Implementation can be found on CCFE GitLab:
JINTRAC repository  branch = rvanschaik/solpsnn_integration
JAMS repository  branch = rvanschaik/solpsnn_integration
submit

## Slide 13: Outline
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Introduction to models:
  JINTRAC, SOLPS-NN, core-edge connector model
JINTRAC-SOLPS-NN coupling implementation
  Desired & current implementation, how I use it
JINTRAC-SOLPS-NN investigation
  Objectives, what I learned (summary), example case study
Proof of concept: D puff scan
Summary & next steps

## Slide 14: JINTRAC-SOLPS-NN investigation: what to learn?
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Know how, where, what? Question remains: when? (every core time step or not?)
Objectives:
Reach consistent/converged state between core and SOL with all three BCs turned on
Understand the behaviour of the coupling scheme depending on which BCs turned on, core time step and BCs update frequency.
Understand the limitations of the scheme for applications and how it can be improved
How will we proceed?:
General summary of what I did/learned
Show what result looks like from one simulation
Dive into specific example case study

## Slide 15: JINTRAC-SOLPS-NN investigation: what I did/learned (summary)
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Journey: (sorry.. lot of text)
Initially focused on reaching consistent state, updating BCs at each core time step with effective iterations (1e-8s core time steps, undamped)
  Coupling in almost all cases fundamentally unstable (BC  flux interplay drives instability)
  In some cases Ti or Te can be stable (depending on core state and NN state)
  ni is most sensitive to instability and never seen stable with this strategy
  Realised this is not a robust approach
Then exploring updating BCs at each core time step with larger time steps (undamped)
  increasing core time step makes coupling more stable (because internal points effectively damp flux response on core side)
  Increasing core time step makes it possible to get Ti or Te stable when turned on individually
  Increasing core time step does not make it possible to get ni stable, and thus also not all three at same time
  Realised I need to drop each core time step update approach as it is not robust
Decouple BCs update from core time step (undamped)
  Realised that this approach is more robust and able to respect assumption of this scheme (more on this later)
  With this strategy it is possible to obtain a consistent converged state for all three BCs, provided that the core has enough time to relax before the next update

## Slide 16: JINTRAC-SOLPS-NN investigation: result example
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
BC updated: Te (@ each core step)
time step: 1e-8s

## Slide 17: JINTRAC-SOLPS-NN investigation: example case study
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Aim: highlight effect of temporal coupling strategy on stability of scheme
Consistent conditions:
Simplified jetto simulation  constant transport coefficients / particle and heat sources and sinks (removed all non-linearities)
Start from same initial profiles (already steady state)
Identical pre-coupling interval: 1ms steps for 1s, same constant BCs
Same perturbation when activating SOLPS-NN (equal NN inputs)
Variations shown:
Δtcore & ΔtSOL_update coupled (Δtcore = ΔtSOL_update )
  ni, Ti, Te  Δt = 1e-8s, 1e-3s
  Ti, Te  Δt = 1e-8s, 1e-3s
Δtcore & ΔtSOL_update decoupled (Δtcore = 1ms)
  ni, Ti, Te  ΔtSOL_update = 1e-2s, 1e-1s, 1s
Δtcore
ΔtSOL_update
Δtcore
ΔtSOL_update
Δtcore
Δtcore
Δtcore
Δtcore

## Slide 18: Example case study: initial conditions
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
NN inputs:
R0 = 3 m
B0 = 2.74 T
Dpuff = 3.4e22 s-1
Npuff = 1.9e20 s-1
Dperp = 0.1 m2 s-1
χperp = ~0.46 m2 s-1
Psep = ~23 MW
ΓD+,sep = ~1.85e21 s-1
Steady state fluxes:

## Slide 19: Δtcore & ΔtSOL_update coupled (Δtcore = ΔtSOL_update )
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
ΔtSOL_update
  ni, Ti, Te  Δt = 1e-8s, 1e-3s
  Ti, Te  Δt = 1e-8s, 1e-3s
Δtcore

## Slide 20: Δtcore & ΔtSOL_update coupled (Δtcore = ΔtSOL_update )
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
  ni, Ti, Te  Δt = 1e-8s, 1e-3s
  Ti, Te  Δt = 1e-8s, 1e-3s
ΔtSOL_update
Δtcore

## Slide 21: Δtcore & ΔtSOL_update coupled (Δtcore = ΔtSOL_update )
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
  ni, Ti, Te  Δt = 1e-8s, 1e-3s
  Ti, Te  Δt = 1e-8s, 1e-3s
ΔtSOL_update
Δtcore

## Slide 22: Δtcore & ΔtSOL_update coupled (Δtcore = ΔtSOL_update )
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
  ni, Ti, Te  Δt = 1e-8s, 1e-3s
  Ti, Te  Δt = 1e-8s, 1e-3s
ΔtSOL_update
Δtcore

## Slide 23: Δtcore & ΔtSOL_update decoupled (Δtcore = 1ms)
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
  ni, Ti, Te  ΔtSOL_update = 1e-2s, 1e-1s, 1s
Δtcore
ΔtSOL_update
Δtcore
Δtcore
Δtcore
Δtcore

## Slide 24: Δtcore & ΔtSOL_update decoupled (Δtcore = 1ms)
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
  ni, Ti, Te  ΔtSOL_update = 1e-2s, 1e-1s, 1s
Δtcore
ΔtSOL_update
Δtcore
Δtcore
Δtcore
Δtcore

## Slide 25: Δtcore & ΔtSOL_update decoupled (Δtcore = 1ms)
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
  ni, Ti, Te  ΔtSOL_update = 1e-2s, 1e-1s, 1s
Δtcore
ΔtSOL_update
Δtcore
Δtcore
Δtcore
Δtcore

## Slide 26: Important note on core-edgeNN coupling
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
If SOL/edge surrogate is steady state  this must be respected physically and numerically
  Dynamic core model   steady state SOL
  Minimum SOL update time should be on the order of SOL equilibration time
  And coupling should be stable (explicit scheme stability might limit update frequency)

## Slide 27: Outline
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Introduction to models:
  JINTRAC, SOLPS-NN, core-edge connector model
JINTRAC-SOLPS-NN coupling implementation
  Desired & current implementation, how I use it
JINTRAC-SOLPS-NN investigation
  Objectives, what I learned (summary), example case study
Proof of concept: D puff scan
Summary & next steps

## Slide 28: Proof of concept: D puff scan
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Fixed core transport and sources
Δtcore=1ms, ΔtSOL_update=1s
NN inputs:
R0 = 3 m
B0 = 2.74 T
Psep = ~23 MW
ΓD+,sep = ~1.85e21 s-1
Npuff = 1e22 s-1
Dperp = 0.1 m2 s-1
χperp = ~0.46 m2 s-1

## Slide 29: Outline
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Introduction to models:
  JINTRAC, SOLPS-NN, core-edge connector model
JINTRAC-SOLPS-NN coupling implementation
  Desired & current implementation, how I use it
JINTRAC-SOLPS-NN investigation
  Objectives, what I learned (summary), example case study
Proof of concept: D puff scan
Summary & next steps

## Slide 30: Summary & next steps
Rick van Schaik – TSVV-H in-person meeting – 18 June 2026
Demonstrated first JINTRAC-SOLPS-NN coupling
Investigated coupling behaviour with three BCs:
  Steady state property of SOLPS-NN and finite core response must be respected (for physical and numerical behaviour)
  Unstable scheme with Δtcore = ΔtSOL_update
  More stable with larger ΔtSOL_update
Demonstrated fast scanning capabilities with example D puff scan
Next steps
Investigate possible improvements to coupling strategy (numerical tricks?)
Implement neutral and impurity communication to core (coupling with Frantic / Sanco?)
Quantify and improve connector NN performance (be open to different ML techniques)
Converge on use cases to challenge, validate and exploit this initial model
Identify and explore methods to expand accuracy and applicability