## Slide 1: ICRF HCD for DEMO: Some information on antenna design
IPP/POLITO: V. Bobkov, H. Faugel, Th. Franke, A. Kostic, D. Milanesio, R. Maggiora, R. Ochoukov, M. Usolceva, W. Tierens, F. Zeus, W. Zhang

## Slide 2: Possible mounting options in relation to area (power capability)
“Poloidally Arranged Halves”:
“Toroidally Arranged Halves”:
“Port plug”:
 Max. size for 9” feeders:
2.16 x 2.12 m (~4.6 m2)
assuming 1.08 wide port
 Max. size for 9” feeders: 1.57 x 2.76 m (~4.3 m2)
assuming 1.08 m port
 Max. size: port limited
1.04 x 2.76 m (~2.9 m2)
assuming 1.08 m port
can port be wider 1.08 m ?
 Largest impact on BB at a fixed area
 Difficult installation with rotation
 Easier to model during optimisation
 Mounting procedure different to ITER
 Some impact on BB
 Mounting procedure as in ITER

## Slide 3: Installation of antenna with toroidally arranged halves into vessel
1) Insert first half deep through port
2) Shift first half to the side
3) Insert second half deep through port (see picture)
4) Shift second half to its end position
5) Shift first half close to the first half and retract to its end position

## Slide 4: Outcome of the optimisation process: still ongoing
TAH antenna mounting procedure:

## Slide 5: Antenna design optimization
 Algorithm: 1) Define geometry and run HFSS calculations
2) Find optimum Pcentral/Pouter for min of E|| near-field at PFCs
3) Compare TL maximum voltages: voltage balance
4) Check k|| spectrum
 First use HFSS code with lossy dielectric for comparative analysis
 RAPLICASOL / TOPICA with DEMO-like (ITER-low) profiles after (on-going)
0
0
p
p
Pcentral
Pouter
 Things to optimize: minimize near fields, minimize TL voltages, balance TL voltages, optimize k|| spectrum (one peak close to 4.5 m-1, avoid k||=0)

## Slide 6: Example: case 10 antenna
Two toroidally arranged halves with maximum width/height:
connection line of halves
2.76 m
1.57 m
Depth reduced from ~0.62 cm to ~0.5 cm
(see explanation later)

## Slide 7
39kV 41kV 41kV 39kV
39kV 41kV 41kV 39kV
Example: case 10 antenna
 Near-fields reduced well
close to Pcentral/Pouter  0.9,
narrow region of decrease

## Slide 8: Example: case 10 antenna
39kV 41kV 41kV 39kV
39kV 41kV 41kV 39kV
 Central septum makes second peak of k|| spectrum significantly stronger
 Near-fields reduced well
close to Pcentral/Pouter  0.9,
narrow region of decrease
Near-fields
Reduced voltage
Voltage balance
k|| spectrum
good
bad

## Slide 9: Further optimized: case 11 antenna
35kV 33kV 33kV 35kV
 Near-fields reduced well
close to Pcentral/Pouter  0.9,
narrow region of decrease

## Slide 10: Further optimized: case 11 antenna
35kV 33kV 33kV 35kV
Near-fields
Reduced voltage
Voltage balance
k|| spectrum
good
bad
 k|| spectrum significantly better than in case 10

## Slide 11: Further optimisation in the future
35kV 33kV 33kV 35kV
case-11:
 Further optimization steps:
comparison between triplets and quadruplets in detailed geometry
using larger depth
for central straps
curvature of return
conductor to match BB banana shape
and toroidal tilting of antenna face
effect of poloidal phasing
 Nevertheless the current state of the TAH antenna should be a good representative for MCNP simulations – further development of antenna design should not affect neutron shielding significantly