## Slide 1: Exploration of optimal breakdown conditions and magnetic configurations for Electron Cyclotron Wall Conditioning scenarios for JT-60SA and ITER
A. Goriaev, J. Buermans, K. Crombé, D. López-Rodríguez
LPP-ERM/KMS
WP PWIE SP F lick-off meeting

## Slide 2: SP F2 D001: Exploration of optimal breakdown conditions and magnetic configurations for Electron Cyclotron Wall Conditioning scenarios for JT-60SA and ITER
Breakdown experiments on TOMAS to complement the TCV experiments and observations on other devices.
  Compare fundamental and second harmonic1
    Fundamental wave is optimal for breakdown, but encounters a density limit, leading to conversions and parametric decay2
    Second harmonic is optimal for increased plasma density, but can cause stray radiation and parametric decay at the start1
  Explore the influence of several parameters on the breakdown time1,2
    Injected power, toroidal/poloidal injection angle, toroidal magnetic field, horizontal/vertical poloidal field, gas pressure and gas species.
  Explore the influence of several parameters on the density build-up1,3
    Injected power, toroidal/poloidal injection angle, toroidal magnetic field, horizontal/vertical poloidal field, gas pressure and gas species.
Paper and presentation (AAPPS-DPP 2026) under preparation:
Exploration of optimal breakdown conditions and magnetic configurations for Electron Cyclotron Wall Conditioning scenarios for JT-60SA
1M. Fukumoto et al, Nucl. Mater. Energy, 2025
2J. Buermans et al, EPS plasma conference, 2024
3J. Buermans et al, EPS plasma conference, 2025
Preliminary results

## Slide 3: Characterization and analysis of H and D mixed wall conditioning plasmas in TOMAS utilizing the improved data analysis methods for TOMAS plasma diagnostics
A. Goriaev, D. López-Rodríguez, K. Crombé, J. Buermans
LPP-ERM/KMS
WP PWIE SP F lick-off meeting

## Slide 4: SP F2 D002: Characterization and analysis of H and D mixed wall conditioning plasmas in TOMAS utilizing the improved data analysis methods for TOMAS plasma diagnostics
Characterization of H+D mixed ICWC plasma at various magnetic field strengths, RF frequencies and power and gas compositions
  Langmuir probes
    Horizontal and vertical scans of electron density, electron temperature and plasma potential
  Time-of-Flight Neutral Particle Analyzer
    Charge exchange neutral ion energy distribution functions -> Average neutral energy and differential flux
  Residual Field Energy Analyzer
    Local ion energy distribution functions -> Average ion energy and ion flux density
  Spectroscopy (see talk of M. Sackers)
    Test of multi-channel high resolution spectrometer in mixed ICWC plasma
Differential flux of neutrals from the ToF-NPA in hydrogen and deuterium at f = 45MHz [D. Lopez-Rodriguez, PhD thesis, submitted]

## Slide 5: SP F2 D002: Characterization and analysis of H and D mixed wall conditioning plasmas in TOMAS utilizing the improved data analysis methods for TOMAS plasma diagnostics
ICWC plasma break-down studies at at various magnetic field strengths, RF frequencies and power and gas compositions
  Langmuir probe scan
    Localization of plasma expansion and density build-up
    Evaluation of break-down time and density build-up time
  Fast cameras
    Localization of plasma expansion and density build-up
    Evaluation of break-down time and density build-up time
    Comparison to Langmuir probe scan
  Determination of the most suitable ICWC break-down scenarios
    Mapping parameter range where ICWC break-down is possible
    Analysis of break-down time dependencies on experimental parameters
Comparison of electron density profiles in hydrogen and
deuterium at matched discharge parameters: B0 = 0.090T,
p = 6 * 10−4 mbar, PRF = 5 kW, and f = 25 MHz

## Slide 6: SP F2 D002: Characterization and analysis of H and D mixed wall conditioning plasmas in TOMAS utilizing the improved data analysis methods for TOMAS plasma diagnostics
Further analysis and extrapolation of ICWC scenarios
  Analysis and comparison with pure H and D plasmas
    Determination of plasma parameters profile dependencies and qualitative trends in isotope mixtures
  Utilizing the mixed ICWC plasma characterization test cases for TOMATOR-1D validation and development of new 3D model
    Support to predict the wave propagation, the per-species power deposition, and the resulting plasma in the low-density, weakly-ionised regime
  Extrapolation to large fusion devices scenarios
    Extension of the available measurements to the low-energy regime relevant for ICWC sample exposure studies
Differential flux of neutrals for ICRF plasmas in TOMAS, Tore Supra and JET, with TOMAS hydrogen and deuterium curves overlaid at PRF = 5 kW, f = 45MHz, B0 = 0.10T. [D. Lopez-Rodriguez, PhD thesis, submitted]