## Slide 1: BEST EUROfusion scientific priorities – proposed high-level priorities
Proposed priorities for BEST (pre-ITER D-T, towards ITER / FoaK / pilot plant)
D-T burning-plasma and alpha / fast-ion physics at Q ≥ 1 –sustainability of the pulses
Power and particle exhaust and PWI in an integrated full-W, neutron, long-pulse environment
Integrated tritium fuel cycle, tritium-inventory control and TBM operation – fr later as sensible topic
Reactor-integrated long-pulse scenarios and real-time control at low torque
added value, strategic interest and complementarity – not “essential for Europe”. Test: each priority is (i) distinctive vs AUG / WEST / TCV / MAST-U / JT-60SA / W7-X in 2028–2034, and (ii) of strategic interest towards ITER or FoaK / pilot plant.
Question of level of Engagement: monitoring to targeted participation?;
Area of diagnostics collaboration
Introduction of EU samples and analysis (?)

## Slide 2: BEST added value – distinctiveness and complementarity
Reactor-relevant research theme | BEST | SA-C | SA-W | AUG | WEST | TCV | MAST | Relevance for ITER / FoaK
D-T burning-plasma / alpha heating |  |  | * |  |  |  |  | High
Power / particle exhaust & PWI (full-W, neutrons) |  |  |  |  |  |  |  | High
Integrated tritium fuel cycle / inventory / TBM |  |  |  |  |  |  |  | High
High-performance long-pulse scenarios (no-ELM) |  |  |  |  |  |  |  | High
Disruption avoidance & runaway-electron control |  |  |  |  |  |  |  | High
Energetic-particle / fast-ion instabilities |  |  |  |  |  |  |  | High
Real-time / AI-ML control & model validation |  |  | ? | Facility review(?) |  |  |  | Medium - High ?
■ distinctive / high added value ■ beneficial / complementary ▨ limited / supporting (dashed) ■ not addressed SA-C / SA-W = JT-60SA carbon / W phase
Read: BEST priority where BEST is green and pull is High (rows 1–3). BEST’s value is timely D-T / nuclear input ahead of ITER D-T (2039); themes 4–6 are led by JT-60SA and the EU fleet.
* Additional ECRH in OP7 to emulate alpha particle physics through e- heating – in addition to the already foreseen 7MW!