## Slide 1: Recent progress on electrons outside the SOL
Indications for in situ flux surface measurements
C. Killer @ TG Scenario, 21.09.2020

## Slide 2: Recap: indications for electron population far outside the SOL
occurring in pure ECRH plasmas with PECRH/ndl > 1 (for PECRH in MW and ndl in 1019m-2)
negative floating potentials seen be probes (where it should be zero, since ni=0)
hot spots on walls, probes, … (at positions that are not expected to receive heat loads)
see also:
  Physics meeting 20.11.2019
  TG scenario 16.03.2020
[video: Aleix Puig Sitjes]
20181002.46

## Slide 3: some progress
identified more possible incidents in badly covered early OP1.2a programs
radiation collapses due to MPM plunges with excess heat loads far outside the expected SOL
over-critical electric field for runaway acceleration can appear transiently at the plasma edge  Pavel Aleynikov

## Slide 4: Video data might provide more insight
New interesting set of programs identified:
  20180801.24-33 (pre-boronization characterization, low density)
negative Vfl outside plasma  indication for electrons

## Slide 5: 20180801.25, video AEQ31

## Slide 6: 20180801.25, video AEQ31 close-up of MPM
sharp, bright stripe
diffuse, dim stripe
“edge of the plasma”

## Slide 7: 20180801.24, video AEQ31 close-up of MPM
sharp, bright stripe
diffuse, dim stripe
“edge of the plasma”

## Slide 8: 20180801.26, video AEQ31 close-up of MPM
sharp, bright stripe
diffuse, dim stripe
“edge of the plasma”

## Slide 9: 20180801.26, video AEQ31 close-up of MPM
sharp, bright stripe
diffuse, dim stripe
“edge of the plasma”
correlation of features to the magnetic topology?
estimation of feature position from
video images
MPM position, probe geometry
R≈6.07m
R≈6.10m
R≈6.17m

## Slide 10: Are the video features seen in the probe data?
on this day: only 2 floating pins worked (issue with MPM interface)
sharp negative spike in Vfl might correlate with sharp stripe

## Slide 11: Position of features in the magnetic topology
5/5 island
enter long Lc region
R=6.07-6.08m
sharp, bright stripe
diffuse, dim stripe
“edge of the plasma”
1
2
3
1
island separatrix R=6.10m
2
10/9 island , R~6.20m (not visible here)
3
this is where we typically see the Te maximum

## Slide 12: tracking the stripe (the presumable 5/5 separatrix)
analyzing the light intensity along this line
px horizontal
light intensity
color code: images of plunge
Ip=0.8kA
peak at 9px
Ip=1.6kA
peak at 8.5px
Ip=2.8kA
peak at 8px
stripe moves radially inwards at ≈ 0.5 px / kA
conversion at MPM in AEQ31: 1px ≈ 2.5mm (no significant projection error since viewing angle onto MPM side is 25°)
this might be an in situ flux surface measurement (!?)
island chain shifts inwards by ≈ 1mm per kA (?)

## Slide 13: Is the power balance affected by electrons?
no significant additional loss channel indicated (within the uncertainties of Prad and Pdiv)

## Slide 14: Similar (and clearer) observations with IPP-FLUC1 in OP1.2a
horizontal px
R≈6.16m
R≈6.10m

## Slide 15: Update: also with IPP-FLUC1
Ipc=-700A
Ipc=0A
stripes move radially out for Ipc=0A
≈4mm for left stripe
≈2.5mm for right stripe
light intensity
light intensity
horizontal px
horizontal px
color code: different images during plunge
R≈6.16m
R≈6.10m

## Slide 16: absolute position determination using probe head features
center screw: typically stripe at dmpm=240mm  R=6.105m at z=-0.153m (Rsep at 6.100m)
top screw: typically stripe at dmpm=230mm  R=6.115m at z=-0.123m (Rsep at 6.108m)
holes for probe head assembly

## Slide 17: Checking plausibility of separatrix shift
field line tracing
separatrix moves outwards (-700A  0A) by 15mm (along MPM path)
experiment
bright stripe moves outwards (-700A  0A) by ≤ 5mm (also indicated by probe head “holes”)
why this mis-match? perhaps bright stripe ≠ separatrix ?

## Slide 18: sanity check, role of connection length
20170927.20
Ipc=0A
20170927.18
Ipc=-700A
why do we see flux surfaces at all, when Lc ≈ 10m ?
stripe position
Lc ≈ 10m
stripe position
Lc ≈ 10m

## Slide 19: configuration space for stripe imprint on probe head
big hot spot
Stripe covers center screw at dmpm=240mm (on average)
screw is at 86mm ahead of R0  Rstripe=6.105m
MPM probe
with stripe
many small hot spots
high mirror configuration
trim coil scan in high mirror configuration (20./26.09.2017 , compass scans)
28 programs with stripe seen on probe
stripe position is identical in all 28 programs  not affected by trim coil setup

## Slide 20: Conclusion
indications for electron population outside the plasma in low density experiments
  potentially harmful for machine safety  impact on scenario development: avoid low density
visible light stripe on MPM probe head, seeming to originate from the plasma
  position and shape of stripe suggest that this might be the 5/5 separatrix  accidental in situ flux surface measurement?
  position of stripe changes with plasma current and Ipc in qualitative agreement with expectations
but:
  electrons on flux surfaces are not really expected there since Lc ≈ 10m,
  no reaction of “flux surface” to trim coil scan
any ideas?

## Slide 21: for reference: orientation of the video image AEQ31

## Slide 22: projection error from viewing geometry
umpm=[ 0.9297 , 0.3683 , -0.005 ]
uaeq31=[ -0.060 , -0.988 , 0.142 ]
estimated conversion px – mm at MPM: 1px=2.5mm
 projection error along MPM plunge ≈1/cos(25°) ≈10%
MPM
PV
AEQ31
top view onto M4
25°

## Slide 23
bad diagnostic coverage for many programs of interest