## Slide 1
Offline tools for IR data analysis
Victor Moncada, Chakib Belafdil, Raphael Mitteau, Léo Dubus
CEA/IRFM/SI²P/GP3
Imaging Meeting - 26/02/2020

## Slide 2: Infrared diagnostic on west and W7-X
Video production for WEST (11 cameras): 350MB/s of plasma
How to process this amount of video data for PWI understanding, Thermal Studies and Machine protection?
Video production for W7-X (OP1.2b, QSV + QRT): ~3GB/s of plasma
Video production for ITER: we don’t want to think about it
► New abnormal hot spot study ( < security threshold)
  1h of expert time
  Full pulse ( > 10 IR views): impossible
LH antenna
A lot of software tools are required, at every level
(Discharge summary, ease Data Mining, Machine Learning algorithms, Data Access optimization,…)

## Slide 3: IR system Dashboard
Step : Simple overview of the last pulses (IR system status, evolution of max T) during experiments
1
If
Else if
Power control
Stop the pulse
WA view
LH view *2
ICRH view *3
Div. View * 4
Disabled for C4
Working on C4:
DWMS

## Slide 4: IR system Dashboard
Available from any web browser - IR system status

## Slide 5: IR system Dashboard
Developped by Leo DUBUS and Chakib BELAFDIL (IRFM)
Based on Dash: Python framework of the Plotly company for building interactive data visualization apps

## Slide 6: Database on plasma scenario
Step : combine IR system Dashboard with Plasma Scenario in a single SQL Data Base
2
Temperature conditions inside ROIs,
Too hot triggers, DWMS feedback
Pulse duration,
Injected power (ICH and LH), plasma current,
Plasma density,
Magnetic configuration,
Pilots comments,
…
Extract meaningful videos/experiments in 1 query using:
Ongoing work for 2020, embbed within Librir (Python access)

## Slide 7: Event database
Step : Narrow a study to specific Thermal Phenomenons only: gather thermal events in an SQL Event Data Base
3
Easy retrieval (get pulses and views for specififc events)
Follow specific events across experiments to check their impact on the components
Extract statistical values (number of occurrences, T evolution)
Provide ground truth to train machine learning algorithms
Thermavip Plugin to access DB from the whole institute
WAQ5B
LH1, LH2
ICR1, ICR2, ICR3
DIVQ1B, DIVQ2B, DIVQ6A, DIVQ6B
Inboard strike point
Outboard strike point
UFO
Reflection
Segmentation artifact
Other-type
Unknown

## Slide 8: Event database
How to feed the Event Data Base ?
Fill from automatic detection algorithms (cf. Chakib BELAFDIL)
Fill with manual annotations from Thermavip

## Slide 9: VIDEO COMPRESSION
Step : Access the real data without re-designing the network infrastructure!
4
Tipical IR video size in C4: ~1GB (10-100s for downloading), more for W7-X!
How to process in parallel dozens of videos: capable video server, reduce video size!
Test of lossless compression algorithms and video codecs:
 | level 1 | level 1 | level 3, coder 2 | preset: slow
 | ZSTD | Blosc+ZSTD | FFV1 | H264
Ratio | 2,55 | 2,92 | 4,24 | 4,4
Speed (fps) | 72 | 77 | 117 | 27
Ratio of 4,4 is good, but can we do better?
Yes, by using lossy compression
H265?
Licencing issues
►Combination of lossless codec (H264) and generated controlled loss ( +-2°C)
►Time trace of each pixel is “flattened” around +-2°C
►No visual loss, 15 < ratio < 20, speed > 25fps

## Slide 10: Video motion correction
Step : Correlate video with the Scene Model: we need motion correction algorithm
5
Efficient subpixel image registration algorithms,
Manuel Guizar-Sicairos et. al
OPTICS LETTERS / Vol. 33, No. 2 / January 15, 2008
Python algorithm based on
2-D rigid translation within a fraction of a pixel using cross correlation and selective upsampling by a matrix-multiply DFT (discrete FT)
Code embedded within Librir, runs at 10fps for 640*512*2 videos

## Slide 11: DSM IRFM Service
Commissariat à l’énergie atomique et aux énergies alternatives
Centre de Cadarache | 13108 Saint Paul Lez Durance Cedex
T. +33 (0)4 42 25 46 59 | F. +33 (0)4 42 25 64 21
  Etablissement public à caractère industriel et commercial | RCS Paris B 775 685 019
THANK YOU!