## Slide 1: New hardware and software for EDICAM
Tamás Szepesi
G. Cseh, G. Kocsis, T. Szabolics,
S. Zoletnik

## Slide 2
T. Szepesi | Image processing meeting | Greifswald | 26.02.2020. | Page 2
Introduction
Why new hardware was needed?
The present hardware is outdated
  PCs are 6-8 years old (used since OP1.0 and before)
  receiver (FPGA) card is 15 years old
Aims with the new hardware
  compatible with present firmware
  significant improvement wrt. the old one
    → capacity for future firmware development
  reasonable cost
  long support (manufacturer)

## Slide 3
T. Szepesi | Image processing meeting | Greifswald | 26.02.2020. | Page 3
New hardware
Intel (Altera) Arria10 GX FPGA card
Most recent FPGA in the Arria series
 | Arria10 GX | Stratix II GX
Price | 4500 EUR | 3500 EUR
Logic Elements | 1,150,000 | 90,960
Adaptive Logic Module | 427,200 | 36,384
new
old

## Slide 4
T. Szepesi | Image processing meeting | Greifswald | 26.02.2020. | Page 4
New hardware
Intel (Altera) Arria10 GX FPGA card
Most recent FPGA in the Arria series
  we can use the old I/O add-on card
  firmware porting is reasonable effort
New PC: CoDaC high performace computer
  10 Gbps and 1 Gbps Ethernet
  fast SSD for data stream
  powerful CPU

## Slide 5
T. Szepesi | Image processing meeting | Greifswald | 26.02.2020. | Page 5
Driver, API, software
Utilizing experience with the existing EDICAM system
Old system: all ROI data is bit-continuous in PC memory
New system: allocated memory is separated for each ROI
  allows more sophisticated streaming and storage
    → writing of small frames (128x64) in batches (e.g. 10 frames)
ROI #1 |  |  |  |  |  |  |  |  |  |  |  |  | 
ROI #2 |  |  |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  |  |  | 
ROI #n |  |  |  |  |  |  |  |  |  |  |  |  | 
0 MB
500 MB
ROI | #1 | #2 | #3 | #2 | #3 | #2 | #3 | #1 |  |  |  |  | 
0 MB
500 MB

## Slide 6
T. Szepesi | Image processing meeting | Greifswald | 26.02.2020. | Page 6
Driver, API, software
Re-writing of control software from scratch
EDIDAQ 2.0 and VIDACS 2.0
  get rid of unhealthy solutions resulting from extensive patching
  optimize code efficiency, better stability

## Slide 7
T. Szepesi | Image processing meeting | Greifswald | 26.02.2020. | Page 7
Driver, API, software
Control, interaction with W7-X
Guideline: everything stays as in OP1.2
  TTE unit: arm, start, stop
  streaming video data real-time to Archive via coda station
    → remove limitations?
      max. 100 fps full frame → increase to 200 (400) fps?
      only 1 stream / camera → increase to 6 streams (smaller)?
  no GeRi
  GenICAM will be considered

## Slide 8
T. Szepesi | Image processing meeting | Greifswald | 26.02.2020. | Page 8
Driver, API, software
Control, interaction with W7-X
Real-time data processing, event detection
  two-level image processing in EDICAM
  integrate into the same system as IR
  BUT: we support ITER-relevant solutions
  major aims
    → hot-spot (PWI) detection
    → plasma size monitoring (detachment)

## Slide 9
T. Szepesi | Image processing meeting | Greifswald | 25.02.2020. | Page 9
Two-level image processing
Possible uses
Hot-spot detection
  need to define the proper algorithm → student topic
    → any ideas (for visible cameras)?
  classification
  two-way communication with other systems
    → ROI start/stop
  UFOs? Moving, appearing, vanishing
Pattern recognition
  plasma radius, even magnetic config!
EJM
FTM

## Slide 10
T. Szepesi | Image processing meeting | Greifswald | 25.02.2020. | Page 10
Two-level image processing
An example: plasma radius
The problem
  3D geometry, camera image = integration along LOSs (pixels)

## Slide 11
T. Szepesi | Image processing meeting | Greifswald | 25.02.2020. | Page 11
Two-level image processing
An example: plasma radius
(A possible) solution of the problem
  generate synthetic images and compare them to measurement

## Slide 12
T. Szepesi | Image processing meeting | Greifswald | 25.02.2020. | Page 12
Two-level image processing
An example: plasma radius
(A possible) solution of the problem
  generate synthetic images and compare them to measurement
  BUT
  → only works for a given magnetic configuration
  → need to generate field line tracing, synthetic images for all configs.
  → this a large database
  → the method is not the fastest ↔ real-time application?
  → the divertor light emission corrupts the algorithm
    still need to find a solution

## Slide 13
T. Szepesi | Image processing meeting | Greifswald | 26.02.2020. | Page 13
Thank you!