## Slide 1
G. Kocsis, Budapest, 20.02.2020
Statistical methods and software for image processing
(for turbulence studies)
G. Kocsis1,
G. Cseh1, M. Lampert1, T. Szepesi1 M. Vécsei1, S. Zoletnik1, L. Zsuga1 and QSV Video Team
1 Center for Energy Research, Budapest, Hungary

## Slide 2
Contents
Plasma visible radiation and video observation
Filaments and cross-correlation images
Quasy-coherent modes and spectrum images
Video data processing in IDL (present solution)
Introduction to Fusion Library of Analysis Programs (FLAP)
Summary
G. Kocsis, Greifswald, 25.02.2020

## Slide 3
Plasma visible radiation and video observation
G. Kocsis, Greifswald, 25.02.2020
Fusion plasma is a volumetric visible light source therefore the reconstruction of the radiation distribution is a challenge if we have limited number of views (which is always the case).
W7-X has a complicated, non axial symmetric 3D magnetic geometry, which makes the reconstruction more difficult.
AEQ30:
EDICAM +
Phantom (MIT)
AEQ31:
EDICAM
AEQ40:
EDICAM
AEQ51:
EDICAM
AEQ50:
EDICAM
AEQ10:
EDICAM
AEQ21:
Photron
AEQ11:
EDICAM
AEQ20:
EDICAM
QSV video diagnostics in OP1:
10 tangential views
8 EDICAMs
400Hz @ 1.3Mpixel
upto 50kHz @ 64x 56 pixels
1 Photron SA5
7.5kHz @ 1Mpixel
upto 1MHz @ 64x64 pixels

## Slide 4
Filaments and cross-correlation images
G. Kocsis, Greifswald, 25.02.2020
filamentary structures, elongated along the magnetic field lines
short lifetime (~100µs), intermittent(?) turbulent eddies
statistical methods needed: cross-correlation or conditional averaging
QSV video diagnostics:
raw movie filtered for low frequencies
(below 1kHz)
Fast framing observation:
20171206.031 2631-2638ms, Hydrogen plasma, EJM-252
45khz, C III filter, divertor radiation

## Slide 5
x pixels
y pixels
x pixels
y pixels
Time axis
x pixels
y pixels
Time lag
Video stream
Cross-correlation
x pixels
y pixels
Correlation calculation
Intensity distribution
at a given time point:
image
Intensity distribution averaged over a time interval:
Long exp. image
Cross-correlation at a
given time lag:
Cross-correlation image
x pixels
y pixels
Reference pixel
G. Kocsis, Greifswald, 25.02.2020
Filaments and cross-correlation images

## Slide 6
2D cross-correlation: example in the divertor region, an 5/5 island magnetic surface is used for selecting the reference signal for cross-correlation calculation
„Open” field lines:
high correlation for several toroidal turns
G. Kocsis, Greifswald, 25.02.2020
Filaments and cross-correlation images
Reference pixel
Magnetic field line started from the reference pixel, a few toroidal turns back and forward

## Slide 7
x pixels
y pixels
x pixels
y pixels
Time axis
x pixels
y pixels
Freq. axis
Video stream
Spectrum
x pixels
y pixels
Fourier transformation
Intensity distribution
at a given time point:
image
Intensity distribution averaged over a time interval:
Long exp. image
Integrated over a
frequency rage:
Band power image
Power at a given
Frequency:
Power image
x pixels
y pixels
x pixels
y pixels
G. Kocsis, Greifswald, 25.02.2020
Quasy-coherent modes and spectrum images

## Slide 8
Quasi-coherent modes and spectrum images
Band power image ([1,2.5]kHz)
In some scenarios a clear quasi-coherent fluctuation is seen at around 1kHz frequency.
Strong light fluctuation ([1.,2.5]kHz) is detected by the camera.
Cross-correlation: no filamentary structure, the radiation fluctuates correlated on almost the whole magnetic surface(?)

## Slide 9
Video data processing in IDL
Data processing: old school style, IDL library
Available functionality:
video data input (HDF5, tif)
magnetic geometry input (pre-calculated for several magn. geometry stored IDL sav files)
Spatial calibration of the different views (linear projection, parameters stored in a database)
Data filtering with various methods, down sampling (binning)
Correlation, conditional averaging calculations
Processed data are stored in IDL sav files
Various plots stored also in pdf (ps) files
Problem: IDL licence, specific, not for general usage
New general solution (not only for video data but also for other type of diagnostics):
G. Kocsis, Greifswald, 25.02.2020

## Slide 10
FLAP:
Fusion Library of Analysis Programs
A program suite for processing large multidimensional datasets
Developer team: Sandor Zoletnik, M. Lampert, Miklós Vécsei, Gábor Cseh
FLAP
G. Kocsis, Greifswald, 25.02.2020

## Slide 11
FLAP features in nutshell
Python 3.7 + numpy + matplotlib
Data input modules: core FLAP and data access methods are separate
All data are in flap.DataObject:
  N dimensional (complex) data + error + coordinates + other data
  Stored in variable or memory storage area
  Save/load to file
Processing: filter, slicing, APSD (Auto Power Spectral Density) , CPSD (Cross Power Spectral
Density) , CCF (Cross-Correlation Function), conditional averaging, ...
flap.DataObject  processing  flap.DataObject
Optimized numpy processing routines operate along 1 (or multiple) dimensions
 processing of many signals in one call
Options configurable for processing methods, data source
Plots for 1D, 2D, 3D data objects, slices of objects
Available on GitHub: https://github.com/fusion-flap
FLAP
G. Kocsis, Greifswald, 25.02.2020

## Slide 12
Available data input modules
testdata: Generates various test signals and image sequences
w7x_abes: W7-X Alkali BES data (locally stored)
mdsplus: General MDS+ module
w7x_mdsplus: MDS+ for W7-X
w7x_webapi: W7-X web database access (experimental)
nstx_mdsplus: NSTX MDS+ access (experimental)
w7x_camera: W7-X EDICAM and Photron camera data (locally stored, HDF5 file)
apdcam: General APDCAM access
FLAP
G. Kocsis, Greifswald, 25.02.2020

## Slide 13
Data processing methods
All processing methods operate on data objects and produce data objects as output.
It is possible to limit processing to intervals:
filter_data: Various scipy filters can be used along one coordinate
detrend: Remove trend with polyfit.
apsd: Auto Power Spectral Density along a coordinate
(e.g. converts Time coordinate to Frequency)
cpsd: Cross Power Spectral Density between all signals in two data objects
(e.g. converts Time coordinate to Frequency)
ccf: Cross Correlation Function between all signals in two data objects
Also multi-dimensional CCF
(e.g. converts Time coordinate to Time lag)
select_intervals: Select intervals in a coordinate either by mouse click or on condition
Output is data object where intervals are described by data and error.
The output data object can be used in slice_data  conditional averaging
arithmetic: +,-,* is implemented between data objects with identical shape and scalars
broadcasting to be implemented soon
FLAP
G. Kocsis, Greifswald, 25.02.2020

## Slide 14
Plotting
flap.plot function implements higher level plots on the basis on Matplotlib:
Handles coordinates, errors, ... automatically
Can plot data vs coordinates, coordinates vs coordinates, constant vs coordinate,
one data object vs another, ....
Handles over plotting: as default prevents over plotting data with incompatible units
(can be overridden)
Plot types as present: xy, multi xy, image, contour, anim-image, anim-contour
Default plots: e.g. 3D data object plotted as anim-...
Multiple part plots. (e.g. complex signal is plot as amplitude/phase or real/imaginary)
Plot ID is returned: possible to over plot to any existing (even multi-part) plot.
FLAP
G. Kocsis, Greifswald, 25.02.2020

## Slide 15
Plotting
‘multi-xy’ plot
‘xy’ plot
‘image’ plot
‘xy’ plot from complex data
FLAP
G. Kocsis, Greifswald, 25.02.2020
‘anim-image’ plot of test video data

## Slide 16
Summary
New solution: FLAP (python)
package has now good functionality
Considered as beta version
Available on GitHub: https://github.com/fusion-flap
flap_tests.py demonstrates possibilities on test data
Users, collaborators are welcome
G. Kocsis, Greifswald, 25.02.2020
Fusion plasma is a volumetric visible light source therefore the reconstruction of the radiation distribution is a challenge if we have limited number of views (which is always the case.
To study turbulence we need statistical analysis and to calculate multi dimensional:
Auto Power Spectral Density
Cross Power Spectral Density
Cross Correlation Function
Conditional Averaging
Old solution: IDL

## Slide 17
Backup slides
G. Kocsis, Greifswald, 25.02.2020

## Slide 18
QSV Video Diagnostics Team
Event Detection Intelligent CAMera
Special 1.3 Mpixel (1280x1024) 12-bit monochrome CMOS camera
  max. frame rate: 400 fps (full frame); 50,000 fps (64x56)
  non-destructive readout → exposure and readout cycles can be decoupled
  magnetic field tolerant (tested upto 3 T and 250 mT/min)
The EDICAM concept: overview diagnostics + event detection + physics investigation
FPGA
cam.head
10 Gbit/s fiber link
Modular design:
camera head + FPGA card
Small
Durable
Image processing
Events
[S. Zoletnik et al, Fus. Eng. Des. 88 (2013) 1405]
QSV Video Diagnostic Team
G. Kocsis, Greifswald, 25.02.2020

## Slide 19
Utilization of multiple ROIs in the non-destructive readout mode
the EDICAM system can handle up to 6 ROIs simultaneously ≡ 6 cameras
time
pixel brightness
expo
reset
NDR readouts
NDR readouts
20171115.039
Helium plasma
Pellet injection
ROI #1: full frame, 100 Hz
Here: still image
ROI #2 and #3:
Small area (160x100), 10 kHz
Pellet penetration is temporally resolved!
Event → only during pellets
Save storage space
Save camera usage
EDICAM application ”science”
G. Kocsis, Greifswald, 25.02.2020

## Slide 20
2D cross-correlation: example in the divertor region, an 5/5 island magnetic surface is used for selecting the reference signal for cross-correlation calculation
„Open” field lines:
high correlation for several toroidal turns
„Connected” field: correlation for one turn
or divertor strikeline
G. Kocsis, Greifswald, 25.02.2020
Filaments and cross-correlation images

## Slide 21
flap.DataObject
All data (experimental, calculated, modeling) are stored in DataObjects
d = flap.DataObject(data=..., error=...)
Data fields:
data: n-dimensional numpy array: integer, float, complex, ...
data_shape: Data array shape (used if no data is present)
error: Optional error values: symmetric (1 array) asymmetric (list of two arrays)
data title: String (e.g. ‘ABES-13’)
data unit: flap.Unit class
name: String (e.g. ‘Signal’)
unit: String (e.g. ‘Volt’)
coordinates: List of flap.Coordinate() objects
Arbitrary number of coordinate values can be assigned to data points:
exp_id: Some kind of experiment ID (shot number, project no..)
data_source: String (e.g. ‘W7X_ABES’)
info: Any other information (Depending on data_source)
history: at present empty for future application
FLAP

## Slide 22
Definitions
Auto-Power Spectral Density (APSD)
Cross-Power Spectral Density (CPSD)
Coherency
signal
Fourier transform
Cross-Covariance
Cross-correlation: normalised cross-covariance