## Slide 1: Towards Plasma Control at W7-X
Long Term Objective and Achievements En Route

## Slide 2: Long Term Objective

## Slide 3: Heat Load Pattern Variation
Heat load limit (MW/m²)
Divertor
Other
Core plasma
High
Edge plasma
Particle exhaust
Power exhaust:
Plasma current evolution varies
Rotational transform and
Radial axis shift …
… and affects the heat load
  Overload
  Impurity release
Divertor heat load (a.u.)
Notes: Plasma parameters are generally dynamic
Iota is a function of the toroidal current which – although small in W7-X can have substantial magnitude due to an establishing plasma current
Additionally the radial position of the magnetic axis is a function of density and temperature which can vary throughout the discharge
These parameters strongly affect the PFC heat load which can lead to excessive heat flux and severe damage to the machine
Their influence is especially large since W7-X is a low shear machine and field line-PFC incident angles are shallow

## Slide 4: Approaching Overloads with Control Theory
Targets
Actuators
Sensors
Core plasma
High
Heating / Current Drive:
ECRH / ECCD
Gas injection:
Fueling
Impurity seeding (N)
Coil System:
Control Coils
Planar Coils (Slow)
Plasma control challenge
“Can we automatically find a trajectory in the operational space of W7-X to ensure the safety of the wall and optimized performance?”
Edge plasma
Particle exhaust
Power exhaust:
Diagnostics:
IR camera system
Magnetic diagnostics
Bolometers
Notes: There are multiple ways to infere with such overloads
The before introduced coils can be used as actuators to counter plasma dynamic
Also manipulaiton of the heating and fueling including current drive can be used
Sensors are potentially any diagnostics
In the language of control theory these can be grouped as Targets, Actuators, and Sensors

## Slide 5: ML in Fusion: Tri-Alpha-Energy & Google
„Optometrist Algorithm“ [Baltz 2017]
  Machine learning tool that aids in optimizing experiment parameters
  Algorithm asks for human advice (Wich discharge is better)
Led to discovery of record confinement regime
  Positive net heating power
  Increased ion temperature and plasma energy

## Slide 6: Semi-Manual Plasma Control/Optimization
Scenario to avoid overload arising from evolution by control coil action [Böckenhoff 2019]
Safe plasma evolution trajectory for ramp up by varying and . [Sinha 2019]
Controlling by ECCD [Turkin 2017]
control with PID feed-back [Krychowiak tbp]
[Böckenhoff 2019]
safe
damage
Local solutions (sensible to variation of orthogonal parameters)
Interdependence with other control targets neglegted
Require ground truth e.g. PID
Notes:   Bilder fehlen
  Emphasis auf dritter Achse erklären
  Bild von sweepspulen
  Formel weglassen
  Scenario für Kontrolle, Bild RL!!!
  This is one instance of rather manual control
  => RL for automation
  Avoiding transient PFC overloads by tuning and
  Baffle and heat shield overload examinations for identifying critical baffle tiles for safety relevant thermo-couple installation ( & FLD + LOWENDEL)
  This is one instance of rather manual control
  => RL for automation
  Avoiding transient PFC overloads by tuning 𝑛 and 𝑃_heat
  Baffle and heat shield overload examinations for identifying critical baffle tiles for safety relevant thermo-couple installation (𝑃_conv & 𝑃_rad FLD + LOWENDEL)

## Slide 7: Choice of Control Method
Plasma physics systems (interplay of environment and actuators) are
  Complex and Chaotic [Escande 2016]
  Non-linear and temporally-varying
  Not Predictable in fine detail e.g.
    Deduction of from first principles
    Perpendicular transport
Interdependent control targets
discharge performance ↔ operation safety
e.g. high neutral pressure ↔ low load on divertor edge
Reinforcement learning (RL) suits well here
[Bucci 2019]
Notes: So which control method should be chosen?
For this we must first characterize our system which is
Chaotic, complex, non-linear and not predictable to the fine detail
As introduced before we have many control targets and some of these targets are interdependent
In this setting reinforcement learning is the right choice.

## Slide 8: Reinforcement Learning
Similar to natural learning behavior
Agent learns to maximize cumulative reward
Major Breakthrough: Deep Q-Network (DQN)
  Approximating by Neural Networks
Short- vs. long-term reward maximization
Impact of new knowledge
state
reward
action
Notes: Reinforcement Learning is a learning scheme which is similar to natural learning behavior
The controller is called agent which is an algorithm which observes the state s_t and learns to choose an action a_t to maximize the cumulative reward r_t
A huge breakthrough was the approximation of the cumulative reward by a recursive update rule
The optimal action given an actual state is then given by the argmax of Q
A problem is now, that the state set is usually not finite and Q which is a table of dimension s cross a becomes infinite and must be approximated by a function
Here the breakthrough was to use NNs which we introduce in the following

## Slide 9: Long Term Objective: Plasma Control with High Level RL
=Low level sensors
Large state-space e.g. pixel / IR-camera
Curse of dimensionality
=High level plasma state
Reduced dimensionality
  Fewer Data required
Lift black box of RL
Robustified RL
Virtual diagnostic
Sensors:
IR camera system
Magnetic diagnostics
Bolometers
…
Actuators:
Coils
ECRH
Fueling (Gas, Pellet)
…
Reward for:
…
First step:
Retrieve reduced state in real time
Notes: Let’s put RL in the context of W7-X
Actuators and Rewards were introduced beforehand
As sensors basically every diagnostic can be added.
However, if you directly use the low level sensor outputs as state description your state-action space becomes very large and your RL Agent will be very data-inefficient.
Because of that I introduce the interpreter which will build a high-level state from the diagnostics input beforehand.

## Slide 10: DQN Success Stories
Super-human Performance in
Atari Games [Mnih 2015]
StarCraft II [Vinyals 2017]
Dota2 [Tobin 2017]
Gaining understanding of a system [Heess 2017]
Possible through
Reinforcement learning
Self-play
Enough computation
Simulation = Real world!
Meta Learning

## Slide 11: Simulation != Experiment
Infrared camera image
Numerical prediction
Compared to the real world, synthetic data is …
  Easy to label
  Less expensive
  Easier to scale
  Not dangerous
  …
Simulation can be qualitatively highly aqurate …
but will mostly qualitatively differ from Experiment
How can we transfer simulation knowledge to the real world?

## Slide 12: How Can We Transfer Simulation Knowledge to Real Data
Use Realistic Simulated Data
  Carefully match the simulation to the world
  Augment simulated data with real data
  Arbitrarily complicated
  Error prown
Domain Confusion [Tzeng 2014]
Domain Randomization

## Slide 13: Manual Domain Randomization (MDR)
If the model sees enough simulated variation, the real world may look like just the next simulator
Example: Real Single-Image Flight Without a Single Real Image [arXiv:1611.04201]
  Quadcopter collision avoidance
  ~ 50% of trajectories are collision-free

## Slide 14: Manual Domain Randomization (MDR)
If the model sees enough simulated variation, the real world may look like just the next simulator
Example: Pose Estimation [Tobin 2017]
Training
Application
Pre-Training is not Necessary

## Slide 15: Automatic Domain Randomization (ADR)
Hypothesis:
  Learning with a sufficiently randomized environment leads to meta-learning, i.e. NN learns to rapidly adapt to actual environment
Workflow:
  NN learns to solve problem at start with nonrandomized environement
  At a performance threshold the amount of domain randomization is increased automatically (Entropy maximization)
  Task becomes harder and NN learns to generalize to more randomized environments
Robust Performance
Parameter reconstruction

## Slide 16: Plasma Control with ADR Requires Simulation Framework
Large amount of simulation data required
Simulation framework
  Very fast codes

## Slide 17: Simulation Framework Sketch
VMEC
Extender
FLT
FLT
DKES
NTSS
EMC3
EIRENE
Timestep

## Slide 18: Accomplishments and Present Work

## Slide 19: Regression with Deep Res-Nets
[Böckenhoff & Blatzheim 2018, 2019]
Adding simulation improves performance despite systematic differences

## Slide 20: Control coil current regression with CNN
CNN
[F. Pisano, B. Cannas, et al., University of Cagliari]
(AEF10)
Shots: 20180815.#
Control coils change island width & phase (also plasma equilibrium effect)
Notes: CNN = Convolutional Neural Network
The CNN takes as input the strike line image (the heatflux image calculated from AEF10 IR camera) and the toroidal current from the Rogowski coils, and makes a regression in order to infer the control coil currents.
On the right side plots, the temporal evolution of the target (in blue) and output (in red) control coil currents superimposed. The six experiments (from OP1.2b), concatenated on the x-axis, are separated by black dashed vertical lines.

## Slide 21: Fast Surrogate: A Supervised Learning Approach
21
MHD Equilibrium Code
Increase run-time from s to s
Enable real-time MHD equilibria
Plasma simulation framework
More adequate state (e.g. )
Integrated data anaylsis
Include equilibrium optimization in robust stellarator optimization
VMEC convergence schemes e.g. adjustment
…
Courtesy Andrea Merlo
Notes: TODO: Add connection slide
21

## Slide 22: Fast Surrogate: Initial Results
22
Even a relatively shallow neural network is able to reproduce features present in the real data.
VMEC Fourier Coefficients
Predicted Fourier Coefficients
VMEC Input features:
Coil currents Array
Pressure profile
Toroidal current profile
VMEC Runtime parameters:
9 poloidal and toroidal modes
20 radial grid points
NN Architecture:
Fully Connected Neural Network (FC-NN)
5 hidden layers with 16 neurons each
R
Courtesy Andrea Merlo
Notes: 22

## Slide 23: Summary
Goal: RL with ADR for (holistic) plasma control
Research questions:
  Is ADR suitable for our problem?
  Can we model the environment W7-X with the main dynamics?
  What states should be used?
  Can control be achieved?
Priority:
  Building framework for speeding up required codes with SL techniques
    VMEC / PIES
    Real-time heat load (Cagliari)
    Field line tracer
    EMC3-EIRENE (?)
    …
    Benefit for the whole project (IDA, Stellarator optimization, …)

## Slide 24: APPENDIX

## Slide 25: Spin-off(s)
20-fold increased simulation speed
(Formalism for) evaluation of PFC integrity
Applied to other analyses already [Sinha 2019, Bonjovi manuscript in preparation]
safe
damage
[Böckenhoff 2019]

## Slide 26: Reconstruction of Proxy for Rotational Transform and Radial Shift
= …

## Slide 27: OP 1.1 Setup

## Slide 28: Data Set(s)
Scan („Config. J“ – Op1.1)
  Sparse Experimental Data:
    Only 6 distinct magnetic configurations
  Same trend but systematic differences in Simulations vs. Experiment
Data Set Size
Infrared
…
4
Synthetic
…
1000
Synthetic
IR
FLD Parameters
Notes: An iota scan was carried out by changing the planar coil current IB.
With 6 different configurations, we got a total of 319 infrared pictures.
Since this is few for the training of a NN, we complement the infrared data set with simulations by field-line-diffusion

## Slide 29: Performance Optimization: Mixing
Optimization:
NN Training Set:
Architecture & Preprocessing:
  Convolutional Neural Network (CNN)
Further techniques tested
  Generative Adversarial Networks
  Transfer Learning
RMSE: 0.007 (~5.4%)
Relative error < 5.4%
[Böckenhoff 2018, Blatzheim 2019]

## Slide 30: OP 1.2 Setup

## Slide 31: NN Input
Divertor mapping
Following physics and engineering constraints
CNN Input
Optimized for MC based simulations
  Factor 20 more training data per time with same statistical significance

## Slide 32: Simulated Data Set
30000 Field Line Diffusion Simulations

## Slide 33: Simulated Data Set

## Slide 34: - Reconstruction
Experiments in NN Depth
and Input Parametrization
Missing (yet):
Application to Experimental Data
[Blatzheim 2019]

## Slide 35: Artificial Neural Networks (NNs)
NN = Mathematical representation of networks of neurons in nervous systems
  Approximation of any continuous function to any degree of accuracy [Cybenko 2003]
Supervised Learning: Split data in 3 sets
  Training ()
    Propagate inputCompare output with target e.g.
    Adjust weights by back-propagation:
  Validation()
    Stop criterion to prevent overfitting
  Test ()
    Evaluate performance
Architecture has impact on abstraction power depth, convolution (CNN), …
epoch
Training
Validation
Test
Training
Validation
Test
Input
Output
Notes: Mathematische Perspektive
The network is built from individual neurons who's individual elements have corresponding counterparts in the biological neurons
  Inputs x (potentials at dendrites)
  Dampened or amplified by individual weights w (length of dendrites)
  Are summed (signal supperposition in the cell body)
  Non-linearly transformed by the activation function (activation potential in the axon)