## Slide 1: Object detection and segmentation
25 February 2020
Chakib BELAFDIL

## Slide 2: definitions
Classification:
Assign only one class label based on the dominant object inside it.
Classification and localization:
Assign only one class label to the object in the image and draw a bounding box around it.
Object detection:
Assign multi bounding box per object instance and classify it.
Instance segmentation:
Assign a class label and an instance for each pixel.
Regular plasma contact
Ion Ripple losses
Outboard strike point
Inboard strike point
Inboard strike point
Outboard strike point
Ion Ripple losses
Regular plasma contact

## Slide 3: The need : detect thermal events
Detect thermal events present in IR films
Ion Ripple losses
Outboard strike point
Inboard strike point
t
t + 1
Localization
Tracking
Classification
ID ThEv | Type | Location | Timestamps | Temperatures | Known
ThEv #1 | Inboard strike point | At location x,y with this contour | From t1 to t2 | Max Mean Etc … | True
ThEv #2 | Reflection | At location x,y with this contour | From t3 to t4 |  | False
Etc…. |  |  |  |  | 
Report file for each target after each pulse.

## Slide 4: A wide variety of thermal events
Many thermal events (ThEv) in the image
Some ThEv close to image maximum intensity, while other important hot spots are just above background level
Some ThEv very large (linear size 1/3 of image, 200 pixels)
Some ThEv have stable position, other moving slowly (moveable probe), some move fast (UFOs = dust, flakes)
ThEv overlap
Textured pattern: the event is the large contour, the smaller hot spots are less relevant
Some ThEv are some very small (3 pixels)
Courtesy of Raphaël MITTEAU

## Slide 5: Image classification
Histogram Equalization
Rolling ball algorithm
Blurring
Texture : Haralick, LBP
High-Level : SIFT, HOG, BoVW
kNN, SVM, Decision Trees, etc.
Image classification :
Classify an image based on the dominant object inside it

## Slide 6: Image classification
Convolutional Neural Network (CNN)
Image classification :
Classify an image based on the dominant object inside it

## Slide 7: CNN
Kernels

## Slide 8: Object detection : traditional approach
Sliding window
Thresholding
Selective search
Image classification
A new Feedback-Based Method for Parameter Adaptation in Image Processing Routines

## Slide 9: Object detection: traditional approach
IR Data Preparation
Segmentation: Sauvola algorithm
Window size = 17
k = 0.13
Region labeling :
Min Area: 9 pixels
Label connectivity: 8
Tracking :
Max distance : 20 pixels
Min Overlap: 30%
Feature extraction
Temperature : Max
Form criterion : Elongation, Area
Localization : X, Y
Duration: Δt
Prediction
Feature extraction
IR Data preparation
WIDE ANGLE
ML Model
Machine Learning Model:
SVM One-vs-Rest with RBF-kernel
C = 10, =
Feature scaling
No validation set (small dataset)
Cross-validation with a stratified 3-fold
Improvement needed for the segmentation step
J. Sauvola and M. Pietikainen, “Adaptive document image binarization,” Pattern Recognition 33(2), pp. 225-236, 2000. DOI:10.1016/S0031-3203(99)00055-2
Notes: 179 samples from 4 labels (after data cleaning)
Gathered from the 20 most energetic and powerful pulses

## Slide 10: Object detection: DEEP LEARNING approach
Selective search
CNN
SVM
R. Girshick and al. Rich feature hierarchies for accurate object detection and semantic segmentation. Technical Report, UC Berkeley, 2014.
R-CNN: Regions with CNN features

## Slide 11: Object detection: DEEP LEARNING approach
Fast R-CNN
Selective search
CNN
FC layers
R. Girshick. Fast R-CNN. Microsoft Research, 2015.

## Slide 12: Object detection: DEEP LEARNING approach
CNN
FC layers
S. Ren and al. Faster R-CNN: Towards Real-Time Object Detection with Region Proposal Networks. 2016.
RPN
Faster R-CNN

## Slide 13: Instance segmentation APPROACH
K. He and al. Faster R-CNN: Towards Real-Time Object Detection with Region Proposal Networks. Facebook AI, 2018.
Mask R-CNN: extending Faster R-CNN from Object Detection to Instance Segmentation

## Slide 14: Instance segmentation APPROACH FOR WEST
Subset | Train | Validation | Test
#images | 11366 | 4112 | 3740
Target : DIVQ2B
# Pulses: 60 most energetic and powerful pulses
Classes: Outboard strike point and Inboard strike point
1st step: Build an annotated dataset

## Slide 15: Instance segmentation APPROACH FOR WEST
2nd step: Train the model
Code: https://github.com/matterport/Mask_RCNN
Hardware :
Training schedule: Transfer Learning on ResNet50 pre-trained on MS COCO with 40 epochs (20 epochs for head layers + 20 for all layers)
Device/Cluster | CPU/GPU | Duration per image | Total duration per test (~15k images, 40 epochs)
i7-6700K | CPU | ~10s | > 2 months
Talitha – 4 x Intel(R) Xeon(R) Gold 5122 CPU @ 3.60GHz | CPU | ~2.8s | ~20 days
Quadro K6000 | GPU | ~1.4s | >9 days
GTX 1060 | GPU | ~800ms | > 5 days
RTX 2080 Ti | GPU | ~230ms | < 2 days

## Slide 16: Instance segmentation APPROACH FOR WEST
3rd step: Monitor learning and check performance

## Slide 17: Instance segmentation APPROACH FOR WEST
3rd step: Monitor learning and check performance
Prediction time: ~200ms w/ RTX 2080Ti
For a 1 minute IR film, it would take roughly 10 minutes.

## Slide 18: What’s next
From inter-pulse to RT prediction
Source: https://www.nvidia.com/en-gb/about-nvidia/ai-computing/

## Slide 19: What’s next
Ontology
Only raw image data used
Inboard strike point
Outboard strike point
UFO
Reflection
Other-type
Unknown
Temporal properties are not used:
Mask R-CNN with one label and class
U-Net
O. Ronneberger and al. U-Net: Convolutional Networks for Biomedical Image Segmentation, University of Freiburg, 2015.

## Slide 20: DSM IRFM Service
Commissariat à l’énergie atomique et aux énergies alternatives
Centre de Cadarache | 13108 Saint Paul Lez Durance Cedex
T. +33 (0)4 42 25 46 59 | F. +33 (0)4 42 25 64 21
  Etablissement public à caractère industriel et commercial | RCS Paris B 775 685 019